## Slide 1: VLSI testing
Test data compression
HEP
Notes: The amount of data required to test integrated circuits is growing rapidly in each new generation of technology. Increasing integration density results in larger designs with more scan cells and more faults. Moreover, achieving high test quality in ever smaller geometries requires more test patterns targeting delays and other models beyond stuck-at faults. Conventional external testing involves storing all test vectors and test responses on an external tester. But these testers have limited speed, memory, and I/O channels. The test data bandwidth between the tester and the chip is relatively small; in fact, it is often the bottleneck determining how fast you can test a chip. Testing cannot proceed any faster than the amount of time required to transfer the test data.

## Slide 2: Volume of test data
Technology nodes
Impact of gate count and increased pattern count
  stuck-at – 1x
  multiple detects – 2x
  transition – 3-5x
  bridging – 2-5x
  small delay – 5-10x
Chart: 
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0
Gate count | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
Volume | 1 | 2 | 8 | 16 | 64 | 128 | 512 | 1024
Approximately 1 KB test data per gate
For 5M gates: 4.77 GB test data
Moore’s law
Notes: As designs grow in size, it also becomes increasingly expensive to maintain a high level of test coverage. This is due to a prohibitively large volume of test data (it grows faster than indicated by the Moore’s law, especially for more advanced fault models) that must be stored in the testing equipment, an increasingly long test application time, and a very high and continually increasing logic-to-pin ratio creating a test data transfer bottleneck at the chip pins. Accordingly, the overall efficiency of any testing scheme strongly depends on a method employed to reduce the amount of test data.

## Slide 3: Test interface bottlenecks
ATE stimuli
ATE reference
The same width and frequency
Mirror images: ATE and scan
Test time: 2 – 10 ¢/s
Notes: DFT based on scan and ATPG has been adopted as a reliable and broadly acceptable methodology that provides very high test coverage. The process of scan insertion and test generation is automated and guarantees very high predictability and quality of results. Conventional ATPG systems can generate test sets that guarantee almost complete fault coverage of several types of fault models. Typically, when an ATPG targets a fault, only a small number of scan cells get specified. The remaining positions are filled with random values. Such a fully specified pattern is more likely to detect additional faults, and can be stored on a tester. As a result of random fill, however, the test patterns are grossly over specified. For large circuits, the growing test data volume causes a significant increase in test cost because of much longer test time and elevated tester memory requirements. For a scan-based test, the test data volume can be approximately expressed as follows:
Test Data Volume  Scan Cells  Scan Patterns
Assuming balanced scan chains, a relationship between test time and the volume of test data is then given by the following equation:
Test time  Test Data Volume / Scan Chains  Frequency

## Slide 4: Motivation
31250 cells per scan
10K scan patterns
312M cycles
20MHz shift frequency
Scan test time: R × 15.6s
10M gates
500K scan cells
16 scan chains
R – the number of repeats for different voltages
Notes: Consider an example circuit consisting of 10M gates and 16 scan chains. Typically, the number of scan cells is proportional to the design size. Thus, assuming one scan cell per 20 gates, the total test time to apply 10,000 scan patterns at a 20 MHz scan-shift frequency will take roughly 312 millions test cycles or equivalently 15.6 seconds. In fact, one may need a minute to deliver all vectors assuming that the whole test is repeated four times for different voltage levels. In many cases, this test application time may not be acceptable (see the previous slide – such a test might cost up to $6.00 per chip). Notice that the resultant test time is primarily determined by limited capabilities of a test equipment (here 16 input channels) that enforce very long scan chains.

## Slide 5: ATPG process
Key observation: fraction of specified bits (scan cells) is very low, typically 0.2% – 5%
1. Target faults
2. Generate test cube
3. Random fill
4. Stimuli on ATE
5. Response on ATE
Notes: The slides illustrates a typical ATPG flow as presented earlier. Many test data compression schemes rest on the fact that deterministic test vectors have typically only between 1 to 5 percent of bits specified. In fact, very often the average number of specified bits is well below 1 percent. The remaining bits are randomly filled with 0s and 1s. The test vectors with partially specified bit positions are defined as test cubes. These test cubes are compressed so that the volume of test data stored on the tester is significantly reduced. The fewer the number of specified bits, the better the ability to encode the information into a compressed form. This ability is exploited by having a number of inputs driving the circuit, whereas the actual circuit has its memory elements configured into a relatively large number of short scan chains. Consequently, a tester that has a few scan channels and a small memory for storing test data could still drive a fairly large circuit.

## Slide 6: Stimuli replication
Test (ATE)
Broadcast scan1
Illinois scan2
Compactor
1) K.-J. Lee et al., ICCAD’98; 2) I. Hamzaoglu, J. Patel, FTCS’99
Notes: The idea is to broadcast the same value to multiple scan chains (a single tester channel drives multiple scan chains). The advantage of broadcast scan is that it is easy to incorporate the decompressor-imposed constraints during ATPG to exploit this degree of freedom. For example, one can tie dependent inputs together in the circuit description given to the ATPG so that the ATPG will produce only test cubes that can be encoded. Using broadcast scan for multiple scan chains might result in reduced fault coverage because some scan cells always hold identical values. To address this shortcoming, a parallel/serial scan architecture, known as Illinois scan, has two modes of operation:
broadcast, which broadcasts one tester channel to multiple scan chains, and
serial, which loads the scan chains serially (scan chains form a daisy chain).
For faults undetectable in broadcast mode, testing can use the serial mode. For multiple tester channels, Illinois scan broadcasts each tester channel to a subset of the scan chains.

## Slide 7: Stimuli conversion
Test (ATE)
Faster ATE
Shorter test application time
Compactor
1) H. Vranken et al., ITC’01
Notes: The stimuli conversion loads the internal scan chains by using serial/parallel conversion of the test data in the boundary-scan chain. The boundary-scan chain is divided into a number of segments driven by a dedicated control scheme. Test stimuli are loaded serially from the tester into the boundary-scan chain segments via the TDI and scan-in pins. Whenever the boundary-scan chain is completely loaded, the data is copied in parallel from the boundary-scan chain into the internal scan chains. This is repeated until the internal scan chains are completely loaded. A similar technique can be used for downloading of test responses.
The maximum length of the segments in the boundary-scan chain is primarily determined by the ratio of the tester frequency and the internal scan shift frequency. If the loading of segments in the boundary-scan chain is performed at 50 MHz, while the internal scan frequency is 10 MHz, a segment can contain up to 5 cells of the boundary-scan chain, and thus 5 internal scan chains can be loaded in parallel from such a segment. The test application time in this case is similar to the test application time of a traditional test in which all pins are contacted by the tester, and the tester frequency and the internal scan test frequency are both 10 MHz.

## Slide 8: Scan chain concealment
Test (ATE)
Compactor
X
O
R
I. Bayraktaroglu, A. Orailoglu, DAC’01
Notes: A linear function of some of the tester channels drives each scan chain. This approach uses simpler hardware and control logic than techniques based on sequential linear decompressors (see the next slides). The drawback is that combinational linear decompressors must encode each scan slice using only free variables shifted in from the tester in a single clock cycle. The number of such variables is clearly equal to the number of tester channels. In this approach, highly specified scan slices tend to limit the amount of achievable compression because the number of tester channels must be sufficiently large to encode the most highly specified scan slices.

## Slide 9: XOR encoding
a
b
c
d
e
a + b + c = 0
a + d + e = 1
b + c + d = 1
a = 1, d = 0 b = 1, e = 0 c = 0
x
1
x
x
1
x
0
a + d + e
a + b + e
a + b + c
b + c + d
c + d + e
a + b + d
b + d + e
+
+
+
+
+
+
+
0
1
0
0
Notes: The XOR encoding utilizes a mapping function, where only a specific number of input signals are XOR-ed together to generate the decompressed outputs. In general, the decompressor can be any linear mapping from N inputs to M outputs. Typically, an XOR network is employed, in which every output is generated by XOR-ing 3 inputs. In order to reduce the probability of linear dependencies, any two outputs share at most one input in their representation. For each test pattern, a number of linear equations per shift are solved in order to represent test data with unspecified bits as an N-bit “seed”, one per each scan shift (on the slide N = 5, M = 7). The compression of the scheme mainly depends on the attainable M/N ratio.

## Slide 10: Combinational compression
Decompressor implemented by combinational, typically linear, logic
Test data provided in a given cycle to encode specified bits only during the same cycle
Relatively low compression rates (many input channels)
Simple integration with ATPG (easy to determine implied values)
Notes: It is worth noting that the combinational compression is relatively easy to integrate with ATPG as the impact of successive seed variables is confined to single clock cycles. It allows test generation programs to easily determine scan cells whose values are already implied by solving equations corresponding to another scan cells of the same time frame (scan slice). Also, there are methods for improving the encoding efficiency of combinational linear decompressors by dynamically adjusting the number of scan chains loaded in each clock cycle.

## Slide 11: Limited sequential expansion
A. Dutta, N.A. Touba, ITC’06
Test (ATE)
Compactor
X
O
R
Notes: This is a hybrid solution that combines a combinational compression with a limited buffering of seed variables. If data arriving from the tester in each clock cycle are defined as a “tester slice”, then one way to perform decompression is to store the last tester slice in a register while still using XOR gates to drive each scan chain. The inputs to these XOR gates can be driven by either the current tester slice or a previous tester slice stored in a register. It offers two benefits. One is that free-variables across 2 (or more if needed) tester slices are used to encode each scan slice. By having access to a larger pool of free variables one can handle more efficiently an occasional heavily specified bit slice. The second benefit is that a larger number of unique free variable combinations can be used to drive the scan chains each clock cycle.

## Slide 12: Stimuli encoding
Static LFSR reseeding
Test (ATE)
Compactor
L
F
S
R
B. Koenemann, ETC’91
N.A. Touba, Compression survey, IEEE D&T’06
Notes: The stimuli encoding belongs to the class of sequential compression schemes. It computes an LFSR seed (its initial state) for each test cube – see the next slide. The LFSR, after loading the seed, runs in autonomous mode and produces a test pattern in scan chains. The technique achieves compression by storing only seeds instead of the entire test patterns. The tester remains idle while the LFSR is running in autonomous mode – it is regarded a drawback of the scheme. Therefore, one can use a shadow register for the LFSR to hold the data coming from the tester while the LFSR is running. Moreover, the LFSR must be at least as large as the number of specified bits in the test cube. One way around this is to only decompress a limited number of scan slices per seed.

## Slide 13: Reseeding of LFSR
a + d
a + c + d
a + b + c + d
b + c + d = 1
a + b + c
b + d
a + c
a + b + d = 0
c + d
b + c
a + b = 1
d
c
b
a
d
c
b
a
a + b = 1
a + b + d = 0
b + c + d = 1
a = 1 b = 0
c = 0
d = 1
Notes: The compression of a test cube is performed by treating LFSR seed bits as Boolean variables. All scan cells are conceptually filled with symbolic expressions that are linear functions of these variables. Given a feedback polynomial, one can obtain a set of linear equations corresponding to scan cells whose values are specified (such scan cells are denoted by red dots in our example). Subsequently, a compressed test pattern (represented by the seed variables) is determined by solving a system of linear equations. If the LFSR is then initialized with these seed variables, all ATPG-specified bits will match. Other (unspecified) bits will be set to pseudorandom values based on the LFSR architecture.

## Slide 14: Static reseeding
LFSR
Phase shifter
Linear expressions
a
a + e
a + c + d
c + d
a + d
a + b + e
a + b + c + d + e
a
b
c
d
e
f
Notes: Consider a decompressor as shown on the slide. The decompressor consists of a 6-bit LFSR implementing primitive polynomial x6 + x + 1 and the corresponding 8-output phase shifter. The phase shifter is comprised of XOR gates connected as shown. The input variables a, b, c, d, e, and f are uploaded at the beginning of a test.

## Slide 15: Reseeding - example
Scan 4
Scan 1
Scan 3
a
a + f
a + e + f
a + d + e + f
a + c + d + e + f
a + b + c + d + e + f
b + c + d + e + f
a + b + c + d + e
b + c
a + b
f
e
d
c
b
a
d + f
c + e
b + d
a + c
a + b + f
e + f
d + e
c + d
a + d + f
a + c + e + f
a + b + d + e + f
c + d + e + f
b + c + d + e
a + b + c + d
b + c + f
a + b + e
a + c + f
a + b + e + f
d + e + f
c + d + e
b + c + d
a + b + c
b + f
a + e
b + c + d + f
a + b + c + e
b + d + f
a + c + e
a + b + d + f
c + e + f
b + d + e
a + c + d
b + c + e + f
a + b + d + e
c + d + f
b + c + e
a + b + d
c + f
b + e
a + d
a + b + c + f
b + e + f
a + d + e
a + c + d + f
a + b + c + e + f
b + d + e + f
a + c + d + e
a + b + c + d + f
Scan 6
Scan 5
Scan 0
1
Scan 7
Scan 2
0
1
0
1
0
Notes: Continuous operation of the decompressor yields linear expressions that fill successive cells of 8 scan chains as shown on the slide for 8 clock cycles. Once the expressions are determined, a system of linear equations is formed for a test cube. These equations are obtained by selecting expressions corresponding to specified positions in the test cube (marked with the red color) and assigning values to them. Suppose the decompressor needs to generate a test pattern based on the following test cube (scan shifting is from left to right):
x x 1 x x x x x
x x x x x x 0 x
x x x x x x x x
x x x x x 1 x x
x x x x x x x x
x x x x x x x x
x x x x 0 x x x
x x x 1 x 0 x x
where x denotes a “don’t care” condition. The corresponding compressed pattern can be determined by solving the following system of equations:
a + e + f = 1
b + c + f = 0
c = 1
a + b + d + f = 0
c + d + e = 1
a + b + c = 0

## Slide 16: Solving linear equations
c = 1
b + c + f = 0
a + b + c = 0
c + d + e = 1
a + b + d + f = 0
a + e + f = 1
c = 1
b + f = 1
a + b = 1
d + e = 0
a + b + d + f = 0
a + e + f = 1
c = 1
b + f = 1
a + f = 0
d + e = 0
a + d = 1
a + e + f = 1
c = 1
b + f = 1
a + f = 0
d + e = 0
d + f = 1
e = 1
c = 1
b + f = 1
a + f = 0
d + e = 0
e + f = 1
e = 1
c = 1
b + f = 1
a + f = 0
d + f = 1
e + f = 1
f = 0
Notes: It can be verified (for example, by using the Gauss-Jordan elimination technique as above) that variables a, b, c, d, e, and f are equal to 0, 1, 1, 1, 1, 0, respectively. This data will subsequently produce a fully specified test pattern having the form shown on the next slide.

## Slide 17: Solution - seed
a
a + f
a + e + f
a + d + e + f
a + c + d + e + f
a + b + c + d + e + f
b + c + d + e + f
a + b + c + d + e
a
0
b
1
c
1
d
1
e
1
f
0
1
1
1
1
0
0
0
0
1
1
1
1
1
0
0
0
1
1
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
0
0
0
0
1
1
1
1
1
0
0
0
1
0
0
1
1
1
1
0
1
1
0
0
0
0
0
0
Phase shifter
Notes: After uploading the initial value (a seed) to the LFSR in the form of 011110, the LFSR will produce a test pattern that matches all desired specified values while producing a random fill on the remaining positions (the random fill is determined by the LFSR feedback polynomial and the phase shifter). The equations on the left hand side correspond to scan cells of the first scan chain.

## Slide 18: Observations
For n-bit LFSR there are
  n variables
  at most n linearly independent equations
The number of encoded positions in scan chains does not exceed the LFSR size
Example:
  10M gate design
  500K flip-flop design
  2% fill rate
  10,000-bit test cube
  combined required LFSR: >10,000 bits
Notes: As mentioned earlier, the encoding capability of the LFSR reseeding is limited by the LFSR size. Usually, because of linear dependencies, large LFSRs are required, incurring a significant area overhead. Another drawback is that the loading of the seed and loading/unloading of the scan chains are done in two separate non-overlapping phases, resulting in inefficient utilization of the tester. This can be alleviated by employing shadow registers. Unfortunately, such an approach doubles the number of required memory elements. Finally, as the number of specified bits may vary significantly in successive test cubes, one has to employ an LFSR with a size matching the highest fill rate among all test patterns. There are several techniques proposed to improve the encoding capability of the conventional reseeding scheme.

## Slide 19: Multiple polynomial reseeding
Encoding may not be possible due to linear dependencies
For s specified bits, an LFSR of size s + 20 guarantees the probability of encoding failure below 10-6
Using multiple polynomials reduces the LFSR size
Polynomial decoder
S. Hellebrand et al., IEEE Trans. Computers, 1995
Notes: It was estimated, based on the analysis of linear dependencies in LFSR sequences, that the LFSR should have the length of s + 20 bits in order to reduce the probability of not finding a seed for a test cube with s specified bits to less than 10-6. Another encoding scheme is based on reseeding of multiple-polynomial LFSR’s (MPLFSR). Since an MPLFSR can operate according to one out of many primitive polynomials, a linear dependency existing between test cube positions for one polynomial may be overcome by another polynomial. A test cube is encoded as the polynomial identifier and the initial seed. It can be shown that with 16 polynomials, which require only 4 + s bits to encode a selected polynomial and the actual test cube, this scheme achieves the same probability of successful encoding as an s + 19 bit single-polynomial LFSR. Encoding a given test cube in an MPLFSR involves solving systems of linear equations for successive polynomials. Despite several polynomials, the process terminates when the first encoding is found. It was shown that the average number of polynomials that are analyzed is less than 2.

## Slide 20: Dynamic reseeding
Test (ATE)
  Reduce
    the number of tester channels
    volume of test data, test time, and memory
    dependence on tester frequency and precision
  SmartBIST1
  Embedded Deterministic Test2
Compactor
L
F
S
R
1) B. Koenemann et al., ATS’01 2) J. Rajski et al., ITC’02
Notes: Dynamic reseeding injects, in a continuous flow mode, free variables from the tester into an LFSR as it loads the scan chains. As a result, the tester is always shifting in data as fast as it can and is never idle. Furthermore, we can use a relatively small LFSR. The embedded deterministic test (EDT), introduced by Mentor Graphics Corporation, belongs to this class of compression schemes. It has been shown to achieve one order of magnitude compression consistently, and up to two orders of magnitude compression for some designs. EDT is widely applicable and easy to deploy because it is based on the standard scan/ATPG methodology and adopts a very simple flow that adheres closely to the conventional ATPG flow. EDT guarantees high test quality as it is possible to target any fault model, such as stuck-at, transition, path delay, multiple detects, etc., that are handled by ATPG tools. The methodology allows the generation of a compressed set of test patterns for these fault models that would provide similar test coverage when compared to any deterministic method.

## Slide 21: EDT architecture
Control
PLL
ATE
Compressed stimuli
Compacted responses
Decompressor
Compactor
J. Rajski et al., ITC’02
Notes: The EDT architecture consists of logic embedded on a chip, which is inserted along the scan path but outside the design core. It consists of two main blocks: an on-chip decompressor and an on-chip selective compactor. No additional logic such as test points or X-bounding logic needs to be inserted into the core of the design. Therefore EDT logic only affects scan channel inputs and outputs, and has no impact on functional paths. The primary objective of the EDT scheme is to reduce tester memory requirements, rather than eliminate them altogether. Minimizing memory usage leads to test time reduction and increases throughput of a tester while maintaining the same test quality.
The ratio of internal scan chains to tester scan channels usually sets the maximum compression level. A design on this slide has three scan channels and many short internal scan chains. From the tester’s point of view, however, the design appears to have three short scan chains. In every clock cycle, 3 bits are applied to the decompressor inputs (one bit on each input channel), while the decompressor outputs load all internal scan chains. This EDT design has the same number of scan channels interfacing with the tester when compared to ATPG, but much more scan chains.

## Slide 22: Sequential decompressor
Phase shifter
x32 + x18 + x14 + x9 + 1
Notes: The EDT decompressor deploys a ring generator. It is a distinct form of a linear FSM, which is further connected to a phase shifter. The phase shifter is necessary to drive a large number of scan chains and to reduce linear dependencies between sequences entering the scan chains. A ring generator can be obtained by applying a number of transformations to the external feedback LFSR featuring the same feedback polynomial. It has three main benefits as compared with conventional LFSRs or CAs:
the propagation delay introduced by the feedback logic is significantly reduced as only at most one 2-input XOR gate is placed between any pair of memory elements,
the maximum internal fan-out is limited to only two devices fed by any stem in the ring generator,
the total length of feedback lines is drastically reduced; such short connections do not cause any frequency degradation.
The compressed test data are provided to the decompressor through input channels connected to taps of the ring generator by means of XOR gates placed between the memory elements. Those connections are referred to as injectors. Each input channel is usually split into a number of internal injectors providing the same test data to several memory elements at the same time. Four external channels feed the ring generator on the slide, each having two injectors. Their locations assure that test data can be quickly distributed to the entire ring generator. The linear phase shifter allows the ring generator to mutually displace the produced sequences in various scan paths. Typically, a phase shifter is made of XOR gates with a limited number of inputs (called XOR taps) to reduce propagation delays.
The whole decompressor operates as follows. At the beginning of every pattern, the first group of data is shifted into the ring generator. These data are referred to as initial variables. Next, another group of variables is scanned for decompression. Loading the scan chains is carried out in parallel with continuous injections of new variables into the ring generator. The total number of shift cycles is equal to the initial cycles plus the length of the longest scan chain.

## Slide 23: Stimuli compression
1
1
0
0
0
1
0
1
1
0
d + e + f + g + k = 1
a + b + d + h + i + j + k + o = 1
c + d + e + j + k = 0
a + b + c + g + h + i + n + o = 0
b + c + e + f + g + i + m + p = 0
a + b + d + f + h + i + k + l + m + o + s + v = 1
e + f + j + l = 0
a + c + f + m + n + r + t = 1
c + g + l = 1
a + b + e + i + n = 0
o
m
k
i
g
e
c
a
p
n
l
j
h
f
d
b
Decompressor
Notes: Similarly to a conventional LFSR reseeding, the compression of test cubes is performed by treating the external test data as Boolean variables. All scan cells are conceptually filled with symbolic expressions that are linear functions of input variables injected into the decompressor. Given:
a feedback polynomial implemented by the ring generator,
structure of the associated phase shifter,
location of injection sites, and
the number of shift cycles,
one can obtain a set of linear equations corresponding to scan cells whose values are specified. Subsequently, a compressed pattern can be determined by solving the system of equations.

## Slide 24: Stimuli compression
0
0
0
0
0
0
1
1
0
1
0
0
0
0
1
1
0
1
0
0
1
1
0
0
1
1
1
1
1
1
1
1
1
1
0
1
0
0
0
0
1
0
1
0
0
0
0
1
0
0
0
1
0
0
1
1
1
1
1
1
1
0
1
0
1
1
0
0
0
1
0
0
1
0
1
0
0
1
0
0
d + e + f + g + k = 1
a + b + d + h + i + j + k + o = 1
c + d + e + j + k = 0
a + b + c + g + h + i + n + o = 0
b + c + e + f + g + i + m + p = 0
a + b + d + f + h + i + k + l + m + o + s + v = 1
e + f + j + l = 0
a + c + f + m + n + r + t = 1
c + g + l = 1
a + b + e + i + n = 0
Decompressor
Notes: In order to achieve a high degree of compression, the ATPG works as follows. Whenever the algorithm generates a test cube (without random fill), the solver is invoked to generate the compressed pattern. If the compressed pattern is scanned in through the decompressor, all the bits that were specified by the ATPG algorithm should match. Other unspecified bits are set to pseudorandom values (based on the decompressor architecture). When dynamic compaction is enabled, the solver works iteratively with ATPG to maximize compression. According to this scenario, as long as the solver can compress a test cube, ATPG attempts to pack more specified bits into that test by targeting subsequent faults. It is worth noting that the solver operates in the incremental mode; i.e., it is invoked several times for a gradually increasing system of linear equations.

## Slide 25: How much can we encode?
Chart: 
| 32.0 | 40.0 | 48.0 | 56.0 | 64.0 | 72.0 | 80.0 | 88.0 | 96.0 | 104.0 | 112.0 | 120.0 | 128.0 | 136.0 | 144.0 | 152.0 | 160.0
injected | 2072 | 2078 | 2084 | 2090 | 2096 | 2102 | 2108 | 2114 | 2120 | 2126 | 2132 | 2138 | 2144 | 2150 | 2156 | 2162 | 2168
128 | 1597.1 | 1838.2 | 1898.1 | 1984 | 2019.8 | 2036.2 | 2038.4 | 2061.6 | 2076.3 | 2084.8 | 2083.6 | 2100.6 | 2105.4 | 2105 | 2118 | 2116 | 2128
256 | 1599.4 | 1833 | 1911 | 1982.6 | 2010 | 2032 | 2034.6 | 2052.3 | 2072.1 | 2082.8 | 2081 | 2098.2 | 2102.4 | 2094 | 2111 | 2114 | 2128
512 | 1579.1 | 1817.4 | 1899.8 | 1964.6 | 2010.5 | 2018 | 2045.2 | 2045.3 | 2074 | 2079 | 2079 | 2092.9 | 2100 | 2094 | 2113 | 2114 | 2125
1024 | 1779.4 | 1875 | 1957.7 | 1994.3 | 2013.2 | 2035 | 2042.2 | 2057.1 | 2071.9 | 2072 | 2089 | 2097.6 | 2090 | 2104 | 2107 | 2117 | 2119
Decompressor size
Encoded bits
16 ATE channels
128-bit scan chains
128 scans
256 scans
512 scans
1024 scans
The number of variables
Notes: This diagram illustrates the actual compression ability of EDT. The upper red line represents the theoretical upper limit of encoded bits as a function of a decompressor size assuming that it is fed by 16 channels and drives 128-bit scan chains. For example, 32-bit decompressor will receive 32 bits as initial variables plus 16 x 128 regular variables, i.e., in total 2080 seed variables. This is also the largest number of bits that can be encoded (assuming that all related equations are linearly independent). When the number of encoded bits is equal to the number of bits used to run the compression process, the encoding efficiency reaches the value of 1.0. The remaining curves illustrate experimental numbers of encoded bits (generated randomly) obtained for different numbers of scan chains. As can be seen, the small decompressors may not yield the expected encoding efficiency. It increases, however, with the increasing decompressor size, but still remains below 1.0 due to linear dependencies.

## Slide 26: Maximum compression rate
1%
0.2%
0
500
1000
1500
2000
2500
3000
3500
4000
4500
5000
64
2112
4160
6208
8256
10304
12352
14400
Test cubes
Specified bits
Notes: Detailed analysis of test cube profiles shows that in many industrial designs, even if they are generated with sophisticated dynamic compression algorithms targeting multiple faults and performing multiple clock compression, the fill rate is 1% to 5% only at the beginning of the process. After the first couple of vectors the fill rate may drop well below 1%. The slide shows an example of a test cube profile for an industrial design. This design has 7M gates and 330K scan cells. In the first 64 patterns the fill rate averages 11318 positions. After 320 patterns the fill rate drops below 1%. The average is then 675 (0.2%). Following this observation, the amount of test data can be further reduced based on the analysis that allows one to eliminate several Boolean variables. The scheme can be subsequently implemented by taking advantage of a tester’s repeat capability.

## Slide 27: Maximum compression rate
?
1%
0.2%
0
500
1000
1500
2000
2500
3000
3500
4000
4500
5000
64
2112
4160
6208
8256
10304
12352
14400
Test cubes
Specified bits
Encoding efficiency
Test cube fill rate
Notes: Consider some basic relationships between factors typically used to characterize test data volume compression. The compression ratio can be roughly estimated as follows:
compression = # scans / # channels
The encoding efficiency is defined as a ratio of specified bits to the number of bits used to encode them:
encoding efficiency = # specified / (# channels × scan length)
Similarly, a fill rate is given as a ratio of specified bits to the total number of bits (or equivalently scan cells):
fill rate = # specified / (# scans × scan length)
Consequently, the encoding efficiency can be alternatively expressed as:
encoding efficiency = (fill rate × # scans) / # channels
And finally, the compression becomes a function of the encoding efficiency and a fill rate (note that if the encoding efficiency approaches its limiting value of 1.0, the compression becomes basically reciprocal of a fill rate):
compression = encoding efficiency / fill rate

## Slide 28: Example
Shift cycles:
1573  10868
1573 patterns
10868
8
Notes: Consider a real design. In ATPG, it was configured into 8 scan chains with a maximum length of 10868. The test required 1573 patterns. As a result, the total number of shift cycles required to apply the test is equal to 17,095,364.

## Slide 29: Example
1584
patterns
8
836 scan chains
104
Shift cycles:
1573  10868
= 96.36x
1584  (104 + 8)
Coverage: 99.88% CPU time: 1.05s
EDT: 64 bits
Area: 0.31%
EDT test: 18 patterns
Notes: In EDT, the same design was configured into 836 internal scan chains with a maximum length of 104, while deploying a 64-bit decompressor (it required additional 18 test patterns to test itself). In total, 1584 test patterns were required to achieve the same fault coverage as that of ATPG. As can be seen, the length of scan chains decreased more than 100 times. The effective reduction of volume of scan test data and scan test time is 96x. Note that the actual compression is lower than the target one. This is because the maximum number of specified bits is, in some cases, greater than the encoding capacity of a decompressor, and thus more test patterns are required. Moreover, handling of a large number of X sources affect the compression as well.

## Slide 30: ATE memory
97 EDT vectors
1 ATPG vector
10868
8
8
112
112
112
112
112
112
112
112
97x
112
112
112
…
Notes: It is also worth noting how the tester memory is utilized in both cases. One ATPG scan pattern takes 10868 locations of the tester memory, while one EDT pattern occupies 112 locations of the same memory. Within the memory required for one ATPG scan pattern, one can store 97 EDT patterns. Moreover, in the time required to apply one ATPG pattern, almost 97 EDT patterns can be applied. However, since EDT requires slightly more patterns then ATPG to achieve the same fault coverage, the total time to apply all EDT vectors is effectively 96 times shorter than ATPG.

## Slide 31: Decompressor as PRPG
“1”
clock
Simple configuration
Clock drives decompressor and scan chains
Decompressor driven by a constant value (pseudorandom generator)
Decompressor
Compactor
Notes: The EDT decompressor can be easily converted into a pseudorandom test pattern generator (PRPG). It suffices to apply a constant value of 1 to the decompressor input channels. As a result, the EDT environment can be reused to perform several operations in a variety of test modes, such as burn-in test or built-in self-test.

## Slide 32: First silicon with EDT – 2001
500K gates
31K scan cells
20 clock domains
Embedded memories
5 EDT channels
65 scan chains
Longest scan chain: 460
20-bit decompressor
Compression: 11.8x
Courtesy of Jun Qian, CISCO Systems
Notes: The slide illustrates a microphotograph of a design incorporating the EDT logic (courtesy of Cisco Systems). This design contains about 500K gates and 31K scan cells. The number of channels and chains are 5 and 65, respectively. The resulting effective compression that was achieved by using 20-bit decompressor is 11x.

## Slide 33: Sequential compression
Data injected during a shift cycle encode specified bits in subsequent time frames
High compression – even for a single input channel
Overdrive mode – data delivered in selected cycles to elevate compression
Sophisticated solvers of linear equations
Notes: Sequential linear decompressors are based on linear finite-state machines such as LFSRs, cellular automata, or ring generators. Their advantage lies in allowing the use of free variables from earlier cycles to encode a scan slice in the current clock cycle. This provides much greater flexibility than combinational decompressors and helps avoid problems when the most specified scan slices limit the overall compression. One of the most pronounced features of the sequential compression is its ability to work even with a single input channel. For some test sets with highly sparse specified bits (very low fill rates) it is also possible to provide data only in selected time frames, thus further increasing compression rates. The ability to combine free variables across multiple clock cycles makes sequential compression very attractive. In fact, most of available commercial tools are based on this type encoding. When working with ATPG, though, it requires a two-step process: generation of a test cube, and then solving linear equations to see if the test cube is encodable.

## Slide 34: Commercial compression solutions
TestKompress (Mentor Graphics), 5-10x, 100x 2001
OPMISR (Cadence), 2x time, 10x volume 2001
40x time, 100x volume 2005
VirtualScan (SynTest), 15x (5x-50x) 2002
SoCBIST (Synopsys), 10x time, 400x volume 2002
Talus ATPG-X (Magma), 40x 2007
Notes: Here are a few examples of commercially available test compression tools. They are listed altogether with the corresponding compression rates they offer.

## Slide 35: Generations of compression
1st generation
  exploits don’t care positions in test cubes
  compresses one scan load at a time
2nd generation
  leverages spatial correlations within test cubes
  channel broadcasting of test stimulus
  modular design, multiple configurations
  dynamic channel allocation
  LBIST enabled embedded compression
Notes: The first generation test compression schemes take advantage of low fill rates. Tester channels deliver compressed test patterns to an on-chip decoder that expands them into the actual data loaded into scan chains. Encoding a test cube using a linear decompressor requires solving a system of linear equations consisting of one equation for each specified bit, to find the free variable assignments needed to generate the test cube.
Similarly to scan-based test, decompression schemes consume more power than a circuit-under-test is rated for. Thus, non-intrusive methods are required to control test power and support embedded compression with high compression ratios. Interestingly, methods developed for lower power on-chip decompression offer higher compression rates than their first generation counterparts. Therefore, when presenting the next generation compression schemes, we will discuss a few techniques used to mitigate power dissipation as their application leads directly to further reduction of test data necessary to recreate original test cubes.

## Slide 36: EDT and scan fill
%
Toggling
Scan shift
Typical scan fill – 50% toggling
Low power decompression < 15%
Reduced switching and accelerated shift
Compressed stimuli
Compacted responses
Decompressor
Compactor
MHz
Notes: Loading scan chains dissipates power dependent directly on the number of transitions that occur in the scan chains and other parts of the CUT. The weighted transition metric (WTM) estimates the resultant switching activity by counting the number of invoked transitions in scan cells and taking into account their relative positions. One can arrive with the average scan power dissipated during test application by summing up results provided by WTM over all scan chains and all test patterns. Typically, a random fill is a side effect of the EDT continuous flow processing when a test pattern goes through the decompressor. The slide illustrates such uncompressed data recorded for a real circuit. This is why the test power consumption for the EDT-based decompression usually remains close to 50 percent. At the same time, scan shift frequency remains relatively low to avoid overheating and likely damage of a circuit under test.

## Slide 37: EDT and scan fill
%
Typical scan fill – 50% toggling
Low power decompression < 15%
Reduced switching and accelerated shift
Compressed stimuli
Compacted responses
Decompressor
Compactor
MHz
Toggling
Scan shift
Notes: The EDT-based compression exploits the common fact that test cubes feature a large number of unspecified positions. The low fill rates make it possible to deliver the identical test data to scan chains for a number of consecutive shift cycles, thereby reducing significantly the total number of transitions (as shown on the slide). To implement this idea, however, one needs mechanisms to sustain the outputs of a decompressor for more than a single clock cycle, while allowing the decompressor itself to change its internal state in order to ensure successful encoding of upcoming specified bits. Furthermore, reduced toggling creates a margin that allows to increase a speed of scan shifting, thus reducing test application time.

## Slide 38: Power dissipation
Decompressor
1
0
1
0
1
0
0
0
1
0
0
1
0
1
1
0
0
1
0
0
0
1
1
1
0
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
0
1
1
0
0
1
0
0
0
1
1
1
1
0
1
0
1
1
0
0
1
0
0
0
1
1
1
1
0
0
0
1
1
1
1
0
1
0
1
1
0
0
1
0
0
0
1
1
1
1
0
1
0
1
1
0
0
1
0
0
0
0
1
0
0
1
0
0
0
1
1
1
0
1
0
1
1
0
0
1
0
0
1
1
1
1
0
1
0
1
0
0
0
1
0
0
0
1
1
1
1
0
1
1
1
0
0
1
0
0
0
1
1
1
1
0
1
0
1
1
0
0
1
1
0
1
0
1
1
0
0
1
0
0
0
1
1
1
0
1
0
1
1
0
0
1
0
0
0
1
1
0
Random fill
1
0
1
0
1
0
0
0
1
Decompressor
Notes: As shown earlier, the test power consumption for the EDT-based decompression remains close to 50 percent. This is due to a random fill occurring as a side effect of the decompression process. This is further illustrated in the lower part of the slide, where the size of red rectangles, one per each transition, corresponds to the amount of power dissipated during scan-in shifting of a given transition from left to right. The total area taken by all rectangles can be regarded as proportional to the whole power dissipated when loading a given test pattern through a decompressor.

## Slide 39: 2nd generation decompressor
Hold register to sustain decompressor output
Identical data for several shift cycles
Ring generator
Constant fill
+
Hold register
Phase shifter
D. Czysz, et al., ITC’08
Notes: The low fill rates make it possible to deliver identical test data to scan chains for a number of shift cycles directly from the decompressor, thereby further reducing the total number of transitions. A low power solution shown on the slide employs the on-chip low power test data decompressor. The same data are now provided to the scan chains for a number of shift cycles through either a constant fill block or a hold register placed between the ring generator and the phase shifter.
The former block is similar to the one presented in the section devoted to low power scan operations. It outputs gating signals such that either the decompressor or a constant value of 0 or 1 can feed scan chains on a per pattern basis. The hold register captures and saves, for a number of cycles, a desired state of the ring generator, while the generator itself keeps advancing to the next state needed to encode another group of specified bits. As a result, independent operations of the ring generator and its hold register allow virtually any state which causes no conflicts with specified bits to reduce a transition count.
In principle, one can use an extra input channel to facilitate the operation of the hold register. Every shift cycle, a control bit is then sent to the decompressor in order to indicate whether the hold register should be reloaded with the current content of the ring generator. If a given control bit is 1, then the hold register updates its state before the ring generator reaches its next state. During the initialization phase of the decompressor, the hold register is reset, and the control channel is de-asserted. Instead of the control channel, one can use decompressor input channels to deliver control information merged with seed variables. The slide shows the corresponding circuitry. All inputs drive an XOR tree which basically computes a parity bit for input variables injected during a given shift cycle. If the parity of inputs is odd, then the hold register is reloaded before new seed variables enter the ring generator. Otherwise, the content of the register remains unchanged.

## Slide 40: Test cube encoding
Extra equations to control hold register
Notes: A compression procedure working with the hold register partitions a given test cube into several blocks comprising a certain number of consecutive slices (time frames) in such a way that there are no transitions inside the blocks. This feature allows one to repeat a given decompressor state many times in succession by using the hold register storing a state that the ring generator entered at the beginning of a block. The ability to encode some of the specified bits occurring within boundaries of the block determines its size. The encoding process begins with a block and the corresponding state of the ring generator which should be applied first, and it gradually moves towards the other end of the scan chains. As long as the solver can compress a test cube, the algorithm works by repeatedly increasing the size of the block, adding new equations (if needed), and invoking the solver again. Clearly, at some point a solution may not exist anymore. This particular time frame is then assigned a new block, and the procedure continues. As a result, we arrive with virtually the smallest number of blocks that cover the entire test cube. Note that the circuit where the same test data drives the decompressor and the shadow register, requires that equations in the seed variables representing both the specified locations and control data be formed to reflect reloads of the hold register.

## Slide 41: Decompressor freeze
0
0
1
1
3
2
4
8
0
1
6
12
9
7
10
5
14
13
15
11
2
11
9
0
D. Czysz, G. Mrugalski, J. Rajski, J. Tyszer, IEEE Trans. CAD, 2008
Notes: Another approach to reduce test power uses a concept of decompressor freeze, and it is a purely software technique. The sparse occurrence of specified bits indicates that successful encoding of test cubes could be still possible even if a decompressor would remain in certain states for more than a single clock cycle. As a result, the identical data would be delivered to scan chains for a number of shift cycles, thereby reducing the number of transitions. We refer to such states as self-loop (SL) states following a common state-diagram notation where certain arrows point to the states that they leave. Consider a 4-bit ring generator with two inputs as shown on the slide. Its 16-state transition graph features four SL states. As can be easily verified, if the input patterns 00, 01, 10, and 11 are applied to the ring generator after it enters the following states: 0000, 1101, 0100, and 1001, respectively, then it will remain in these SL states.

## Slide 42: Decompressor freeze
0
0
1
1
3
2
4
8
0
1
6
12
9
7
10
5
14
13
15
11
2
11
9
0
D. Czysz, G. Mrugalski, J. Rajski, J. Tyszer, IEEE Trans. CAD, 2008
Notes: Due to so many transitions between states of the decompressor, moving from one SL state to another SL state takes only a few clock cycles. As a result, one may expect that the amount of scan slices not covered by any SL state due to such transitions will be minimal.

## Slide 43: Power dissipation again
0
0
1
1
1
0
0
0
1
1
1
1
1
0
0
0
0
0
1
1
0
0
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
0
1
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
Low power fill
s1
s2
s0
Decompressor
Decompressor
Notes: Given a test cube, the encoding procedure works as follows. First, every scan shift cycle having specified bits is assigned one of SL states (if any) such that if a ring generator enters such a state, then there will be no conflicts between the specified bits of the test cube and the actual decompressor-produced content of the scan chains in this particular cycle. Next, following the standard EDT framework, the EDT solver is invoked for equations representing values required for the test cube in order to guarantee its compression. Finally, the test cube is partitioned into a number of clusters in such a way that a single SL state covers the largest possible number of subsequent cycles in each cluster. This is accomplished by solving equations associated with positions implied by a given SL state at both ends of the corresponding cluster. Although initial selection of the cluster boundaries assume its largest possible span, it may not be possible to switch a decompressor from one SL state to another SL state within a single clock cycle. In such a case, there would be no solution for equations representing a given cluster, and the test cube could not be compressed. Therefore, as long as the solver cannot encode a given SL state, the algorithm works by repeatedly decreasing size of the cluster, selecting a new set of equations, and invoking the solver again.
The pink rectangles in the lower part of the slide represent the amount of dissipated power when using the conventional EDT (their sizes are proportional to the amount of power dissipated by a given transition when moving from the left to right), whereas the red rectangles illustrates the same power dissipation after applying power aware encoding.

## Slide 44: Design with modular compression
Notes: The ability to work even with a single input channel allows the EDT-based compression to become an attractive option for System-on-Chip (SoC) designs, where a number of cores (modules) must be tested in parallel by using their own compression environments. An example of such an arrangement is shown on the slide. Identical cores may share the same input channels, while different modules can still receive their compressed data in parallel due to a relatively low bandwidth they may require.

## Slide 45: Maximum compression rate
1%
0.2%
0
500
1000
1500
2000
2500
3000
3500
4000
4500
5000
64
2112
4160
6208
8256
10304
12352
14400
Test cubes
Specified bits
Encoding efficiency x Regularity factor
Test cube fill rate
Notes: For modular designs such as the one on the previous slide, one can modify a well-known compression formula by including a regularity factor which accounts for the number of cores that can be tested by deploying the same compressed test data.

## Slide 46: 3rd generation compression
Leveraging time correlations between vectors
Vector clustering to compress incompatible vectors
Compresses multiple incompatible vectors
Notes: The EDT-based compression uses cube merging to gradually expand a test pattern by incorporating compatible test cubes with non-conflicting values assigned to unspecified positions. Two cubes are compatible if in every position where one cube has a value of 0 or 1, the other one either features the same value or don’t care. With the concerns over test compression and test time, one needs to maximize the number of test cubes forming a given test pattern. Unfortunately, the cube merging process terminates when either no new compatible cube can be found in a reasonable amount of time, or the resultant pattern cannot be encoded anymore. The encoding efficiency and the compression ratio could be significantly higher, if the cube merging process continued despite conflicts on certain positions. Clearly, such bits would not be the subject of the mainstream EDT-based encoding, but they would have to be recovered in a different way to eventually load scan chains with patterns that feature the original test cubes. Furthermore, their quantity should be selected so as not to adversely affect the compression ratio. The third generation compression involves a deliberate attempt to increase the overall test data reduction by merging a large number of cubes having a predetermined number of mutually conflicting locations at most.

## Slide 47: Vector clustering
0
1
1
0
0
1
1
1
0
…
0
0
0
0
0
0
0
0
0
…
1
1
1
1
1
1
1
1
1
1
1
0
1
1
x
x
x
x
x
x
x
0
0
0
Parent
Incremental
1
x
x
x
x
x
x
x
0
0
0
0
x
x
x
x
x
x
x
0
0
0
x
1
x
x
x
x
x
x
0
0
1
x
0
x
x
x
x
x
x
0
0
1
x
x
x
x
x
x
x
1
1
1
1
x
x
x
x
x
x
x
0
1
1
1
0
1
1
0
0
1
1
1
0
…
…
(100 + 4) ×16
111 + 100 + (4 ×16)
= 6.05
1664
275
=
J. Rajski et al., ITC’09
Notes: Consider an experiment in which test patterns are obtained by merging incompatible test cubes. The objective is to estimate the actual amount of data that would become the subject of encoding. Let a circuit under test feature 111 inputs as shown on the slide. A part of this device is an 8-input multiplexer. In order to detect stuck-at-0 and stuck-at-1 faults on its inputs, one needs to apply test patterns listed over there. These patterns cannot be merged as they all feature mutual conflicts either on data or control lines of the multiplexer. As a result, a conventional compression scheme would need to handle 16 separate test patterns by encoding 16  (100 + 4) = 1664 bits. Since 100 specified bits are identical in all vectors, they can be used to form a base (parent) pattern, while conflicting bits will occur in successive 16 incremental patterns. Their use is determined by a single control pattern driving a multiplexer put in the front of a scan chain. Clearly, the number of specified bits that have to be encoded is now equal to 100 (parent) + 16  4 (incremental) + 100 + 8 + 4 (control) = 275. The amount of bits that become the subject of encoding is a fraction of data that the conventional EDT would need to handle, and in this particular case the reduction ratio is 6.05. Recall that the parent pattern and the corresponding control pattern must be applied 16 times for all incremental vectors.

## Slide 48: Tri-modal decompressor
load
Ring generator
Ring generator
Incremental pattern
Control pattern
Parent pattern
…
…
…
…
…
Hold register
Phase shifter
Phase shifter
Phase shifter
Notes: The slide shows a third generation decompressor. It comprises three modules designated to decompress the parent, the incremental, and the control patterns. All techniques adopted here follow the EDT-based continuous flow decompression modus operandi. However, due to particulars of patterns the decompressor is to handle, each block is designed in a slightly different way. 2-input multiplexers are placed in the front of scan chains. They are intended to route decompressed test data from one of two sources:
the basic EDT-like decompressor that primarily handles the parent patterns,
another decompressor that consists of ring generator 2 with phase shifter 2, which takes care of the incremental patterns.
The actual source is determined by applying select signals to the muxes. These signals are provided by the third decompression logic employed here to handle the control patterns.
Ring generator 1 and phase shifter 1 constitute a sequential continuous flow decompressor. This part of decompressor is deployed to decode the parent patterns, which are subsequently fed to the scan chains unless the control signals decide otherwise. The control patterns feature a large number of zeros (corresponding to the specified bits of the parent patterns) with the sparse presence of ones (corresponding to conflicting bits). To encode such patterns it suffices to target only a small subset of 0-bits as long as they occur in sequences no interspersed with 1-bits. A hold register is placed between ring generator 1 and phase shifter 3 to keep the decompressor outputs unchanged. It captures and saves, for a number of cycles, a desired state of ring generator 1, while the generator keeps advancing to the next states in order to encode upcoming specified bits. Note that low control pattern fill rates make it possible to use ring generator 1 as its encoding ability usually suffices to handle both parent and control patterns. The decompressor input channels facilitate the operation of the hold register by using seed variables to deliver a load enable signal. Buffers placed in parallel with the decompressor inputs drive an XOR tree computing a parity of input variables, including current data and those injected in the previous cycles. If set to 1, this signal reloads the hold register with the content of ring generator 1 before new seed variables enter the generator, and it reaches its next state.
The third part of the decompressor is used to decode the incremental patterns. It consists of ring generator 2 and phase shifter 2. As the incremental patterns feature extremely sparse specified bits (corresponding to conflicts), they do not require all variables, which would be injected within the conventional EDT framework. Hence, injections of new test data occur in selected scan shift cycles only. Such an approach further elevates the compression ratio and adheres to the ATE ability of repeating the same data multiple times.

## Slide 49: Test environment
Incremental patterns
Parent/control patterns
…
ATE
Decompressor
Notes: The tri-modal decompressor can be interfaced with an external tester in a number of ways. All of them assume that an ATE memory stores a single copy of each parent and incremental pattern in different configurations dependent on a communication protocol. In one of the techniques, a compressed parent pattern is delivered to a circuit under test only once, and then stored on chip by deploying circular registers as shown on the slide for a decompressor with two inputs serving parent and control patterns. Initially, using a single channel, a tester uploads a parent pattern directly to registers forming a daisy chain. Note that the decompressor is also receiving this data, so during this phase it can produce and feed scan chains with pseudorandom test patterns. Subsequently, the parent pattern is repeatedly streamed to the decompressor and back to its host circular registers while the same ATE channel delivers successive incremental patterns in the repeat-every-bit mode. Connecting the ATE channel to the decompressor inputs is done through steering logic controlled by the first bit of each test pattern. That bit allows test logic to differentiate between parent and incremental patterns, and is sampled synchronously with the EDT update signal resetting EDT test logic at the beginning of each test pattern.

## Slide 50: Compression and efficiency
 | Scan | Conf | Parent | Inc | Efficacy | Comp [x]
D1 | 122 × 104 | 20 | 23 | 1963 | 3.40 | 373
D2 | 128 × 353 | 32 | 84 | 6938 | 4.12 | 416
D3 | 80 × 1081 | 32 | 73 | 5209 | 3.59 | 754
D4 | 80 × 878 | 32 | 70 | 8810 | 7.93 | 1132
D5 | 120 × 119 | 32 | 972 | 36287 | 3.71 | 317
D6 | 244 × 588 | 28 | 169 | 25520 | 2.43 | 4570
D7 | 378 × 787 | 32 | 1547 | 51721 | 3.09 | 1451
Notes: Experiments were conducted with six industrial designs. The basic data regarding the designs (scan architecture) are listed in the left part of table. All experiments were performed for stuck-at tests. The results are summarized in the right part of the table. It lists the following statistics: the maximal number of allowed conflicts when merging original test cubes - this number gives the largest quantity of locations on which every single incremental pattern differs from its parent pattern (note that, given a parent pattern and its derivates, the total number of conflicting bits is higher and its maximal value was set to 256), the number of parent and incremental patterns (recall that the number of control patterns is the same as that of the parent patterns), the encoding efficiency, i.e., the ratio of the total number of specified bits and the number of bits (test data) use to encode them, the effective test data volume compression.
As indicated by data in the table, application of the scheme produces remarkable compression levels. In all test cases, compression rates are significantly higher than those of the conventional EDT. The observed increase varies from 3.5 to almost 36 times (or well above 4,500x in absolute numbers). Note that the test coverage remains unaffected in each case. The average encoding efficiency computed across the examined designs is equal to 4.09 with the maximal efficiency reaching the value of 7.93. Clearly, the third generation scheme elevates compression ratios and the encoding efficiency to levels far beyond what is achievable through the conventional static and dynamic reseeding.

## Slide 51: Maximum compression rate
1%
0.2%
0
500
1000
1500
2000
2500
3000
3500
4000
4500
5000
64
2112
4160
6208
8256
10304
12352
14400
Test cubes
Specified bits
Encoding efficiency x Clustering factor
Test cube fill rate
Notes: The third generation schemes elevates compression by working with clusters of incompatible test cubes that otherwise could not be merged. As shown earlier, it may have a significant impact on the resultant compression and encoding efficiency. These two factors appear in the corresponding formula that defines a compression rate for this type of test data reduction in a manner similar to that of the previous schemes.

## Slide 52: Code-based compression
Use data compression codes to encode test cubes
Run-length (variable-to-fixed) codes
  encode runs of repeated values
  Golomb, frequency directed, variable-input Huffman codes
Dictionary (fixed-to-fixed) codes
  replace test data with index in dictionary
  some combinations may remain unencoded (bypass mode)
Statistical (fixed-to-variable) codes
  shorter code words assigned to data occurring more frequently
  selective Huffman coding (complex decoder)
Constructive (fixed-to-variable) codes
  incrementally flips bits in successive scan slices
No commercial tools available
Notes: Code-based schemes use data compression codes to encode test cubes. These methods partition the original data into symbols, and then replace each symbol with a code word to form the compressed data. To perform decompression, a decoder converts each code word in the compressed data back into the corresponding symbol. The advantage of the code-based schemes is that they can efficiently exploit correlations between specified bits and are usable on any set of test cubes with no ATPG constraints. Therefore, they are effective for IP cores for which no structural information is available. The drawback is that these schemes are generally not as efficient in exploiting don’t-cares as linear techniques. Because industrial test cubes typically have fill rates below 5%, linear techniques generally provide greater compression.

## Slide 53: Hybrid solution: BIST + compression
Hybrid BIST schemes with top-up patterns
Reuse of existing BIST infrastructure to decompress test patterns
Embedding test vectors by means of weights or perturbing pseudorandom patterns
Low power BIST generators to act as power-aware test data decompressors
Notes: Test compression quickly became the main stream DFT methodology. However, it is unclear whether test compression will be capable of coping with the rapid rate of technological changes. Interestingly, logic built-in self-test (LBIST), originally developed for board, system and in-field test (see Section 6), is now gaining acceptance for production test as it provides very robust DFT and is used increasingly often with test compression. This hybrid approach seems to be the next logical evolutionary step in DFT. It has the potential for improved test quality; it may greatly augment the abilities to run at-speed power aware tests, and it can reduce the cost of manufacturing test while preserving all LBIST and scan compression advantages.

## Slide 54: Low power PRPG
Ring generator
Phase shifter
…
…
Pattern count
Shift register
Toggle control register
Switching
…
Weighted logic V
Off
Notes: See Section 6 for further details regarding a low power PRESTO generator for BIST applications.

## Slide 55: Low power PRPG
Ring generator
Phase shifter
…
…
Pattern count
Shift register
Toggle control register
Toggle
Hold
Switching
…
Weighted logic V
Off
T
Weighted logic H
Notes: As presented in section 6, two parameters kept in 4-bit Hold and Toggle registers determine how long the generator remains either in the hold mode or in the toggle mode, respectively. In order to terminate either mode, a 1 must occur on the T flip-flop input. The T flip-flop allows selecting a source of control data that will be used in the next cycle to possibly change the operational mode of the generator.

## Slide 56: Toggling in scan chains
Toggle
Hold
T
T
H
T
H
H
Notes: Recall that in the hold mode all phase shifter inputs are frozen due to disabled hold latches, whereas the toggle mode allows certain inputs of the phase shifter to receive data from the ring generator provided the corresponding bits of the toggle control register are asserted. Since this register is updated once per pattern, scan chains driven only by disabled hold latches are loaded with constant values, and thus remain in the low power mode for the entire pattern. The remaining chains receive either constant values (the hold duty cycles) or results of XOR-ing certain outputs of PRPG (during the toggle duty cycles) among which at least one is enabled.

## Slide 57: Main features
Fully programmable low power test compression
Integrated with power-aware BIST
No hardware penalty
Efficient hybrid solution
Notes: The fully programmable low power PRPG (PRESTO – Section 6) can also successfully act as a test data decompressor, thus allowing one to implement a hybrid test methodology that combines LBIST and ATPG-based embedded test compression. This is the first low power test compression scheme that is integrated in every way with the BIST environment and lets designers shape the power envelope in a fully predictable, accurate, and flexible fashion. As a result, it creates an environment that can be used to arrive at an efficient hybrid solution combining advantages of scan compression and logic BIST. Moreover, both techniques can complement each other to address, for example, a voltage drop caused by a high switching activity during scan testing, constraints of at-speed ATPG-produced test patterns, or new fault models.

## Slide 58: New decompressor
Ring generator
Phase shifter
…
…
Pattern count
Shift register
Toggle control register
Switching
…
Weighted logic V
Off
Weighted logic H
No Hold
First cycle
offset
…
Toggle
Hold
T
Down counter
Notes: In order to facilitate test data decompression while preserving its original functionality, the PRESTO generator is re-architected. This is illustrated on this slide. The core principle of the new decompressor is to disable both weighted logic blocks (V and H) and to deploy deterministic control data instead. In particular, the content of the toggle control register can now be selected in a deterministic manner due to a multiplexer placed in front of the shift register. Furthermore, the Toggle and Hold registers are employed to alternately preset a 4-bit binary down counter, and thus to determine durations of the hold and toggle phases. When this circuit reaches the value of zero, it causes a dedicated signal to go high in order to toggle the T flip-flop. The same signal allows the counter to have the input data kept in the Toggle or Hold register entered as the next state.
Both the down counter and the T flip-flop need to be initialized every test pattern. The initial value of the T flip-flop decides whether the decompressor will begin to operate either in the toggle or in the hold mode, while the initial value of the counter, further referred to as an offset, determines that mode’s duration. As can be seen, functionality of the T flip-flops remains the same as that of the low power PRPG but two cases. First of all, the encoding procedure may completely disable the hold phase (when all hold latches are blocked) by loading the Hold register with an appropriate code, for example, 0000. If detected (No Hold in the figure), it overrides the output of the T flip-flop by using an additional OR gate. As a result, the entire test pattern is going to be encoded within the toggle mode exclusively. Moreover, all hold latches have to be properly initialized. Hence, a control signal First cycle produced at the end of the ring generator initialization phase reloads all latches with the current content of this part of the decompressor.
Finally, external ATE channels (feeding the original PRPG) allow one to implement a continuous flow test data decompression paradigm such as the dynamic LFSR reseeding. Given the size of PRPG, the number of scan chains and the corresponding phase shifter, the switching code, the offset, as well as the values kept in the Toggle and Hold registers, the entire decompressor will produce deterministic (decompressed) test patterns having a desired level of toggling provided the scan chains are balanced. The corresponding encoding procedure, including an appropriate selection of the aforementioned parameters, consists of steps presented on the next slides.

## Slide 59: Low power template
Durations of Toggle and Hold periods
The number of offset cycles
Content of the toggle control register
Determined prior to test encoding
No repetitions in flow
Hold
Toggle
Offset
Notes: The values of T and H, the offset cycles, as well as the content of the toggle control register form low power templates (LPT). They are determined prior to further encoding steps based on the analysis of test cubes forming a cube pool. As a result, they allow merging and encoding successive test cubes in an incremental fashion, with no repetitions in a flow, as explained in the following.

## Slide 60: Transitions in test cubes
…
0
1
0
0
0
0
1
1
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
0
0
1
1
0
0
1
0
1
1
1
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Initially Toggle to Hold ratio minimal
No transitions within a single Hold period
Notes: First, c test cubes from the cube pool are used to initialize c low power templates. The algorithm begins by mapping the test cubes into lists of transitions. Each transition is determined by two successive specified bits of the opposite logic values located in the same scan chain. In addition to its flanking bits x and y, each transition is characterized by a span, i.e., the number of clock cycles separating x from y. It is worth noting that some specified bits contribute to two transitions, whereas other bits are not involved in forming any transitions, as shown on the slide.
Having instantiated a given empty template, the corresponding list of transitions is used to arrive with the initial durations of the toggle (T), hold (H), and offset (O) periods. These values are chosen conservatively such that the ratio T/H is minimal, and there are no transitions within a single hold period. The former condition ensures that the template can still accommodate some of newly produced test cubes. The latter condition can be rephrased as follows: for each transition either its span is greater than H or at least one of its flanking bits lies within a toggle period.

## Slide 61: Encoding algorithm
Toggle
Notes: The algorithm to yield the desired values of T, H, and O can be summarized as follows (compare the next two slides):
(1) Given a test cube and its transitions, find the earliest transition ending point e (a black arrow) and assign a single bit toggle phase (T = 1) to cycle e.
(2) Mark all transitions crossing e, as they will not end up within a single hold period.
(3) Increase the toggle period by extending it up to the next unmarked transition starting point. Repeat this step as long as the duration of the toggle period does not exceed a certain threshold.
(4) Find the next unmarked transition ending point e’ – it determines a duration H of the hold period unless H is larger than a certain threshold. In the former case skip the step.

## Slide 62: Encoding algorithm
Offset
Toggle
Hold
Toggle
Notes: (5) Find the value of H that minimizes the ratio T/H and, by adding new hold and toggle phases, keeps the cycle e’ within a toggle period.
(6) Set the offset period O to e mod (T + H) – H, if we begin with an incomplete toggle period, and O = e mod (T + H), otherwise.
(7) Adjust the values of H, T, and O if some of the remaining unmarked transitions lie entirely within a single hold period (this slide illustrates this phenomenon for a newly added red transition that must not stay within the hold period). Ensure that the sum T + H remains unchanged. The ratio T/H, on the other hand, may vary, thus its minimizing can guide this step towards the most optimal solution. Note that, for example, enlarging the toggle period reduces the length of the hold period and it may also impact the number of offset cycles.

## Slide 63: Further compression steps
Scan chains with transitions enabled
One active input of PS XOR gate suffices
Minimum hitting set problem solved to determine the control toggling register
The resultant template toggling verified against the desired switching activity
T
T + H
active chains
50
all chains
Notes: Once the procedure completes, one has to make sure that all scan chains hosting transitions are enabled. This can be achieved as long as there is at least one enabled phase shifter input that feeds a given scan through an XOR gate within the phase shifter. Finding the minimal subset of the toggle control register stages needed to activate the required scan chains is equivalent to solving the minimum hitting set problem. Furthermore, the switching activity associated with the template is checked and compared against the desired toggling ratio t. If the resultant toggling is below t, then the test cube can be finally accepted as a part of the template. Otherwise, the test cube is not compressible given power constraints and has to be discarded. The template returns to its initial status.
When all templates have been initialized, we attempt to link them with the remaining (new) test cubes. If a template cannot accommodate certain transitions featured by a newly picked test cube, then the durations of toggle, hold, and offset periods can be further adjusted. If the cube fits to the template, and new active scan chains are known, then both the content of the toggle control register and the toggling rate are recalculated. Again, if the toggling is above t, then the template returns to its previous form, while the test cube is passed to the next template. Moreover, if none of the existing templates can accommodate the cube, it remains in the pool until another set of templates is generated such that this particular cube can be eventually assigned to its designated LPT.

## Slide 64: Solving linear equations
For each cell, 7 different equations
Hold latches
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
a+c
Hold
b
a+b
c
b+g
b+g
b+g
b+g
b+g
b+g
b+g
b+g
b+d
a+d
b+d+e
b+h
b+e+f
b+a
b+c
b+e
Notes: The compression of test cubes treats the external test data as Boolean variables used to create linear expressions filling conceptually all scan cells. However, an equation assigned to a given scan cell depends not only on what is yielded by the ring generator, but also on whether a given phase shifter input is enabled or not. If a scan chain is disabled, then a single expression, produced during the first shift-in cycle, represents all of its cells. On the other hand, if a cell belongs to an active scan chain, then its equation is formed by XOR-ing (1) the corresponding outputs of the ring generator if they are enabled through the hold latches, and (2) expressions produced during the first shift-in cycle on the disabled ring generator outputs. This expression will be used provided a scan cell is in the toggle mode. If it enters the hold mode, then its equation is going to be the same as that of the preceding and nearest cell which is in the toggle mode and belongs to the same chain. Since we only use 3-input XOR gates to create a phase shifter, there are 7 different scenarios with at least one XOR tap enabled. Consequently, prior to any compression actions and to save CPU time, we prepare all possible equations for each scan cell, and subsequently select an appropriate expression when working with a particular low power template.
Having prepared all necessary equations, one can proceed with the test cube encoding. This is carried out in a manner similar to that of the conventional EDT flow. It is worth noting, however, that participation of a given test cube in a template does not guarantee its actual merging and compression because of either conflicts on certain specified bits with other test cubes or limited encoding capabilities. Another notable difference between the presented approach and the traditional EDT scheme is the way compression aborts are reported. Typically, a test cube is regarded uncompressible if it cannot be encoded when merged as the first component of a test pattern. Here, the test cube is first employed, with other cubes, to form a template, which in turn modifies equations. Hence, an abort is reported only if the cube is used to make up a low power template, is then chosen as the first component of a test pattern, and its encoding fails. All compressed test cubes are removed from the cube pool, which is subsequently refilled. The algorithm continues by creating a new set of templates as long as the pool is not empty.