## Slide 1: VLSI testing
Fault simulation
HEP
Notes: Fault simulation is more complex task than logic simulation due to an additional dimension: the behavior of the circuit containing modeled faults that must be taken into account. When simulating one fault at a time, the computational complexity of this process is approximately proportional to the circuit size, the number of test patterns, and the number of faults. Since the number of faults is closely related to the circuit size, the overall time complexity of fault simulation is O(pn2), where p is the number of test patterns, and n is the number of logic gates. Clearly, for large circuits, fault simulation may become infeasible. Consequently, various techniques have been proposed to improve fault simulation performance. In this chapter, we will discuss the key fault simulation techniques assuming a single stuck-at fault model.

## Slide 2: Definition
Fault simulation is a technique to study behavior of circuits in the presence of faults
Given a circuit and a fault model
  for a given vector it determines which faults are covered and which are undetected
  for a given test set it determines fault coverage (fault grading)
  it determines signatures of different faults for fault diagnosis (fault location)
Notes: Fault simulation plays an important role in test generation, where it is used to evaluate a given test set, and then change that test set according to the results of fault simulation until the obtained fault coverage is regarded satisfactory. The test set is modified by adding new patterns or discarding some of them that do not contribute to a good test coverage. Furthermore, many test generation algorithms produce a test pattern for one specified (target) fault. As the same test pattern detects many other faults, they can be determined by means of fault simulation. Then all detected faults are discarded from the list of simulated faults and a new target fault is selected from the remaining ones. Fault simulation is also employed to construct fault dictionaries that store the output response of every faulty circuit corresponding to simulated faults. Such dictionaries are then used in the process of fault diagnosis. Finally, fault simulation can be deployed to analyze the operation of a circuit in the presence of faults, as faults can induce races and hazard conditions, may cause oscillations or deadlocks, may inhibit a proper circuit initialization, and eventually can even transform a purely combinational device into a sequential one.

## Slide 3: Methods
Parallel fault simulation
Parallel-pattern single-fault propagation (PPSFP)
Deductive fault simulation
Concurrent fault simulation
Critical path tracing
Stem regions
Differential fault simulation
Notes: The list presented above is by no means a complete list of proposed fault simulation techniques. However, in the remaining part of this chapter we will focus our attention on those techniques that explain best the key concepts used in the process of fault grading, and gained a reasonable amount of popularity. We will start with the simplest scenarios, and then illustrate how various heuristic and different techniques were gradually applied to enhance performance of fault simulators, especially in order to remain scalable with the increasing size of circuits.

## Slide 4: Parallel fault simulation
S. Seshu, IEEE Trans. Electronic Computers, 1965
a = 1
b = 1
c = 1
a/0
a/1
b/0
b/1
c/1
c/0
ff
Wa
Wb
Wc
m0
m1
Fault-free and faulty values are computed by
Wc = Wa Wb m0 + m1
Wa, Wb, Wc – words representing vectors of logic values
m0, m1 – masks for injecting c-stuck-at-0 and c-stuck-at-1
a/0
a/1
b/0
b/1
c/1
c/0
ff
1
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
0
1
0
0
0
0
0
0
1
1
0
1
0
1
0
1
Notes: One of the simplest techniques – parallel fault simulation – takes advantage of computer bitwise operations to reduce fault simulation time. As a result, the good circuit and the number of faulty circuits are simulated simultaneously. The values of a signal in the good circuit and the values of the corresponding signals in a number of faulty circuits are packed together in the same memory location – typically one or more words. Consider an example shown on the slide. Assuming that the width of a computer word is 7, the first bit stores the fault-free (ff) circuit response, while the remaining bits store the faulty responses in the presence of faults a/0, a/1, b/0, b/1, c/0, and c/1. The output of AND gate is computed as shown on the slide. Note, that faults c/0 and c/1 and injected by forcing the two rightmost bits to the values of 0 and 1, respectively. This is achieved with the help of masks m0 and m1, as illustrated above. Faults detected by a particular test pattern (in our case, vector 11) can be easily determined by comparing bit ff with the remaining bits of a word associated with a line considered as a primary output or another observation point. In our example, faults a/0, b/0, and c/0 are detected by test pattern 11.
Parallel fault simulation is only applicable to unit or zero delay models as several faults are evaluated at the same time. It becomes impractical for multivalued logic. Moreover, it cannot take full advantage of selective trace simulation or reductions in the number of faults caused by fault dropping.

## Slide 5: PPSFP
The method combines
  single-fault propagation, and
  parallel-pattern evaluation (b test patterns are packed into b-bit word and simulated for fault-free and faulty circuits)
After b vectors have been fault-free simulated, SSFs are inserted one at a time and simulated for these tests
The values in every faulty circuit are computed by the same fault-free simulation and compared to their corresponding good values
The computation of faulty values starts at the fault site and continues until all faulty values become equal with the good values or the fault is detected
J.A. Waicukauski et al., VLSI Systems Design, 1985
Notes: In a manner similar to that of parallel fault simulation, parallel-pattern single-fault propagation (PPSFP) takes advantages of bitwise parallelism that this time is used to simulate test patterns in parallel. For a computer with a b-bit data word, the signal values for a sequence of b test patterns are packed into a data word. Again, for the fault-free or faulty circuit, b test patterns can be simulated in parallel by utilizing bitwise logic operations. Interestingly, a fault simulator using the PPSFP framework cannot be event-driven, as events may occur only in some of the b vectors simulated in parallel. This implies that all gates in the circuit should be evaluated in every vector, in the order of their level. Let g denote the average fraction of gates that have events on their inputs in one vector. Then PPSFP will simulate 1/g more gates than an even-driven simulator. However, because we simulate in parallel b vectors, PPSFP is more efficient if b > 1/g. For example, b > 20 will suffice to compensate for g = 5%. The overall speedup is equal to gb. The original work by J.A. Waicukauski et al. used b = 256 to successfully evaluate large sets of random test patterns.

## Slide 6: PPSFP
First, fault-free simulation of a group of vectors is run
The remaining undetected faults are serially injected and faulty values are computed in parallel for the same set of vectors
The propagation of fault effects continues as long as faulty values are different from the good values in at least one vector
Detected faults are dropped and the above steps are repeated until all vectors are simulated or all faults are detected
Notes: PPSFP is best suited for simulation of test patterns that come later in the test sequence, where the fault drop rate per pattern is low. It is worth noting that conventional parallel fault simulation does not perform well in this case as it cannot terminate a given pass until all faults being processed are detected. On the other hand, PPSFP cannot be used for sequential circuits since the circuit state for test pattern p in the b-bit word is dependent on the previous p – 1 patterns in the word, and this state is not available when the patterns are processed in parallel.

## Slide 7: Pros and cons
Parallel fault simulation
  a large number of faults are detected by each pattern when simulating the beginning of a test sequence
  only applicable to the unit or zero delay models
  faults cannot be dropped unless all (b – 1) faults are detected
PPSFP
  fault is dropped as soon as detected
  best for simulating test patterns that come later, where fault dropping rate per pattern is lower
  not suitable for sequential circuits
Notes: This slide basically compares advantages and disadvantages of two primary fault simulation techniques that rest on bitwise parallelism inherent in the computer to reduce fault simulation time. As shown earlier, there are two ways to bring parallelism into fault simulation: process faults in parallel, or alternatively handle test patterns in parallel.

## Slide 8: Deductive fault simulation
The method deduces faults that cause each signal to have a value different than its fault-free value
Two steps:
  the fault-free simulation to determine all values of signal lines
  for each line in the circuit, a list of single faults is determined such that each fault changes the line value, if it occurs
Lists processed in a levelized order of signal lines
Lists of faults associated with the primary outputs determine all faults detected by the input vector
D.B. Armstrong, IEEE Trans. Computers, 1972
Notes: The deductive fault simulation is based on logic reasoning rather than simulation, as done in the previous techniques. Given a test pattern, this approach identifies, all at once, faults that can be detected. In principle, the deductive fault simulation can be very time-efficient since the actual simulation has to be performed for a fault-free circuit only.
The method links a fault list Lx with a signal line x. The list Lx is comprised of faults that cause x to differ from its fault-free value. Given the fault-free values and the fault lists associated with the inputs of a gate, the basic step in deductive simulation is to compute the fault-free output value and the output fault list. The latter step is called fault-list propagation. Before we proceed to show how fault-list propagation can be carried out, it is worth noting that deductive fault simulation can save lots of memory. Indeed, parallel fault simulation needs to store the value of a given signal line for all faulty circuits, despite the fact that the value of the line in most faulty circuits can be the same as in the good machine. This waste is avoided in deductive fault simulation by keeping only fault id’s that do corrupt the line value.

## Slide 9: Calculation of fault lists - AND
a
b
c
0
0
0
a
b
c
1
0
0
a
b
c
0
1
0
a
b
c
1
1
1
Lc = La  Lb  c1
Lc = La – Lb  c1
Lc = Lb – La  c1
Lc = La  Lb  c0
La, Lb, Lc – lists of faults associated with lines a, b, c
Notes: This slide illustrates how to determine the output fault lists for the AND gate and all possible input vectors assuming that there are two fault lists La and Lb associated with inputs a and b of the gate. Recall that faults occurring on list La (Lb) causes line a (b) to differ from its fault-free value. Now, if the input vector ab is equal to 00, then only a fault that occurs on both lists La and Lb will cause the output c to be erroneously 1. Indeed, we need to change (erroneously) both inputs from 0 to 1 to force such a change on the gate output. This is why the output list becomes an intersection of both input lists. Furthermore, the output may differ from its fault-free value due to a local fault c/1. This fault is therefore added to the final list.
Let now ab = 01. Then c = 0, and any fault that causes a to be 1 without changing b, will cause c to be in error, i.e., c = 1. These are the faults in La that are not in Lb. That’s why we will use here a set difference. Note that a fault whose effect propagates to both a and b does not effect c. Again, the local fault c/1 is added to the final output list Lc.
If ab = 11, then any fault that propagates to either a or b, or both at the same time, will cause the output to be erroneously 0. Thus, the output fault list is simply a union of La and Lb, that is, it is the set of all faults which are members of either La or Lb (plus a local fault c/0).

## Slide 10: Calculation of fault lists - OR
a
b
c
0
0
0
a
b
c
1
0
1
a
b
c
0
1
1
a
b
c
1
1
1
Lc = La  Lb  c1
Lc = Lb – La  c0
Lc = La – Lb  c0
Lc = La  Lb  c0
Notes: The fault list propagation for OR gate is done in a similar manner to that of AND gate.
If ab = 00, then any fault that propagates to either a or b, or both at the same time, will cause the output to be erroneously 1. Thus, the output fault list is simply a union of La and Lb, that is, it is the set of all faults which are members of either La or Lb (plus a local fault c/1).
Let now ab = 01. Then c = 1, and any fault that causes b to be 0 without changing a, will cause c to be in error, i.e., c = 0. These are the faults in Lb that are not in La. That’s why we will use here a set difference. Note that a fault whose effect propagates to both a and b does not effect c. Again, the local fault c/0 is added to the final output list Lc.
If the input vector ab is equal to 11, then only a fault that occurs on both lists La and Lb will cause the output c to be erroneously 0. Indeed, we need to change (erroneously) both inputs from 1 to 0 to force such a change on the gate output. This is why the output list becomes an intersection of both input lists. Furthermore, the output may differ from its fault-free value due to a local fault c/0. This fault is therefore added to the final list.

## Slide 11: Example
La = {a0} Le = Lb – La  {e1} = {b1, e1}
Lb = {b1} Lf = {b1, f1}
Lc = {c0} Lg = {b1, f1, g0}
Ld = {d0} Lh = Le – Lc  {h1} = {b1, e1, h1}
Lk = Lg  Ld  {k0} = {b1, d0, f1, g0, k0}
Ln = Lk – Lh  {n0} = {d0, f1, g0, k0 , n0}
d
a
b
c
e
f
g
h
k
n
0
0
0
1
1
1
1
1
1
Notes: Consider the circuit shown on the slide. Suppose the applied test vector is abcd = 1011. Clearly, the fault lists associated with the primary inputs comprise just local faults with the opposite polarizations than that of the fault-free values. Hence we have: La = {a/0}, Lb = {b/1}, Lc = {c/0}, and Ld = {d/0}. The fault lists for lines e and f (the fault-free value is equal here to 0) must contain faults that will cause these lines to differ from the fault-free value. In addition to local faults e/1 and f/1, any fault on list Lb is able to change the output of the first AND gate provided that there is not the same fault on the list La. Thus, we have a difference of Lb and La, which is essentially equal to {b/1}. The list Lg is simply a copy of Lf extended by a local fault g/0. The list Lh and Lk are determined in a similar fashion by using the formulas derived earlier. Finally, the output fault list is obtained by subtracting Lh from Lk as the fault free values on the inputs of the OR gate are equal to 0 and 1, respectively. Note that fault b/1 occurs on both lists, and therefore it is eventually missing on the list associated with primary output. Indeed, as can be easily verified, fault b/1, if present, would cause both lines: h and k to change erroneously their values at the same time, thus preserving the correct value on the output. As a result, this particular fault would not be detected. As can be seen, the output list is comprised of all faults that test pattern 1011 can detect in the circuit. Note that in this example we did not perform any form of fault collapsing to initially reduce the fault list.

## Slide 12: Concurrent fault simulation
The method simulates
  the good circuit, and
  for every faulty circuit only those elements that are different from the corresponding ones in the fault-free circuit
The differences are maintained for every element in the circuit as a fault list
E.G. Ulrich, T.G. Baker, IEEE Computer, 1974
Most of the time during simulation, most of the values in most of the faulty circuits agree with their corresponding values in the fault-free circuit
Notes: Because a fault only affects logic in the fan-out cone from the fault site, the good circuit and faulty circuits typically differ in small areas. Concurrent fault simulation exploits this observation and simulates only the differential parts of the entire circuit. In principle, this approach is a conventional event-driven technique with the fault-free circuit and faulty circuits simulated altogether.
In the concurrent fault simulation, each gate retains (conceptually) a list of items each of which stores the status of a fault exhibiting a difference from a fault-free value. Theoretically, all faults in a circuit could be processed in a single pass. Memory explosion problem, however, restricts the number of faults in each round.

## Slide 13: Fault list
a = 0
b = 1
c = 0
1
1
1
0
0
0
1
1
1
0
1
0
A
B
a1
b1
Fault-free
A, B – faults whose effects propagate to the gate and cause a = 1 and b = 0, respectively
Local faults remain on the list even if all values agree with the fault-free ones
Compare: deductive fault simulation Lc = {A, a1}
More storage required
Notes: As mentioned earlier, in the concurrent fault simulation, every gate maintains a fault list, which consists of a set of faulty gates (yellow gates on the slide). A faulty gate of gate G represents an imaginary copy of gate G in the presence of a fault. Every faulty gate contains a fault index and the associated gate I/O values in the presence of the corresponding fault. Initially, the fault list of gate G contains local faults of gate G. The local faults of gate G are faults on its inputs or outputs. As simulation proceeds, the fault list contains not only local faults but also faults propagated from preceding stages of a circuit. Local faults of gate G remain in the fault list of G until they are detected.
Consider, as an example, a list shown on the slide. The fault-free circuit consists here of a single AND gate with the input stimulus ab = 01. Faulty gates A and B represent faults whose effects reach the inputs of the gate in such a way that inputs a and b becomes erroneous, respectively. Note that in the first case the output of gate is erroneous as well. In the second case (B) the output remains unaffected, but since one of the inputs is different from its corresponding fault-free value, we retain a copy of the faulty gate of the list. The two remaining faulty gates correspond to local faults: line a stuck-at-1 and line b stuck-at-1. Only fault a1 causes the output to change its value, but as a local fault, also b1 is kept on the list until detected. By contrast, the fault list of c in deductive fault simulation would comprise only two elements: A and a1.

## Slide 14: Handling fault lists
Initially, every list L(x) consists of entries corresponding to the local faults of element x
During simulation new entries represent element xf, whose values are different from values of x – they diverge from x
Entries removed from the list represent element xf whose values are identical to x – they converge to x
Removing a fault leads to removal all corresponding entries from all lists
Event-driven simulation
Notes: Most of the time, the concurrent fault simulation spends updating data structures that represent the fault lists. Fault insertion takes place during the initialization phase; the initial content of every list L(x) consists of entries corresponding to the local faults of x. During simulation, new entries in L(x) represent elements whose values become different from the values of x; these are said to diverge from x. Conversely, entries removed from L(x) represent elements whose values become identical to those of x; these are said to converge to x. A fault is dropped by removing its entries from every list where it appears.

## Slide 15: Changes in fault lists
1
1
0
1
1
0
1
0
1
0
0
1
1
0
1
0
1
1
1
0
1
0
1
1
a1
a
a
b
c
d
c1
d1
a
b
e
0
1
1
1
1
0
0
0
1
0
0
1
1
0
1
0
1
1
1
0
1
0
1
1
a1
a
c1
d1
a
b
a
0
1
1
1
1
0
0
0
1
1
0
1
0
0
1
1
0
1
1
1
0
1
1
0
a1
a1
c1
b
d1
1  0
0  1
1  0
Remains on the list as a local fault
Notes: The leftmost part of the slide shows a circuit in a stable state with the logic values and associated fault lists. Assume that the primary input a changes from 1 to 0. This event occurs not only in the good circuit but also in all the faulty circuits that do not have entries in L(c): the entries in L(c) have to be analyzed separately. In the good circuit, c is scheduled to change from 0 to 1. The event on a does not propagate in the circuit a1, hence that gate is not evaluated. Evaluating gate ca does not result in any event. When the value of c is updated, the fault a1 becomes visible. In the good circuit, the change of c propagates to the gate e. At the same time, we propagate a list event to indicate that a1 is a newly visible fault on line c (see the figure in the center of the slide). The evaluation of gate e in the good circuit does not produce any output event. An entry for the newly visible fault a1 is added to L(e). The other entries in L(e) are analyzed as follows (the rightmost figure): c does not change in the circuit c1 – the entry for c1 remains in the list because c1 is a local fault of gate e; gate e in the circuit d1 is evaluated and generates a 1/0 event – the same event occurs in the circuit beta; c does not change in the circuit alpha – the entry for alpha is deleted from the list.

## Slide 16: Pros and cons
Deductive fault simulation
  very efficient
  simulate all faults in one pass
  not easy to handle unknowns
  only for zero-delay timing model
  potential memory management problem
Concurrent fault simulation
  efficient
  memory problem: size of the fault list changes at run time
Notes: Various arguments suggest that concurrent fault simulation is faster than the deductive method. One significant difference between the two techniques is that a concurrent simulator processes only the active faulty circuits. This difference becomes more apparent when changes occur only in faulty circuits and especially when a faulty circuit oscillates. The reason is that a deductive simulator always re-computes a complete fault list (even to add or to delete a single entry), while a concurrent simulator propagates changes only in the active circuit. Another difference is that a concurrent simulator, being based on evaluation of individual elements, can make use of fast evaluation techniques, such as lookup tables or input counting.
The main disadvantage of concurrent fault simulation is that it requires more memory than the other methods. The reason is that values of every element in a fault list must be available for the individual evaluation. However, this disadvantage can be overcome by partitioning the set of faults for multi-pass simulation.

## Slide 17: Critical path tracing
For every test pattern the method first simulates the fault-free circuit, then determines detected faults by ascertaining critical values
A line x has a critical value v in test pattern T if and only if T detects fault x s-a-v’ – line x is critical in T
Lines critical in test T immediately indicate faults detected by T
The primary outputs are critical in any test
The other critical lines are found by backtracking from primary outputs; this process determines critical paths
M. Abramovici et al., IEEE Design & Test, 1984
Notes: Critical path tracing is another popular fault simulation technique. To demonstrate its particulars we need first to introduce a few key terms. A line L is said to be critical with respect to a pattern T if and only if T detects the fault L/v’ when the fault-free value of L is v in T. A path consisting of critical lines only is a critical path. In other words, a critical path is a path, usually staring from a primary output, in which each line has a fault detected by the applied pattern. Hence, by tracing the critical path from a primary output to a primary input gives a critical lines and therefore a list of detected faults. It is worth noting that the primary outputs are always critical in any test pattern.

## Slide 18: Sensitive inputs
A gate input is sensitive in test T if complementing its value changes the value of the gate output
If only one input has a controlling value of the gate, then this input is sensitive
If all inputs have a non-controlling value, then all inputs are sensitive
Otherwise, no input is sensitive
If a gate output is critical, then its sensitive inputs, if any, are also critical
Notes: We can link the global property of criticality with the local property of sensitivity. A gate input x is sensitive, if complementing the value of x changes the value of the gate output. For example, an AND gate with the output value of 1 has all its inputs sensitive, while with the output value of 0, it has one of its inputs to be sensitive provided it is set to 0, and the other inputs are set to 1. In general, If only one input has a controlling value of the gate, then this input is sensitive. Moreover, if all inputs have a non-controlling value, then all inputs are sensitive. In the remaining cases, no input is sensitive. The relation between sensitivity and criticality (that forms the basis of the critical path tracing approach) is that a gate input x is critical with respect to a test pattern T, if the gate output is critical, and x is sensitive with respect to T.

## Slide 19: Fanout-free circuit - example
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
0
0
This part does not have to be analyzed it is not critical
sensitive input
Notes: This slide shows a circuit, its line values for a given test pattern, and the sensitive gate inputs (marked by dots). Critical path tracing starts by marking the primary output as critical. The other critical lines are identified by a recursive application of the rule from the previous slide. The critical lines are shown here as the red (bold) lines. It is worth observing that critical path tracing has completely avoided the indicated (lower) part of the circuit, because by working backward from the output, it first determined that the two lower inputs of the OR gate are not critical. It is in a visible contrast to a conventional fault simulation that would propagate the effects of all faults in this area to the inputs of the OR gate, just to eventually discover that these faults are not detected on the output of this gate (because of the controlling value occurring on the first input of the gate). The presented approach can be easily adopted for fan-out-free circuits, as a simple depth-first tree-traversal suffices to mark as critical and recursively follow every sensitive input of a gate with critical output. However, it becomes more complicated when it comes to handling designs with reconvergent fan-out structures, as shown on the next slide.

## Slide 20: Stem analysis
1
0
1
1
1
1
1
0
1
1
0
1
Problem: is a stem critical given that some of its branches are critical ?
Stem is self-masking
Stem is critical
Notes: Consider and example shown on this slide. Let the upper circuit be stimulated by the test pattern 111. Critical path tracing starts at the primary output, and by repeatedly applying the rule from the previous slides, it identifies critical lines (in red). It cannot, however, determine whether the stem (here the second primary input) is critical without additional analysis. Indeed, the effects of the stem fault stuck-at-0 propagate on two paths with different inversion parities such that they cancel each other when they reconverge at the OR gate. This phenomenon, referred to as self-masking, does not occur for the test pattern 110 shown in the lower figure. This is because the propagation of the fault effect along the path starting at the input of the inverter stops at the subsequent AND gate. In this case, therefore, the stem is critical. The main problem is now to determine whether a stem x is critical, given that some of its fan-out branches are critical.

## Slide 21: Capture lines
T – test that activates fault F in a single-output combinational circuit
x – line with level L(x), sensitized to F by T
If every path sensitized to F either goes through x or does not reach any line with level greater than L(x), then x is a capture line of F in T
Test T detects the fault F if and only if all the capture lines of F in T are critical in T
1
1
1
1
1
1
1
1
1
0
1
s-a-0
1
Notes: To solve the problem of stem criticality, critical path tracing employs the concept of capture lines. Let T be a test that activates fault F in a single-output combinational circuit. Let also x be a line with level L(x), sensitized to F by T. If every path sensitized to F either goes through x or does not reach any line with level greater than L(x), then x is said to be a capture line of F in T. A capture line, if one exists, is a bottleneck for the propagation of fault effects, because it is common to all the paths on which the effects of F can propagate to the primary output in test T. If T detects F, then there exists at least one capture line of F, namely the primary output itself. If the effect of F propagates on a single path, then every line on that path is a capture line of F. For example, the capture lines of the fault stuck-at-0 (as shown on the slide) are indicated by the red lines. The above observations bring us to the following conclusion: test T detects the fault F if and only if all the capture lines of F in T are critical in T.

## Slide 22: Critical stem
To determine whether a stem is critical, there is no need to propagate the stem fault effects to a primary output as in explicit fault simulation
It suffices to propagate fault effects to the closest capture line of the stem fault – the stem is critical iff the capture line is critical
Since capture lines are defined for a single-output circuit, a circuit is partitioned into single-output cones with logic feeding one primary output
Within each cone, fanout-free regions (FFR) are identified
  the inputs of an FFR are checkpoints of the circuit
  the output of an FFR is either a stem or a primary output
Notes:   The last observation on the previous slide and the transitivity property of a set of capture lines indicate that in order to determine whether a stem is critical, there is no need to propagate the stem fault effects to a primary output as in explicit fault simulation. On the contrary, it suffices to propagate fault effects to the closest capture line of the stem fault – the stem is critical if and only if the capture line is critical. Since capture lines are defined for a single-output circuit, circuits with more than one primary outputs are typically partitioned into single-output cones with logic feeding one primary output. To take advantage of the simplicity of critical path tracing in fan-out-free circuits, so-called fan-out-free regions (FFR) are identified within each cone. The inputs of an FFR are checkpoints of the circuit (branches and/or primary inputs), whereas the output of an FFR is either a stem or a primary output. Constructing cones and FFRs is a preprocessing step of the main procedure.

## Slide 23: Cones and FFRs in full adder
CO
CI
B
A
S
FFR
FFR
Notes: This slide shows a structure of a full adder with three primary inputs A, B, and CI (carry in), as well as with two primary outputs: S(um) and CO (carry out). All FFRs are shown in the figure using different colors for two cones (corresponding to the primary outputs).

## Slide 24: CPT algorithm - outline
We assume that fault-free circuit simulation is done, and the circuit is decomposed with sensitive inputs determined
for every primary output w
stems to check = 0
perform critical path tracing inside FFRs (w)
while (stems to check ≠ 0)
r = the highest level stem in {stems to check}
remove r from {stems to check}
if (stem r is critical) then
perform critical path tracing inside FFR(r)
Notes: This slide outlines the critical path tracing algorithm for evaluating a given test pattern. It assumes that fault-free simulation, including the marking of the sensitive gate inputs, has already been performed. The algorithm processes every cone starting at its primary output and alternates between two main operations: critical path tracing inside an FFR, and checking a stem for criticality. Once a stem is found to be critical, path tracing continues from that stem. Performing critical path tracing inside a given FFR is done recursively by backtracking all the critical paths inside an FFR starting from a given critical line by following lines marked as sensitive. The procedure stops at FFR inputs and collects all the stems reached in the corresponding set of stems to check. Checking whether a given stem is critical is done by a breadth-first propagation of the effects of the stem fault.

## Slide 25: Example
1
1
0
1
1
0
1
1
0
1
1
Test pattern 111 detects faults on critical lines
For the second output the analysis is similar
S
Notes: The figure shows the critical paths in the full-adder cone driving the primary output S for the test pattern 111. These results were obtained after running critical path tracing for the first cone (the sum output) starting at the primary output S and then processing successive FFRs (shown as yellow triangles in the figure). Note that when we analyze a stem, we have already backtracked a critical path between a primary output and one of the fan-out branches of the stem. The effect of the stem fault would propagate on the same critical path, unless self-masking occurs. This may take place only when effects of the stem fault reach a reconvergence gate on paths with different inversion parities.

## Slide 26: Stem regions
Reconvergent fanout stem has its stem region
This region is bounded by exit lines such that when the stem fault is detectable on the exit line, and the line is critical, then the stem fault is detectable on the corresponding primary output
Stem faults need not be explicitly simulated beyond the exit lines, contrary to being propagated to primary outputs, as done in exact fault simulation
Stem regions may overlap; its degree corresponds to the maximum number of stem faults that may have to be processed on a line
F. Maamari, J. Rajski, IEEE Trans. CAD, 1993
Notes: It was shown that employing critical path tracing in PPSFP may result in a substantial simulation speed-up as it eliminates explicit fault simulations for faults within fan-out free regions. Furthermore, the dominator concept can be used in a single fault propagation. It can be readily applied to PPSFF to again reduce explicit fault simulation area. Finally, the stem region concept was introduced to decrease explicit fault simulation area for multiple output circuits. This approach simulates each region only once. Each stem region is first simulated to the exit lines (see the next slide) in the forward order and then the fan-out free regions in the backward order. The detectability of each stem is computed at the exit lines of the stem. If a stem S is not detectable at any of its exit line, the input cone of the stem, FFR(S), is pruned off. The backward simulation enables the computation of the global detectability of each signal line (with respect to primary outputs). If the detectability of a signal line is 0, then the input cone of the line is pruned off.

## Slide 27: Stem regions
Exit lines
Stem region for the second stem includes all lines and nodes except the primary inputs
G1
G2
G3
G1
G2
Notes: Let x be a line in the stem region of a stem A. x is an exit line for stem A if the following two conditions are met:
x is an output line of a node that is in the stem region of A,
x is an input line of a node that is not in the stem region of A.
The exit lines of a stem region are the lines through which a logic signal can exit the stem region. The exit lines for the red stem region are shown in the figure. As can be further verified, the two reconvergent fan-out stems in the lower figure have one exit line each.
Two circuits are used here to illustrate some concepts deployed by the stem region method. In the upper circuit, red circles are reconvergent fan-out stems. Gates G1 and G2, are primary reconvergence gates for the leftmost stem, while gate G3 is a primary reconvergence gate for the second stem. In the lower circuit, the red and blue circles are both reconvergent fan-out stems, and G1 and G2 are primary reconvergence gates for the red and blue stem, respectively. The stem region of a reconvergent fan-out stem A is composed of all the circuit nodes such that they are reached by the reconvergent fan-out stem, they reach a closing reconvergence gate of stem A, and of all the output lines of these nodes (fan-out branches of a stem and output of a gate). There are two stem regions in the first circuit. The stem region of the leftmost red circle is composed of all nodes. The other stem region is composed of red gates and lines. Two stem regions (red and blue) are also present in the lower circuit, where they are disjoint, as opposed to the stem regions of the upper figure that overlap each other.

## Slide 28: Fault simulation complexity
Computational complexity of fault simulation may determine efficacy of various ATPG techniques
Worst-case time complexity is O(N2), where N is the number of lines
Linear time algorithm for fault simulation is very unlikely
Average time for deductive simulation is O(G3) and for concurrent simulation O(G2), G – the number of gates
For long experiments, most of the time taken by fault-free circuit simulation
Notes: The computational complexity of fault simulation is proportional to the product of the circuit size, the number of faults, and the test set size. In general, there is a linear dependency of the test set size and the single stuck-at fault number on the circuit size which can be represented by the number of gates. Then the complexity of fault simulation is O(G3) – see, for example, the deductive simulation. This is higher than logic simulation but remarkably lower than test pattern generation. This is why fault simulation is used instead of ATPG whenever possible. The number of faults is one of three dimensions of complexity. It primarily depends on an assumed fault model, and may range from O(G) for single stuck-at faults to O(2G) for single path delay faults. Clearly, the number of faults can be significantly reduced by fault collapsing, e.g., simple local fault collapsing can reduce the number of single stuck-at faults by almost 50%, as we have seen earlier. Moreover, whenever a fault is detected, it can be dropped, thus effectively reducing the size of a fault list (unless fault simulation is performed for applications such as built-in self-test).
PPSFP and concurrent fault simulation techniques are currently the most popular fault simulation techniques for combinational circuits, with concurrent simulation being also adopted for sequential designs.

## Slide 29: Statistical fault analysis
00000
01010
10101
a
b
c
C1(a) = 0.6
C0(a) = 0.4
S(a) = 0.4
C1(b) = 0.4
C0(b) = 0.6
S(b) = 0.6
C1(c) = 0.0
C0(c) = 1.0
O(c) = 1.0
From logic simulation of a fault-free circuit
Cx(L) – probability of having line L in state x
S(L) – probability that line L is sensitive
O(L) – probability of observing an error from line L on the output (observability; for primary outputs = 1.0)
Notes: Statistical fault analysis (STAFAN) is a popular alternative to fault simulation. This type of analysis requires only fault-free simulation of a circuit. It utilizes the calculation of controllability and observability of the circuit nodes which are further computed as the probabilities estimated from the signal statistics provided by fault-free simulation. The detection probability of a fault and fault coverage are then computed from the appropriate controllability and observability measures. These measures are defined as follows. C1(a) or 1-controllability of line a is the probability of setting line a to the value of 1 by a random pattern. Similarly, C0(a) or 0-controllability of line a is the probability of setting line a to the value of 0 by a random pattern. C0(a) and C1(a) are typically given by the number of times the node a assumes the value of 0 or 1, respectively, divided by the total number of input vectors.
The observability of line a represents the probability that given patterns propagate the fault effect on line a to the primary outputs. During fault-free simulation, STAFAN counts the number of times that every gate input is sensitized to its gate output. The sensitization probability S(x) is then obtained by dividing the sensitization count of gate input x by the number of test patterns. The observability of primary outputs is 1, because fault effects on primary outputs are always observed. The observability of a gate input x is S(x) times the observability of its gate output. The observability of every line can be calculated from primary outputs to primary inputs. Every line in the circuit has a sensitization counter. This counter is incremented when the path from the corresponding line to the output is sensitized. As in the case of controllability, the sensitization probability for line a can be determined as a ratio of the sensitization counter and the total number of input vectors.

## Slide 30: STAFAN
S.K. Jain, V.D. Agrawal, IEEE Design & Test, 1985
P(line x stuck-at-1) = C0(x)*O(x)
P(line x stuck-at-0) = C1(x)*O(x)
The probability of detecting a fault
Observability computed from the outputs. A fault from input x of a gate must propagate to the output m of the gate, and then to the circuit output:
O(x) = S(x)*O(m)
By assumption, events are independent (not always satisfied – see re-convergent fanouts)
Notes: The circuit is back traced until the observability for each node is determined. The observability is calculated as the probability that an error on a given input will propagate to the gate output, multiplied by the corresponding observability of the gate’s output node. Finally, the probability of detecting a given fault is determined as a product of the corresponding controllability (fault excitation) and observability (propagation of fault effects to at least one observation point).
It is worth noting that the observability calculation becomes complicated in the presence of fan-out branches. The lower bound of the observability of a fan-out stem is the maximum value of the observability of its branches. The upper bound of a fan-out stem is the union of the observability of its branches. This particular bound assumes that observing the fault effect via each fan-out branch is an independent event. Eventually, the observability of a fan-out stem is a linear combination of its upper and lower bounds. Unfortunately, in the presence of fan-out reconvergence, the independent observation of fan-out branches is not a valid assumption anymore.