## Slide 1: VLSI testing
Memory test
HEP
Notes: The rapid growth in complexity of random access memories (RAM), read-only memories (ROM), and other types of semiconductor storage devices, as well as their unprecedented increase in density, have triggered interest in memory testing capable of providing composite tests of ultimate quality. Because of numerous ways memories can fail, memory test procedures are required to detect a wide spectrum of complex faults and provide information that can be used for diagnosis and repair purposes. Embedded memories can present even more serious testing problems. The integration of RAMs and ROMs with other logic on the same chip precludes applying test patterns directly to the memory, as the embedded memory's data, address, and control signals are not directly accessible through the primary inputs and outputs of the integrated circuit. The memory test has already established itself as one of the mainstream VLSI test technologies with many distinguished features, properties, methodologies, and even with its own fault models. This chapter will tackle some of the key concepts in this vital area of science and industrial practice.

## Slide 2: Basic problems
Embedded memories often take up most of a chip’s area in SoC designs
Many embedded memories with different architectures implemented on a single chip
High performance devices
High density – interactions between memory cells
Need for efficient diagnostic tools allowing built-in repair based on spare elements
Notes: International Technology Roadmap for Semiconductors predicts that embedded memories will occupy over 90% of the silicon real estate on most system-on-chip (SoC) designs in 2014. Due to their ultra large scale of integration and vastly complex structures, memory arrays are far more vulnerable to defects than the remaining parts of integrated circuits. Embedded memories have already started introducing new yield loss mechanisms at a rate, magnitude, and complexity large enough to demand major changes in test procedures. Many types of failures, often not seen earlier, originate in the highest density areas of semiconductor devices where diffusions, polysilicon, metallization, and fabricated structures are in extremely tight proximity to each other. Failing to properly test all architectural features of the embedded memories can eventually deteriorate the quality of test, and ultimately hinder yield. Moreover, simple fault detection is no longer enough for embedded memories in the SoC era. In fact, memory diagnosis is quickly becoming a critical issue as far as manufacturing yield and time-to-volume of SoC products are concerned. Some solutions may not be adequate to support advanced failure analysis that typically help improving yield of SoC designs.
Memory testing was the key methodology behind bringing up new technology nodes. This is because memory structures are very dense, but relatively easy to test. However, in recent technology nodes it becomes apparent that one can no longer learn from memory alone since the structures are too regular. Logic cells (AND, OR, …) are more irregular, and need more complicated DRC / DFM rules.

## Slide 3: Types of memories
SRAM (static)
  uses latches, does not require refresh, fast, volatile
DRAM (dynamic)
  needs refresh, volatile, very dense
Flash
  performs read and write, non-volatile
ROM
  programmed at manufacturing time, non-volatile
EPROM
  programmed by the user, data is erased by UV radiation
EEPROM
  data is erased electrically
CAM, MRAM and others
Notes: The memory type may determine test methods used to detect and diagnose certain faults that occur in these devices. Semiconductor memories can be split into two main types, according to the way in which the memory operates:
RAM - Random Access Memory: this is a form of semiconductor memory technology that is used for reading and writing data in any order as required. Data is stored and read many times to and from this type of memory.
ROM - Read Only Memory: here the data is written once and then not changed. It is used where data needs to be stored permanently, even when the power is removed.
There is a large variety of ROMs and RAMs. These arise from the variety of applications and also the number of technologies available. They include:
DRAM: it uses a capacitor to store each bit of data, and the level of charge on each capacitor determines whether that bit is a logical 1 or 0. However, these capacitors do not hold their charge indefinitely, and therefore the data needs to be refreshed periodically. This dynamic refreshing justifies its name. DRAM is often used in equipment including personal computers and workstations where it forms the main RAM for the computer.
SRAM: Static Random Access Memory gains its name from the fact that, unlike DRAM, the data does not need to be refreshed dynamically. It is able to support faster read and write times than DRAM, and its cycle is much shorter because it does not need to pause between accesses. However, it consumes more power, is less dense and more expensive than DRAM. As a result, it is normally used for caches, while DRAM is used as the main semiconductor memory technology.
SDRAM: Synchronous DRAM. This form of memory can run at faster speeds than conventional DRAM. It is synchronized to the clock of the processor and is capable of keeping two sets of memory addresses open simultaneously. By transferring data alternately from one set of addresses, and then the other, SDRAM cuts down on the delays associated with non-synchronous RAM, which must close one address bank before opening the next.
MRAM: This is Magneto-resistive RAM, or Magnetic RAM. It is a non-volatile RAM memory technology that uses magnetic charges to store data instead of electric charges. Unlike technologies including DRAM, which require a constant flow of electricity to maintain the integrity of the data, MRAM retains data even when the power is removed. An additional advantage is that it only requires low power for active operation.
PROM: It stands for Programmable Read Only Memory. It is a semiconductor memory which can only have data written to it once – the data written to it is permanent. These memories come in a blank format and they are programmed using a special programmer. Typically a PROM will consist of an array of fuses some of which are "blown" during the programming process to provide the required data pattern.
EPROM: This is an Erasable Programmable Read Only Memory. It can be programmed and then erased at a later time. This is normally achieved by exposing the silicon to ultraviolet light.
EEPROM: or Electrically Erasable Programmable Read Only Memory. Data can be written to it and it can be erased using an electrical voltage. This is typically applied to an erase pin on the chip. Like other types of PROM, EEPROM retains the contents of the memory even when the power is turned off. Also like other types of ROM, EEPROM is not as fast as RAM.
Flash memory: Flash memory may be considered as a development of EEPROM technology. Data can be written to it and it can be erased, although only in blocks, but data can be read on an individual cell basis. To erase and reprogram areas of the chip, programming voltages at levels that are available within electronic equipment are used. It is also non-volatile, and this makes it particularly useful.
CAM: content-addressable memory is a special type of computer memory used in certain very high speed searching applications. It is also known as associative memory or associative storage. Unlike standard computer memory in which the user supplies a memory address and the RAM returns the data word stored at that address, a CAM is designed such that the user supplies a data word and the CAM searches its entire memory to see if that data word is stored anywhere in it. If the data word is found, the CAM returns a list of one or more storage addresses where the word was found (and in some architectures, it also returns the data word or other associated pieces of data).

## Slide 4: Functional model
b0
b2
b1
bB-1
4 words in a row
Column decoder
I/O register
Address
Row decoder
Notes: This slide shows the actual memory architecture (or more precisely, its functional model used in the majority of test generation schemes). Every row consists of W words (here W = 4), each B-bit long. Bits belonging to one word can be either placed one after another or be interleaved to form vertical segments, as illustrated on the slide by the white squares. Decoders guarantee the proper access to memory cells in either a fast row or a fast column addressing mode. Throughout this chapter, we assume that the memory is addressed in the fast column mode, and bits are interleaved in the memory words, though the algorithms presented on the remaining slides can easily extend to other memory organizations, as well.

## Slide 5: SRAM cell structure
BIT
BIT
word
word
VDD
T1
T2
T3
T4
T5
T6
Notes: The slide illustrates a six-transistor CMOS SRAM cell. It consists of the enhancement mode NMOS devices T1, T2, T5, and T6, and the enhancement mode PMOS devices T3 and T4. Transistor T1 forms an inverter together with depletion load device T3 – this inverter is cross-coupled with the inverter formed by T2 and T4, thus forming a latch. This latch can be accessed (for read and write operations) via the pass transistors T5 and T6. Addressing of the cell is done by using a two-dimensional addressing scheme consisting of a row address and a column address as shown on the previous slide. The row decoder allows only one row of cells to be selected at a time by activating the line “word” of that particular row. The selection of a particular cell in a row is done under control of the column decoder that activates the set of complementary bit lines (BIT and BIT’) of that particular cell. Data can be written by setting line “word” to 1 and driving lines BIT and BIT’ with data having complementary values. Because the bit lines are driven with more force that the force with which cell retains its information, the cell will be forced to the state presented on the lines BIT and BIT’. In the case of read operation, a row is selected by activating the corresponding “word”. The contents of the cells on a row are passed to the corresponding sense amplifiers via the BIT and BIT’ lines.

## Slide 6: Memory test time
Memory cycle: 60 ns
Memory size (n) | Algorithm complexity |  |  | 
 | n | nlog2n | n3/2 | n2
1M | 0.063s | 1.26s | 64.5s | 18h
4M | 0.252s | 5.54s | 515.4s | 293h
16M | 1.01s | 24.16s | 1.15h | 4691h
64M | 4.03s | 104.7s | 9.17h | 75060h
256M | 16.11s | 451.0s | 73h | 1200960h
1G | 64.43s | 1932.8s | 586h | 19215358h
2G | 128.9s | 3994.4s | 1658h | 76861434h
Notes: Assuming that a memory operational cycle takes 60 nanoseconds, this table demonstrates how the complexity of the memory test algorithm may impact test application time. The test complexity is expressed as a function of a memory size n, and the corresponding test time has been computed for four different classes of algorithms as well as for seven different memory sizes ranging from 1M to 2G. As can be seen, with the increasing complexity of the algorithm, memory test application time quickly increases and reaches virtually unacceptable values measured in tens and hundreds of hours. The same rule applies to the increasing size of tested memories. It is, therefore, of high importance to make sure that any algorithm used to test contemporary memory is feasible and offers a reasonable trade-off between test application time and the resultant test quality.

## Slide 7: Test levels
Chip level (reduced functional chip model)
Array level (memory chips with the chip select and control logic)
Board or system level
  refresh logic
  address registers
  data registers
  buffers
  error detection and correction logic
  board selection and the memory board controller
Notes: Memories are tested at different levels including stand alone memory arrays, arrays with their surrounding logic, and the entire boards or systems comprising memory blocks. Due to imperfections of the manufacturing process, there are memory dies that contain faulty cells. Manufacturers improve their yield by applying a laser repair process (in fact, the use of electrical fuses is increasing and becomes a dominant technique). This process cuts away the known bad memory cells and replaces them with spare cells on the same die (see the end of this chapter). In order to isolate the bad cells, one has to excite the entire memory array on the chip. That means every cell on the chip has to be exercised and tested. Selected test patterns are written into each cell and read back in special sequences and orders to verify their proper functionality. In order to reduce the test time, parallel chip testing is performed, usually with 8 to 16 chips in a row. The above test is performed at the wafer level with automatic die stepping probes. A special ink jet is also used to color mark the bad dies. The wafer is then sent off for laser repair and to the backend for die separation and final packaging. Functional test is performed again at the post package level.

## Slide 8: Fault models
Stuck-at-0 and stuck-at-1
Transition /0 and transition /1
Dynamic coupling
Idempotent (set/reset) coupling
Inversion coupling
AND bridging and OR bridging
Passive neighborhood pattern sensitive faults
Active neighborhood pattern sensitive faults
Address decoder faults
Retention faults
A.J. van de Goor, John Wiley & Sons, 1991
Notes: Although various types of failures can occur in memories, they are usually modeled by means of the following four functional faults: the stuck-at fault (SAF), the transition fault (TF), the coupling fault (CF), and the neighborhood pattern sensitive fault (NPSF). Formal definitions of these faults, as well as conditions that have to be satisfied to detect them, are given, for example, in the book by A.J. van de Goor (see above) and numerous other books and papers devoted to memory test.

## Slide 9: Testing for stuck-at faults
The memory scan (MSCAN) test procedure
  write 0 in all cells
  read all cells
  write 1 in all cells
  read all cells
Complexity – 4n
MSCAN will not detect any stuck-at fault in the memory address register or in the decoder
At the end of the test we only know that there is at least one cell in the memory that is functionally correct (a fault could have occurred in the decoder such that the same cell is always referenced)
Notes: The memory scan is probably the simplest memory test procedure that targets stuck-at faults. This test writes each word, first with a 0, and then with a 1, and verifies the writing with two read operations. It is unable to detect any stuck-at fault in the memory address register or in the address decoder. Assuming, however, that these parts are fault-free, the MSCAN can detect any stuck-at fault in the memory array, in the memory data register, or in the read/write logic. Once the test is completed, one can only be sure that there is at least one cell in the memory that is functionally correct.

## Slide 10: The algorithmic test sequence (ATS)
Memory cells partitioned into 3 groups
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
G0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
G1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
G2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
G0 |  | w1 |  |  |  | r1 | w0, r0 | 
G1 | w0 |  | r0 | w1 |  | r1 |  | 
G2 | w0 |  |  |  | r0 |  |  | w1,r1
Decoder test
Complexity – 4n
w0 – write 0
w1 – write 1
r0 – read (expected) 0
r1 – read (expected) 1
Notes: ATS was proposed by Knaizuk and Hartmann in 1977. It detects any combination of stuck-at-0 or stuck-at-1 multiple faults in a RAM. In this approach, the memory cells are grouped into three partitions G0, G1, and G2 such that G0 = {Ck, k = 0 modulo 3}, G1 = {Ck, k = 1 modulo 3}, and G2 = {Ck, k = 2 modulo 3}. These partitions are shown in the upper table on the slide. The lower table illustrates the eight phases of the actual ATS procedure. It further assumes that the address decoder is of “noncreative” nature, that is, a single fault within the decoder does not create a new memory address to be accessed without also accessing the programmed address. As can be easily noticed, any stuck-at fault in any bit position at any cell in the memory array will prohibit reading either the all-0 word or the all-1 word from this place in the memory. Since ATS reads these two words from all storage locations, such a fault is detected. The next slides illustrates how ATS handles decoder faults (the red ovals on the current slide indicates test steps when the decoder faults are detected).

## Slide 11: Decoder faults
1
0
0
0
1
1
1
0
0
1
1
1
35
43
Write 0 in cell with address k
Write 1 in every cell whose address is Hamming distance 1 apart from k
Read cell with address k – expected 0
No cell is accessed with a given address
A given cell is never accessed
Multiple cells are accessed with a single address
A single cell is accessed with multiple addresses
Notes: Consider faults in the decoder input. Since memory locations are grouped into three different (disjoint) partitions, no single stuck-at fault in the decoder input can map an address in one partition into another address in the same partition. The sequence shown on the slide detects any fault in the input of the decoder. Clearly, any fault in the input causes a certain address from a given partition and at least one of addresses from another partition to access the same location. Thus, any multiple stuck-at fault in the decoder input will be detected by ATS. Since the decoder is noncreative, any stuck-at-0 fault in the decoder not masked by another stuck-at-1 fault will be propagated to the output of the decoder. This will inhibit the selection of at least one word line, causing a constant reading of 0 or 1, depending on the RAM implementation. Hence, the fault is detected because ATS must read both 0 and 1 from all cells. For example, let 43 be the address that will place 1 on a faulty stuck-at-1 line and also sensitize a path to the corresponding memory cell. Consider the address 35 that is Hamming distance 1 apart from 43 such that it places 0 on the site of the stuck-at-1 fault. This address will also sensitize the same path to the memory cell 43. Since cells 35 and 43 cannot be in the same partition of the address space, the fault will be detected due to reading 1 instead of 0 (or vice versa) as shown on the previous slide.

## Slide 12: Elements of march test
 (w0)
x
x
x
x
x
x
x
x
7
6
5
4
3
2
1
0
0
 (r1,w0)
1
1
1
1
1
1
1
1
 (w1)
 (r0,w1)
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
Notes: The algorithms most frequently used to detect SAFs, TFs, and CFs belong to a class of tests known as marches. The march tests consist of a sequence of operations (march elements) which are applied to each cell before proceeding to the next cell. The set of operations includes writing 0 (w0) and 1 (w1) into a cell and reading a cell (r). The cells are addressed according to the ascending (denoted by ) or descending order (denoted by ); for instance, w0 indicates that all the memory cells are initialized to 0 from address 0 to wk – 1. If the address order is irrelevant, it is denoted by .The following seven march tests are commonly used in practice:
MATS++:  w0; (r,w1,r); (r,w0,r);
MATS:  w0; (r,w1);  r;
MATS+:  w0; (r,w1);  (r,w0);
MATS++:  w0;  (r,w1,r); (r,w0,r);
March C:  w0;  (r,w1); (r,w0); r; (r,w1); (r,w0);  r;
March A:  w0; (r,w1,w0,w1); (r,w0,w1); (r,w0,w1,w0); (r,w1,w0);
March B:  w0; (r,w1,r,w0,r,w1);  (r,w0,w1); (r,w0,w1,w0); (r,w1,w0);
March G: March B + Delay; (r,w1,r); Delay; (r,w0,r);

## Slide 13: The MATS procedure – 4n
Modified Algorithmic Test Sequence
MATS is the shortest test that covers all stuck-at faults in RAMs, independently of the decoder design
Much simpler implementation than ATS
Every partition contains a single cell
 (w0),  (r0,w1),  (r1)
Notes: In 1979, Nair proposed a test sequence called Modified ATS (MATS) that detects any combination of stuck-at faults, irrespective of the design of the decoder combinational circuitry. The original test procedure was re-architected as illustrated on the slide. In terms of functionality, it is virtually the same as that of ATS, but has much simpler structure (resulting in a simple implementation). Furthermore, the concept of partitions has been changed in such a way that each single memory cell acts as a separate partition (note that it is expected that any single stuck-at fault in the input of the decoder cannot map an address in one partition into another address in the same partition – obviously having n partitions satisfies this criterion). Consequently, the test covers all stuck-at faults in RAMs, independently of the decoder design. A proof of MATS ability to detect all targeted faults is similar to that of ATS (discussed earlier).

## Slide 14: Testing for coupling faults
An aggressor cell (coupling cell) can couple into its neighbor cell (victim, coupled cell) and cause it to go to an erroneous state (a), or cause it to falsely transition (b)
A victim cell must be read after an aggressor cell changes its state (a)
A victim cell must be read after an aggressor cell changes its state an odd number of times (b)
Many algorithms detect coupling faults: Marching 1/0, Galpat, Walking 1/0, various march tests
Notes: Coupling faults can occur as a result of a short circuit or a circuit’s parasitic effects such as current leakage or stray capacitances. It is worth noting that when targeting the coupling faults (and their more complicated version known as pattern sensitive faults) memory bits cannot be treated as being functionally independent, as they could in the stuck-at fault model. For the sake of simplicity, therefore, we will assume that the memory under test is an array of n bits rather than an array of multiple-bit cells. Various test procedures such as Columns Bars, Marching 1/0, Galloping 1’s and 0’s (Galpat), Walking 1/0 have been introduced and are used in practice to test for different classes of coupling faults and stuck-at faults at the same time. Their complexity ranges from O(n) to O(n2). Depending on the erroneous behavior caused by a coupling fault – cases (a) and (b) on the slide – a test must comprise a certain sequence of actions as shown above.

## Slide 15: Coupling faults
A write operation which generates transition 0-1 or 1-0 in an aggressor cell changes the content of a victim cell (dynamic coupling fault)
A transition in an aggressor cell forces the content of a victim cell to a certain value (set/reset coupling fault)
A transition in an aggressor cell inverts the content of a victim cell (inversion coupling fault)
Notes: There are several classes of coupling faults (CF), as defined on the slide. They include dynamic CFs, set CFs, reset CFs, and inversion CFs.

## Slide 16: Linked faults
, 1
a
b
, 0
c
d
, 0
a
c
b = d
, 1
 (w0),  (r0,w1),  (w0, w1),  (r1)
Faults are detected
Faults are NOT detected – linked faults can mask each other
A victim cell has an expected content forced by another fault
Notes: When multiple faults occur in the memory array, then these faults can be either unlinked or linked. A fault is unlinked if that fault does not influence the behavior of other faults. On the other hand, a fault is linked when the fault may influence the behavior of other faults. Consider two coupling faults shown at the top of this slide. The first coupling fault is that cell b assumes the value of 1 when cell a undergoes transition from 0 to 1. The second fault is that cell d assumes the value of 0 when cell c undergoes transition from 0 to 1. The march test shown on the slide will detect both faults if b is different from d. In particular, the first fault will be detected by the “r0” operation of march element (r0,w1) when operating on cell b. The second fault will be detected by the “r1” operation of the last march element, when it operates on cell d.
The same test will not detect the combination of the faults which occurs when b = d (as shown at the bottom of the slide). The relation between faults can cause the effect called masking. The “r0” operation of the march element (r0,w1) will not detect the linked CF because when operating on cell b the cell will contain a 0 value due to the coupling fault (,0). The “r1” operation of the last march element will not detect the linked CF because, when operating on cell b, it will contain a 1 value due to the coupling fault (,1) sensitized by the march element (w0,w1) when it operates on cell c.

## Slide 17: Marching 0/1 – 14n
While scanning the memory in ascending order, any direct coupling between the current cell and a higher order cell is detected when reading the second cell
Scanning the memory in the descending order detects all the effects on lower numbered cells
All components of the MATS exist in the Marching 0/1
The algorithm features redundant actions
 (w0),  (r0,w1,r1),  (r1,w0,r0),  (w1),  (r1,w0,r0),  (r0,w1,r1)
0
0
n – 1
Coupling faults not detected
1
Notes: The idea behind Marching 0/1 algorithm is that, while scanning the memory in ascending order, any direct coupling between the current cell and a higher order cell is detected when reading the second cell. Similarly, scanning the memory in the descending order detects all the effects on lower numbered cells. As Marching 0/1 includes all elements of MATS, it covers all stuck-at faults. Unfortunately, there are coupling faults that may escape detection when deploying Marching 0/1. Among them, the most noticeable are as follows:
the coupling fault between cells A and B for B > A such that a 0-to-1 (1-to-0) transition in cell A will write a value of 0 (1) in cell B, as illustrated on the slide,
any two coupling faults that mask each other; for example, consider cells A, B, and C such that A < B < C; if a 0-to-1 (1-to-0) transition in cell A writes 1 (0) in cell C, and a 0-to-1 (1-to-0) transition in cell B writes 0 (1) in cell C, the fault between cells A and C is masked by the fault between cells B and C.
The complexity of this algorithm is O(14n).

## Slide 18: March C – 10n
Fault coverage: AFs, SAFs, TFs, CFins , CFids
 (w0)
 (r1,w0)
1
1
1
1
1
1
1
1
 (r0,w1)
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
 (r0,w1)
0
0
0
0
0
0
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
 (r1,w0)
1
1
1
1
1
1
1
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
 (r0)
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Notes: This is a test for unlinked idempotent coupling faults. Algorithm or March C is a test for unlinked inversion, idempotent 2-coupling faults and dynamic 2-coupling faults. This test is semi-optimal as the fourth march element is redundant – it may be removed without affecting the fault coverage. The resulting optimal test is called March C–.

## Slide 19: Marches A (15n) and B (17n)
 (w0),
 (r0,w1,w0,w1),  (r1,w0,w1),
 (r1,w0,w1,w0),  (r0,w1,w0)
 (w0),
 (r0,w1,r1,w0,r0,w1),  (r1,w0,w1),
 (r1,w0,w1,w0),  (r0,w1,w0)
Fault coverage: AFs, SAFs, TFs, CFins , CFids; march A is capable of detecting coupling faults and stuck-at faults when only one type of fault is present
If a memory does not contain multiple access decoder faults, then March B detects any combination of stuck-at faults or coupling faults
D.S. Suk, S.M. Reddy, IEEE ToComputers, 1981
Notes: Stuck-at and coupling faults can be detected by so-called March A provided only one type of fault is present. The authors of March A has also proposed another test called March B. It was shown that if a RAM under test does not contain multiple access decoder faults, then March B detects the presence of any combination of stuck-at or coupling faults.

## Slide 20: Nair’s test
In order to detect all stuck-at and coupling faults:
  each cell must undergo transition 0-1 and transition1-0, and must be read after each transition and before undergoing any subsequent transition
  for every pair of cells (i,j), cell i must be read after cell j makes a transition and before cells i and j make any further transitions, for all the possible states of cell i and all possible transitions in cell j
  For every cell triple (i,j,k), if the test makes transition y-y’ in cell j after cell i makes transition x-x’ and before cell k in state z is read, then the test must possess another sequence, where either cell k in state z is read after transition x-x’ in cell i and before transition y-y’ in cell j, or cell k in state z’ is read after transition y-y’ in cell j and before transition x-x’ in cell i
R. Nair, S.M. Thatte, J.A. Abraham, IEEE ToComputers, 1978
Notes: Assuming that the decoder does not convert into a sequential circuit when faulty, Nair, Thatte and Abraham proved that in order to test a RAM for stuck-at and coupling faults, it suffices to target faults in the memory cell array. Other faults can be represented as certain equivalent faults occurring in the memory array. Subsequently, the same authors gave a set of necessary and sufficient conditions for all faults in the memory cell array to be detected by a test sequence. These three conditions are stated on the slide. The corresponding test procedure is shown on the next slide. It is worth noting that if one of these conditions is not satisfied, then:
a cell stuck-at-0 or stuck-at-1 fault will not be detected,
a coupling fault between a pair of cells may not be detected,
a coupling fault between cell j and cell k may mask the effect of another coupling fault between cells i and k (this phenomenon would escape detection when using Marching 1’s and 0’s procedure).

## Slide 21: Nair’s test – 30n
 (w0),
 (r0,w1),  (r1),  (r1,w0),  (r0),
 (r0,w1),  (r1),  (r1,w0),  (r0),
 (r0,w1,w0),  (r0),
 (r0,w1,w0),  (r0),
 (w1),
 (r1,w0,w1),  (r1),
 (r1,w0,w1),  (r1)
Detects all stuck-at faults, decoder faults, and multiple coupling faults between every pair of cells
Notes: One can easily demonstrate that the above procedure detects all the faults in the fault model by showing that it satisfies the three conditions stated earlier. The number of operations required to perform the entire memory test is about 30n, where n is the number of memory cells. The Nair’s test is considered very efficient given its high fault coverage and relatively short test application time.
Further enhancements of this algorithm (of complexity n + 32nlog2n) allow detection of unlinked coupling faults, where an aggressor cell forces a victim cell to go to a certain state provided yet another cell assumes a pre-defined state (restricted 3-coupling faults)

## Slide 22: Checkerboard test
Designed to test refresh operations of DRAMs
Maximizes leakage current and detects leakage faults
Used as data retention test, e.g., by detecting defective resistance discharging the storage capacitor at a faster rate than nominal
To be effective it must consider address scrambling and layout
1
0
1
0
0
1
0
1
0
1
0
1
1
0
1
0
Notes: Checkerboard detects shorts (two cells erroneously connected) between adjacent cells assuming that the address decoder is fault-free. Observe that each cell containing 1 is surrounded by four cells containing 0 (or vice versa), which maximizes the leakage current between the cells. The proper application of this test requires the prior knowledge of all memory cell locations – this is crucial when working with memory devices that feature address scrambling.

## Slide 23: Checkerboard – 4n
address
time
Repeat for the inverted values
Detects all stuck-at faults provided the decoder is fault-free
Does not detect all decoder faults, all transition and coupling faults
w0
w1
w0
w1
w0
w1
w0
w1
w0
w1
w0
w1
w0
w1
w0
w1
r1
r0
r1
r0
r1
r0
r1
r0
r1
r0
r1
r0
r1
r0
r1
r0
Notes: Originally designed to test refresh operations of dynamic RAMs, the checkerboard test is a simple and short test which divides the memory cells into two groups: cells-1 and cells-2 forming a checkerboard pattern. During step 1 the algorithm writes 1 in all cells-1 and 0 in all cells-2. Next it reads all cells. The next phase simply repeats the former steps by writing 1 into cells-2 and 0 into cells-1. Checkerboard detects all stuck-at faults provided the decoder is fault free (otherwise it can only be guaranteed that two cells will be accessed and possibly found fault-free). Not all transition faults are detected – it cannot be guaranteed that for all cells-1, transitions from 0 to 1 are generated; similarly it cannot be guaranteed that for all cells-2 transitions from 1 to 0 are generated. Not all coupling faults are detected – for the cells-1 it cannot be guaranteed that all transitions from 0 to 1 are generated, and certain CFs are not detected because the result of these CFs is identical to the expected value of the read operation. For the cells-2 similar arguments apply.

## Slide 24: Galpat – Galloping pattern – n2
It verifies that every cell can be set to 0 and 1 without causing any other cell to change its state
All stuck-at faults in the decoder and in the memory array as well as most of the coupling faults are covered
write 0 in all cells
for each cell k do
write 1 in cell k
for each cell j different than k do
read cell j (expected 0)
read cell k (expected 1)
write 0 in cell k
repeat previous steps interchanging 1s and 0s
0
0
n – 1
Coupling faults not detected
1
k+1
k
Walking 1/0 reads cell k once for loop is terminated
Notes: With memories becoming more deeply embedded and with the corresponding growth in their density, there is an increasing interest in applying more robust stimuli with ability to both detect and locate most memory failures, including stuck-ats, transitions, various types of couplings, and address mismatches. Galloping patterns may serve here as a good example of this class of tests. A galloping pattern provides a ping-pong action between the base cell under test and the remaining cells of the memory. Although the time complexity of this approach is quadratic with respect to memory size, its exceedingly high test coverage may justify its usage, especially for relatively small embedded memories populating various integrated circuits employed, for example, by the communication industry. Still, it is extremely challenging to handle test data as it raises concerns derived from both the volume of the data itself and the diagnostic information it represents. Consider 1KB memory block where galloping patterns produce 4MB of test results. In order to mitigate the risk of disruption, this data must be appropriately recorded and flushed out, preferably in a compressed form, for diagnostic processing.

## Slide 25: Sliding diagonal – n1.5
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
1
0
0
0
0
1
0
0
0
0
1
1
0
0
0
0
0
1
0
0
0
0
1
1
0
0
0
0
1
0
0
0
0
0
1
1
0
0
0
0
1
0
0
0
0
1
0
Repeat for inverted values
Detects all stuck-at and transition faults
Does not detect all decoder and coupling faults
Notes: Isolating the galloping within a row, a column, or a diagonal can also derive high quality tests. Some reduction of complexity can be also achieved by employing sliding diagonals, rows, or columns. Cells on the diagonal are used because each cell has a different row and column address, thereby checking the row and column decoder in parallel. The algorithm writes a diagonal of 1s to a background of 0s. All memory cells are read, after which the diagonal is shifted. This is repeated until every base cell has been on the diagonal. The whole sequence is then repeated for inverted data. Sliding diagonal detects (and locates) all stuck-at and transition faults. Moreover, it detects some address decoder faults and some coupling faults. In particular, certain address faults will escape detection as faults on cells on the same diagonal may mask each other. Similarly, all diagonal cells are written consecutively, and thus some coupling faults can mask some other coupling faults.

## Slide 26: Butterfly – nlog2n
5
1
8
4
2
6
3
7
5
1
8
4
2
6
3
7
5
1
6
8
4
2
3
7
5
1
2
6
8
4
3
7
5
1
2
6
8
4
3
7
r0
w1
r1
The base cell is written at the beginning of each cycle comprising four read operations, and is read after this cycle
Repeat for inverted values
Notes: The butterfly test is reducing the number of operations used by the GALPAT with the purpose to detect only stuck-at faults and address decoder faults. The memory is filled with 0s (or 1s) except for the base cell, which contains a 1 (respectively 0). During the test, the base cell walks through the memory. The read action is as follows: the algorithm reads the four cells directly adjacent to the base cell. Depending on the implementation, other neighboring cells on the same column and row as the base cell can also be read. This is illustrated on the slide for (in total) 8 neighboring cells. In general, the maximum possible distance from the base cell (assuming that the number of rows is equal to the number of columns) is 2N/2-1 in all four directions. As a result, the number of read operations in 5(N/2 – 1). The initialization takes n operations, and thereafter each cell is written twice and the read operations follow. Thus, 2n writes and n read operations from the adjacent cells are carried out. All of these actions are repeated with inverted data. Hence, the total number of operations is 2(2N + 2n + 5n(N/2 – 1)), which is of order O(nlog2n).

## Slide 27: Testing for pattern-sensitive faults
The content of a base cell, or the ability to change that content, is influenced by the content of a group of cells (which is a pattern of 0s and 1s), or changes in this content
Tests for neighborhood pattern sensitive faults (NPSF) assume that only the adjacent neighbors are likely to contribute substantially to faulty behavior
Two kinds of neighborhood
Notes: With the increasing density of memory chips, pattern-sensitive faults (PSF), also known as adjacent pattern interference faults, become the predominant failure mode. Other faults that affect the memory cells can be regarded as special types of PSFs. Testing for all possible PSFs is virtually infeasible from the practical point of view because of its expected test length. Consequently, a concept of neighborhood was introduced to reduce the complexity of this fault model. This approach assumes that a given cell can only be affected by the adjacent cells in a twofold manner, as shown on the slide: (1) the 5-cell neighborhood consisting of a base cell (in red) and its four neighboring cells (in blue) located at the top, bottom, left and right of the base cell, (2) the 9-cell square neighborhood, consisting of a base cell and all 8 neighboring cells.

## Slide 28: Neighborhood pattern-sensitive faults
Active NPSF (ANPSF) – the base cell changes its content due to a change in one of the neighboring cells while remaining cells keep successive combinations
  each cell must be read in state 0 and in state 1, for all possible changes in the neighborhood pattern
Passive NPSF (PNPSF) – the content of the base cell cannot be changed due to a neighborhood pattern
  each cell must be written and read in state 0 and in state 1, for all permutations of the neighborhood pattern
Static NPSF (SNPSF) – the content of a base cell is forced to a certain state due to a neighborhood pattern
  each cell must be written and read in state 0 and in state 1, for all permutations of the neighborhood pattern
Notes: This slide lists the basic types of PSFs altogether with conditions that must be satisfied by a test procedure to detect this particular type of failure.

## Slide 29: General rules
Sensitize every fault using the appropriate neighborhood pattern and read the state of the base cell after each sensitizing pattern to detect a fault
The number of patterns needed to sensitize all ANPSF of a neighborhood of size k is (k – 1) × 2k
Rationale:
  base cell – assumes states 0 and 1
  a single cell from (k – 1)-cell neighborhood exercises transitions 0-1 and 1-0
  the remaining (k – 2) cells take all 2k-2 possible states
  in summary: 2×(k – 1)×2×2k-2 = (k – 1)×2k
The respective number of patterns for PNPSF and SNPSF is 2k
Notes: The basic two steps must be carried out in order to test the base cell for active and passive neighborhood pattern sensitive faults. They are summarized on the slide within the first bullet. The number of patterns needed to sensitize all ANPSFs of a neighborhood of size k is (k – 1)2k because each one of the k – 1 neighbors of the base cell must exercise both the 0-to-1 and 1-to-0 transitions, while the other k – 1 cells take all the possible binary values. A pattern that sensitizes one of the ANPSFs is called an active neighborhood pattern. Similarly, the number of patterns needed to sensitize all PNPSFs in a k-cell neighborhood is 2k. In these patterns, the base cell will be assigned both the 0-to-1 and 1-to-0 transitions, while the other k – 1 cells take all the possible binary states. These patterns are called passive neighborhood patterns.

## Slide 30: Test generation
000
001
101
100
110
010
011
111
Edge 101  001 determines test 01
k = 3
Each pattern can be represented by an edge in a graph in which there is a node for each binary k-tuple and there is an edge between two nodes having Hamming distance equal to 1
Generation of sensitizing patterns is equivalent to finding an Eulerian path in the graph such that all the edges are traversed exactly once
Notes: Efficient generation of the sensitizing patterns is equivalent to finding an Eulerian path in the graph such that all the arcs are traversed exactly once. The length of such an Eulerian path is k2k. The procedure to construct the Eulerian path can be as follows:
Construct a reflected k-bit Gray code Rk with initial state S0 = 00 … 0.
Let X = x0x1 … xk-1 denote any element of Rk. Define a transformation T1 as follows: T1(x0x1 … xk-1) = xk-1‘ x0x1 … xk-2’. Let Ti denote i consecutive applications of T1.
The sequence of length k2k + 1, formed by concatenating Rk, T1(Rk), T2(Rk), …, Tk-1(Rk), and S0 is the sequence of nodes visited by the desired Eulerian path.
The write sequence constructed as shown above will sensitize all the PSFs caused by transition writes affecting the base cell of a neighborhood of size k. This sequence has to be now applied to every neighborhood in the memory.

## Slide 31: The tiling method
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
4
2
0
3
1
The memory is covered by a group of non-overlapping neighborhoods
Every cell in a k-cell group is assigned an integer; the same test is repeated for each group
Every cell different than “2” is also a base cell for other groups not shown explicitly
The number of write operations
(n/k) × k × 2k = n × 2k
Length of the Eulerian path
The number of base cells
Notes: Every cell in the k-cell neighborhood is assigned an integer number from 0 to k – 1. When the tiling neighborhood is used, then every k-cell neighborhood in memory is marked with all members of {0, 1, 2, …, k – 1}, as shown on the slide for 5-cell tiling neighborhood. Let Nk = v0, v1, …, vr, where r = k2k, denote the transition write sequence obtained from the Eulerian path of a k-cell neighborhood. The following procedure shows how to construct an optimal transition write sequence Nn for a memory of size n with tiling neighborhoods of size k:
Generate an optimal transition write sequence Nk = v0, v1, …, vr, for a k-cell neighborhood.
Assign a fixed pattern of numbers from {0, 1, 2, …, k – 1} to each member of independent neighborhoods that tile the memory.
For each vi in Nk that writes x into cell C, from the sequence Vi = vi,0, vi,1, …, vi,p-1, where p = n/k, in which vi,j writes x into any cell C’ of the memory such that the number assigned to C’ is equal to the number assigned to C, for 0 ≤ j ≤ p-1. Thus Vi performs the same operation as vi on cell in the same position in each independent neighborhood.
Nn is formed by concatenating the sequences V0, V1, …, Vr-1, where r = k2k.

## Slide 32: Fault coverage
Two designs with SRAMs (a few hundred samples)
MSCAN
Diagonal
GALCOL
MATS-OR
MATS-AND
MATS+
Marching 0/1
March C
March A
March B
TLSNPSF1G
40
50
60
70
80
90
100%
Notes: This slide illustrates empirical test coverage results for two SRAM designs when applying different types of memory test. All data have been collected by using test results for a few hundred samples of tested memories. Successive rows of the diagram correspond to several test schemes, including the most popular marches. The X axis represent the actual fault coverage. Just to summarize the previous discussion – recall that the MSCAN and checkerboard tests are the simplest test algorithms among the traditional tests. The MSCAN test covers all SAF, however does not cover TF, CF, AF. The checkerboard test also covers all SAF, but not all TF, CF, AF are detected. The GALPAT and walking 1/0 have the same algorithm except the read operation’s cell access order. The GALPAT and walking 1/0 detect all AF, SAF, TF, and CF. The sliding diagonal was developed to shorten the GALPAT algorithm. It covers all SAF and TF, however fails to cover all AF and CF. The butterfly test was also developed to reduce the GALPAT test which requires a long testing time for a large memory array. This algorithm covers all SAF, but not all AF are detected.
March tests have been proposed to detect TF, CF, as well as SAF while traditional tests failed to detect TF and CF. March test algorithms are superior to detect faults other than SAF, and they also have reduced test time. MATS detects all SAF and AF if the technology is known. MATS+ allows two or more cells having different values to be read simultaneously. It also detects all SAF and AF. Marching 1/0 algorithm detects all SAF and TF. MATS++ algorithm optimized the marching 1/0 algorithm to reduce the march element since the marching 1/0 is not an irredundant test. March X1 detects AF, SAF, TF, and CFin (inversion coupling fault). March C- detects CFin (inversion coupling fault), CFid (idempotent coupling fault), CFst (state coupling fault), CFdyn (dynamic 2–coupling fault) as well as SAF, AF and TF. March C- is an optimum test obtained from the March C test by reducing march element, which does not affect the fault coverage. March A is a well known to detect linked CFid. It is the shortest algorithm to detect AF, SAF, linked CFid, and unlinked TF. March B detects SAF, TF, AF, CFid, CFin, and it is an irredundant test set.

## Slide 33: Data backgrounds for word memories
D0 D1 D2 D3 D4 D5 D6 D7
0 0 0 0 0 0 0 0
1 1 1 1 1 1 1 1
0 0 0 0 1 1 1 1
1 1 1 1 0 0 0 0
0 0 1 1 0 0 1 1
1 1 0 0 1 1 0 0
0 1 0 1 0 1 0 1
1 0 1 0 1 0 1 0
Multiple data backgrounds to detect coupling and bridging faults between cells of the same word
For every pair of cells all four combinations are checked
2 (log2w + 1) backgrounds
16 backgrounds for 128-bit wide memory
Normal and inverse
Notes: Word-oriented memories contain more than a single bit per word. Read operations read therefore a number of cells in parallel, write operations write data into these cells whereby the data to be written into each cell can be specified independently of the data for the other cells. The address decoder accesses the memory chip at the word level such that address faults within a word do not occur. The fact that a memory is w bits wide does not impact the detectability of stuck-at and transition faults as they involve only a single cell. In principle, the tests for these faults (as shown earlier) can be used for word-oriented memory. However, they have to be modified as follows:
all w0 (or w1) operations should be replaced with w-data background (or w-inverted data background) , where any data background is acceptable,
r0 and r1 operations have to be changed accordingly.
When it comes to testing coupling or bridging faults, data background must be selected more carefully. For example, in order to be able to detect a SCF between cells in a word, all four states of two arbitrary cells i and j should be checked. Thus, the number of data backgrounds required to check half of these states (the second part will be examined with the inverted data) is log2w + 1. For w = 8, the recommended backgrounds (normal and inverse) are shown on the slide.

## Slide 34: Data in word-oriented memory
 (wb)
 (rib,wb)
 (rb,wib)
 (rb,wib)
Notes: This slide illustrates how a few simple march elements are conducted on word-oriented memory when using different data backgrounds. Note that wb, wib, and rb correspond to write-background, write-inverse-background, and read-background operations, respectively.

## Slide 35: ROM testing
Mostly stuck-at faults
Three basic methods for testing ROMs
  parity checking (XOR trees)
  checksum checking – the checksum is formed by the modulo-N arithmetic sum of all data words in the ROM; if this sum is not equal to the pre-stored checksum, one or more errors must have occurred
  cyclic redundancy checking (CRC) – the ROM is extended by a string computed based on all bits in the ROM and the generator polynomial g(x); if during testing it appears that the resultant sequence is not divisible by g(x), one or more errors must have occurred
Notes: A functional model employed for ROMs remains similar to that of RAMs with relevant fault types such as stuck-ats and bridges being tackled through functional test algorithms. Also, all addressing malfunctions are covered by memory cell stuck-at fault tests as there are no writes in the mission mode. Typically, the basic test reads successive memory cells, and processes output responses by performing a polynomial division to compute a cyclic redundancy code (signature). The same procedure can be used to detect certain classes of dynamic faults provided memory cells are designed with additional DFT features.
The main strategy for ROM diagnosis is to have users provide an initialization file that describes the content of the ROM. The initialization sequence can be random as far as the test is concerned. During the MBIST session, the content of the ROM is read multiple times using different addressing schemes and compressed into a signature. The signature is downloaded at the very end of the algorithm. Although the data transferred to the memory is minimal, the diagnostic procedures employed for ROMs are complex. Current techniques either rely on downloading the signature value at certain intervals (based on binary search techniques) such that one can corner the test step when the MISR gets corrupted. Some other techniques suggest downloading the content of the entire ROM when a failure occurs. Such techniques can get to the failing address and data, but they are complicated, time consuming, and often prohibitive in practice. Therefore, additional hardware is added to allow downloading the content of the entire ROM. As the ROM needs to be stopped after every read operation, the time needed to diagnose ROM failures increases significantly.

## Slide 36: Memory BIST – challenges
Increased node to node coupling due to higher density
Large total capacity and chip area, up to 90%
Many arrays, various configurations
High operating speed
Need for diagnostics and redundancy reconfiguration
Notes: Following a significant increase in the chip area occupied by memory arrays, the International Technology Roadmap for Semiconductors predicts memories to take up more than 90% of the silicon area within the decade. Due to their extremely large scale of integration, many types of failures such as time-related or complex read faults, often not seen earlier, originate in the highest density areas of semiconductor chips. In order to perform a high quality test, the memory built-in self-test (MBIST) has emerged as a valuable choice due to:
very regular test patterns and expected responses that can be generated, compressed, and stored by using a relatively simple testing circuitry,
the reduced number of input/output channels – they usually suffice to control BIST operations such as activation, scan-in, scan-out, and others,
on-chip location of the entire test logic; in particular it facilitates at-speed testing allowing detection of time-related faults.

## Slide 37: Memory BIST – requirements
High quality with at-speed test
Choice of algorithms:
  “menu”, synthesizable, field-programmable
Support of diverse types of memories
  different addressing schemes
  synchronous and asynchronous
  SRAM, DRAM, Flash, ROM, CAM
  Multi-port
Low area, low routing, sharing of controllers
Automation, including RTL insertion
Support of diagnostics, DFM and reconfiguration
Notes: Although certain MBIST controllers are designed as hard-wired finite state machines, in majority of cases some flexibility is needed to operate memory test logic. Consequently, more popular implementations comprise programmable (micro-coded) devices that can be customized to meet requirements of up-to-date embedded memory structures. In order to test memory against time-related faults, it must be tested at speed. However, a relatively low bandwidth at the I/O channels makes it impossible to quickly download failing signatures or address location of failing sites. This problem grows in significance when another fault is detected while downloading the previous diagnostic data. Hence, many BIST schemes are modified to enable one of the following two modes of operation:
pause and resume – assuming a single register to store the failing data, the BIST controller goes into a hold mode; once the information is completely scanned out, the BIST controller resumes its operations,
stop and restart – the BIST controller moves to its initial state once a fault is detected and the corresponding diagnostic data is flashed out; this way one can still detect defects related to timing problems between the address where the controller is currently holding and the next target location (where it otherwise would resume its operations); clearly, in successive repetitions the controller skips monitoring the memory output until it crosses the last failing step.

## Slide 38: Parallel memory BIST
BIST
Clock
Start
Done
Pass/Fail
FSM
Control generator
Data generator
Address generator
Memory
DATA IN
DATA OUT
ADDRESS
CTRL
BR
TAP controller
Functional logic
Memory controller at the top level
  TAP controller as test engine
Memory BIST controller
Notes: An example of parallel memory BIST architecture is shown on the slide. The march algorithms can be easily implemented in this environment by a BIST controller. A steering logic placed around the memory consists of multiplexing circuitry enabling the memory to be fed during a self-test mode by the controller, rather than by the mission logic. Although the march tests normally write and read words of either all 0s or all 1s, recall that their detection capability can be significantly improved by using different data backgrounds. Thus, the BIST controller uses patterns like 00001111, 00110011, 01010101, etc., instead of all 0s, and then their complements instead of all 1s. The test response processing can be carried out using an MISR or by employing a comparator. The latter solution is of practical importance as the read data expected for a fault-free memory can be efficiently recreated on the fly due to high regularity of the march tests.

## Slide 39: Address generation
Binary up- and down-counters
Linear feedback shift registers
  with all-0 state
  bidirectional
Microprocessor
  allows implementing many algorithms
Notes: Test generators used by memory BIST schemes consists of an address generator and a data generator. The first module is usually implemented by means of a counter, an LFSR, or a microprocessor. The actual data is produced by an LFSR, a finite state machine (FSM), or is directly retrieved from the current address. The response data evaluation is often carried out in the form of deterministic comparison, or more often, by conventional compaction devices such as MISRs. On the following slides we discuss several memory BIST scenarios in which either deterministic or pseudo-random patterns are used, and various architectural particulars are reused to arrange test procedures.

## Slide 40: Test response compaction
Comparison
  the output data from the memory is compared with the expected data during a read operation; the result reduced to a single bit
  golden test responses are needed
Mutual comparison
  the memory array partitioned into two parts
MISR
  suitable for ROM testing
  test results are not available until the end of test
  possibility of aliasing
Processor using adders and other devices
  provided it has an access to the memory
  flexibility of implementation
Notes: A simple comparator can be placed directly on the outputs of the memory under test in order to arrive with error patterns that feature 1s on corrupted bits. Clearly, this approach requires expected (golden) data to be available during read operations. Furthermore, the error responses can be further reduced (compressed) by means of various forms of test response compaction, as discussed in the section devoted to BIST. In particular, a signature register is often used to collect memory test responses and produce error signatures. It works in a continuous manner starting with the all-0 state. The content of the register is typically downloaded once per run, i.e., after sweeping the whole address space (see march tests, for example) or at the end of the entire test. Clearly, a non-zero content of the register indicates failures in the memory array. Collecting multiple signatures may significantly help in running effective fault diagnosis.
A ring generator with multiple inputs driven by outputs of the test response comparator can be used to implement the signature register and act as a MISR. Ring generators can operate at very high speeds as they feature a significantly reduced number of levels of XOR logic, minimized internal fan-outs, and simplified circuit layout and routing, as compared to canonical forms of LFSRs. This circuit resembles, to some extent, test data decompressors used in the embedded deterministic test environment (compare a chapter on test data compression) except for the injector network handling the increasing number of input channels. Increasing the input fan-out k, and then connecting each input to randomly selected k stages of the compactor, makes it possible to uniquely recognize errors arriving from different input channels. As a result, one may expect a significantly improved diagnostic resolution.

## Slide 41: Serial memory BIST
Data output
Serial output
Serial input
Minimal logic and routing
Increased test application time
Functional logic
Memory
Address
0 0 0 0
r0 0 0 0 0
w1 1 0 0 0
r0 1 0 0 0
w1 1 1 0 0
r0 1 1 0 0
w1 1 1 1 0
r0 1 1 1 0
w1 1 1 1 1
r1 1 1 1 1
Notes: As shown earlier, the regularity of march tests makes them particularly suitable for BIST applications. The scheme shown on this slide uses a serial access mechanism in which multiplexers are added to the inputs of the write drivers. Each multiplexer selects between the normal data input and a latch driven by a sense amplifier of the left-neighboring bit. As a result, a shift register structure is created in the BIST mode in which a write operation causes each cell to obtain data from its left neighbor (that is, only the leftmost bit is directly controlled) and a read operation causes only the rightmost bit to be directly observed. If w0, w1 and r now denote the write and read operations according to this scheme, and (x)n represents an operation x repeated n times, then the following algorithm for n-bit word memories, similar to March C, is as follows:
(w0)n(r,w0)n; (r,w1)n(r,w1)n;
(r,w0)n(r,w0)n;
(r,w1)n(r,w1)n; (r,w0)n(r,w0)n;
(r,w0)n(r,w0)n;
The remaining march tests can be implemented in this serial BIST environment in a similar way. The scheme can be also used to test several RAM blocks by entering a daisy chain mode, in which the serial output of one memory is connected to the serial input of another memory unit, so that they appear as one larger block.

## Slide 42: Programmable algorithms
Selection of algorithms
  March1, March2, March3, Unique Address, Checkerboard, …
  address jumping
Synthesizable algorithms
  user defined prior to synthesis
  simple language
  number of sequences, backgrounds, sequence elements etc.,
Programmable algorithms
  defect mechanisms may not be known before fabrication
  memory BIST controller implements a class of algorithms
  field programmable parameters define active elements of tests
Notes: When using memory BIST, a user can select one of pre-synthesized test algorithms. However, it is often required to design customized test algorithms to target specific memory defects that are difficult to detect with the existing algorithms. To effectively test the memory, one might need to apply multiple algorithms to the same memory in a specific sequence. In some cases, one might choose to apply several algorithms to diagnose memory defects that are otherwise too difficult to identify. Memory BIST tools provide programming capabilities to develop custom algorithms for memory testing. These algorithms can be hard-coded. They cannot be changed after the memory BIST controller is generated. The test algorithms can also be downloaded into the memory BIST controller for execution at runtime. Such methods are referred to as soft-coded algorithms. They are defined using the automation tool after the memory BIST controller is instantiated. The algorithm programming allows certain memory BIST controller registers to be loaded with initial values prior to executing the algorithm. These controller registers may include address registers, write data register, expect data register, counters, delay counters, etc.

## Slide 43: Built-in self-repair
Built-in repair analysis (BIRA) determines if memory is defect free, repairable, or non-repairable
Reconfiguration instructions computed for repairable memories
Repair analysis performed concurrently with testing
Information stored in real time in row and/or column/segment fuse set registers
Repair information accumulated over multiple tests
After repair, a test session is repeated
Notes: Memory repair can be used to improve manufacturing yield of integrated circuits. There are different types of memory repair: column repair, row repair, or a combination of both. Column repair includes replacing single columns or blocks of columns up to the full width of a column multiplexer. The full width case is often referred to as IO repair. A row repair includes replacing blocks, rows, or even a subset of a row, down to a single word. The memory repair is performed in two steps. The first step consists of analyzing failures reported by the memory BIST controller during test execution to determine, if the memory is repairable and, if repairable, determining the values to be applied to the repair inputs of the memory. This step can be implemented in two ways. The first consists of collecting failure information using the diagnostic features of memory BIST and determining if the memory is repairable using specialized software running on the tester. However, the tester time spent on repair analysis becomes prohibitive as the number of memories to repair increases. The other way of performing repair analysis for several memories is to use BIRA (built-in repair analysis) circuitry automatically generated by CAD tools and inserted into a design.
The second step of memory repair is to effectively apply the values calculated during the repair analysis step to the repair inputs of the memory each time the circuit is powered up. This step can be implemented in two ways. One implementation is to directly connect memory repair inputs to metal fuses programmed using a laser. This method requires specialized test equipment and long programming times and is more difficult to use as the number of memories increases. The other implementation uses BISR (Built-In Self-Repair) circuitry automatically generated and inserted by MBIST tools. The BISR controller permanently stores repair information in an array of eFuses (electrically programmable fuses), reads the information back each time the circuit is powered up, and repairs memories requiring it. This method is more efficient because eFuses are faster to program and easier to share.

## Slide 44: Repair analysis
44
Bad
allocation
Good
allocation
P. Ohler, S. Hellebrand, H.-J. Wunderlich, ETS, 2007
Notes: Several repair analysis techniques use a binary search tree. Each node in the search tree corresponds to decision “row repair” or “column repair” for a fault in the memory. As long as the tree is under construction, a node is called “closed”, if all decisions starting from this node have already been explored, else it is called “open”. A leaf is reached when a successful repair scheme is found or no more repair resources are available. In case of a successful repair, the path from the root to the leaf provides the repair signature.
For a memory with r redundant rows and c redundant columns the maximum height of the tree, i.e., the maximum length of a path from the root to a leaf node, is r + c. The leaf nodes in a complete search tree correspond to all solutions exploiting all resources. As there are r rows distributed among r + c spares, there are b(r + c, r) leaf nodes in a tree enumerating all possible repair configurations. To reduce the size of the search tree a “must repair” phase is typically conducted before starting the binary search. This particular steps indicates that for a memory with r redundant rows and c redundant columns the following repair decisions are mandatory: if there are more than c faults in a row, then there are not enough columns to cover all the faults, and a row must be selected for repair. Similarly, more than r faults in a column require a column repair.
The actual search starts with resetting the repair registers and the repair counters. Furthermore, the root node is pushed on the stack with repair code ‘00’ and status code ‘00’. Then during each step of the search the node on top of the stack is analyzed. If the node is already closed, then it is popped off the stack, i.e. backtracking is started. If the node is open, then the next repair decision depends on the status code, the availability of resources, and the repair strategy, e.g., “row first”, “column first”, “random” or “balance remaining resources”, etc. Whenever a new node is pushed on the stack, then the address of the faulty row or column is stored in the address register of the first available redundant row (column), and the row (column) counter is updated. Since the spare rows and columns are used in a fixed order during the search, canceling repair decisions during backtracking simply corresponds to decrementing the row or column counter. To continue the search after backtracking, the test must be restarted with the partial repair signature derived from the valid addresses in the repair registers.

## Slide 45: Self-repair architecture
Controller
Other memories
Spare rows
Memory
Spare columns
Fuse box controller
Fuse pool
Comparators
Repair port
BISR row
BISR column
BIRA
TAP
Row fuse set
Column fuse set
Notes: Repairable memories implement spare or redundant rows and/or columns, enabling access to any faulty row or column to be redirected to a redundant element. The existing memory BIST diagnostic capabilities are not optimal solutions for the repair analysis of repairable memories. Each solution requires large test times or state-of-the-art high speed memory testers. In addition, post execution analysis of the results must be done to determine if a memory is repairable and what repair, if any, is required. To facilitate repairable memories in production testing environments, the built-in repair analysis (BIRA) feature can be used to determine if a memory is repairable and the repair information based on the specified redundancy scheme. The repair analysis is performed during the execution of the memory BIST controller, and the repair results are scanned out of the controller after execution. The slide shows the location of the BIRA circuit. Usually the BIRA circuitry is in the same location as the comparators. That is, BIRA is located in the BIST controller. Note that a central fuse box is connected to a chip-level BISR controller. The central fuse box can be instantiated inside or outside the BISR controller module. When the fuse box is located outside the BISR controller module, extra connections between the fuse box and the BISR controller are required.

## Slide 46: Transparent tests
Performed in the mission mode
The memory content is unaffected
Rules to transform conventional tests into transparent ones
  discard the memory initialization phase
  read operations r0, r1 and write operations w0, w1 replaced with actions ra, ra’, wa, wa’, where a and a’ are the actual memory content and its inversion
  unique addressing scheme (if the original algorithm allows some flexibility)
  golden signature computation – remove all write operations from the original algorithm
Notes: Transparency is the attribute that enables a memory test scheme to perform tests periodically without destroying the content of a RAM. This property allows continuing normal operations between test sessions and prevents a circuit from difficulty in restoring the RAM’s content. Transparent algorithms and architectures attempt to achieve this goal by using the stored data in the RAM such that, during testing, it is complemented an even number of times. In other words, one can execute a test session by writing, into each memory cell, particular data which is a function of the initial data read from that cell.
Let cell c contain value v. In order to convert a nontransparent test technique into a transparent one, the following steps are performed:
add initial read operations to the original algorithm,
substitute every write-x operation on cell c with write-(x  v).
if the data stored in cell c during the last write operation of the original algorithm is v’, add an extra read operation and a write operation such that the initial data is restored.
A signature representing the results of a test is computed by compacting the sequence of values produced by the read operations. After all the test patterns are applied, the actual signature is compared with the reference signature predicted by invoking only the read operations of the test obtained in the above three-step procedure. This phase is executed just prior to the actual testing consisting of both read and write operations.

## Slide 47: Transparent tests
 (w0),  (r0,w1),  (r1,w0,r0)
 (r0,w1),  (r1,w0,r0)
 (ra,wa’),  (ra’,wa,ra)
 (ra),  (ra’,ra)
Original MATS++ test
Test with no initialization
Test transformed into transparent
Computation of signature
Test begins with computation of golden signature
During actual read operations a signature is determined
This signature is compared at the end of the test with the golden signature
Notes: The transparent testing of RAMs within BIST environment requires only slightly more complex circuitry to be implemented than that of the corresponding standard hardware. First, a customized BIST controller has to be used to facilitate generation of not only the test sequence, but also the signature-predicting sequence before the actual test. Second, the read and write instance generator has to be designed such that it allows switching between the test application mode and the signature production mode, to avoid invoking write cycles in the latter mode. Finally, a register has to be added to store the contents of the addressed cells. This information is then used for the test data generation. The transparent BIST area overhead for 32K byte RAM with March C is 1.2%, that is, only 0.2% more than that of the conventional BIST solution.