## Slide 1: VLSI testing
Test pattern generation
HEP
Notes: Not surprisingly, test pattern generation (or in fact, automated test pattern generation) is a central problem of paramount importance in the entire VLSI test realm. It dates back to fundamental works by P.J. Roth published in 1966 and 1967, and in particular to his famous D-algorithm. Today, finding high quality test patterns is a complex issue with many interacting aspects. They include the cost of test generation, the quality of the resultant patterns, and finally the cost of their application. The cost of test generation depends on the complexity of the test generation method (algorithm). Generation of pseudorandom vectors, for example, is a simple process (especially, if one employs a hardware on-line techniques – compare the chapter on built-in self-test). However, to achieve a high-quality test process, one needs to produce a large set of random patterns whose application will take time that cannot be by all means neglected. Furthermore, in order to determine the quality of such patterns (most often in terms of the resultant fault coverage), some form of expensive fault simulation might be required. On the other hand, deterministic test generation produces test vectors by processing a model of the circuit under test. This approach is more expensive, but it yields shorter and higher quality tests. In this section, we will focus our attention on patterns generated in an automatic manner – this methodology will be further referred to as automatic test pattern generation or ATPG.

## Slide 2: Functional vs. structural testing
Functional – some crucial functions are tested for arbitrary chosen arguments
Test gives some confidence in the correctness of a design but the quality of test is usually unknown
Typically functional patterns yield low fault coverage and are not useful in high quality production testing
Structural – based on the knowledge of failures likely to occur during fabrication
The quality of test is measured by fault coverage
Currently predominant strategy
Notes: Let us recall that functional testing attempts to verify that a device under test functions according to its specification. Therefore, a user does not need to know the detailed structure of a device. The advantages of functional testing include a high correlation to customer experience, relatively short test application time, and accurate measurement of test speed. Furthermore, it avoids over-testing since it is performed in a functional mode. Preparing functional tests requires both architectural design knowledge and testing expertise, and this process cannot be readily automated. Typically, functional patterns yield low fault coverage and are not useful in high quality production testing. In contrast, structural tests are used in production test of most VLSI digital circuits because these tests are easier to create and evaluate with the help of many tools. They also facilitate simpler diagnosis of faults than functional tests. The primary objective of structural tests is to identify structures that deviate from a declared defect-free design, which is a much narrower objective than for functional (specification-based) tests.

## Slide 3: Exhaustive testing
All input combinations applied
All combinational faults detected
No fault simulation or test pattern generation for combinational faults
The number of tests grows exponentially with the number of primary inputs
Test time and storage requirements may exceed acceptable limits
Detection of CMOS stuck-open and delay faults not guaranteed
Notes: Most likely, the exhaustive testing is the simplest approach to generate test patterns. It applies all 2n possible input vectors to a combinational circuit with n primary inputs. Exhaustive tests, extremely simple to produce, detect all faults that do not transform the circuit into a sequential device. These faults are referred to as combinational failures in contrast to other faults that may escape detection as they introduce a feedback and may increase the number of internal states of a circuit. Some bridging or stuck-open faults in CMOS circuits may serve here as good examples. The exponential growth of test patterns restricts the applicability of the exhaustive testing to cases where the number of primary inputs is relatively small (say, below 30). This is because of test application time that may exceed acceptable limits, and because of excessive storage requirements – wee still need to keep the correct test responses for the purpose of test results evaluation. Moreover, detection of certain delay faults may not be guaranteed, either, as they require a proper sequence (order) of test patterns that a conventional exhaustive tests may not provide, especially if they are produced by simple binary counters or similar circuitry.

## Slide 4: Pseudo-exhaustive testing
All vector combinations applied to a subset of inputs driving the same output
Test time = max {2k1, 2k2, ..., 2kn}
k1
k2
Notes: Pseudo-exhaustive testing achieves many of the benefits of exhaustive testing but typically requires far fewer test patterns. The concept of pseudo-exhaustive testing is applicable to designs where every single primary output depends only on a subset of primary inputs (such designs are sometimes referred to as partial-dependence circuits). In other words, it relies on various forms of circuit segmentation and attempts to test each segment exhaustively. Note that segments need not be disjoint. In this case, the actual testing boils down to applying all 2k combinations to k inputs feeding a given segment and the corresponding primary output. Clearly, the total test application time is equal to the maximum value computed over all test times corresponding to successive cones of logic found in the process of circuit segmentation. Another segmentation technique is based on path sensitization, as explained later. Finally, there are schemes using a physical segmentation with possible use of bypass storage cells placed on various signal lines (in the normal mode, the bypass cells remain transparent). One of the key problems that one has to solve when using the pseudo-exhaustive tests is designing a test pattern generator for this form of testing. Many proposed solutions include syndrome-driver counters, constant-weight counters, combined linear-feedback shift registers and pure shift registers, condensed linear-feedback shift registers, cyclic linear-feedback shift registers, and others.

## Slide 5: Other forms of testing
Pseudorandom testing
Weighted pseudorandom testing
For more information, see the chapter on BIST
Notes: In addition to exhaustive and pseudo-exhaustive testing, test patterns can be easily generated on-line in such a way that their characteristics remain similar to those of random or actually pseudorandom vectors. Yet another form of test generation produces patterns such that the distribution of 0s and 1s on the outputs of a generator is not uniform. As these techniques are amenable to built-in self-test (BIST) schemes, their detailed discussion is included in the chapter devoted to this particular form of test.

## Slide 6: Test vector
Let hu(x) be a faulty circuit version (function) with fault u
A test vector t detects fault u iff
h(t) ≠ hu(t)  h(t)  hu(t) = 1
All vectors satisfying the above equation form a set of tests detecting fault u
A test set is complete for a fault set F if for every fault from F, there is a test vector that detects it
Notes: Let hu(x) be a faulty circuit version (function) of a circuit (function) h with fault u being present (x represents an arbitrary input vector). Clearly, the presence of fault u transforms h into a new circuit hu. A given input vector t detects fault u if and only if h(t) ≠ hu(t), and thus test t can be obtained by solving the equation h(t)  hu(t) = 1, where  is the exclusive-OR operation. This is because a test t that detects u makes h(t) = 0 and hu(t) = 1 or vice versa. All vectors satisfying the aforementioned equation form a set of tests detecting fault u. Furthermore, a test set is complete for a fault set F if for every fault from F, there is a test vector that detects it. We will demonstrate that test vectors can be determined directly from the equation. Its applicability is confined, however, to very simple circuits as handling formulas corresponding to more complex designs becomes quickly infeasible and impractical, and thus we need more realistic methods to deal with fault-free and faulty circuits. Nevertheless, it is worth noting that test generation methods that rest on solving non-linear equations do exist, and they take advantage of very time-efficient SAT (satisfiability) solvers, which are deployed to determine if the variables of a given Boolean formula can be assigned in such a way as to make the formula evaluate to a logic value of 1. For example, the formula a + b is satisfiable because one can find the values (for example) a = 1 and b = 0, which make a + b being equal to 1.

## Slide 7: Example
h(a, b) = ab
ha/1(a, b) = 1b = b
Test set
h(a, b)  ha/1(a, b) = 1
ab  b = 1
Solution
abb + abb = 1
(a + b)b = 1
ab = 1  ab = 01
a
b
h
s-a-1
0
1
0
0
1
1
1
Notes: The function implemented by a circuit on the slide (a simple AND gate) is h(a, b) = ab. Let a fault be line a stuck-at 1. In the presence of this fault, the faulty function becomes just 1b = b. The test generation equation is then ab  b = 1. This equation can be transformed as shown on the slide. Eventually, it reduces to a’b = 1, and thus a = 0 and b = 1. As can be easily verified, applying this particular vector leads to the fault-free output 0, and to the output being equal to 1 in the faulty circuit. Hence, the pattern 01 is indeed a test vector detecting the target fault.

## Slide 8: Finding test vector
h = ab + bc + ac
haL/0 = bc + ac
Test set
h  haL/0 = 1
(ab+bc+ac)  (bc+ac) = 1
Solution
0 + ab(bc + ac) = 1
ab(b + c)(a + c) = 1
abc = 1  abc = 110
a
b
c
0
0
1
0
1
1
0
aL
h
Notes: This slide illustrates a bit more complicated case. The function implemented by a circuit on the slide is h(a, b, c) = ab + bc + ac. Let the upper branch of the input line a be stuck-at 0 (as shown by a red oval). In the presence of this fault, the circuit function becomes h(a, b, c) = bc + ac (note that the logic value of 0 forced by the fault eliminates the upper AND gate). The test equation assumes then the following form: (ab+bc+ac)  (bc+ac) = 1. This equation can be further reduced to a simple formula abc’ = 1, which yields the solution as follows: a = 1, b = 1, c = 0. We can verify that vector 110 is indeed a test detecting the target fault. Note that in the fault-free circuit the output is 1, while in the presence of the fault (as shown on the slide) the output becomes 0.

## Slide 9: Deterministic tests
Algorithmic methods used in automatic test pattern generation (ATPG)
Many ATPG tools originate from D-algorithm (J.P. Roth)
Efficient algorithms restricted to combinational circuits
Deterministic test vectors have to be stored explicitly
Gate-level models imply technology independence
Generation is done based on the circuit netlist
Typically the circuit hierarchy ignored
Diagnosis requires fault simulation
J.P. Roth, IBM Journal on Research and Development, 1966
Notes: The D-algorithm was developed by J.P. Roth at IBM in 1966, and was the first complete deterministic test pattern generation algorithm designed to be programmable on a computer. A test generation algorithm is complete if it is able to propagate a failure to an observable output. The D-algorithm entails finding all sets of inputs to the circuit that will bring out a fault within the circuit. It uses a notion of a primitive D cube of failure (PDCF), which is a set of inputs that sensitizes a path for a particular fault within a circuit. On the other hand, the propagation D cube (PDC) is a set of inputs that propagates an error (symbol D – see slide 20) from the inputs to the output. The D-algorithm picks all possible PDCF's for the circuit under test and applies them to the circuit with their corresponding PDC's to propagate various faults to the output. While the PDCF's and PDC's are being applied, the implied values for other circuit nodes are tested for consistency, rejecting sets of inputs that cause a circuit violation. The application and testing of various PDCF's and PDC's for a circuit is done repeatedly and recursively, until the minimal set of input patterns necessary to test the circuit for the targeted faults is determined.

## Slide 10: Complexity of ATPG
The longest phase of the IC design cycle
NP-complete problem – in the worst case test generation time grows exponentially with a design size
Typically, ATPG time grows as a square in the number of nodes
Nonminimalities and redundancy increase ATPG time considerably
Occasional aborts – given a number of decisions, ATPG cannot determine if a fault is testable
Notes: The test pattern generation algorithmic methods are all computation-intensive and can be quite expensive, not to mention the numerous difficulties that may be encountered in complex cases. In fact, in some circuits, the use of such algorithms may not be feasible or practical. In principle, the combinational ATPG problem is NP-complete as it is mathematically equivalent to the problem of Boolean satisfiability. This means that there cannot exist an algorithm which solves an arbitrary instance of the test generation problem in polynomial time (unless, of course, P = NP). Hence, the entire history of ATPG has been a process of improving heuristics and procedures that find test patterns as quickly as possible. As early as 1980, it was shown that for practically encountered instances of the test generation problem, the complexity of ATPG can be O(n2), where n is the number of logic gates. Since fault simulation is typically faster (with complexity of logic simulation being O(n)), it is reasonable to employ fault simulation in the process of test generation whenever it is possible, and resort to ATPG computations only for hard-to-test faults.

## Slide 11: ATPG references
ATPG may require path sensitization of arbitrary multiplicity and excessive amount of backtracking
Theoretical intractability of test generation process motivated other techniques: PODEM1, FAN2, CONT3, SOCRATES4, QUEST5, recursive learning6, FASTSCAN, TetraMax
1) P. Goel, IEEE Trans. Computers, 1981
2) H. Fujiwara, T. Shimono, IEEE Trans. Computers, 1983
3) Y. Takamatsu, K. Kinoshita, Proc. FTCS-17, 1987
4) M.H. Schultz et al., IEEE Trans. CAD, 1988
5) H. Cox, J. Rajski, Proc. ITC, 1990
6) W. Kunz, D.K. Pradhan, IEEE Trans. CAD, 1994
Notes: As mentioned earlier, the excessive amount of processing incurred by a hypothetical complete ATPG algorithm has resulted in developing several test generation schemes that feature various heuristics aimed at accelerating all phases of the test generation process. They include PODEM, FAN, CONT, SOCRATES, QUEST, recursive learning, FASTSCAN, and others. Some of these methods may not guarantee a solution, but they do work in most situations. They differ, for example, in selecting a starting point. While the D-algorithm begins at the faulty line, the critical path-based techniques starts from the primary outputs. On the other hand, PODEM begins from primary inputs. Its most pronounced improvements, such as FAN, use extra heuristics to minimize time spent on backtracking. Similarly, SOCRATES is an improvement over FAN and employs testability measures to facilitate backtracking.

## Slide 12: Sequential ATPG
Sequential ATPG is an extension of combinational ATPG, but is much more difficult
Efficient handling of time, unknown states, circuit initialization, internal clocks, embedded counters, RAMs, mixed data, etc. requires many heuristics
Some available algorithms: Extended Back Trace, STG, STG3, HITEC
Notes: Test generation for sequential circuits has long been recognized as a much more complex task than that of combinational ATPG. In particular, unstructured random sequential designs are very difficult to test. The difficulty in generating test patterns lies with (a) setting the state variables (the memory elements) into a certain combination so that the fault under test is excited and (b) propagating the fault effect to the primary outputs. In general, the longer the length of the shortest input sequence needed to perform both steps, the more difficult it is to find an input sequence to test the circuit. Several approaches have been proposed to solve the problem of test generation for sequential circuits. They are either extensions of the classical D-algorithm or are based on random techniques. When the number of circuit internal states is large and tests demand long input sequences, they can be quite ineffective for test generation. For example, in the extended D-algorithm, a large amount of effort may be wasted in trying to find short sequence tests for faults that require long ones. Random testing techniques can be very time consuming too for faults that have a few long test sequences. Additional factors, such as unknown states, circuit initialization problems, internal clocks, embedded counters and RAMs may add extra performance overhead to already complex test generation algorithms. Although there are several sequential ATPG techniques, they did not gain popularity that could match that of the combinational ATPG.

## Slide 13: General flow
Since ATPG is much more time consuming than fault simulation, these two modules are used together
Initially, random patterns may be applied to detect easy to test faults before passing other faults to ATPG
Create a fault list
ATPG
Test pattern
Fault simulation
Faults detected
Update fault list
Select a fault
Notes: The slide illustrates a general flow adopted in a generic test generation process. We begin by creating a list of target faults. Typically, phenomena such as fault equivalence and fault dominance are used here to perform fault collapsing that results in a relatively short fault list. Given a fault list, one can start the main loop. It repeatedly picks a fault from the list and invokes the main ATPG engine. It yields the corresponding test pattern unless it does not exist or ATPG exceeds backtrack and/or decision limits. In the latter case, we report an ATPG time-out causing an ATPG abort, and proceed to the next fault on the list. Once a test pattern is available, a fault simulation is invoked in order to determine other faults (still on the list) that are detected by a newly found test pattern. These faults are then removed from the list, and the whole process repeats. Typically, at the very beginning, pseudorandom test patterns can be used to eliminate easy-to-detect faults from the initial fault list.

## Slide 14: Fault sensitization
A test vector that detects a fault
  generates different values in fault-free and faulty circuits at the fault site
  propagates the fault effect to a primary output
All lines along at least one path have different values in fault-free and faulty circuits
A line changing its value in the presence of fault is sensitized; a path of sensitized lines is a sensitized path
1 - 0
1
1
0
0
1 - 0
0
0
1
0
1
1
0
G1
G2
G3
G4
Notes: There are two basic concepts in fault detection. First, a test T that detects a fault F activates F, i.e., it generates an error (or a fault effect) by creating different values at the site of the fault in the fault-free and in the faulty circuit. Second, T propagates the fault effect to a primary output, that is, it makes all the lines along at least one path between the fault site and the output have different values, again in the fault-free and in the faulty circuit. Sometimes we use the term “fault propagation” instead of “error propagation” or “fault-effect propagation”. A line whose value in the test T changes in the presence of the fault F is said to be sensitized to the fault F by the test T. A path composed of sensitized lines is called a sensitized path. For example, in a two-input AND gate, sensitizing the path of one input requires the other input to be set to 1. In the circuit shown on the slide, a sensitized path for the indicated stuck-at-0 fault goes from the output of gate G1 to gate G4, and then to the primary output. Note that in order to activate the fault, one needs to apply 1 to the first input. Creation of a sensitized path requires another 1 applied to the second input (to allow propagation through G1), and then the third input set to 0 ensures that a fault effect will propagate through the OR gate, as well.

## Slide 15: Gate on a sensitized path
If G is a unate gate with inversion i and controlling value c, whose output is sensitized to a fault f by a test t, then
  all inputs of G sensitized to f have the same value (say a)
  all inputs of G not sensitized to f (if any) have value c’
  the output of G has a value of a  i
c’ is an enabling value, as it allows error propagation
1 – 0
0 – 1
1
Notes: A gate whose output is sensitized to a fault F has at least one of its inputs sensitized to F as well. In general, the following properties characterize of a gate on a sensitized path. If G is a unate gate with inversion i and controlling value c, whose output is sensitized to a fault F by a test T, then:
all inputs of G sensitized to f have the same value (say a),
all inputs of G not sensitized to f (if any) have value c’,
the output of G has a value of a  i.
The value of c’ is often referred to as an enabling value. Consider an NAND gate shown on the slide. If this gate satisfies the above conditions, then it has either all inputs (sensitized or not) set to 1 or all sensitized inputs set to 0 and the remainig inputs (if any) set to the enabling value of 1. In our case, one of the inputs is sensitized, while the other one is set to the enabling value, and thus the output is sensitized, too (it has the value of a  i = a  1 = a’.

## Slide 16: Sensitized path
Let n be a line sensitized to the fault k s-a-v by a test t and let p be the inversion parity of a sensitized path between k and n
Applying repeatedly property from the previous slide
  the value of n in t is v’  p
  if there are several sensitized paths between k and n, then all of them have the same inversion parity
1 – 0
0 – 1
0 – 1
1
k
n
Notes:   By repeatedly applying the third property from the previous slide, one can arrive the following properties of sensitized paths. Let n be a line sensitized to the fault k s-a-v by a test t and let p be the inversion parity of a sensitized path between k and n. Then, the value of n in t is v’  p, and if the are several sensitized paths between k and n, then all of them have the same inversion parity. These properties are again illustrated by an NAND gate placed on a sesnitized path, as shown on the slide.

## Slide 17: Path sensitization
Technique of deriving a test from the circuit diagram
Producing a test for a fault on line k
  find a path from k to the output
  find signals that must be present on the gates along the path to enable propagation of a fault
  find input signals necessary to produce signals at the gate inputs (justification)
  determine input signals necessary to produce the appropriate signal on line k (excitation)
Single-path sensitization may fail to generate a test even if one exists – we need to consider all multiple paths!
Notes: As we have seen earlier, a path sensitization refers to finding a path in the circuit that allows an error to show up at an observable output of a device, if it is faulty. Clearly, this approach requires a prior knowledge of a circuit under test structure. In order to arrive with a test pattern for a fault on line k, we need to:
find a path from a fault site to the output or another observation point,
find signals that must be present on the gates along the path to enable propagation of a fault effect,
find (justify) input signals necessary to produce the above signals at the gates inputs,
determine additional input signals necessary to produce the appropriate signal on line k to activate (excite) the fault.
The main drawback of the classical path sensitization is that only a single path is examined (and sensitized) at a time. This does not guarantee that a test will be found for a fault even if one exists. In fact, it might be necessary to sensitize more than one path in deriving tests for certain faults and this is a principal idea behind many algorithmic test generation methods. It is worth noting that the number of multiple paths that a test generation method may need to examine tends to grow exponentially, thus having a negative impact on CPU time. Consequently, various APTG techniques employ variety of heuristics in an attempt to keep this number within reasonable limits.

## Slide 18: Single path sensitization
1
1
1
1
1
1
1
0
0
1
0
conflict
1
G1
G2
G3
G4
G5
G6
G7
G8
Notes: A simple example was reported by Schneider in 1967. The circuit is shown on the slide, and the fault in question is G2 output stuck-at-1. To generate the value of 0 at the output of G2 requires two 1s applied to the inputs of G2, and thus to the corresponding primary inputs. Note that this is a necessary assignment that cannot be relaxed. According to the single path sensitization paradigm, one can arbitrarily select a fault propagation path, as shown on the slide (bold red lines). This path requires yet another primary input to assume the value of 1 in order to establish a propagation path through gate G5. The very same path reaches subsequently gate G8, where all its inputs but the second one must be 1 to further propagate the fault effect to the primary output. Asserting the first input of G8 is not a problem – by implication the output of G4 is already 1 due to 0 on the output of G1 caused by earlier assignments on the corresponding primary inputs. An attempt to assert the remaining inputs, however, results in a conflict. Indeed, the lower input of G6 must be 0 to assure its high output. Unfortunately, this assignment causes the output of G3 to be 1, which in conjunction with another 1 on one of the primary inputs leads to 0 on the output of G7. This result, in turn, will stop fault propagation, rendering the obtained pattern useless.

## Slide 19: Multiple path sensitization
1
1
1-0
1
1
1
1
1
1
0
0-1
0-1
0
1
G1
G2
G3
G4
G5
G6
G7
G8
Notes: The Schneider’s example illustrates that a single path sensitization may not produce a test pattern for a target fault. Interestingly, however, in our case such a test pattern does exist. As shown on this slide, it suffices to apply vector 1111 to detect the fault. But in order to obtain this test, one has to consider two fault propagation paths in parallel. The fault excitation assignments remain the same as on the previous slide. On the other hand, in this new approach, only two inputs of G8 are set to non-controlling values. The remaining two inputs are both used to propagate the fault effect, as presented in the figure. Since the parity of inversions along both paths is the same, there is no mutual fault masking, and the primary output sees an error arriving from the original fault site – the fault is detected.

## Slide 20: D algebra
A pair of symbols describes fault-free and faulty circuits
0
1
D
D
X
AND
0
0
0
0
0
0
1
D
D
X
0
D
D
0
X
0
D
0
D
X
0
X
X
X
X
0
1
D
D
X
NOT
1
0
D
D
X
0
1
D
D
X
OR
0
1
D
D
1
1
1
1
D
1
D
1
D
1
1
D
X
1
X
X
X
1
X
X
X
0
1
D
D
X
Fault-free Faulty D alphabet
0 0 0
1 1 1
1 0 D
0 1 D
X – don’t care
0
1
D
D
X
Notes: Most algorithmic test generation methods refer to the composite symbols D and D'. They were introduced by the D-algorithm and have been adopted by other algorithms since then. D simply stands for a 1 in a good circuit and a 0 in a faulty one. On the other hand, D', which is the opposite of D, stands for 0 in a good circuit and 1 in a faulty circuit. Thus, propagating a D or D' from the inputs to the output simply means applying a set of inputs to a device to make its output exhibit an error if a fault within the circuit exists. Functionality of every logic gate can be expressed in terms of the D algebra. Examples for functions NOT, AND and OR and a 5-value algebra are given on the slide. Note that 0 and 1 in the tables are the composite values representing cases 0/0 and 1/1, respectively, while x represents a don’t care value. All entries in the tables can be easily obtained by separately processing the fault-free and faulty values, then composing the results. For example, D + 0 = 1/0 + 0/0 = 1+0/0+0 = 1/0 = D. Also, D + D’ = 1/0 + 0/1 = 1+0/0+1 = 1/1 = 1.

## Slide 21: ATPG general rules
Assign x to all lines
Select a fault and inject D or D’ at the fault site
Propagate the fault forward, so that D reaches one of the primary outputs, by making assignments to the other inputs of the gates
Make assignments to the inputs so that the assignments made earlier and the value required to excite the fault are justified
{0,1}
{0,1,D,D’}
{0,1}
{0,1}
D
Notes: Algorithmic pattern generation basically consists of the following steps:
fault selection, or choosing a fault that needs to be detected,
initial assignment, or finding an input pattern that sets up a D or D' at the output of the faulty gate,
forward drive, or propagating a D or D' to an observable output using the shortest path possible,
justification, or assigning of values to other unassigned inputs in order to justify the assignments made during the forward drive.
If an inconsistency arises during justification, backtracking or back propagation is performed, i.e., forward drive is done again using an alternate path. This recursive cycle is performed until the right set of input patterns needed to sensitize a path and propagate the fault to an observable output is determined. The figure on the slide illustrates regions of the circuit under test which are affected by the test generation process. The symbols from the D algebra that may occur on successive lines of the circuit are denoted within each region.

## Slide 22: Basic operations
Fault excitation (backward)
Fault-effect propagation (forward)
Line value justification (backward)
Line value implication (forward)
There might be many fault propagation paths (to primary outputs) and many value justifications
All of them have to be tried if necessary
Notes: To summarize our earlier observations, it is fair to say that any test generation process is comprised of a number of generic operations performed in a certain order. These operations include:
fault excitation – this is a process of creating a fault effect at one or more outputs of the faulty circuit element; the local value assignments for fault effect excitation can be derived from so-called fault-excitation cubes that can be easily deduced based on D algebra tables; for example the only combination of values that may be applied to two inputs of a faulty NOR gate to activate the stuck-at-0 fault on its output is 00; in the fault-free circuit it will produce 1 on the output, while in the faulty circuit we will observe 0, and thus the composite value 1/0 or D,
fault effect propagation – this is a process of assigning values to circuit lines such that a fault effect propagates from an output of the faulty circuit element to a primary output of the circuit; as shown earlier, one or more paths must be examined between the fault site and a primary output such that each line along at least one of them has D or D’ for the fault effect to be propagated to that output,
line value justification – this is a task of identifying values to be assigned to primary inputs such that a desired value is implied at certain internal circuit lines,
line value implication – this is a process of determining the logic values that appear at various lines of a circuit as a consequence of the values assigned to some of its remaining lines; in particular, this process can identify any inconsistency between the desired value at any line and the value determined at the line via implication.

## Slide 23: Examples
D
D
1,D
1
1
1
0
0
0,1,D,D’
0
0
0,1,D,D’
How to get a desired value?
Forward propagation
The resultant value
Backward implication
Notes: One can view the implication process as a simulation where we start with some values to be assigned. These assignments may determine (imply) new values, and so on, until no more values can be generated. Unlike simulation, however, values may propagate forward (toward primary outputs) and backward (toward primary inputs). Thus, to generate a test for the fault “line L stuck-at-1”, the initial two entries in the assignment pool (for further processing) will include (L, 0, backward) and (L, D’, forward), where the second parameter is the value to be assigned to the first one (a line), and the last parameter indicates a direction. The first gate on the slides illustrates forward propagation of values. The second gate shows backward propagation (to get 1 on the output of the gate, we need to apply 1s to both inputs of the gate). Note that both forward and backward propagation may induce further backward and forward propagation, respectively.

## Slide 24: Circuit dominators
A line d such that every path from L to any primary output passes through d is a dominator of L
A fault on line L represented as D is observed on a primary output only if D or D’ occurs on all dominators of L
D
L
Dominators of L
{D, D’}
{D, D’}
Notes: In the combinational logic, if all the paths from a line L to primary outputs go through line d, then line d is said to be the dominator of line L. It there is no other dominator between a signal and its dominator, the dominator is said to be an immediate dominator. Clearly, a fault on line L is observed on a primary output only if a fault effect occurs on all dominators of L. This observation may reduce ATPG processing time as a detailed analysis of dominators indicates that it is necessary to propagate the fault effect via certain nodes for a test vector before it finally reaches one of the primary outputs. In other words, we must set the inputs to dominators that are not in the fault effect cone to non-controlling values to propagate the fault effect through the dominator. These are mandatory assignments, and they can be determined by topological circuit analysis rather than by search. This would sometimes cause faults to be proved redundant without any search. During search, whenever any dominators of a fault become the constant values of 0 or 1, fault propagation can be stopped, and the algorithm can back-up immediately saving lots of time.

## Slide 25: Phase I – fanout-free circuits
JustifyFanoutFree(Circuit C, line L, bool v){
L = v;
G = gate driving L;
if(G == primary input)return;
if(G == AND){
if(v == 1)
for(all inputs k of G)JustifyFanoutFree(C, k, 1);
else { // v == 0
k = pick one input of G which is X; // guidance required
JustifyFanoutFree(C, k, 0);
}
if(G == OR){
…
}
}
z
a
d
c
b
h
g = 1
e
JustifyFanoutFree(C, g, 1);
JustifyFanoutFree(C, a, 1);
JustifyFanoutFree(C, e, 1);
JustifyFanoutFree(C, b, 0);
abcd = 10XX
Notes: Given a target fault “line L stuck-at-v” in a fan-out-free combinational circuit C, a simple procedure to generate a test vector would comprise the following steps:
initialize the circuit by setting all values to X,
excite the fault by justifying line L to v’, i.e., call procedure JustifyFanoutFree(C, L, v’),
propagate fault effect from L to a primary output.
The JustifyFanoutFree function recursively justifies the predecessor signals of L until all signals that need to be justified are indeed justified from the primary inputs. The simple outline of this function is shown on this slide. In the line indicated by the comment “guidance required”, controllability measures can be used to select the best input to justify. Selecting a good gate input may help to reach a primary input sooner. Consider a circuit shown on the slide. Suppose the objective is to justify g = 1. According to the algorithm, the sequence of recursive calls to JustifyFanoutFree, as shown above, will yield an input vector abcd = 10XX.

## Slide 26: Phase I – reconvergent fanout
g = 1;
JustifyFanoutFree(C, g, 1);
JustifyFanoutFree(C, a, 1);
JustifyFanoutFree(C, f, 1);
JustifyFanoutFree(C, d, 0);
JustifyFanoutFree(C, c, 0);
abc = 1X0,
z
a
b
c
h
g
f
d
e
z = 0
JustifyFanoutFree(C, z, 0);
JustifyFanoutFree(C, g, 0);
JustifyFanoutFree(C, f, 0);
JustifyFanoutFree(C, d, 1);
JustifyFanoutFree(C, c, 1);
JustifyFanoutFree(C, h, 0);
JustifyFanoutFree(C, e, 0);
JustifyFanoutFree(C, c, 0);
JustifyFanoutFree(C, b, 0);
conflict
Backtracking needed
Notes: Consider a circuit shown on this slide. Suppose again that the objective is to justify g = 1. Although the circuit features a re-convergent fan-out, function JustifyFanoutFree still works for the objective of trying to justify the signal g = 1. The sequence of recursive calls is listed on the slide. It produces an input vector abc = 1X0. In fact, in fan-out-free circuits, function JustifyFanoutFree will always be able to set a line to a desired value and conflict will ever be encountered. However, this is not always true for circuits with fan-outs, where signals propagating along fan-out branches are correlated due to a common stem (thus setting arbitrary values on these correlated paths may not always be possible). Consider the circuit shown above and let the objective be this time to set z = 0. The JustifyFanoutFree will first justify both g = 0 and h = 0. To justify g = 0, it picks the signal f, and though the recursive calls of JustifyFanoutFree will eventually assign c = 1. Next, to justify h = 0 it cannot choose e = 0 as it causes a conflict on signal c. Clearly, a different decision has to be made for justifying h = 0. In our case, it should be b = 0. This simple example illustrates that there is possibility of making wrong decisions resulting in time-consuming backtracks. As indicated earlier, various ATPG tools use many heuristics to avoid conflicts like the one presented on the slide.

## Slide 27: Decision tree
1
G1
a
b
c
d
e
f
g
h
i
j
k
l
m
n
F
F
S
m
n
n
k
i
{i,k,m}
{k,m,n}
{m,n}
Notes: Consider a circuit shown on the slide and a stuck-at-1 fault on the input of G1. Test generation for this fault can be represented by a decision tree depicted on the slide. The execution of a test generation algorithm can be traced by a depth-first traversal of the tree. A failure (F; here represented by a red vertex) terminal node indicates the detection of inconsistency. A success terminal node (S) represents finding a test. A branch departing from a decision node shows the decision taken, that is, the gate selected for error propagation. Note, that we first try to propagate the error solely through i, then through i and k, and eventually we succeed when all three paths from g (through i, k, and m) are simultaneously sensitized. The actual processing steps would be as follows:
activate the fault and propagate through g: a = 0, h = 1, b = 1, c = 1, g = D,
propagate through i: d = 1, I = D’, d’ = 0,
propagate through n: j = 1, k = 1, l = 1, m = 1, n = D, e’ = 0, e = 1, k = D’ – contradiction,
propagate through k: e = 1, k = D’, e’ = 0, j = 1,
propagate through n: l = 1, m = 1, n = D, f’ = 0, f = 1, m = D’ – contradiction,
propagate through m: f = 1, m = D’, f’ = 0, l = 1, n = D.

## Slide 28: Phase II
PropagateFanoutFree(Circuit C, line L) {
if(fanout of L == 1){
gate G = fanout of L;
if(none of inputs of G is X)backtrack;
}
else G = pick one fanout gate of L that is unjustified;
if(G == AND)
for(all inputs k of G such that k ≠ L)
if(k == X)JustifyFanoutFree (C, k, 1);
if(G == OR)
for(all inputs k of G such that k ≠ L)
if(k == X)JustifyFanoutFree (C, k, 0);
if(G == …) …
PropagateFanoutFree(C, output of G);
}
PropagateFanoutFree(C, g);
JustifyFanoutFree(C, h, 0);
JustifyFanoutFree(C, b, 0);
PropagateFanoutFree(C, z);
abc = 100 for g/0
Simulation (implication) may simplify the process
Notes: Let us carry on the first example from the previous slide with the target fault “line g stuck-at-0”. Suppose JustifyFanoutFree have successfully activated the fault. The next step is to propagate the fault effect to a primary output. This is accomplished by means of a recursive function PropagateFanoutFree shown on this slide. It propagates the fault effect one gate at a time until it reaches a primary output. The sequence of calls for our fault g/0 is demonstrated at the bottom of the slide. It will lead to the test vector abc = 100. Interestingly, once g/0 has been excited after JustifyFanoutFree (C, g, 1), it is also propagated to z, because ac = 10 makes h = 0. In other words, step JustifyFanoutFree (C, h, 0) is redundant. However, this is only possible if logic simulation or implication capability is deployed by the basic test generation algorithm to reveal such relationships.
It is important to recall that functions JustifyFanoutFree and PropagateFanoutFree are meant for fan-out-free circuits only (and for the presentation purposes), and hence will not always be applicable in more general scenarios due to possible conflicts. Typically, a mechanism that allows ATPG to handle conflicts in a systematic manner is based (conceptually) on a decision tree enforcing backtracks whenever an inconsistency or a state that precludes further error propagation are encountered.

## Slide 29: Undetectable faults
If no test is found, the fault is undetectable
For an undetectable fault f Zf(x) = Z(x) and no test can simultaneously activate f and create a sensitized path to a primary output
An undetectable fault may invalidate the single fault assumption
  a complete test set for single faults may fail to detect, otherwise detectable fault, if an undetectable fault occurs in the circuit, or
  both faults may become undetectable
Two undetectable single faults may become detectable if simultaneously present in the circuit
Notes:   A fault F is said to be detectable if there exists a test T that detects F; otherwise, F is undetectable. For an undetectable fault F we have ZF(x) = Z(x), and no test can simultaneously activate F and create a sensitized path to a primary output. Since undetectable faults do not change the function of the circuit, it may appear that they are harmless and hence can be ignored. However, an undetectable fault may invalidate the single fault assumption. For example, a complete test set for single faults may fail to detect, otherwise detectable fault, if an undetectable fault occurs in the circuit, or both faults may become undetectable. On the other hand, two undetectable single faults may become detectable, if simultaneously present in the circuit.

## Slide 30: Undetectable fault
The stuck-at-1 fault is not detectable
The error does not reach the output
1
1
1-0
1
1
1
1
0
0
0-1
0-1
0
1
G1
G2
G3
G4
G5
G6
Notes: Consider a circuit shown on the slide with the indicated stuck-at-1 fault on the input of gate G1. This fault is undetectable. All assignments made in the circuit are necessary in order to properly activate the fault, and then to propagate the fault effect. Unfortunately, the error propagation stops at gate G6, as shown by the bold red line. This is because of the controlling value (0) arriving at the other input of the same gate from gate G5. This signal is a consequence of earlier assignments made in the circuit in order to either excite the fault or create a sensitized path (the only one that exists).

## Slide 31: Testable fault
Stuck-at-0 fault is detected by xx01 provided it is the only fault in the circuit
1
1
1-0
1
1
1
0
0
0-1
0-1
0
0
G1
G2
G3
G4
G5
G6
Notes: One can easily observe that another fault in the same circuit, this time stuck-at-0 of the G3 input is detected by test xx01, i.e., one of the following four combinations: 0001, 0101, 1001, or 1101 may act as a test pattern for this particular fault. The excitation and propagation conditions are illustrated on the slide.

## Slide 32: Masking
Fault stuck-at-0, when it occurs as a single fault, is detected by vector 1x01
The same test vector fails to detect both faults
1
1-0
1-0
1
1
1
0-1
0-1
0
0
1
1
0
G1
G2
G3
G4
G5
G6
Notes: The fault at the input of G3 is no longer detected by tests 1001 or 1101, if the undetectable fault stuck-at-1 at the input of G1 is also present. This is because both faults will mask each other at the inputs of gate G6 (note that the fault stuck-at-0 propagates as D on the output of G3 and then as D’ on the output of G5, while the fault stuck-at-1 appears on the output of G1 as D’, and subsequently as D on the output of G4; as a result, we will get DD’ = 0 on the output of G6). Thus, if test 1001 is the only one that detects the fault stuck-at-0 in a complete test set T for this circuit, then T is no longer complete in the presence of the fault stuck-at-1. The fault stuck-at-0 is sometimes called a second-generation redundant fault (as it becomes undetectable in the presence on another undetectable fault).

## Slide 33: Redundancy
A combinational circuit with undetectable faults is redundant
Redundant circuit can be simplified by removing at least one gate or gate input
A combinational circuit with all stuck-at faults detectable is irredundant
Notes: A combinational circuit that contains an undetectable stuck-at fault is said to be redundant, since such a circuit can always be simplified by removing at least one gate or gate input. For example, suppose that a stuck-at-1 fault on an input of an AND gate is undetectable. Since the function of the circuit does not change in the presence of the fault, we can permanently place a 1 on that input. But an n-input AND gate with a constant 1 on one input is logically equivalent to the (n – 1)-input AND gate obtained by removing the gate input with the constant signal. Similarly, if an AND gate input stuck-at-0 fault is undetectable, the AND gate can be removed and replaced by a 0 signal. Since now we have a new signal with a constant value, the simplification process may continue. Clearly, the same rules applies to an OR gate, where a constant 1 on its input implies removal of such a gate. One can easily derive similar steps for NAND and NOR gates.

## Slide 34: Redundancy is undesirable
In the presence of a redundant fault a previously testable fault can become undetectable
In the presence of a redundant fault a previously generated test vector can become invalid
Redundant faults slow down test tools by increasing ATPG time and fault simulation time
Notes: Logic redundancy is, in general, not desired. In many cases, redundant logic circuit is slower and consumes more power. As we have demonstrated earlier, in the presence of a redundant fault a previously testable fault can become undetectable. Also, in the presence of a redundant fault a previously generated test vector can become invalid. These are serious concerns from the reliability point of view. Redundant faults slow down test tools by increasing ATPG time and fault simulation time – typically it may take a lot of time to conclude that a test vector for a particular fault actually does not exist.

## Slide 35: Sources of redundancy
Unintentional redundancies occur in manual designs and in automated synthesis if the initial circuit contains redundancy
Global redundancies can be introduced by connecting irredundant blocks
Intentional redundancies are introduced to
  increase driving capabilities
  correct errors
  remove hazards
Notes: Fully-testable subassemblies with no redundant logic may be combined into an assembly that has redundant hardware, and therefore, is slower, dissipates more power and may be unreliable if multiple stuck-at faults are present. Consider a large design that must be partitioned before its logic synthesis. The act of partitioning introduces the potential for redundant hardware, and ATPG-based approach is one of the best techniques for finding this redundant logic.
Redundancy can be introduced on the purpose. It is a well-known fact that including additional (redundant) implicants/implicents in two-level logic synthesis is a common practice deployed to avoid hazards. Redundant logic is also employed to correct errors in fault-tolerant designs. In more general techniques, such as triple modular redundancy (TMR), three identical and redundant modules are used to mask faults occurring in one of them by means of a majority voting system. In certain situations, redundancy may not be avoidable. For instance, when an irredundant circuit is mapped into a standard cell library it may become necessary to have extra gates to minimize the overall area or to arrive with an optimum-speed circuit.

## Slide 36: Redundancy removal
Local redundancy can be avoided by use of proper synthesis tools
Intentional redundancies should be avoided by
  proper transistor sizing
  avoidance of hazard sensitive design
Global redundancies can be identified by ATPG
Redundancies should be removed one at a time
Notes: Identifying redundancy is closely related to the problem of test generation. To show that a line is redundant means to prove that no test exists for the corresponding fault. It should be noted, however, that identifying all redundancies in large designs as an exact solution is infeasible as this is an NP-hard problem. Instead, we try to identify as many as possible redundancies in a reasonable run time.