## Slide 1: VLSI testing
Built-in self-test
HEP
Notes: An attractive alternative to the classical testing scenario, where test patterns are applied from an external tester, is built-in self-test (BIST). In BIST, the original circuit designed to perform the system function is appended with additional modules for generation of test patterns and compaction of test responses. Thus, the BIST approach can be applied at all levels of testing, starting from wafer and device to system and field testing. It is widely accepted that appending these modules to the original circuit satisfies reasonable fault coverage requirements while reducing test application time, volume of test data, and the dependence on expensive testing equipment. However, it is also agreed that this solution compromises a circuit's area and performance as it inevitably introduces either a hardware overhead or additional delays and increased latency. These delays may be excessive for high-speed circuits. Therefore, BIST schemes are evaluated thoroughly on the basis of the fault coverage they provide, area overhead they require, and the performance penalty they introduce. Numerous BIST schemes have been proposed to cope with these objectives for various types of failures, errors, and a variety of test scenarios. In this chapter, we will outline several schemes used in different BIST environments. They have gained an acceptance by BIST practitioners, and have been successfully applied in several test technologies, either as leading or supporting test methodology.

## Slide 2: External testers
Limitations of ATE
  limited overall accuracy
  limited capacity and bandwidth
  long test application time
  excessive cost
Exploding volume of test data
Potential yield loss due to ATE inaccuracy
A T
E
Notes: Although several testability problems can be alleviated by using certain DFT techniques as shown earlier, the actual testing still requires the application of test stimuli and the comparison of test responses with the correct reference. These operations are traditionally carried out by means of external testing equipment such that the tester applies test vectors one by one and then compares the responses with the fault-free responses, also one by one. For large circuits this approach may become infeasible: the patterns can be difficult to generate and the number of tests can be so large that it would be difficult to store and handle them efficiently by the tester hardware. The time to apply the vectors can be unacceptable. In addition, the testers are very expensive, and testing cannot be performed once the device is in the system.

## Slide 3: Expensive testers
$3,000 per ATE channel
Test cost: from 5 to 25 cents per second
1970s
1980s
1990s
2000s
Notes: High demand in the consumer electronics market, accompanied by the fact that it was difficult and expensive to build the test equipment in-house, created an environment for the emergence of the third party manufacturers of automated test systems. ATE to test digital IC’s appeared first; and ATE for digital and analog IC’s were separate systems. The analog and mixed-signal ATE industry was started when Teradyne, Inc. and the LTX Corporation were founded in the late 1960’s, and the early 1970’s, respectively. These companies began by developing automated test equipment to test linear analog IC’s, where the void was greatest. Over the next several years the capabilities of their ATE products evolved to serve the testing needs of mixed-signal (digital and analog) ICs. It is an open question whether the development of purely analog ATE has disappeared. However, today’s mixed signal ATE’s, even if equipped with “analog only” instruments, rely totally on digital signal processing based measurement methods (i.e., the measured analog signals are digitized and DSP algorithms are used to extract the desired performance parameters). Since today’s ATE is developed using IC’s obtained with yesterday’s technologies, even the most advanced ATE is challenged to test IC’s that represent the latest state-of-the-art solutions. For example, the increasing performance of IC’s for storage devices is resulting in increasingly more stringent demands on the timing parameters of today’s ATE’s. The clock jitter (phase noise) of no more than 10 ps rms is required to properly test the read channel IC’s that are realizing more than 100 Mb/s data rates. Some of the mixed-signal ATE vendors provide special modes which increase the digital capture rates up to 400 MHz.

## Slide 4: Built-in self-test (BIST)
BIST – testing is accomplished through built-in hardware and software features
Large circuits include on-chip circuitry to generate test vectors and evaluate responses
Simple devices (LFSR) produce test patterns, in particular pseudorandom
Test responses compacted into a short statistic by computing a signature
The signature obtained from the circuit under test compared with a fault-free reference
Notes: In BIST, an additional on-chip circuitry is included to generate test vectors, evaluate test responses, and control the test. While the idea of a digital circuit testing itself is many decades old (for example, the earliest switches from AT&T had some self testing capabilities), the use of BIST in commercial designs has become popular only in 90’s, and since then had its own ups and downs. Random, or in fact pseudorandom, patterns are generated by simple circuits, and test responses are compacted into a short statistic by calculating a signature. This signature, obtained from the CUT, is subsequently compared with a fault-free signature. BIST may significantly change the way the integrated circuits are tested. It reduces the cost of testing by shortening the test application time, minimizing the amount of test data stored, and lowering the cost of testing equipment. Its implementation can result in a reduction of the product development cycle and cost, as well as a reduction of the cost of system maintenance. The latter benefits may have a dramatic impact on the economics of testing. It follows from the fact that built-in test circuitry can test chips, boards, and the entire system virtually without very expensive external automatic test equipment.
The ability to run tests at different levels of the system's hierarchy significantly simplifies diagnostic testing, which in turn improves troubleshooting procedures and sanity checks during assembly, integration, and field service. Since the BIST hardware is an integral part of the chip, BIST, in principle, could allow for at-speed testing, thus covering faults affecting circuit timing characteristics. Also, BIST can be a good solution to test a secure device. Scan provides information and access to internal registers that someone can use to learn about the device. BIST can be used in a non-secure environment without providing secure information or access to the inside of the device.

## Slide 5: BIST and STUMPS
Test pattern generator
Compactor
Golden signature
Control
Notes: One of the most popular BIST arrangements is shown on the slide in conjunction with so-called self-testing using MISR and parallel shift register sequence generator (STUMPS) architecture. In this approach, an LFSR used as a test generator feeds parallel scan chains, while the serial outputs of the scan chains drive compactor inputs. The use of multiple scan chains can significantly reduce the test application time, as discussed earlier. Since the scan paths may be of different lengths, every time a pattern is to be produced, the generator is run for c clock cycles, where c is the size of the longest scan chain.
As can be seen, the use of BIST is also associated with certain costs. Additional silicon area is required for the test hardware to perform test pattern generation and test response compaction. Some performance degradation may be introduced due to the presence of multiplexers needed to apply test patterns in the test mode (in addition to a scan environment). Some testing equipment may still be needed to test the BIST hardware and to carry out the parametric testing. BIST also requires more rigid design. In particular, unknown states are not allowed since they can produce unknown signatures. We will also return to these problems later on.

## Slide 6: Pseudorandom testing
Though generated deterministically, test vectors have characteristics of random patterns
Applicable mainly to combinational circuits
Fault simulation required
No input test data to store
Tests generated by very simple hardware
Must be supplemented by other techniques to target random-pattern-resistant faults
Probability of detecting a fault with v vectors assuming that its detection probability by a single vector is p: 1 – (1 – p)v
Notes: In pseudorandom testing, test vectors have the characteristics of random patterns in spite of being generated deterministically. As there is no need to cover all 2n input combinations, a test length can be significantly shorter than that of the exhaustive or pseudo-exhaustive testing. On the other hand, the produced sequences could be still very long in order to achieve complete fault coverage. This is due to the presence of random pattern resistant faults, which may effectively elevate both the cost of test application and the cost of fault simulation. Thus, in many practical circuits, pseudorandom patterns have to be supplemented by deterministic tests (we will return to this later on) unless the circuit is designed as random pattern testable. An advantage of the pseudorandom testing stems from its potential for a very simple hardware and small design efforts required to implement test generation.
Assuming a sufficiently large pseudorandom test pattern generator (PRPG), we may determine expected test length and fault coverage as follows. Let us first consider the probability of detecting a fault with v random test vectors, assuming that the detection probability is p. This probability can be expressed as Pv = 1 – (1 – p )v, where (1 – p)v is the probability that a fault will not be detected by any of v test vectors. Thus, the expected fault coverage of a set of n faults characterized by detection probabilities pi, i = 1,2,…, n, can be obtained by summing Pv‘s over all faults, as shown on the next slide.

## Slide 7: Fault coverage by random patterns
Fault coverage of an n-fault set characterized by detection probabilities pk achieved by v vectors
1 – n–1
(1 – pk)v
S
k = 1
n
Fault coverage
0
20
40
60
80
100
0
20
40
60
80
100
Test patterns
%
?
Notes: In addition to the fault coverage formula, the slide illustrates an example of fault coverage curve (a dependence of fault coverage on the number of test patterns applied) obtained from the formula and by assuming certain fault detection probabilities. Generally, the coverage of pseudorandom patterns can seldom achieve 100%. Usually, the fault coverage curve levels off and reaches the “the area of diminishing returns” after a number of tests have been applied. The remaining faults can be covered using, at least, three different strategies. The first one modifies the CUT by means of test point insertion. The second approach targets test generators such that they can be used to tackle more efficiently the random pattern resistant faults. We will demonstrate several techniques belonging to both classes soon. The third method attacks the problem neither at the site of the faults nor at the source of the stimulus generation. Instead, it applies deterministically-produced test patterns by deploying various forms of test data encoding. We will return to this approach in another chapter.

## Slide 8: Test generators
Capable of generating “good” pseudorandom patterns
  long aperiodic sequences
  no structural dependencies
  low linear dependencies
Capable of driving large number of scan chains
Very simple hardware, small area
Fast operational speed
Easy to synthesize and analyze
Notes: Pseudorandom test patterns are the most commonly produced vectors by test generators (TG) found in BIST applications. Thus, a good TG, in addition to ability of yielding a long random (though repeatable) sequences of binary values, should address additional concerns that include structural and linear dependencies. While structural dependencies create problems in multiple scan chains, linear dependencies can be observed in any BIST architecture. In both cases, their represent degree of inability to produce certain combinations either because of a generator structure or due to mutual relationships between successive bits leaving the TG.

## Slide 9: Linear feedback shift register (LFSR)
2
1
0
3
6
9
12
15
4
5
7
8
10
11
13
14
2
1
0
3
6
9
12
15
4
5
7
8
10
11
13
14
Feedback provided by XOR gates
The characteristic polynomial: x16 + x10 + x7 + x4 + 1
Fibonacci and Galois configurations
Notes: By far the most popular devices in use as a source of pseudorandom test sequences are linear feedback shift registers (LFSRs). An n-bit LFSR consists of n memory elements and XOR gates connected as shown on the slide (the upper part). The modulo 2 sum of the selected stages goes back to the leftmost stage of the register forming so called Fibonacci LFSR. The lower part of the slide shows an alternative LFSR implementation with interspersed XOR gates. It is referred to as Galois LFSR. Its distinctive feature is that the output of the rightmost stage of the LFSR feeds those stages, which are indicated by the characteristic polynomial.
The depth of the linear logic in feedback paths limits the operating speed of Fibonacci LFSRs. Similarly, Galois LFSRs may cause frequency degradation due to long feedback lines, and may take up a considerable area as it involves a large fan-out on the rightmost stage output. These limitations are noticeably pronounced for polynomials with a large number of terms.

## Slide 10: Primitive polynomials
An n-bit LFSR with nonzero seed and primitive characteristic polynomial generates maximum length sequence (m-sequence) with period of 2n – 1
1 1 1 1 0 1 0 1 1 0 0 1 0 0 0
1
0
0
0
1 3 7 15 14 13 10 5 11 6 12 9 2 4 8
Degree: large enough so the states do not repeat and to reduce linear dependencies
Type: primitive, avoid trinomials (increased linear dependencies), use at least pentanomials or septanomials
Seed value: selected through fault simulation or reseeding
Notes: An LFSR can be represented by the characteristic polynomial xn + hn-1xn-1 + … + h1x + h0, where hk refers to the kth flip-flop of the register. If hk = 1, then there is a feedback tap taken from this flip-flop. A characteristic polynomial, which causes an n-bit LFSR to go through all possible 2n – 1 nonzero states before entering the initial state is called a primitive polynomial, while the corresponding LFSR is known as a maximum-length LFSR producing the output sequence termed a maximum-length sequence or m-sequence.

## Slide 11: Properties of m-sequence
Starting from a nonzero state the LFSR traverses all possible 2n – 1 states before repeating
It consists of 2n-1 1s and (2n-1 – 1) 0s
There is one pattern of n consecutive 1s and one pattern of n – 1 consecutive 0s
Any pair comprising an m-sequence and its circularly shifted version is identical in 2n-1 – 1 positions and differ in 2n-1 positions
A sum of an m-sequence and its circularly shifted version is another shifted version of that m-sequence
Notes: Any m-sequence produced by a maximum-length n-bit LFSR has the following properties.
(1) It consists of 2n-1 1s and 2n-1 – 1 0s (all n-bit combinations appear except all 0s).
(2) There is one pattern of n consecutive 1s and one pattern of n-1 consecutive 0s.
(3) The autocorrelation property. Consider two m-sequences, the original one and its circularly shifted version. Any pair of such sequences will be identical in 2n-1 – 1 positions and will differ in 2n-1 positions. Furthermore, a sum of an m-sequence and its circularly shifted version gives another shifted version of that m-sequence. This feature, resulting from the superposition principle, will be used to construct, in a time-efficient manner, circuits that can alleviate some drawbacks of LFSR-generated test patterns. We will get back to this issue a bit later.

## Slide 12: Fast simulation
0
1
0
0
0
0
1
0
1
0
0
1
1
0
0
0
Step
1
2
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
Simulation
Superposition
1
0
0
0
0
0
0
1
0
1
0
0
1
0
0
0
1
1
0
0
3
2
1
0
J. Rajski, J. Tyszer, JETTA, 2003
Notes: The ability to quickly arrive with a state that an LFSR reaches after applying a given number of clock cycles is instrumental in many applications. Such a state could be determined by simply running the generator for up to 2n clock cycles. This approach clearly fails for large values of n. Here, we discuss a technique which handles hundreds bits-long LFSRs in a time-efficient manner.
Consider a 4-bit LFSR implementing the primitive polynomial x4 + x + 1. To determine a state that it reaches after a given number of clock cycles, we will use a lookup table that consists of four rows and four columns, as shown on the slide. The entry located in ith row and jth column represents a state which the LFSR enters after 2i steps assuming that the initial state features a single one on the jth position in its binary representation. Single simulation steps determines the content of the first row of the table. It contains states reachable after applying a single clock cycle. As a result, the first row entry in column j stores the state that immediately follows a state comprised of all zeros but a single one on position j. For instance, the LFSR initialized with state 0010 moves to state 1001 in one step, and this is represented by the entry in the first row and the third column of the table. Entries in the remaining rows of the table can be easily determined by using the principle of superposition. So, besides the first step, there is no need to use logic simulation!
Suppose one wants to determine a state that the LFSR reaches after two clock cycles assuming that its initial state was 0010. This problem reduces to finding a state that the LFSR reaches after one clock cycle provided its current state is 1001 (see the first row of the lookup table). The principle of superposition allows further decomposition of the problem into two simpler tasks: finding immediate successors of states 1000 and 0001, as these are the states whose superposition yields state 1001. From the first row of the lookup table we get that the LFSR moves in one step from states 1000 and 0001 to states 0100 and 1000, respectively. Their bit-wise sum results in state 1100. This is the state that should be placed in the second row and the third column of the lookup table.

## Slide 13: O(n2) processing time
0
1
0
0
0
0
1
0
1
0
0
1
1
0
0
0
1
1
0
0
0
0
1
0
1
0
0
1
0
1
0
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
0
1
0
1
1
0
1
1
1
1
0
0
1
0
1
Step
1
2
4
8
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
Superposition
3
2
1
0
1
0
0
0
Notes: Entries in the remaining rows are obtained in a similar fashion by using iteratively data computed in the previous steps. Thus, any state that the LFSR reaches after 2k cycles is determined by adding respective states reachable after 2k-1 clock cycles. Using tables as the one shown on the slide, we can find a state reachable after an arbitrary number C of cycles in at most n basic steps, each comprising up to n lookups. The computational complexity of this process is thus O(n2). It starts by expressing C as a sum of powers of 2, and then follows the rules presented earlier. The animated example on the slide illustrates this technique for C = 15 (and thus it can also be used to verify whether a given polynomial is a primitive one – the LFSR must return to its initial state, though it does not suffice to declare a primitiveness of a given polynomial).

## Slide 14: Hybrid LFSR and cellular automaton
1
1
1
1
1
0
0
0
Notes: Other forms of linear finite state machines include hybrid LFSRs and cellular automata (CA). The former class combines certain features of Fibonacci and Galois LFSRs in such a way that the resultant circuits have some XOR gates placed outside the shift registers, whereas the remaining gates are interspersed between flip-flops. This approach alleviates, to some extent, drawbacks of conventional LFSRs. Unfortunately, hybrid LSFRs can only be obtained for selected characteristic polynomials.
A cellular automaton is a collection of cells connected in such a way that each cell is restricted to local neighborhood interactions. The linear cellular automaton (LCA) considered here is a circuit composed of a one-dimensional array of cells, which only communicate with their immediate neighbors. These relationships are expressed by means of rules used to determine the next state of a given cell based on information received from its neighbors. If cell c can communicate only with its two neighbors, c-1 and c+1, the so-called rules 90 (denoted by 0) and 150 (denoted by 1) are usually employed. The rule 90 can be implemented by a linear logic according to the formula xc(t+1) = xc-1(t)  xc+1(t), while the rule 150 satisfies the equation xc(t+1) = xc-1(t)  xc(t)  xc+1(t), where xc(t) represents the state of cell c at time t. The LCA on the slide features null boundary conditions. It behaves as if the boundary always supplies a zero from beyond the automaton.

## Slide 15: Ring generator
One source per one destination
Limited fan-out
Fast – a single XOR gate delay
Modular
x24 + x17 + x14 + x6 + 1
17
14
6
2
1
0
3
6
9
4
5
7
8
10
11
21
22
23
20
17
14
19
18
16
15
13
12
G. Mrugalski, J. Rajski, J. Tyszer, IEEE Trans. CAD, 2004
Notes: A ring generator is a linear finite state machine obtained by forming a circle (ring) that consists of memory elements, and then by adding gradually feedback connections, which correspond to successive terms of a characteristic polynomial. Given tap xk, we create a feedback loop by encompassing k adjacent flip-flops, always beginning with the leftmost ones. Note that in this approach, two feedback lines cannot cross each other. Instead, they form a very regular rack frame provided a suitable characteristic polynomial is deployed. Since a subset of k adjacent flip-flops can be chosen in different ways as long as the resultant feedback line does not cross any other feedback line, the ring generator offers certain degree of flexibility in forming its structure. Two implementations of a feedback tap x17 illustrate this phenomenon on the slide. The resultant ring generators will feature different state trajectories, still producing the same m-sequence though, just differently phase-shifted in each case. Indeed, it can be proved that given a primitive polynomial, the ring generator remains a maximum-length finite state machine.

## Slide 16: Ring generator
14
6
2
1
0
6
9
4
5
7
8
10
11
21
22
23
17
14
19
18
16
15
13
12
G. Mrugalski, J. Rajski, J. Tyszer, IEEE Trans. CAD, 2004
17
3
20
One source per one destination
Limited fan-out
Fast – a single XOR gate delay
Modular
x24 + x17 + x14 + x6 + 1
Notes: The ring generator has many advantages over conventional LFSRs. It features significantly reduced levels of XOR logic – only one 2-input XOR gate occurs between designated flip-flops if feedback logic is to be inserted. Such a design style maximizes the operating speeds as a single 2-input XOR gate delay and short feedback lines do not cause any frequency degradation.
Besides the simplicity of feedback connections, the reduced internal fan-outs are the most noticeable feature of the ring generators. Any stem in the ring generator feeds (at most) only two devices. Due to simplified circuit layout and routing, the ring generators are highly modular. In many designs, connecting a ring generator with other nodes may result in a large number of wires that would have to be routed across a chip. To alleviate this problem, different segments of a ring generator can be used to drive different regions of the circuit. The placement of the ring generator can be easily accomplished because of a clean separation and a simple interface between successive components of the generator. In particular, one can use any connection (a wire) in a generator as a cut between segments since it links only two memory elements, and it does not feature any extra fan-outs.

## Slide 17: Two-dimensional generators
Structural
dependencies
...
Notes: If an LFSR is to feed parallel scan chains, the resultant patterns occurring in successive chains can be highly correlated (in fact, almost identical) due to structural dependencies, as shown on the slide, where binary sequences in adjacent scan chains are just shifted (by a single bit) replicas of each other. This phenomenon may invalidate the whole test set.

## Slide 18: Two-dimensional generators
Find XOR network which guarantees minimum channel separation
Phase shifter
Notes: If it is necessary to drive a large number of scan chains and to reduce structural dependencies between sequences leaving the test generator, it has to be connected to a phase shifter. In principle, logic synthesis of a phase shifter entails finding a set of linear combinations of the generator outputs such that each of the resulting sequences, obtained by summing up these outputs, will be shifted with respect to every other sequence by at least a pre-specified number of bits.

## Slide 19: Linear dependencies
a + d
a + c + d
a + b + c + d
b + c + d
a + b + c
b + d
a + c
a + b + d
c + d
b + c
a + b
d
c
b
a
Cannot generate
test 111 !
1
1
0
1
0
1
0
1
1
0
0
0
Only these 4
combinations
are possible
d
c
b
a
Notes: In addition to structural dependencies, a test generator should be also designed with the objective of minimizing the probability of having linearly dependent test sequences. Their impact on test patterns is illustrated on the slide. Assume that a 4-bit LFSR (shown above) is to supply a test vector that detects stuck-at-0 fault on the output of a 3-input AND gate. It requires three 1s occurring in scan cells indicated by red dots. If the LFSR is initialized with a 4-bit vector dcba, then the indicated scan cells will receive binary values that can be expressed in terms of a, b, c, and d as follows: a + b + c + d, a + b + d, and c. As can be easily verified, these three expressions are linearly dependent, and thus only four out of eight binary vectors can be obtained, as shown above. In particular, it is impossible to produce a test pattern with three 1s on the desired (red) positions, since setting c = 1, and a + b + d = 1 leads immediately to a + b + c + d = 0. There are many other locations that are linearly dependent in the illustrated sequence – some of them are represented by blue dots (interpreted vertically).

## Slide 20: LD probability
k
n = 30
Chart: 
| 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
 | 3e-06 | 7e-06 | 1.5e-05 | 3e-05 | 6e-05 | 0.00012 | 0.00024 | 0.00048 | 0.00097 | 0.001951 | 0.0039 | 0.0078 | 0.0155 | 0.0302 | 0.0612 | 0.1198 | 0.2298 | 0.42242 | 0.71121
Õ
k - 1
i = 0
P(n,k) = 1 −
2n – 2i
2n – i – 1
C.L. Chen, IEEE Trans. Computers, 1986
Notes: C.L. Chen has arrived with the probability that a randomly selected combination of k bits being a part of an m-sequence produced by an n-bit LFSR are linearly dependent. Clearly, for k > n, this probability is equal to 1.0. Otherwise, it is given by a formula shown on the slide, along with an example of how it works for n = 30 and k going from 12 to 30. One has to remember, however, that typically sequences produced by LFSRs as scan test patterns are much shorter than the corresponding m-sequences that consist of 2n – 1 bits. Consequently, the probability of having linearly dependent positions in a given scan test pattern can be much higher than that indicated by the Chen’s formula.

## Slide 21: PRPG with phase shifter
...
Notes: As mentioned earlier, if the scan chains are fed directly from adjacent bits of the LFSR, then this very close proximity will cause neighboring scan chains to contain test patterns which are highly correlated. This phenomenon can adversely affect fault coverage, as the patterns seen by the CUT will not be pseudorandom. In order to alleviate this problem as well as to allow a large number of scan chains to be driven by a relatively short LFSR, an extra circuitry is placed between the LFSR and the serial inputs of the scan chains, and this part of the generator is referred to as a phase shifter. The probability of linear dependencies can be then reduced in a manner similar to that of structural dependencies. A typical phase shifter consists of an XOR network employed to avoid shifted versions of the same data in various scan chains. Every scan chain is driven by a circuitry which corresponds to a linear combination of LFSR stage outputs. This circuitry generates a test sequence with the desired separation from other sequences by employing the "shift-and-add" property of m-sequences (see one of the earlier slides).

## Slide 22: Application of LFSR duality
Determine a dual LFSR
Initialize it to 10 ... 0 pattern
Run it for k cycles
Read the resulting content of the dual LFSR
Locations of 1s point out stages of the original LFSR whose sum produces a sequence shifted by k bits
2
1
0
3
4
2
1
0
3
4
J. Rajski, J. Tyszer, VTS’98
Notes: Designers can obtain large and fast phase shifters by virtue of dual LFSRs. Given a Fibonacci LFSR, that is, the LFSR with "external" XOR gates, its dual LFSR, which is always Galois LFSR (with "internal" XOR gates), can be obtained by reversing the direction of all feedback taps but the rightmost one (see the slide). Similarly, given a Galois LFSR, its dual Fibonacci LFSR can be derived by reversing all the feedback taps except the rightmost one.
Assuming its initial state with a single logic 1 in the ith stage, the state of the dual LFSR after q clock cycles is of particular interest. Indeed, locations of logic 1s in this vector identify the outputs of the original LFSR to be added modulo 2 to produce a sequence spaced q shifts up a reference. The reference is a sequence originating from a stage pointed out by the logic 1 in the initial state of the dual circuit. In other words, logic simulation of a dual LFSR suffices to create a channel with a phase delay equal to q clock cycles with respect to the ith stage of the original generator. This is further demonstrated by an example on the following slide.

## Slide 23: Phase shifter synthesis
1 0 0 1
1 1 0 1
1 1 1 1
1 1 1 0
0 1 1 1
1 0 1 0
0 1 0 1
1 0 1 1
1 1 0 0
Shift (back)
4
5
6
7
8
9
10
11
12
Reference
Dual
1
0
0
0
Notes: Assume that the dual LFSR on the slide is initialized with the following pattern: 1 0 0 0. The content of this vector indicates that a sequence produced by flip-flop 0 (where logic 1 is located) of the original circuit will serve as a reference sequence for those produced by a phase shifter. After nine clock cycles the dual LFSR reaches state 1 0 1 0. The above pattern indicates that by adding modulo 2 the content of flip-flops 0 and 2 of the original LFSR, one may arrive with a sequence, which is a shifted, by 9 bits, replica of a sequence produced by flip-flop 0 of the same generator. The corresponding phase shifter circuitry is shown on the slide. It also demonstrates other outputs of the phase shifter obtained for space shifts ranging from 4 to 12.

## Slide 24: Random pattern resistance
The average number of tests needed to detect s-a-0 fault:
pseudorandom: 0.5-32 = 232 (4 billion)
weighted: (1 - 2-7)-32  1.2853
s-a-0
Notes: Consider the AND structure shown on the slide. This circuit contains random pattern resistant faults. In order to detect the output stuck-at-0 fault, all inputs must be set to 1, and if uniformly distributed pseudorandom patterns are applied by a 32-bit LFSR, the detection probability is 2–32, which clearly leads to an unacceptable test application time – on the average roughly 4 billion test vectors would be required. On the other hand, if each input is set to 1 with a probability of 1 – 2–7 (the corresponding signals are produced by a 7-input OR gate connected to the LFSR stages), the same fault can be detected with a probability of (1 – 2–7)32 = 0.778, implying that, on the average, 1.3 test vectors would be needed to achieve this goal. This example illustrates the essence of weighted pseudorandom testing which can be used to address the random pattern resistant faults.

## Slide 25: Weighted random patterns
Control register
0.5
0.25
0.125
0 | 0 | 1 | 0 | .5
0 | 0 | 1 | 1 | .5
0 | 1 | 0 | 0 | .25
0 | 1 | 0 | 1 | .75
0 | 1 | 1 | 0 | .625
0 | 1 | 1 | 1 | .375
1 | 0 | 0 | 0 | .125
1 | 0 | 0 | 1 | .875
1 | 0 | 1 | 0 | .5625
1 | 0 | 1 | 1 | .4375
1 | 1 | 0 | 0 | .34375
1 | 1 | 0 | 1 | .65625
1 | 1 | 1 | 0 | .671875
1 | 1 | 1 | 1 | .328125
H.-J. Wunderlich, ITC’88
Notes: Basically, the weighted pseudorandom testing extends the LFSR-based pseudorandom test generators by biasing the probabilities of the input bits so that the tests needed for hard-to-test faults are more likely to occur. This concept is illustrated by the circuit shown on the slide. Let us assume that each stage of the LFSR has a probability of 0.5 of being either a 0 or a 1. More precisely, the probability of having 1 is 2n–1/(2n – 1), where n is the size of the LFSR. Let us also assume that these events are statistically independent of which states occur on other bits. Then, feeding k such signals into an AND gate will result in a value of 1 at the output of the AND gate with the probability of 0.5k. Other probabilities can be also obtained by using OR gates and inverters, as listed in the table for successive values provided by the control register (its rightmost bit enables inversion). Unfortunately, there are no common weight sets for different faults, and therefore a circuit may require several sets of weights, and, for each weight set, a number of random patterns have to be applied. Thus, the major objective of the weight generation process is to reduce both quantities.

## Slide 26: Low transition PRPG
T FF
1 0 1 0 1 0 1 0 1 0 1 0 0
1 1 0 1 0 1 0 1 0 1 0 0 0
1 1 1 0 1 0 1 0 1 0 1 0 0
1 1 1 1 0 1 0 1 0 1 0 0 0
1 1 1 1 1 0 1 0 1 0 1 1 1
1 1 1 1 1 1 0 1 0 1 0 0 1
1 1 1 1 1 1 1 0 1 0 1 1 0
1 1 1 1 1 1 1 1 0 1 0 0 0
S. Wang, S.K. Gupta, ITC’99
Notes: Another form of pseudorandom test pattern generator is shown on this slide. It can be applied in circuits where lower transition counts are required due to test power constraints. The output T-type flip-flop reduces the number of transitions that occur in a test sequence leaving the original LFSR. Moreover, it works with an AND gate that further decreases the number of 1s in the output sequence. The original and final transitions are indicated by red and blue dots, respectively.

## Slide 27: PRESTO architecture
PRPG
Phase shifter
T
…
…
Pattern count
Switching
Shift register
Toggle control register
Toggle
Hold
G. Mrugalski, et al., ITC, 2012
Notes: PRESelected TOggling (PRESTO) scheme is a low power BIST pseudorandom test pattern generator where a user can select a desired level of toggling in scan test patterns. The slide illustrates the basic structure of a PRESTO generator. An n-bit PRPG connected with a phase shifter feeding scan chains forms a kernel of the generator producing the actual pseudorandom test patterns. A linear feedback shift register or a ring generator can implement a PRPG. n hold latches (in blue) are placed between the PRPG and the phase shifter. Each hold latch is individually controlled via a corresponding stage of an n-bit toggle control register. As long as its enable input is asserted, the given latch is transparent for data going from the PRPG to the phase shifter, and it is said to be in the toggle mode. When the latch is disabled, it captures and saves, for a number of clock cycles, the corresponding bit of PRPG, thus feeding the phase shifter (and possibly some scan chains) with a constant value. It is now in the hold mode. It is worth noting that each phase shifter output is obtained by XOR-ing outputs of three different hold latches. Therefore, every scan chain remains in a low-power mode provided only disabled hold latches drive the corresponding phase shifter output.

## Slide 28: Scan selection
PRPG
Phase shifter
T
…
…
Pattern count
Switching
Shift register
Toggle control register
Toggle
Hold
Notes: The toggle control register’s content comprises 0s and 1s, where 1s indicate latches in the toggle mode, thus transparent for data arriving from the PRPG. Their fraction determines a scan switching activity. The control register is reloaded once per pattern with the content of an additional shift register. The enable signals injected into the shift register are produced in a probabilistic fashion by using the original PRPG with a programmable set of weights. The weights are determined by four AND gates producing 1s with the probability of 0.5, 0.25, 0.125, and 0.0625, respectively. The OR gate allows choosing probabilities beyond simple powers of 2. A 4-bit register Switching is employed to activate AND gates, and allows selecting a user-defined level of switching activity. For example, the switching code 0100 will set to 1, on the average, 25% of the control register stages, and thus 25% of hold latches will be enabled. Given the phase shifter structure, one can assess then the amount of scan chains receiving constant values, and thus the expected toggling ratio.
An additional 4-input NOR gate detects the switching code 0000, which is used to switch the low power functionality off. The switching level selector ensures statistically stable content of the control register in terms of the amount of 1s it carries. As a result, roughly the same fraction of scan chains will stay in the low power mode, though a set of actual low toggling chains will keep changing from one test pattern to another. It will correspond to a certain level of toggling in the scan chains. With only 15 different switching codes, however, the available toggling granularity may render this solution too coarse to be always acceptable. Thus, there are additional features that make the PRESTO generator fully operational in a wide range of desired switching rates.

## Slide 29: Slice selection
PRPG
Phase shifter
…
…
Pattern count
Switching
Shift register
Toggle control register
T
Toggle
Hold
Notes: Much higher flexibility in forming low-toggling test patterns is achieved by splitting up a shifting period of every test pattern into a sequence of alternating hold and toggle intervals. To move the generator back and forth between these two states, a basic T-type flip-flop is used that switches whenever there is a 1 on its data input. If it is set to 0, the generator enters the hold period with all latches temporarily disabled regardless of the control register content. This is accomplished by placing AND gates on the control register outputs to allow freezing of all phase shifter inputs. This property can be crucial in SoC designs where only a single scan chain crosses a given core, and its abnormal toggling may cause locally unacceptable heat dissipation that can only be reduced due to temporary hold periods. If the T flip-flop is set to 1 (the toggle period), then the latches enabled through the control register can pass test data moving from the PRPG to the scan chains.
Two additional parameters kept in 4-bit Hold and Toggle registers determine how long the entire generator remains either in the hold mode or in the toggle mode, respectively. In order to terminate either mode, a 1 must occur on the T flip-flop input. This weighted pseudorandom signal is produced in a manner similar to that of weighted logic used to feed the shift register. The T flip-flop controls also four 2-input multiplexers routing data from the Toggle and Hold registers. It allows selecting a source of control data that will be used in the next cycle to possibly change the operational mode of the generator. For example, when in the toggle mode, the input multiplexers observe the Toggle register. Once the weighted logic outputs 1, the flip-flop toggles, and as a result all hold latches freeze in the last recorded state. They will remain in this state until another 1 occurs on the weighted logic output. The random occurrence of this event is now related to the content of the Hold register, which determines when to terminate the hold mode.

## Slide 30: Toggling in scan chains
Toggle
Hold
T
T
T
T
T
H
H
H
Test pattern 1
Test pattern 2
Notes: A scan switching profile when deploying the PRESTO generator in a hypothetical environment with 23 scan chains is illustrated on this slide for two test patterns. Blue (0s) and grey(1s) stripes make up the low power-toggling pattern, while orange areas correspond to periods of toggling. All-blue and all-grey scan chains are fed by the constant values only. Note that their quantity does not change between patterns though they are not exactly the same in each case. As can be seen, test patterns are divided into hold and toggle intervals of random length, while low power scan chains remain still for the entire duration of a single test pattern.

## Slide 31: Selection of controls
Switching code
Chart: 
| 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
 | 16 | 8 | 20 | 4 | 18 | 11 | 21.5 | 2 | 17 | 9.5 | 20.75 | 5.75 | 18.875 | 12.3125 | 22.1562
1
160
Scan chains
1s in control register
44
30
48
17
46
37
48
09
45
32
48
21
46
39
49
Toggling [%]
Notes: Performance of the PRESTO generator depends primarily on the following three factors (in the BIST mode they are delivered only once, at the very beginning of the entire test session): (1) the switching code (kept in the Switching register), (2) the hold duty cycle (HC), and (3) the toggle duty cycle (TC). Given the size of PRPG, the number of scan chains and the corresponding phase shifter, the switching code as well as HC and TC values can be selected automatically in such a way that the entire generator will produce pseudorandom test patterns having a desired level of toggling T provided the scan chains are balanced. The procedure of selecting these parameters consists of the following steps.
For each switching code k, k = 1, …, 15, determine the corresponding probability pk of injecting a 1 into the shift register. These values are as follows: p1 = 0.5, p2 = 0.25, p3 = 0.625, p4 = 0.125, p5 = 0.5625, p6 = 0.34375, p7 = 0.671875, p8 = 0.0625, p9 = 0.53125, p10 = 0.296875, p11 = 0.6484375, p12 = 0.1796875, p13 = 0.58984375, p14 = 0.38476563, and p15 = 0.69238281. The values pk determine as well the probability of asserting the T flip-flop input for each hold (toggle) code k, and then the corresponding duration hk (tk) of the hold (toggle) duty cycle. Clearly, hk = tk = 1 / pk.
Given the size n of PRPG, determine, for each switching code k, the average number nk of 1s occurring in the control register. As can be easily verified, nk = pk  n.
For each value of nk (the number of enabled hold latches), find the average number ak of active scan chains, i.e., scan chains that are not in the low power mode. This number is determined by the phase shifter architecture, and it also depends on the actual locations of 1s in the control register. Therefore, 1,000 n-bit random combinations having exactly nk 1s can be generated, as shown on the slide, to obtain the number of active scan chains in each case, and finally the number ak of active scan chains is averaged over all 1,000 samples.

## Slide 32: Selection of controls
Enabled chains =
160
Scan chains
Desired toggling × scan chains
50%
1
25%
44
30
48
17
46
37
48
09
45
32
48
21
46
39
49
Toggling [%]
Notes: Given a desired level of toggling T (%), one can determine the resultant (hypothetical) number A of active scan chains from the following equation (see also the slide):
A = (T  S) / 50%,
where S is the total number of scan chains. The above proportion assumes that if all S scan chains are active, then the resultant toggling is about 50%.

## Slide 33: Selection of controls
h
L
t
A
a
a
h
t
– 1
A
a
=
Find the best values of h and t matching a/A – 1
(a – A) × L = a × h × v
(h + t) × v = L
Notes: Now, for each switching code k, and thus the resulting number ak of active scan chains, we can determine how many additional scan chains should be disabled. In each case, this quantity is given by dk = ak – A. If dk ≤ 0, then disregard the next steps, as the switching code k does not guarantee even the smallest (required) number of active scan chains. Since disabling extra scan chains cannot be implemented through the control register, this action is carried out by equivalent disabling – with help of hold duty cycles – of selected cells belonging to active scan chains. The value of dk is therefore converted into the number of corresponding cells in active scan chains (see the example on the slide). Let L be the scan chain length. Then we have:
dk  L = (ak – A )  L = ak  hk  v,
(hk + tk) v = L,
where v accounts for the number of hold (toggle) duty cycles. From the above formulas we get that
r = hk / tk = (ak / A) – 1.
Ratio r is now evaluated for each value of hk and tk (in total 15  15 = 225 combinations) to find the best matching between the actual value of r and the theoretical value of the expression (ak / A) – 1.
Values of switching, hold and toggle codes that yield ratio r with the smallest deviation from the theoretical value are selected as the PRESTO setup parameters.
Results presented on the next slides demonstrate that despite certain simplifications (in particular, it is assumed that hold and toggle duty cycles are of the same constant size; furthermore, certain cell locations, typically used in computing weighted transition metrics, are not taken into account when looking for active scan cells to be disabled), the above procedure yields controls that allow producing pseudorandom patterns with switching activities tracking very closely the desired levels of toggling.

## Slide 34: Validation
Chart: 
 | 1.3253 | 2.4783 | 3.1798 | 4.1572 | 5.189 | 6.0472 | 6.9716 | 8.0025 | 9.254 | 9.9388 | 10.7853 | 11.8247 | 12.7466 | 13.4539 | 14.0401 | 15.1815 | 16.7535 | 17.8509 | 19.1567 | 19.9099 | 21.196 | 21.9831 | 23.0129 | 23.9271 | 24.917 | 25.8962 | 26.9471 | 29.2846 | 29.0639 | 29.9537 | 31.1389 | 32.4283 | 33.3856 | 34.0427 | 34.944 | 35.6159 | 36.9731 | 37.8605 | 39.0409 | 39.8315 | 40.6077 | 41.6286 | 42.6189 | 43.5646 | 44.1521
 | 6.7059 | 8.5898 | 10.382 | 13.4614 | 12.5249 | 14.5589 | 15.1909 | 22.0068 | 19.5545 | 18.0809 | 20.1188 | 20.5652 | 19.2062 | 20.6838 | 24.9294 | 23.1195 | 23.9724 | 28.2651 | 26.2116 | 31.5993 | 29.7043 | 28.2665 | 29.35 | 30.9105 | 31.8513 | 35.8866 | 38.7155 | 42.9107 | 40.0141 | 38.9633 | 39.7337 | 41.1385 | 41.8484 | 44.095 | 42.445 | 48.174 | 46.0214 | 47.0399 | 47.3384 | 47.4584 | 48.8032 | 49.1609 | 49.3114 | 49.5572 | 49.6069
 | 0.54391 | 1.2947 | 1.6102 | 1.9678 | 3.5524 | 3.7863 | 4.8826 | 5.0666 | 6.0926 | 7.7287 | 7.7454 | 8.8559 | 10.9859 | 11.5508 | 10.4672 | 12.8614 | 14.203 | 14.625 | 17.1887 | 16.4256 | 18.4877 | 20.0842 | 21.0085 | 21.7573 | 22.7873 | 23.0118 | 22.8526 | 25.0959 | 25.6861 | 27.3197 | 28.6594 | 29.9046 | 30.8472 | 30.831 | 32.5764 | 30.8109 | 33.7776 | 34.7264 | 36.0673 | 36.9906 | 37.2406 | 38.3257 | 39.664 | 40.8384 | 41.6401
 | 2.1066 | 3.6619 | 4.7494 | 6.3466 | 6.8256 | 8.3082 | 9.0606 | 10.9383 | 12.4155 | 12.1489 | 13.8252 | 14.7936 | 14.5073 | 15.3569 | 17.613 | 17.5017 | 19.3041 | 21.0767 | 21.1247 | 23.3943 | 23.9043 | 23.8819 | 25.0173 | 26.0968 | 27.0467 | 28.7807 | 31.0417 | 33.4732 | 32.4417 | 32.5877 | 33.6185 | 34.9521 | 35.9241 | 37.2544 | 37.3116 | 40.4209 | 40.1685 | 40.9947 | 42.0144 | 42.6725 | 43.9748 | 44.9315 | 45.5738 | 46.2908 | 46.664
Requested toggle rate [%]
Actual WTM [%]
average deviation maximum
5 designs
33-bit PRPG
10,000 pseudorandom patterns
Notes: The approach presented earlier has been validated by experiments run on five different scan architectures (203  300, 122  104, 84  416, 128  353, 160  541) used in five industrial designs, and with a 33-bit ring generator implementing a primitive polynomial x33 + x25 + x16 + x8 + 1 and feeding 33-input phase shifter for 10,000 pseudorandom test patterns. The average toggling rates measured by means of the weighted transition metric (WTM) are plotted on this slide against successive values of a desired switching activity (the requested toggling). The standard deviation is used to assess a possible dispersion from the average toggling values. The presented plot consists of four different curves. The central red line represents the average value of the toggling ratio computed over all examined designs and all test patterns for successive values of the desired (user-selected) toggling rate varying from 1% to 45% in steps of 1%. Two black lines correspond to standard deviation bounding the average value curve from the top and the bottom. The last (blue) curve represents maximal values (averaged over maximal values obtained for all examined designs) recorded for each toggling rate. As can be seen, the resultant switching activity follows closely, with small values of standard deviation, the requested rates.

## Slide 35: Validation
Chart: 
 | 1.3253 | 2.4707 | 3.1798 | 4.1572 | 5.189 | 6.0472 | 7.0229 | 8.0025 | 8.8054 | 9.9388 | 10.7853 | 11.8463 | 12.7466 | 13.905 | 14.7797 | 15.6286 | 16.7885 | 17.8509 | 19.1567 | 19.9099 | 20.9412 | 21.9831 | 23.0129 | 23.9994 | 24.966 | 25.932 | 26.9471 | 27.599 | 29.0639 | 29.9537 | 31.1255 | 32.2875 | 33.3607 | 34.0427 | 34.944 | 35.867 | 36.9731 | 37.8605 | 38.9934 | 39.8315 | 40.6459 | 41.6286 | 42.6189 | 43.5646 | 44.1521
 | 0.54391 | 1.3819 | 1.6102 | 1.9678 | 3.5524 | 3.7863 | 4.9338 | 5.0666 | 6.0001 | 7.7287 | 7.7454 | 9.5942 | 10.9859 | 10.968 | 12.9745 | 13.3035 | 12.9036 | 14.625 | 17.1887 | 16.4256 | 19.1789 | 20.0842 | 21.0085 | 20.4355 | 22.2164 | 24.1139 | 22.8526 | 24.7174 | 25.6861 | 27.3197 | 28.6768 | 29.5688 | 30.3925 | 30.831 | 32.5764 | 32.8761 | 33.7776 | 34.7264 | 36.2445 | 36.9906 | 37.9062 | 38.3257 | 39.664 | 40.8384 | 41.6401
 | 2.1066 | 3.5595 | 4.7494 | 6.3466 | 6.8256 | 8.3082 | 9.1121 | 10.9383 | 11.6107 | 12.1489 | 13.8252 | 14.0985 | 14.5073 | 16.8419 | 16.5849 | 17.9538 | 20.6734 | 21.0767 | 21.1247 | 23.3943 | 22.7035 | 23.8819 | 25.0173 | 27.5632 | 27.7156 | 27.75 | 31.0417 | 30.4807 | 32.4417 | 32.5877 | 33.5742 | 35.0063 | 36.329 | 37.2544 | 37.3116 | 38.8579 | 40.1685 | 40.9947 | 41.7422 | 42.6725 | 43.3856 | 44.9315 | 45.5738 | 46.2908 | 46.664
 | 6.7059 | 8.7181 | 10.382 | 13.4614 | 12.5249 | 14.5589 | 15.7434 | 22.0068 | 18.8622 | 18.0809 | 20.1188 | 20.1999 | 19.2062 | 22.7486 | 21.392 | 22.9133 | 27.1238 | 28.2651 | 26.2116 | 31.5993 | 26.9866 | 28.2665 | 29.35 | 34.5367 | 33.2873 | 31.8383 | 38.7155 | 37.7108 | 40.0141 | 38.9633 | 39.8026 | 41.0815 | 42.8026 | 44.095 | 42.445 | 44.7218 | 46.0214 | 47.0399 | 47.2028 | 47.4584 | 47.8589 | 49.1609 | 49.3114 | 49.5572 | 49.6069
average deviation maximum
Actual WTM [%]
Requested toggle rate [%]
5 designs
32- & 33-bit PRPG
10,000 pseudorandom patterns
Notes: This slide gathers experimental results similar to those of the previous slide but obtained in a slightly different way. Before plotting the actual values of toggling rates and the remaining statistics, experiments for every single toggling rate were performed for 32- and 33-bit PRPGs (the 32-bit ring generator uses a primitive polynomial x32 + x25 + x15 + x7 + 1). Phase shifters are separately synthesized in each case. The resultant toggling rates were compared, and switching activity with a smaller absolute dispersion from the expected value was chosen as the final result. It appears that in certain cases it is preferable to pick a 32-bit PRPG rather than a 33-bit one, or vice versa. This strategy yields virtually a straight line with respect to toggling rates, as shown on the slide, hence offering an accurate mapping between the user-selected values of switching activity and the actual circuit response. One can also observe reduced maximal values and smaller standard deviations in this case.

## Slide 36: Fault coverage
Chart: 
Test patterns
[%]
WTM [%] 49.67 24.85 18.67 14.14
9.46
5.22
32-bit PRESTO
Industrial design
Single stuck-at faults
Notes: The objective of the second group of experiments is to evaluate tests produced by a 32-bit PRESTO and determine their fault coverage for various requested toggling rates. The results for one industrial design are presented on this slide. The curves correspond to (requested) toggling rates from 5% to 25% in steps of 5%. In each test case, an additional red curve reports a reference fault coverage obtained by applying purely pseudorandom test patterns with the effective toggling rates around 50%. As can be seen, performance of the PRESTO generator remains highly predictable. In particular, with the increasing switching activity single stuck-at fault coverage increases as well. Typically, however, one may observe a coverage gap between PRESTO-produced tests and their random counterparts. Fortunately, PRESTO has ability to reduce this gap by a proper selection of the control register content (see the next slide).

## Slide 37: Fault coverage – BIST ready
Chart: 
Test patterns
WTM [%] 49.75 24.53 21.49 14.55
9.04
4.96
[%]
32-bit PRESTO
BIST-ready industrial design
Single stuck-at faults
Notes: Results similar to the outcomes on the previous slide, this time, however, obtained for a BIST-ready design, are shown on this slide. In fact, sometimes fault coverage of certain low power tests can be higher than that of conventional pseudorandom patterns. More stringent BIST-specific design rules are employed to deal with unknown states (X-bounding). Also, as pseudorandom patterns are mostly used for BIST test generation, additional test points are typically inserted to improve the fault coverage.

## Slide 38: Deterministic control
PRPG
Phase shifter
T
…
…
Pattern count
Switching
Shift register
Toggle control register
Toggle
Hold
Notes: It can be shown that PRESTO-produced low power test patterns are also capable of visibly improving a fault-coverage-to-pattern-count ratio. Assuming that the toggle control register can also be driven by deterministic test data (see location of an additional multiplexer in the front of this register on the slide), test patterns can be produced with better-than-average fault coverage. The method begins by computing the PRESTO parameters. Subsequently, ATPG is repeatedly invoked until either a desired PRESTO pattern count or a fault coverage limit is reached. ATPG produces test cubes in one per fault fashion. The obtained test cubes are now deployed to arrive with the content of the control register, as described in the following.
Given the PRESTO switching code, a goal is now to find the corresponding distribution of 1s in the control register that maximizes the fault detection probability. The procedure starts by reducing each ATPG-produced test cube to a set of scan chains containing more than one specified bit. This set will be further referred to as a base. For example, let a test cube feature the following specified scan cells: {(s, c): (4, 13), (4, 2), (13, 34), (13, 31), (45, 11)}, where s is a scan chain, and c is a cell location within the scan chain. The base is thus given by {4, 13}; note that chain 45 is not included as it features only one specified scan cell. A good chance (50%) of producing a given logic value in a purely pseudorandom fashion is a rationale behind excluding from any base scan chains hosting a single specified bit. As a result, more bases can be subsequently combined together to produce a single control setting.
Given the phase shifter architecture, one can determine, for each base, the minimal number of phase shifter inputs – or equivalently the number of 1s in the toggle control register – required to activate the specified scan chains. These inputs are obtained by solving the minimum hitting set problem, where we find, in a greedy fashion, the minimal set of phase shifter inputs that intersects all subsets of phase shifter inputs capable of activating specified scan chains of a given base. Recall that the number of such inputs (and thus the number of 1s in the control register) is further constrained by the preselected switching code. For example, the switching code 0100 sets the limit on the number of 1s in the 32-bit control register to 8. Hence, if a base exceeds the limit, it is excluded from subsequent steps of the procedure. Finally, each base is assigned weight w which is simply the number of specified bits in the corresponding test cube. It is worth noting that a reciprocal of w can be regarded as the likelihood of yielding the test pattern by a generator of purely pseudorandom vectors. Let C be an initially empty set of bases. Once all weights are determined, we add to C a minimum-weight base. Next, every remaining base B is assigned a cost value which is equal to the smallest number of 1s in the control register that would be required to activate all scan chains in {C ∪ B}. A minimum-cost base (or a minimum-weight base if there are two or more bases with the same minimal cost) is then added to C, and costs associated with the remaining bases are recomputed accordingly. The procedure continues until either the limit of 1s in the control register is reached or all bases are already in C. The control register content that activates all scan chains from C is then provided to PRESTO. For each control register setting, PRESTO is run to produce a certain number of pseudorandom test patterns. These patterns are subsequently fault-simulated, and detected faults are dropped from the list.

## Slide 39: Test points
Types of control points
  AND – enhance controllability of “0”
  OR – enhance controllability of “1”
  XOR – balance control of “0” and “1” without reducing observability
Source of stimuli
  generator of test patterns – pseudorandom and switching independently
  additional scan cells – pseudorandom and switching independently
  phase decoder – quasi-static and strongly correlated
Test
Test
S
b
Notes: Test points can be added to a circuit to make it easier to either activate faults (control points) or to observe them (observation points). The slide shows so-called 0- and 1-injection circuits where two extra gates are used to achieve 0- and 1-controllability of a line. For example, in the 1-injection circuitry, when Test = 0, the circuit operates in its normal mode. Setting Test = 1 allows us to inject a 1 on line S, and subsequently on line b. Line S can be controlled by an extra primary input, or it can be driven by a flip-flop being a part of a scan chain (this architecture is illustrated on the next slide). In general, optimal test point insertion in circuits with reconvergent fan-out is an NP-complete problem, and therefore numerous empirical guidelines and approximate techniques have been proposed to identify locations in a circuit to introduce control and observation points.

## Slide 40: Test points driven by scan
Test mode
Test mode
Tester
Notes: As mentioned on the previous slide, test points can be efficiently controlled thorough some scan cells. During their selection, one designates locations in the circuit to introduce test points facilitating the detection of “hard-to-test” faults using either exact fault simulation or approximate testability measures. The results of fault simulation can be used to determine signal correlations and places at which signal propagation stops, in order to insert test points eliminating the correlation and allowing fault excitation and fault effect propagation. Conversely, to avoid time-consuming simulation experiments, the second group of methods utilizes the controllability and observability measures to identify the hard-to-control and hard-to-observe sectors of the CUT, at which origins the test points are subsequently inserted. Regardless of the test point selection process, all of these techniques attempt to improve the detection probabilities of faults while minimizing a hardware overhead. Notice that, depending on how a test point is driven or observed, its insertion may require a few extra gates (compare the previous slide) and a wire routed to or from an additional flip-flop to be included in the scan chain.

## Slide 41: Multiphase test point insertion
98%
4192
8384
16768
12576
Fault
coverage
0
User controls
Target fault coverage
Number of test points
Pattern count
Fault detections per test point
Number of phases
Phase decoder
N. Tamarapalli, J. Rajski, ITC’96
Notes: This slide illustrates a constructive test point insertion technique for scan-based designs. A divide-and-conquer approach is used to partition the entire test into multiple phases. Each phase contributes to the results achieved so far, moving the solution closer to complete fault coverage. Within each phase, a group of control and observation points are activated such that they maximize the fault coverage calculated over the set of still undetected faults. A probabilistic fault simulation, which computes the impact of a new control point in the presence of the control points already selected, is used as a vehicle to select the test points. In this way, in each test phase, a group of control points, driven by fixed values and operating synergistically, is enabled. In addition, observation points maximally enhancing the fault coverage are selected by a covering technique that utilizes the probabilistic fault simulation information.

## Slide 42: MTPI example
Pattern counter
A
C
B
D
0
4
a
b
c
d
Notes: Consider again the AND tree. In order to increase probability that input signals reach the primary output, several OR-type control points are employed. The entire test experiment is divided into four distinct phases: F1, F2, F3, and F4. In each phase, a set of control points is enabled by a phase decoder outputs and a specific number of test patterns are applied. The value of the test signal a is 1 during phase F1, forcing the right hand side AND gates to pass signals from the input group A, regardless of the input values of groups B, C, and D. However, during phases F2, F3, and F4, a is set to 0, and other control lines take over. Similarly, b's value is 1 during phase F2, forcing the output AND gates to pass signals from the input group B, irrespective of status of inputs from groups A, C, and D. Much of the same can be said about control lines c and d. Note that phase F0 corresponds to the mission mode of operation.

## Slide 43: Control and observation points
Outputs of bistable devices
Set and reset inputs of bistables
Junctions of large fan-ins for monitoring
Stems of large fan-outs for inserting values
Midpoints of long counter chains
Data and address bus lines of bus-structured designs
Master clock lines
Logically redundant nets
Notes: This slide lists examples of a circuit internal nodes which are good candidates for test point insertion. Typically, selection of observation points is carried out in such a way that the detection probability of a maximum number of faults meets a user specified threshold. Given the detection profile, a greedy heuristic selection continues until a pre-specified number of observation points are chosen or no observation point satisfies the minimum-benefit-per-cost criterion. The set of candidate locations for control point insertion is then determined by an estimation technique computing two estimates, E0 and E1, for various nodes in the circuit. These measures give an indication of the number of faults that could potentially be detected by placing an AND/OR type control point, respectively. Nodes for which E0 or E1 exceeds a minimum acceptable value are retained for subsequent evaluations. For each candidate node, a 0 or 1 value, depending on whether an AND or an OR type control point is simulated, temporarily injected, and the resulting change in the propagation profile is determined. Since the insertion of a control point at a node perturbs the list of faults associated with itself or nodes in its fan-out cone, it is necessary to recalculate the list for this set only. Accordingly, an incremental probabilistic fault simulation is performed to determine the new list of faults at various nodes in the fan-out cone of the candidate signal. The rank of a candidate is defined as the number of additional faults that propagate to primary outputs or observation points. The candidate with the highest rank is then selected for control point insertion.

## Slide 44: Arithmetic BIST
Some designs feature modules that can be reused to generate test patterns and compact test responses
  adders, ALU units
  multipliers
  digital filters
  floating point units
No performance degradation
At-speed tests
No area overhead
Software employed to mimic test pattern generators and test response compactors
J. Rajski, J. Tyszer, Prentice Hall, 1998
Notes: Arithmetic BIST uses several generic building blocks, which are already in the high-performance data-path architectures, as well as its very flexible and powerful control circuitry to generate patterns and compact test responses. This permits design of complex software-based, and thus very portable, BIST functions. These functions produce test vectors in the form of control signals, such as the type of ALU operation, the addresses of registers, the input to shifters, etc., rather than data, as it is done in all other systems. In such an environment, the need for extra hardware is either entirely eliminated or drastically reduced, test vectors can be easily distributed to different modules of the system, test responses can be collected in parallel, and there is virtually no performance degradation. Furthermore, the approach can be used for at-speed testing, thereby providing a capability to detect failures that may not be detected by conventional low-speed testing. These characteristics make this method an attractive testing scheme for a wide range of circuits including high performance DSP systems, microprocessors, and microcontrollers.

## Slide 45: Pseudo-exhaustive tests
56 0000111000
56 + 569 mod 210 = 625 1001110001
625 + 569 mod 210 = 170 0010101010
170 + 569 mod 210 = 739 1011100011
739 + 569 mod 210 = 284 0100011100
284 + 569 mod 210 = 853 1101010101
853 + 569 mod 210 = 398 0110001110
398 + 569 mod 210 = 967 1111000111
xi = xi – 1 + c mod 2n
n = 10, k = 3, x0 = 56, c = 569
All k-bit combinations obtained in 2k steps for all contiguous input subspaces
Notes: An n-bit ALU or accumulator featuring a binary adder can be used to implement a scheme in which a constant binary vector is successively transferred to the adder and added to the previous contents of the register. The state xk of the register after k external vectors have been applied is given by the following iterative formula:
xk = xk–1 + c mod 2n.
The contents x of the register can now be used as a source of test patterns to test the accumulator itself or other modules in the circuit. The generation scheme is described completely by its width n, initial state x0 and the constant increment value c.
A method to evaluate the quality of the test-pattern generator is to examine its state coverage. It indicates the number of different patterns that can be produced and is an indication of the real capacity of the signals that appear on the output of the generator. In particular, a sequence of n-bit vectors is said to cover exhaustively a specified k-bit contiguous subspace, if all 2k different patterns appear on the bit positions of this subspace. An arithmetic generator shown on the slide covers exhaustively all 3-bit contiguous subspaces in exactly 8 steps. As can be verified, there are in total 64 generators with different values of c and x0 with the same ability. Clearly, exhaustive coverage of k-bit contiguous subspaces also guarantees the exhaustive coverage of all contiguous subspaces of size less than k.

## Slide 46: Compaction of test responses
Reduce the volume of test data and still be able to determine if the response is correct
Ideal compactors
  simple hardware and small area
  tested as part of the embedded test circuitry
  simple software
  compute the signature at the speed of the test
  perform logarithmic compaction of data
  no aliasing
No scheme meets all criteria, but some come close
Notes: In conventional testing, test responses are all compared with the pre-computed correct reference values, which may pose a high volume of test data to be stored. In BIST, such an approach becomes infeasible, as it requires a significant amount of memory storage and slows down the whole test session. Here, we analyze an alternative method known as a test response compaction. Its general objective is to reduce, through the use of small circuitry, the volume of test data to a short statistic, called a signature, and still be able to detect faults in the circuit. It is expected that ideal compactors would have the following properties:
the compaction algorithm should be easy to implement as part of the BIST circuitry,
the implementation should not be a limiting factor with respect to test time,
the compaction algorithm has to provide a logarithmic compression of the test data in order to minimize the size of signature,
the compaction technique must not lose information concerning faults.
Unfortunately, there is no known compaction algorithm that satisfies all these criteria. In particular, it is difficult to ensure that a signature obtained from a faulty circuit is not the same as that of the fault-free circuit. This phenomenon is often referred to as error-masking or aliasing and is measured in terms of the likelihood of its occurrence. Thus, the aliasing probability is usually defined as the average probability of no faults being detected due to compaction after a sufficiently long test experiment.

## Slide 47: Compaction schemes
Time (infinite memory) compactors
  polynomial division – signature analysis
  arithmetic accumulation
  various forms of counting
Space compactors
  XOR trees
  error code-based
Finite memory compactors
  convolutional compactors
  block-based compactors
Notes: Similarly to test generation, the LFSR is the most popular compaction device used in practice. In its simplest form, as introduced by Hewlett-Packard, the LFSR is modified to accept an external input in order to act as a polynomial divider. The input sequence, represented by a polynomial, is divided by the characteristic polynomial of the LFSR. As the division proceeds, the quotient sequence appears at the output of the LFSR and the remainder is kept in the LFSR. Note that Fibonacci LFSRs do not always produce the correct remainder. However, the divisor polynomial maps to a remainder of 0 in either case, thus assuring that both, Fibonacci and Galois, LFSRs have the same masking properties. Once testing is completed, the content of the LFSR can be treated as a signature.
Several test-response compaction schemes have been developed based on counters. In a ones-count compaction, the number of 1s in the output stream is counted, i.e., the weight of the output is determined. Another version of the count-based compaction is transition counting, in which the number of 0 to 1 and 1 to 0 transitions that occur at the CUT output is counted. The compaction circuitry in this case consists of a regular counter and a transition detector, which comprises a flip-flop to save the last output, and an XOR gate to compare the last output with the current one, i.e., to detect the actual transition. A slightly different compaction scenario, known as the edge counting, assumes that only positive (from 0 to 1) or negative (from 1 to 0) transitions are counted.
Another class of test-response compaction schemes employs the concept of checksums. The checksum of a group of n-bit output responses is formed by adding together all of these vectors modulo m, where m can be arbitrary. The choice of m limits the number of bits in the checksum. The use of the checksum technique requires a more complex hardware than other compaction schemes, and is therefore suitable for circuits already containing adders, ALUs, and other arithmetic structures.
Space (or combinational) compaction schemes use various forms of parity counting in a per cycle mode. Finally, the schemes that combine features of both previous techniques include convolutional and block-based compactors. All of these schemes will be discussed later on.

## Slide 48: Error models and aliasing
Single-bit and burst errors
Equally likely errors
Stationary and non-stationary independent errors
Asymmetric errors
Aliasing or error masking – signature obtained from a faulty circuit is the same as that of the fault-free circuit
How likely is aliasing?
S. Pilarski, T. Kameda, IEEE Computer Society Press, 1995
Notes: How likely is it that a fault will generate a signature identical to a fault-free signature? To answer this question, numerous approaches have been proposed to derive a closed-form solution for the aliasing probability. Since circuit simulation may not be practical, the aliasing is often estimated based on probabilistic models of erroneous sequences generated by faulty circuits. These error models reflect some basic features of the CUT, and use a concept of error polynomials. Let T(x) and T'(x) represent a fault-free and faulty test-response sequence, respectively. Then the error polynomial is defined as E(x) = T(x) + T'(x); that is, each nonzero coefficient of E(x) represents an error in the corresponding bit position of the output sequence.
The analysis of the compaction process can be now carried out using an error polynomial and its signature rather than the actual test responses and corresponding signatures. In this alternative description, the aliasing occurs if an error signature equals 0, provided the test-response sequence is erroneous. Among several types of error polynomials, the following ones have been used the most frequently:
single-bit error – E(x) contains only one erroneous bit,
burst errors – all erroneous bits occur in E(x) within a limited number of consecutive bit positions,
equally likely errors – all possible forms of E(x) have the same probability of occurrence,
stationary independent errors – every bit of E(x) can be in error independently with the same probability p,
nonstationary independent errors – every bit of E(x) can be in error independently with the probability depending on its position in the sequence E(x),
asymmetric errors – similar to the previous cases; the probability of being in error is, however, conditional and takes into account the fault-free response; that is, this model uses the probability of an error provided the correct response is 0, and the probability of an error provided the correct response is 1.

## Slide 49: Markov model
Aliasing
error (1)
OK (0)
Fault-free response
Faulty response
Error polynomial
010
101
110
111
011
001
100
000
p
1 – p
Notes: To determine the probability of aliasing, an LFSR-based compactor can be modeled by a Markov chain, as shown on the slide. Consider a 3-bit LFSR with the characteristic polynomial h(x) = x3 + x2 + 1. The state transition graph of the LFSR is shown above, where p is the probability of error occurrence in the error polynomial. The state 000 now corresponds to the state of aliasing. As can be seen, there are exactly two predecessors for each state of the signature register. Transitions from these predecessors to the actual state are always performed with probabilities p and 1 – p. Since it is possible to reach any state from any other state, the system is ergodic, and, in its steady state, the probabilities of being in any of the 8 states is 1/8. Thus, in particular, the probability of aliasing is also 1/8, irrespective of the initial conditions.

## Slide 50: Aliasing probability
The Markov chain representing the n-bit LFSR-based compaction is irreducible, aperiodic, and has a doubly stochastic transition matrix; thus the probability that it enters any state is
p = 2-n
provided that a steady state is reached
For n = 20, p = 10-6 and n = 30, p = 10-9
Notes: In general, it can be proved that assuming the stationary independent errors model, the probability of aliasing approaches asymptotically (that is, as the length of the test sequence tends to infinity) the value of 2–n, where n is the size of compactor. This is one of the most celebrated theoretical results in the entire test realm. However, one needs to determine the dynamic behavior of the compaction process, that is, to estimate how fast the final value of the aliasing probability can be reached.
One can use the z-transform to find the probability of being in any state of a given LFSR as a function of test sequence length. It has been concluded that, in general, primitive polynomials are better than non-primitive polynomials with respect to their rate of convergence to steady state, and that the upper bound for the aliasing probability can be approximated by rather cumbersome formulas.

## Slide 51: Transient period
0.00
0.00
0.00
0.00
0.00
1.00
0.00
0.00
pe = 0.25
0.75
0.00
0.25
0.00
0.00
0.00
0.00
0.00
0.00
0.0625
0.00
0.5625
0.1875
0.00
0.1875
0.00
0.1406
0.1406
0.4219
0.0156
0.0469
0.1406
0.0469
0.0469
Notes: Similar results can be derived from a simple simulation of a Markov process representing a given compaction process. The slide illustrates four consecutive computing steps for a 3-bit LFSR-based compactor (as shown on the former slide), where an initial probability mass concentrated in a single state (000) is then gradually redistributed among the remaining states. By observing values associated with each state, in particular that one of aliasing, one can obtain aliasing values for successive test steps.

## Slide 52: Transient period
Probability of error injection
0
0.5
10
20
30
40
50
The number of test patterns
Aliasing probability
(primitive polynomial)
0.9
0.8
0.2
0.1
h(x) = x3 + x2 + 1
0.4
0.3
0.2
0.1
Notes: The importance of transient analysis can be clearly seen in plots on this slide. They illustrate the aliasing probability as a function of the test length, the error probability p, and the polynomial employed. One may find the aliasing probability for primitive polynomials is less than that for non-primitive ones. Similarly, the aliasing probability converges to the steady-state value of 2–n much faster in the case of primitive polynomials. Interestingly, the probability of aliasing in successive steps is strongly related to the probability of error injection. The presented numerical data has been obtained from simulations of respective Markov chains. These observations have also been confirmed by experimental studies performed in the fault domain.

## Slide 53: Multiple input signature register (MISR)
Parallel data acquisition from multiple scan chains
Multiple error injections
High compaction speed
Simple hardware
Compacts test responses to a small signature with negligible aliasing
Compaction ratios  108 x
Unable to handle unknown states
Multi-pass, complicated fault diagnosis
2
1
0
3
6
9
12
15
4
5
7
8
10
11
13
14
Notes: A natural extension of the LFSR-based compactor is a multiple-input LFSR, known as a multiple-input signature register (MISR), which is used to test multiple-output circuits in a parallel fashion. MISRs feature a number of XOR gates added to the flip-flops. The CUT outputs (or serial outputs of scan chains) are then connected to these gates as shown on the slide. In a similar way, the cellular automata can be modified to act as parallel test-response compactors.

## Slide 54: BILBO
Built-in logic block observer
B1
B2
clock
Q
D
Q
D
Q
D
Q
D
00 – shift register
01 – LFSR
10 – parallel load register
11 – MISR
B. Koenemann, J. Mucha, G. Zwiehoff, ITC’79
Notes: Several BIST architectures target maximum multiple utilization of the hardware to perform test generation, response compaction, and even system functions. The built-in logic block observer (BILBO) was one of the earliest structures designed specifically for test-per-clock BIST schemes. It combines the function of a register, shift register, LFSR, and MISR built around one set of flip-flops. Therefore, each BILBO module can act as either generator or compactor, although in a given test session two of these blocks are required to test a module of the CUT, one assuming the role of generator, the other acting as a compactor. In the next test session these roles can be exchanged, and the content of a BILBO acting formerly as a compactor can be treated as a seed in a test generation mode. This scenario assumes, pessimistically, that the content of a MISR cannot be considered as valuable pseudorandom vectors, whereas some experimental results demonstrate that the MISR performing test-response compaction can simultaneously act as a source of random patterns. This allows a designer to reduce the number of test phases, as the same BILBO can be employed to observe as well as to stimulate two different blocks of the CUT, or even, under special circumstances, a single BILBO can capture responses which are subsequently used as tests for the same CUT.

## Slide 55: Unknown (X) states
Uninitialized memory elements
False and multi-cycle paths
Bus contentions
Non-scan flip-flops
Floating buses
Internal three-state logic
1
0
1
1
conflict
0
Z
0
floating
Notes: One of the key requirements for a reliable test response compactor is to preserve observability of any scan cell for a wide range of unknown (X) state profiles, while (1) maintaining very high compaction ratios, (2) providing ability to detect a variety of failures found in real silicon, and (3) assuring design simplicity. X states are increasingly often identified as having potential for rendering test useless. Sources of X states include uninitialized memory elements, bus contentions, non-scan flip-flops, floating buses, internal three-state logic, and multi-cycle and false paths when generating at-speed tests. In many scan-based designs, X states, once captured in scan cells, may subsequently be injected into a test response compactor. Hence, they can severely affect test results, especially if a time compactor is used, where X states quickly multiply (due to a feedback fan-out), contaminate a signature, and stay there until a read out operation. Combinational compactors are relatively immune to X states, but in order to avoid masking and to allow diagnosis they have to observe each scan chain on two or more outputs.

## Slide 56: X states and MISR
Every X state can double the number of “correct” signatures
0011010010111100101
0011010010111X00101
0011X10010111X00101
Test response
Signature
32-bit MISR
for 32 Xs there are no signatures left for fault detection
0
1
1
00
01
10
11
Notes: Consider, as an example, a test response to be injected into a MISR acting as a compactor. If a design is clean (no X states), a MISR will produce a unique signature (a white box on the slide). If one of the response bits is unknown, then there are two possibilities depending on its actual value – as a result a MISR will yield two different signatures, as shown above. With two unknown values, there are four different test responses that one must consider – they clearly result in four different signatures. With the increasing number of X’s, the number of actual test response sequences is quickly (exponentially) growing. For example, with only 32 X’s, we need to consider 232 different scenarios – this is the total number of different signatures a 32-bit MISR can produce. Clearly, this modest amount of unknown states can render the entire test (using the MISR of a reasonable size) completely useless.
It is worth noting that if a test pattern with 100,000 scan cells features typically 100 scan cells with X states, i.e., an X-fill rate is equal to 0.1%, and there are 100,000 of such patterns, then a time compactor would have to handle a huge volume of roughly 107 unknown states.

## Slide 57: MISR channel masking
R0
C0
C1
1 0 x 0 1 x 0 x 0 1 0 1 0
x 1 0 x 0 x 1 0 1 x 0 1 x
0 1 0 1 0 1 1 1 0 0 1 1 0
0 0 1 0 0 1 0 1 0 0 0 0 0
1 0 0 1 0 1 0 0 0 1 0 0 1
C0
C1
0 1
1 0
1 1
R0
R1
C0 | C1 | Mask
0 | 0 | None
1 | 0 | R0
0 | 1 | R1
1 | 1 | All bits
Compactor
R1
V. Chickermane, B. Foutz, B. Keller, ITC’04
Notes: Even if a compactor is designed to tolerate a pre-specified amount of X states, its vulnerability to X states may quickly take over, and thus it requires protection in the form of a scan chain selection (X-masking) mechanism. Otherwise, certain combinations of X states not eliminated by ATPG would prevent observability of some scan cells and cause a fault coverage drop. Many schemes addressing selective observation of scan chains (scan cells) have been proposed. A channel masking scheme shown on the slide allows either disabling all scan chains, or selecting scan chains belonging to one of two groups at the price of possible over-masking.

## Slide 58: X-masking scheme
…
…
Selection
logic
Control
X-masking data
MISR
D. Czysz et al., VTS’09
Notes: This slide shows another X-masking scheme placed in a test environment with multiple scan chains. A test response compactor consists of a MISR and a scan chain selector, which in turn comprises a group of circular mask registers and selection logic. The latter one is driven by mask data kept, in a compressed form, in the registers. The selector outputs gating signals to AND gates in a per-cycle mode so that X states originating at various scan cells do not reach a compactor. Scan chains whose content during a given shift cycle is not regarded critical may receive either 0 or 1 as their gating signals. It is worth noting that the proposed scheme can work with any type of compaction device. The use of MISR, however, offers the highest compaction ratios provided one can entirely eliminate X states occurring in test responses that enter the compactor.

## Slide 59: X states clustering
Notes: Many industrial designs exhibit a crucial feature: X states are not randomly distributed in test responses. On the contrary, they have identical or similar patterns occurring in contiguous and adjacent areas of scan chains for many test patterns. This observation remains valid after scan chain reordering. Scan insertion is guided by hierarchy, clock domains, proximity to certain modules, routing overhead, and other criteria. As a result, cells receiving X’s are usually located close to each other when stitched into scan chains. Reordering typically involves segments of scan chains either within or between them. Thus, adjacent cells belonging to the same clock domains can be moved together, if needed, to a separate chain. As reordering tools maintain lockup cells in the boundaries (created by clock transitions), they may move all cells between the boundaries in chunks, thus likely preserving clusters of cells that capture X’s, as illustrated on the slide for several test patterns.

## Slide 60: X-state profiles
1,000 test responses
Notes: Here are real examples of exclusive propagation of X states to certain areas of scan chains. All X locations, represented by black dots, were recorded in two industrial designs by collecting 1,000 test responses. These responses were subsequently superposed. The observed clustering of X states can be a key factor in reducing the volume of test data as one may deliver identical mask bits to the gating circuitry for a number of scan shift cycles. Moreover, a noticeable appearance of scan chains free of X’s may further reduce the burden of mask data encoding. Not only are X states highly clustered but also effects caused by faults often propagate to the same scan cells, as confirmed by many experimental results. Thus, grouping several test responses into a single item may help reduce the amount of data required to both govern the X-masking process and to protect fault propagation sites.

## Slide 61: Selection logic
…
…
Enable
Clk
C
+
Ring generator
Phase shifter
Hold register
Notes: Essential components of selection logic include a ring generator, a hold register, a phase shifter, and an enable register driving additional OR gates. Compressed mask data are delivered through c inputs in a continuous manner, i.e., a new c-bit word is injected into the ring generator every scan shift cycle moving effectively the selector from one of its states to another. This design addresses the presence of clustered X states of high density. Indeed, the hold register provides a mechanism to sustain the outputs of the selector for more than a single clock cycle, while allowing the selector to change its internal state to ensure encoding of the next group of mask bits. In other words, the hold register captures and saves, for a number of cycles, a desired state of the ring generator, while the generator itself keeps advancing.
Functionality of the masking logic is further enhanced by an enable register. Its content, uploaded only once for all test patterns, is employed to enable/disable selected masking signals by means of 2-input OR gates. One input of each gate is supplied by a designated output of the phase shifter, while the other input is driven by the enable register. If its k-th bit is asserted, then the values captured in k-th scan chain enter the compactor independently of other masking signals. Hence, the use of the enable register relieves the masking logic of taking care of a large number of errors that occur in otherwise clean scan chains. This reduces control data volume. Bits of the enable register corresponding to scan chains with X states are reset to allow efficient operations of the masking and gating logic. The selector control information is merged with the mask variables by reusing data stored in the mask memory. Mask bits go through the small buffers and drive an XOR tree, which computes a parity signal for the corresponding input variables. If their parity is odd, then the hold register is reloaded before new variables enter the ring generator. Otherwise, the content of the register remains unchanged. It is worth noting that this technique allows one to use even a single input if encoding capabilities of the selector permit. The encoding of masking signals is similar to that of low power test data compression. For further details, refer to the section on test compression.

## Slide 62: Spatial compactors
Smaller compaction than time compactors
Handling of unknown states
Notes: As mentioned earlier, a characteristic feature of time compactors is the infinite impulse response property. They are capable of compacting gigabits of test response data into a small signature, for instance 32-, 64-, or 128-bit long, achieving compaction ratios between 106 and 108. This is possible because an error, once injected into this type of a compactor, will remain there until another group of errors erases it in the rare case of aliasing. These schemes, however, require that all values in test responses be known. Since many designs produce X states in test responses, and it might be too intrusive to remove them, time compactors may not ensure a desired test quality.
Space compactors are combinational circuits, predominantly built of XOR networks to generate n test outputs from m primary outputs of the circuit under test (CUT), where n < m. They offer smaller compaction than the time compactors, but they can handle unknown states in responses without circuit modification. The simplest space compactors comprise a number of XOR trees, each of which is handling a given number of inputs (typically scan chains). The same class includes compaction schemes using error codes and many other compaction techniques with abilities to tolerate X states and identify certain errors (fault diagnosis).

## Slide 63: Spatial compactors
Certain minimum number of outputs required
Improved diagnostic capabilities
S. Mitra, K.S. Kim, IEEE Trans. CAD, 2004
Notes: The X-Compact technique (shown on the slide) is based on the original Saluja-Karpovsky scheme, and by increasing the input fan-out it handles simultaneous errors and unknown logic values, both arriving from multiple scan chains. As other spatial compactors, the X-compact reduces a negative impact of X states to a single scan shift cycle. It also allows identification of certain errors per cycle. In particular, it can uniquely identify a single failing scan chain provided that only one scan chain produces an error at any scan-out cycle. Output failures that cannot be mapped directly to a single scan chain needs an exhaustive checking. It can be guided by statistical data regarding faulty sites determined earlier in the same process. This scheme requires certain minimum number of outputs. For example, every scan chain must be observed by, at least, two outputs. This property, in turn, may reduce the compaction capacity below acceptable limits.

## Slide 64: Convolutional compactors
Errors identified by unique syndromes
J. Rajski, J. Tyszer, C. Wang, S.M. Reddy, ITC’03
Notes: This slide illustrates an example of a finite memory compactor – a third class of compaction schemes obtained by combining time and space dimensions. These compactors have the characteristics of finite impulse response, i.e., a single scan cell is observed in a finite number of cycles, and because of adopted polynomial multiplication, they are referred to as convolutional compactors. They support output response compaction with effective ratios going beyond 100x, they offer consistent properties, such as ability to detect errors with very low probability of aliasing, for a whole range of configurations, starting from a single output. Finally, they can handle unknown states and allow in-production diagnosis by identifying faulty scan cells directly from compacted responses.
The slide shows a convolutional compactor with 10 inputs (observing 10 scan chain outputs), one primary output, and 6 memory elements. The spatial part of the compactor consists of 6 single-output XOR networks connected to the registers by means of additional 2-input XOR gates interspersed between memory elements. Each network, by assuming a balanced XOR tree structure, introduces a delay of only log2n, where n is the number of scan chains connected to a given memory element. As can be seen, every scan cell error can reach the memory elements and then the output in several ways. In fact, each scan chain has its own and unique injection pattern (shown in red) that allows simple identification of a location where an error is arriving from. The circuit presented on the slide does have memory but no feedback. As a result, any error or X state injected into the compactor is shifted out after at most 6 cycles.
.

## Slide 65: Error masking
Notes: It is worth noting that due to injector XOR trees deployed by the convolutional compactor shown on the slide, no odd number of errors or two errors injected at the same time or in different time frames can mask each other completely. As mentioned earlier, single errors injected in each scan propagate to the output in a different recognizable pattern.

## Slide 66: Handling of X states
Single error detected in the
presence of a single X state
X
Notes: The injection network architecture can be further customized in order to increase an X-tolerance of the compactor. Although X states are flushed out in a number of scan shift cycles, they can mask errors injected from scan chains and thus reduce the actual observability of certain scan cells. The circuit on the slide is an X-tolerant compactor. All its injectors feature fan-out of 3, and every two injectors share at most one memory element. In other words, a given pair of flip-flops is used only by one injector. As a result, one or two X states (blue lines and dots) injected in parallel with an error (red lines and dots), i.e., at the same scan-out cycle, cannot mask the error entirely. The compactor is said to tolerate at most two X states.
Interestingly, the combinational X-Compact scheme with 8 outputs can observe at most 56 scan chains with the resulting maximum compaction of 7x. A convolutional compactor with the same number of outputs (it deploys 8 registers) can observe up to 504 scan chains using 16 flip-flops, and 2936 scan chains connected to 32 flip-flops. The corresponding compaction ratios are 63x and 367x, respectively.

## Slide 67: Arithmetic compaction
All bit positions affected by error propagation (1’s complement arithmetic)
Error propagation only towards more significant bits – high probability of aliasing
…
Binary adder
Carry out
Carry in
…
…
…
Binary adder
Notes: In the scheme shown on the slide, an accumulator with an n-bit binary adder is employed as a compactor, which, by adding sequences of binary numbers, compacts the test responses to a final sum – signature. As with other compaction schemes, the key question is, how likely is it that the sum representing a faulty response is the same as that of the fault-free response? It appears that the probability of aliasing introduced by accumulators with binary adders is 2–k, where k is the number of bits in the adder that a fault can reach. It indicates that, in the worst case, that is, when a fault is injected from the most significant bit, the limiting probability of aliasing is 0.5, independently of how big an accumulator is used. In such a situation the binary adder performs a single-bit parity check. Since the limiting probability of aliasing depends on the number of positions a fault can reach, a feedback connection can be established between the output carry line and the input carry line as shown n the slide. This connection effectively enables any fault, regardless of the rank, to reach any bit of the register. This structure is similar to the architecture of an accumulator performing the addition of 1's complement numbers. In this case, the aliasing probability for a fairly general class of faults is (2n – 1)-1, where n is the size of the adder. Clearly, the last result is similar to that of LFSRs, MISRs, or cellular automata, and as that is superior for variety of applications, since with adders being a part of the tested circuits, the need for extra hardware is either completely eliminated or drastically reduced.

## Slide 68: Diagnosis and compaction
Single cell observed per test
  simple control
  identifies any number of errors
  excessively long test application time
Partitions: the same test experiment repeated several times for each group of scan cells
Successive tests capture responses from disjoint subsets of scan cells
Approximately the same number of scan cells involved in each test
Given partition, every scan cell associated with only one test
Notes: The basic objective of fault diagnosis performed in a BIST environment is to identify a fault that has occurred in the CUT, based solely on the recorded signature(s). Such a fault diagnosis is a very challenging task because of very high reduction of output test data volume. Although very accurate, methods that observe only a single scan cell per test are virtually unacceptable due to excessively long test application times. Therefore, other methods monitor several scan cells in parallel. The essence of these techniques is to make, during a single test experiment, only selected scan flip-flops observable by a test response compactor. The same tests are then applied several times in order to collect a number of signatures corresponding to different groups of scan cells. Next, an off-line analysis of the obtained error-free and possible erroneous signatures is performed such that one can isolate scan cells driven by erroneous signals.

## Slide 69: Random partitioning
A random number in a given range assigned to every cell
Only cells with label n observed during nth test
A next sequence of random numbers generated once test patterns for a given partition group are completed
2 partition groups
4 clusters
0
1
0
3
1
1
0
2
3
1
0
0
3
2
1
2
0
3
1
0
0
3
2
3
3
0
0
1
2
2
0
0
2
3
1
2
3
0
1
1
3
0
1
3
2
2
Notes: Scan cells that are observable can be selected in a pseudorandom fashion. The partitioning procedure has then the following properties:
for each partition group every scan cell is assigned a pseudorandom integer R, uniformly distributed between 0 and b – 1, where b is the number of clusters used for one partition group,
during Rth test only scan cells labeled with the number R are observed for test response compaction purposes,
once tests from a given partition group are completed, a new sequence of pseudorandom numbers is generated in order to create a new partition of the scan chain(s).

## Slide 70: Scan partitioning for diagnosis
To compactor
Clock
Scan chain
Next
pattern
Next
partition
Next
partition group
. . .
Pattern counter
MP-LFSR
Partition counter
Shift counter
R
Polynomial
J. Rajski, J. Tyszer, ITC’97
Notes: A scan cell selector is the only hardware required to implement random partitioning. It is used to gate the test-response data serially streamed from the scan chain before capturing it by the compactor. The selector consists of the following three blocks: a pseudorandom number generator, a reference comparator circuitry, and a test counter. Also, the selector uses signals received from the shift counter and the pattern counter – two circuits employed commonly in any scan-based architecture.
A programmable LFSR capable of implementing, at least, g polynomials, where g is the number of test groups, implements the pseudorandom generator. Since the output of any r stages of the LFSR can be regarded as an r-bit binary number representing a label associated with a particular scan cell, these stages can be used to select the scan cells. A test response is then serially fed to the compactor in synchronization with the LFSR clock. Every shift, a label produced by the LFSR is compared with the current test number. If a match occurs, a corresponding bit from the scan chain enters the compactor. After n shifts, the LFSR is initialized due to a carry signal from the shift counter, and the process repeats until all patterns are applied.
The polynomial decoder logic is driven by higher bits of the test counter such that every time a carry occurs from rth bit of this counter, a new feedback polynomial is selected. It guarantees a new sequence of pseudorandom numbers when a next test group starts. When a single test is completed, a carry is generated at the output of the pattern counter. Consequently, the contents of the test counter is incremented and this new value will be used in comparisons when applying test patterns during the next experiment. After b tests, a carry occurs at the output of rth stage of the test counter, where r = log2b. This signal is employed to initialize the LFSR.

## Slide 71: Deterministic partitioning
Clk
To compactor
Clk
. . .
. . .
Pattern counter
Offset counter
Group counter
Diffractor LFSR
Partition counter
Shift counter
Load
Load
Clk
Scan chain
I. Bayraktaroglu, A. Orailoglu, IEEE Trans. Computers, 2005
N1
N2
Notes: Instead of random partitioning, one can use its deterministic version. A scan cell selector comprises four registers. The up counters partition and group keep indexes of the current partition and the current group, respectively. They act as an extension of the shift and pattern counters belonging to a BIST controller. An LFSR with a primitive polynomial implements a diffractor providing successive powers of a generating element of GF(2n), which are subsequently used to selectively invert data arriving from the partition register. The same register can be initialized when its input load is activated. Similarly, one can initialize a down counter offset by asserting its input load.
In principle, the selector implements the following formula used to determine members r of partition p within group g:
r = Sk + (p  (g  k)), k = 0, 1, …, P – 1,
where S is the size of partition, P is the number of partitions,  is a bit-wise addition modulo 2, and g  k is a state that the diffractor reaches after k – 1 steps assuming that its initial state was g. If k = 0, then g  k = 0.
Selection of scan cells within a partition, a group, and finally the whole test is done as follows. The offset counter is reloaded periodically every time the n least significant bits of the shift counter become zero (this is detected by the NOR gate N1). Once loaded, the counter is decremented to reach the all-0 state after p  (g  k) cycles. This is detected by the NOR gate N2 associated with the counter. Hence, its asserted output enables observation of a single cell within every S successive cycles. As indicated by the formula, the initial values of the offset counter are obtained by adding the actual partition number to the current state of the diffractor. The latter register is initialized by using the group number at the beginning of every test run, i.e., when the shift counter is reset. Subsequently, the diffractor changes its state every time the offset register is reloaded. As the period of the LFSR-based diffractor is 2n – 1, and the offset counter is reloaded 2n times, the missing all-0 state is always generated at the beginning of a test run by means of the AND gates placed at the outputs of the diffractor.

## Slide 72: BIST controller
Reset
Scan enable
Done
Run
...
Clock
...
Scan chain
Scan in
Scan out
Test generator
Shift counter
Pattern counter
Test response compactor
Scan chain
Mask generator
SE
SE
Notes: The principal functions of BIST controller include resetting and seeding registers, keeping track of the number of shift commands required in scan operations, keeping track of the number of test patterns that have been applied, communicating with other test controllers, and inhibiting test and system clocks. Two generic designs for the BIST controllers are frequently encountered in practical solutions. The first approach augments the classical microprogrammed controllers by adding circuitry that allows clocks to be started, stopped, and pulsed for a predetermined number of steps. However, if the CUT does not feature a microprogrammable control unit, a hardwire test controller might be a more feasible solution. Such a solution is shown on the slide.

## Slide 73: BIST session
Reset
Scan enable
...
...
Scan chain
Test generator
Shift counter
Pattern counter
Test response compactor
Scan chain
Hold
Mask
Clock
SE
loading
unloading
128
16000
0
0
Scan chain
Scan chain
0
C
Scan chain
Scan chain
1
1
15999
SE
SE
Notes: A generic sequence of operations which are executed in the BIST mode consists of two nested loops. The outer loop handles the number of test vectors to be applied. The inner loop iteratively performs actions required to shift data into and out of the scan chains. While in a particular state, certain operations occur. The execution of this finite state machine is carried out as follows. It remains in the initial state until a pulse occurs on the START line. It takes the controller to the next state where initial values of two counters Pattern and Shift are loaded. These counters are used to control the number of test vectors applied and the number of shift operations performed, respectively. As long as the shift register is greater than 0, shift and Decrement Shifts control signals are produced. Any subsequent detection of 0 in Shift will result in a move to a state in which the counter Shift is reloaded, a test vector is applied, and the counter Pattern is decremented. If this counter has nonzero content, the controller returns to the sequence of shift operations. Otherwise, it sends the signal Done and settles into the initial state. The same FSM outputs signal gating a signature register in order to protect this device again unknown states leaving scan chains.

## Slide 74: Boundary scan and BIST
74
TDI
TRST*
TCK
TMS
TDO
Instruction decoder
Instruction register
Application logic
Boundary scan register
Output buffer
Device ID register
BR
TAP
Pattern counter
Shift counter
PRPG / MISR
Load BIST registers
RUNBIST
Unload MISR
Notes: The concept of BIST can be easily merged with internal and external scan paths. Further and more formal integration of BIST circuitry with the boundary scan architectures has been proposed in the IEEE 1149.1 to allow effective testing of integrated circuits once they have been mounted on a board. A provision of the RUNBIST instruction permits a consistent access to self-test features of a chip in a way which is independent of a particular type of a BIST scheme implemented by a user. In fact, the test generator, signature analyzer, and the BIST controller appear to the EEE 1149.1 master as test data registers which can be selected by sending the proper sequence to the TAP controller. In some designs, the boundary scan register itself can take part in the application of test vectors or gathering test responses. In this case, selected boundary scan register cells can be configured to act as an LFSR, MISR, or cellular automaton.
In order to execute the RUNBIST instruction correctly, the logic involved in the test has to be initialized automatically within the chip. For instance, the test generator would be loaded with a predetermined seed in the first clock cycle following entry into Run-Test/Idle TAP controller state. While a BIST session is in progress, the boundary-scan register can be used to hold the chip's primary outputs at a fixed value. This is done to ensure that signals generated by the on-chip logic during the test does not cause unwanted or hazardous operations within chip's downstream components. Typically, for two-state outputs, the value can be defined by the user. For three-state outputs, they could be alternatively set to the high-impedance state. Also, all primary inputs are isolated from the chip's internal logic during the test. This prevents unknown logic values from propagating to the test-response compactor. Clearly, this interference could easily invalidate results of the entire BIST experiment.

## Slide 75: BIST-ready designs
BIST-ready designs should have
  scan
  no internal bus conflicts or floating buses
  no X states propagating to observable outputs
Should be random-pattern testable
X states are bounded by test logic
Random pattern testability improved by test points
ATPG patterns used to achieve the highest possible coverage
Notes: In a BIST automation tool flow, the BIST structures are usually generated at the front end of the design process. As BIST blends both the design and test paradigms, merging test functions into the design flow at these early stages reduces the product development cost and possible impact on the functional design. Some operations, however, still have to be invoked and run at the back end of the design process. It applies, in particular, to tools performing test point and scan insertion, as they require knowledge of the gate-level circuit description. The synthesis of the BIST hardware is comprised of two steps. First, the cores are designed to be BIST-ready. This process involves the insertion of internal scan paths, test points, a repeater circuitry, and a space-time compactor. The repeater receives serial data from the central generator and expands it to a parallel format to drive multiple scan chains. It consists of a short shift register and a phase shifter. The space-time compactor converts the parallel format of the core responses to a serial one. Again, it consists of a short register and an XOR network. The process of design of BIST-ready cores also involves fault coverage analysis of the patterns which will be applied in the system. To ensure the repeatability of test vectors which are applied to the core, the order of the core inputs is determined and fixed. This order is implemented by the core isolation mechanisms - scan or reduced boundary scan. For a specific generator defined by its characteristic polynomial and seed, given number of vectors, and the compaction polynomial, the simulation determines the fault coverage and resulting signatures. The signatures are computed for each output separately. Once the order of the outputs is determined in the system by the order of scan inputs, the final signature is determined using the principle of superposition. This analysis ensures that when the core is integrated in the system it will be exposed to the same vectors, and the fault coverage is therefore guaranteed.

## Slide 76: Logic BIST flow
Gate level netlist
Final core netlist
RTL for controller
top level wrapper
Fault coverage
reports
PRPG and MISR
values per pattern
Scan chain load/
unload data
Verilog / VHDL
testbench
WGL vectors
Results
Scan insertion
X-Bounding
Test points
BIST controller synthesis
Parallel pattern simulator
RTL to gates
Time-based simulations
Testbench & test vector generation
ATE
Notes: The second step involves integration of BIST-ready cores into a system. The random logic cores are connected to the central BIST which has a PRPG with programmable polynomial and seed, a single input signature register (SISR) with programmable polynomial, and a controller with a programmable number of test vectors and the length of shift. With such extensive programmability of the key functions, the BIST hardware can accommodate cores which were designed independently and have different requirements. All cores which have the same parameters can be tested concurrently, if the power constraints allow it. The central BIST hardware is programmed with these parameters, and the cores are selected by the separate chain of core selection flip-flops This feature can be further employed for BIST diagnostic purposes. The serial inputs of scan registers or reduced boundary scan registers separating cores are driven by the repeater circuits of the cores which they drive. This guarantees that the input vectors are completely repeatable. The serial outputs of those registers are connected to compactors of the cores which drive them. This way it is possible to compute a signature which comprises all outputs of the core.
It is worth noting that designers spend more time at the architectural levels, and more tools and libraries are being developed to support this change. Several CAD tools accept a circuit specification in Verilog or VHDL and generate a complete RTL description of the BIST controllers, pattern generators, and response compactors. This approach enhances design portability by simplifying reuse across different technologies. The support for automated integration of BIST controllers with the IEEE 1149.1 standard is also commonly available. The RTL code can be then simulated and synthesized using any EDA industry tool.

## Slide 77: Logic BIST summary
Ideally suited for applications where stored patterns are prohibitive, i.e., system test
Test coverage objectives are achieved by pseudorandom patterns and test points
Unknown states have to be eliminated to allow signature based compaction
For manufacturing test ATPG top up patterns are required to achieve the desirable test quality
For very long test experiments some unmodeled defects can be detected
Notes: Logic BIST has emerged as a viable alternative testing technique which can alleviate many problems resulting from conventional testing: large volumes of test data to be stored and handled, long test application times, the necessity of using expensive external testing equipment, and problems with at-speed tests. BIST assumes that the original circuit is appended with additional modules for on-chip generation of test vectors and on-chip evaluation of test responses. Application of BIST introduces certain costs. The major penalties include the area overhead (including that of X-bounding logic) and performance degradation. Also, the use of BIST automation tools imposes several rules that have to be obeyed in the design process. The on-chip test generation schemes employ a variety of techniques, virtually providing the complete spectrum of test patterns, from deterministic to random ones, ensuring efficient implementation of hardware generators at the same time. LFSRs are the most popular structures used for this purpose. The same devices are commonly used to perform test response evaluation. By far, the most prevalent approach is compaction of test data into a short signature. Although a faulty circuit and the fault-free circuit may yield identical signatures (aliasing), the probability of such event has been shown to be asymptotically equal to 2-n, where n is the size of a compactor. Vast majority of BIST schemes can be easily integrated with existing DFT architectures and, because BIST technology addresses various dimensions of testing. It can be run at different stages of the product life cycle, from wafer and device domain to system and field maintenance operations.