## Slide 1: VLSI testing
Fault modeling
HEP
Notes: Physical defects take a wide variety of forms, from localized spot defects (e.g. extra or missing material caused by contamination) to defects affecting much larger areas (e.g. transistor changes caused by implantation variation). Some of them affect circuit behavior. They occur in random places and can have unpredictable effects. In this chapter, we first briefly overview certain defect mechanisms, with special emphasis on the CMOS technology. This is followed by a discussion of some specific fault models which are in common use today.

## Slide 2: Common defects in CMOS
Shorts – conduction occurs when undesired
Caused by
  extra conducting material
  missing insulating material
Examples
  photolithographic printing errors
  conductive particle contamination
  incomplete etch
  incomplete material polish
  crack in the insulator
  gate oxide defect causing pinhole
R.C. Aitken, Defect-oriented testing, Springer, 2006
Notes: Shorts are a major source of defects. Some of them are due to classis effects such as particle contamination, while others result from chemical/mechanical polishing scratches or dishing (see slide 5), optical effects, and more. Shorts involving many lines are typically catastrophic, so while they are vital to yield calculation, they are less important for fault modeling. The electrical behavior of the short is determined by the physical properties (material, thickness, length, temperature) and the location, e.g., a high resistive bridging defect behaves differently than a low resistive one at the very same location. Shorts at the diffusion level often involve only the terminals of a single transistor. Shorts in poly or metal 1 affect the internals of one or more standard cells. Shorts in higher levels of metal interconnect typically involve gate outputs, power, and/or ground. A short defect must have opposite polarity voltages across involved nodes in order to activate its presence. A conducting path is formed from the power supply through active P transistors through the short, then through active N transistors to ground. The shorter (less resistive) the short, the more likely this conducting path will disrupt circuit operation.

## Slide 3: Common defects in CMOS
Opens – desired conduction does not occur
Caused by
  missing conducting material
  extra insulating material
Examples
  photolithographic printing errors
  step coverage
  incompletely filled via
  electromigration and silicide agglomeration
  incomplete via etch or via foreign material
  insulating particle contamination
Notes: Open faults are also a cause for serious concerns. As the number of wiring levels in circuits increases, the number of vias proliferates. The effect of missing vias, partial vias, and resistive vias on circuit operation are not easily modeled. As with shorts, the behavior of an open is determined by where it is located, whether in the transistor structure or in the interconnect between transistors. Logically, opens can be within a cell, or between cells. In many cases, a complete open results in a node that is electrically isolated from its surroundings. Charge stored on this node during fabrication can affect its subsequent operations. For small opens, Fowler-Nordheim tunneling can slow down a circuit below an acceptable threshold. In practice, many opens are partial ones. They are challenging to detect and handle.

## Slide 4: Common defects in CMOS
Parametric changes
Begins with a physical change
Affects the circuit via electrical change
Examples
  transistor gate length
  dopant concentration
  material and oxide thickness
Designs can tolerate some parametric variation
Notes: Defective behavior is not always caused by a single isolated problem such as a short or an open. Sometimes a circuit parameter is out of specification across a wide area, and this can cause a failure, or an increased susceptibility to other problems (e.g., temperature effects, crosstalk, etc.). Parametric variations begins with a physical change (e.g., variation in printed transistor gate length) and affects the circuit via electrical change (e.g., transistors that are faster and leakier than expected). In addition to gate length, other parameters of interest include dopant concentration (device mobility, capacitance), metal thickness (resistance, capacitance), oxide thickness (leakage, performance). Some variations are expected, and a design must accommodate them, but at some point variation exceeds the tolerance or margin in the design, and it becomes a defect.

## Slide 5: Copper-related defects
Chemical/mechanical polishing
  under polishing
  dishing
  erosion
  scratches
Voids – partial opens due to incomplete copper deposition
  thermal expansion of the copper into the void
  delays at low temperatures
  tests should be applied at two temperatures
Erosion
Dishing
R.C. Aitken, Defect-oriented testing, Springer, 2006
Notes: The chemical/mechanical polishing (CMP) process for copper leads to four major defect mechanisms:
under polishing leaving copper or slurry remaining where it is not wanted, which can lead to shorts,
dishing where over polishing has occurred,
erosion where insulator has been polished as well as copper,
scratches that result in combination of shorts and opens, spread across relatively large areas.
In each case, the defect leaves a surface that is poorly planarized and susceptible to defects at higher levels (e.g. wide metal dishing on one layer can cause shorts in the layer above as wires fold in on each other). In addition to CMP-induced defects, voids (partial opens) are another major defect mechanism. These defects often manifest themselves as delays at low temperatures. This happens because of thermal expansion of the copper into the void. As temperature increases, the void shrinks and the two metals make better contact. The copper void defect mechanisms show that while high temperatures are the worst operating conditions for defect-free circuits, defective circuits may have worst-case behavior at room temperature, or even lower. If possible, tests should be applied at two temperatures to account for void defects and process variation at tolerance limits.

## Slide 6: Optical defects
Mask errors
  OPC fixes lead to shorts or opens when features interfere with one another
  typically mask defects are catastrophic
Design rule checking (DRC) escapes
  OPC cannot fix a feature because of neighboring circuitry
Hammerheads added by OPC
No OPC foreshortening
Notes: At 130nm and below, many features of a layout are below the wavelength of light used during photolithography. As a result, optical proximity correction (OPC) is applied to masks to ensure accurate printing. OPS leads to two major defects: mask errors and Design Rule Checking (DRC) escapes. In a mask error, OPC fixes result in a short, open, or a parametric change resulting in a defect when features interfere with one another. In general, mask defects are catastrophic and result in 100% yield loss as all chips manufactured using the bad masks are faulty. In a DRC escape, OPC is meant to fix a particular feature, but cannot, due to neighboring circuitry. Consider the layout shown on the slide where hammerheads should be added to each gate, but nearby circuitry prevents this from being possible on the leftmost gate. As a result, the gate is foreshortened. The resulting channel is shorter in on portion and narrower as well. This defect will typically behave as a delay fault, and can often be detected by transition fault tests.

## Slide 7: Design-related defects
Decision made by routing tools to determine which wires are likely to short
Low power designs
  multiple voltage domains
  use of high and low threshold voltage transistors
Notes: The impact of design methodology should not be ignored on forming types of defects. For example, decisions made by routing tools determine which wires are likely to short and which are not. Other mechanisms are related to low power design appearing in advanced manufacturing technologies. Low power design techniques are increasingly using variable power supply voltages. Keeping voltage domains separate is accomplished by using physical isolation together with level shifting circuitry. When they interact, a new defect behavior is possible. For example, bridging faults usually assume that a fault is not activated if the involved nodes are at the same logic value. However, by using both high and low threshold voltage transistors may allow a faulty value to propagate even if that assumption is satisfied. For instance, consider a P transistor in the transmission gate where both its gate and source have 1 in the low voltage domain (the gate is off then in the fault-free case). A short with the higher voltage domain may lead to a voltage on the source above VDD of the low voltage domain. This causes the difference between the gate and source voltages of the transistor to be greater than its threshold value, turning the transistor on.

## Slide 8: Fault models
Fault model – abstraction of defect behaviour
Fault models represent diversity of VLSI defects
  they should accurately reflect the behavior of defects
  they should be tractable
Many fault models proposed
Factors affecting fault modelling
  increasing circuit size
  increasing defect subtlety
  decreasing numbers of manufacturing processes
Uses of fault models
  test generation
  fault simulation
  quality prediction
  fault diagnosis
Notes:   It is extremely difficult to generate tests for real physical defects. Therefore, in order to simplify the process of identifying faulty circuits, an infinite defect space is typically approximated by a finite set of faults (or fault models) that extrapolate and simplify defect behaviors. A fault is deterministic, discrete change, that, in particular, can be regarded as a transformation changing the Boolean function of a circuit. The fault effects associated with fault models can be as simple as replacing a circuit node function with a constant value or be so complex as to require SPICE simulation to evaluate. The choice of fault model depends on its intended use, e.g., test generation, quality prediction, defect diagnosis, characterization of defect tolerance, etc. Clearly, no single model suffices to represent all possible defects that may occur. This is why many fault models have been proposed. The factors affecting fault modeling can be divided into three broad categories: increasing circuit size, increasing defect subtlety, and decreasing numbers of manufacturing processes. Also, fault models allow the use of metrics (such as the number of faults detected, undetected, etc.) that allow to compare two test sets, allow to stop ATPG, or the test engineer’s work, when a preset test quality level has been reached, and so on.

## Slide 9: Taxonomy of faults
Defined in conjunction with circuit description
  structural faults – assume that components are fault-free and only their connections are affected
  functional faults – use functional model of a circuit (truth tables are changed)
Based on time behavior
  permanent faults
  intermittent (transient faults) – caused by ionic and electromagnetic radiation
Based on multiplicity – single and multiple faults
Notes:   One can easily distinguish several dichotomies in the fault models domain. First of all, faults defined in conjunction with a structural model of a circuit are referred to as structural faults – typically it is assumed that they modify the interconnections between circuit components (in other words, components are fault-free and only interconnects are affected). Their counterparts – functional faults – are defined in conjunction with a circuit functional model. The effect of functional fault may be to change the truth table or to inhibit an RTL operation. Based on time behavior, one can distinguish intermittent (or transient) and permanent faults. If no stated otherwise, we will always assume that we deal with permanent faults only. Transient faults (caused by, for example, ionic and electromagnetic radiation) are typically handled by on-line testing methods. Finally, there are single and multiple faults. The single-fault assumption is the most prevailing rule used by a vast majority of existing test generation tools. It basically states that there is at most one fault in the system. The rationale behind this assumption is that in most practical cases, a multiple fault (if exists) can be detected by tests derived for the individual single faults that the multiple fault is comprised of (see the next slides).

## Slide 10: Single stuck-at faults
Signal line is stuck at a fixed value of 0 or 1
Represents many different physical failures
Independent of technology – can be applied to any structural model and to model other faults
Tests detecting SSFs detect many other faults
The number of SSFs (2n in n-line circuit) is manageable
VDD
Notes: The single stuck-at fault (SSF, also referred to as classical or standard) model is the earliest and still the most common fault model. A single node in the circuit is assumed to have taken a fixed logic value of 0 or 1. It typically represents a direct connection between a node and power (for stuck-at 1) or ground (for stuck-at 0). The stuck-at fault model has many advantages:
the model is applied at the gate level, and thus the number of SSFs (2n in an n-line circuit) is tractable,
it can be used to represent a wide variety of different physical failures,
it remains independent of technology – it can be applied to any structural model and to model other faults,
there are many experimental evidences showing that tests detecting SSFs detect many non-classical faults.
Although new fault types continue to become more common, and high stuck-at coverage is not enough to guarantee high quality, the single stuck-at fault model will most likely remain dominant as a baseline needed in virtually all designs

## Slide 11: Single vs. multiple faults
There are 3n – 1 possible multiple stuck-at faults (MSFs)
In an irredundant two-level circuit, any complete test set for SSFs also detects all MSFs1
In a fanout-free circuit any complete test set for SSFs detects all double and triple faults, and there exists a complete test set for SSFs detecting all MSFs2
A test set detecting all MSFs defined on all primary inputs without fanout and all branches detects all multiple faults3
1) I. Kohavi, Z. Kohavi, IEEE Trans. Computers, 1972 2) J. Hayes, IEEE Trans. Computers, 1971
3) D.C. Bosen, S.J. Hong, IEEE Trans. Computers, 1971
Notes: The multiple stuck-at fault (MSF) model is a simple extension of the SSF model. Let n be the number of possible SSF sites. Then there are 3n – 1 possible multiple stuck-at faults (each line can be in one of three states: s-a-0, s-a-1, or fault-free – all combinations except one having all lines in the fault-free state are counted as faults). This number is usually too large to handle all multiple faults explicitly. Nevertheless, there are several results obtained as a response to the following question: how many multiple faults can be detected by a complete test set designed for single stuck-at faults? The slide summarizes some of the most important observations derived for combinational circuits. Still, the MSF model is mainly of theoretical interest, unless circuits are used in extremely high-reliability applications. Although the MSF model is more realistic than the SSF model, the use of the latter is justified since fault masking conditions that cause multiple faults to escape detection when using complete test sets for SSFs are seldom encountered in practice.

## Slide 12: Bridging faults
Input BF – a short among two or more inputs of a gate
Non-input shorts
Feedback BF – a feedback path created due to a fault (can cause oscillations or introduce memory)
Non-feedback BFs
Input BF may be of a feedback type (see figure)
Notes: This fault model assumes that circuit nodes are permitted to be shorted to one another. Bridging faults (BF) have been found to be the most common defect type in CMOS circuits. The number of bridging faults in a circuit with n lines (or nodes) is on the order of n2. Thus, for large circuits, only a subset of bridging faults can be considered in practice during test generation. In order to limit the number of target bridging faults, a set of realistic bridging faults is selected based on layout information. This selection identifies faults that are most likely to occur taking into account that physical defects are more likely to bridge two lines if the lines are closer to each other. There are several types of bridging faults. A short can be confined to two or more inputs of the same gate. This fault is called an input BF. Other types of bridges belong to the category of non-input BF (or shorts). A bridging fault may create a feedback in the circuit, thus converting a combinational circuit into a sequential one. Such a feedback BF changes the circuit behavior and may also cause oscillations. Even worse, an input BF may act as a feedback BF at the same time, as shown on the slide.

## Slide 13: Modeling of bridging faults
L1
L2
L1’
L2’
AND model
OR model
Bridging faults replaced by stuck-at faults
s-a-0
L1
L2
L1’
L2’
C
s-a-1
L1
L2
L1’
L2’
C
Notes: If two signals are shorted together, then it is not trivial to decide what it means in terms of circuit behavior. One of the models postulates that the additional connection would form an implicit logic gate, such as an AND or OR (in fact, some logic processes behave this way in practice). Such a behavior can be conveniently modeled by means of “implicit” stuck-at faults placed as shown on the slide. Consider, for example, the AND model. The original circuit (just two wires) is conceptually replaced by four fault-free gates, as illustrated above. Now, if there is no short, then we put 1 on the control line C, and the entire circuit behaves exactly as two separate wires. In order to inject a bridging fault, we use a stuck-at-0 fault of the control line. With this fault in place, both outputs (L1’ and L2’) receive signals being equal to L1L2. In a similar manner we can mimic an OR-type bridging fault. Unfortunately, CMOS circuits may not behave this way. In many cases, CMOS bridge behavior is simple: a wire driven by large powerful transistors will always overpower one driven by smaller transistors.

## Slide 14: Bridging faults
Similar strengths
“Byzantine Generals” behaviour
Bridged line is interpreted differently by different downstream logic gates with different gate thresholds
0
1
0
0/1
0/1
1/0
?
?
Notes: When strengths of transistors are similar, the result is less clear. It may resemble so-called “Byzantine Generals” behavior (see the slide), where a bridged line is interpreted differently by different downstream logic gates with different gate thresholds. A short in a CMOS circuit results in an intermediate voltage level (somewhere between supply and ground) often interpreted as a 0 by one gate and a 1 by another.

## Slide 15: CMOS stuck-open fault
NOR gate
P1
P2
N2
N1
00
01
10
11
An exhaustive test fails to detect the fault if applied in the following order:
0 1 0 1
0 0 1 1
1 0 0 0
Z is floating and retains the previous state
G.R. Case, Proc. DAC, 1976
R.L. Wadsack, Bell System Technical Journal, 1978
A
B
Z
Notes: The best-known open model is the stuck-open fault, introduced by Case, and then Wadsack. In this model, the gate to a given transistor is fixed at the “open” or off value. As a result, the transistor will be unable to pull the cell output to its voltage. Consider the NOR gate shown on the slide. If the N2 transistor connected to input B is permanently off, then when input B is 1, the output Y will remain unchanged. If A had been 1 for the previous vector, then the output will be correct (logic 0). A stuck-open fault requires a two-pattern test. The first sets up the fault by pulling the circuit output to a known value (applying AB = 00 sets the output to logic 1). The second pattern activates the fault (applying B = 1 will not cause Y to change, hence a 1 will be observed rather than the expected 0). Note that a wrong order of patterns may cause even an exhaustive test set to miss this stuck-open fault. Despite its attractiveness, the stuck-open model has not been found to be representative of many actual CMOS defects.

## Slide 16: CMOS stuck-short fault
NOR gate
P1
P2
N2
N1
10
10
01
0(1,0)
Both the N and P parts may conduct
Increased quiescent current
The voltage on the output depends on the ratio of resistances
A
B
Y
Notes: The same NOR gate as on the previous slide may witness a short affecting, for example, transistor N2, as shown on this slide. In this particular case, however, when applying patters AB = 11 and then AB = 00, both the N and P parts may conduct causing increased quiescent current (this is called IDDQ fault, and will get back to this type of defects on the subsequent slides). This current is usually several orders of magnitude larger than the normal quiescent current of a CMOS circuit. Thus, a measurement of the device current will detect the fault. The voltage on the output depends on the ratio of resistances. This type of defect is also known as a stuck-short fault, and it belongs conceptually to the class of bridging faults discussed earlier.

## Slide 17: Transition faults
Slow-to-rise (0 to 1) transition
  requires a pair of vectors (v1, v2) to detect it
  v1 sets the line to 0
  v2 tests the line for stuck-at-0 fault (applies 1 forcing a transition and making it observable on an output)
Slow-to-fall (1 to 0) transition
  requires a pair of vectors (v1, v2) to detect it
  v1 sets the line to 1
  v2 tests the line for stuck-at-1 fault (applies 0 forcing a transition and making it observable on an output)
Cover CMOS stuck-open faults and “gross delay faults”
Some combinations of small delays are not covered
Notes:   Not all defects alter circuit behavior the way the stuck-at fault model does. With the increasing speed of integrated circuits, violations of the performance specifications are becoming a major factor affecting the product quality. There are failures causing incorrect operation only at certain frequencies. In particular, one can distinguish two types of transition faults associated with a gate: a slow-to-rise fault (i.e., a slow 0 to 1 transition on the output of the gate) and a slow-to-fall fault (i.e., a slow 1 to 0 transition on the output of the gate). To detect a transition fault in a combinational circuit it is necessary to apply two input vectors (v1, v2). The first vector, v1, initializes the circuit, while the second vector, v2, activates the fault and propagates its effect to some primary output. Vector v2 can be found using stuck-at fault test generation methods. For example, for testing a slow-to-rise transition, the first vector sets the line to 0, and the second vector tests the line for stuck-at-0 fault (applies 1 forcing a transition and making it observable on an output). A transition fault is considered detected if a transition occurs at the fault site and a sensitized path extends from the fault site to some primary output.
  The transition fault model covers “gross delay faults” – see the next slide. However, unlike the gate delay fault model presented next, it does assume that the increased delay will affect the performance independent of the propagation path through the fault site.

## Slide 18: Delay faults
Gate delay fault – input or output of a gate has a slow 0 to 1 or 1 to 0 transition
  gross gate delay – greater than the system clock period
  small gate delay
Path delay fault – a path whose propagation delay exceeds the specified worst case delay has this fault
  captures distributed delays
  covers transition, gate delay, multiple stuck-at faults
  large number of paths to analyze
Notes:   The more general type of timing-related faults is known as a delay fault model, and it is further partitioned into two groups (or classes): gate delay faults, which model defects local to individual circuit components, and path delay faults, which model defects resulting from parametric shifts across larger portions of the circuit. A gate delay fault occurs when a gate operates slower than expected. One may assume that the extra delay caused by the fault is large enough to prevent the transition from reaching any primary output at the time of observation. Thus, such a delay fault can be observed independently of whether the transition propagates through a long or a short path to any primary output. This model is referred to as the gross-delay fault model. On the other hand, a path delay fault assumes that a logic transition is delayed along the entire path. It is worth noting that even small tolerable gate or interconnect delays (each one not large enough to cause a defective behavior) may contribute to an unacceptable path delay fault due to accumulative nature of delays. The path delay fault model captures distributed delays and covers transition, gate delay, and multiple stuck-at faults. In fact, nowadays the interconnect delays along a path dominate the overall delay. Clearly, a major problem with this particular approach is the number of possible propagation paths a test generation system must analyze.

## Slide 19: IDDQ faults
Quiescent state – CMOS just draws leakage current
Faults detected by quiescent supply current (IDDQ) monitoring
Abnormally high current indicates a defect
VDD
0,1
0,0
1,0
T1
T2
T3
failure
time
IDDQ
Vin
Vout
Notes: IDDQ testing is a peculiar method of testing CMOS circuits. It relies on measuring the supply current (IDD) in the quiescent state (when the circuit is not switching, and inputs are held at static values). The current consumed in this state is commonly called IDDQ for IDD (quiescent). IDDQ testing uses the principle that in a correctly operating quiescent CMOS digital circuits there is no static current path between the power supply and ground, except for a small amount of leakage. Many common manufacturing faults will cause the current to increase by orders of magnitude, which can be easily detected. This has the advantage of checking the chip for many possible faults with one measurement. Another advantage is that it may catch faults that are not found by conventional stuck-at tests. IDDQ testing is somewhat more complex than just measuring the supply current. If a line is shorted to VDD, for example, it will still draw no extra current if the gate driving the signal is attempting to set it to 1. However, a different vector set that attempts to set the signal to 0 will show a large increase in quiescent current, signaling a bad part. Typical IDDQ test vector sets may have 20 or so vectors. Note that IDDQ test vectors require only controllability, and not observability, as the latter is achieved through the shared power supply connection.

## Slide 20: IDDQ tests
Advantages
  cover most bridging faults
  cover some open faults
  higher defect coverage than stuck-at tests
  easy to write CAD tools reliability benefits
Disadvantages
  circuit must be designed with low IDDQ
  long test application time
  some open and timing faults escape IDDQ tests
  current threshold has to be empirically established
Notes: IDDQ testing has many advantages. It is a simple and direct test that can identify physical defects. The area and design time overhead are very low. Test generation is fast. Test application time is fast since the vector sets are small. It catches some defects that other tests, particularly stuck-at logic tests, do not. Compared to other testing scenarios, however, IDDQ testing is time consuming, and then more expensive, since is achieved by current measurements that take much more time than reading digital pins in mass production.
As integrated circuits shrink, the leakage current becomes much higher and less predictable. This makes it difficult to differentiate a low leakage part with a defect from a naturally high leakage part. Also, increasing circuit size means a single fault will have a lower percentage effect, making it harder for the test to detect.

## Slide 21: Cell-aware fault model
Gate level abstraction & stuck-at fault model no longer sufficient to ensure high quality & low DPM
Cell-aware test generation targets undetected internal faults based on actual cell layout
D0
D1
D2
S0
S1
Z
Z
D2
S1
D0
S0
D1
vdd
gnd
Standard ATPG view
Cell-aware ATPG view
F. Hapke, et al., IEEE Transactions on CAD, Sept. 2014
Notes: Although transistor-level ATPG has been performed for some time, this approaches has quickly turned inept when applied to multimillion transistor designs. As a result, a new cell-aware fault model has been proposed. This model is based on a post-layout transistor-level net-list, including parasitic objects, resulting into a defect-based ATPG approach, which can be applied to large, state-of-the-art designs. The cell-aware test (CAT) methodology consists of two major parts. The first part is the technology-dependent CAT view generation flow, which is a one-time task that is performed once for each technology library. The flow is a combination of traditional functions/tools and new functions and algorithms that were developed for the CAT approach. The flow starts with layout extraction, followed by an analog fault simulation, and fault model synthesis to create the CAT library models. The second major part is a design flow, where a CAT ATPG is used instead of a traditional test generation. The CAT-ATPG is a defect-based test pattern generation that uses the technology-dependent and transistor-level-based CAT view to
generate high-quality test patterns to significantly reduce the defect level of delivered ICs. The CAT-ATPG is able to generate patterns for very large multimillion gate designs. Many experimental results show a significant increase of the defect coverage and as such a significant reduction of the defect rate measured in DPPM.

## Slide 22: Cell-aware tests
In wafer-sort test insertion, CAT patterns detected 10.5% unique CA static fails and 21% unique CA delay fails
Total CA fails = 100%
Total 23.7%
Total 84.2%
0%
5.3%
55.3%
7.9%
10.5%
21.0%
0%
IDDQ & other tests
Cell-aware static
Cell-aware delay
Notes: This Venn diagram illustrates how cell-aware tests can improve test quality beyond what is achievable with conventional fault models and test pattern generation techniques. The results have been obtained on a test floor of one of silicon manufactures.

## Slide 23: Cell-aware diagnosis
Diagnose to physical locations inside the cell
  works for all pattern types
Leverages cell-aware fault model
  Spice model extracted from layout
  internal defects mapped to input excitation conditions
Diagnosis flow identical to traditional layout-aware diagnosis
  Results show on average 22x resolution improvement
Notes: The CAT approach allows one to perform an efficient fault diagnosis. The first step of this process extracts a SPICE transistor-level net-list, which includes all transistors, all parasitic elements (resistors and capacitors), and all layout properties such as layer information and Cartesian coordinates. The next step performs an analog diagnosis fault simulation for all extracted defects. The stimuli used for this fault simulation are just the failing and passing cell input conditions that have been retrieved from the traditional gate level-based electrical diagnosis run. This step is different from the analog simulations where an exhaustive set of stimuli is used. For diagnosis, a subset of stimuli is deployed that is actually used in the test pattern set of the cell instance that was called out to be suspect. Subsequently, CA defect scoring is carried out. It calculates the probability that a specific defect is a root cause of the faulty behavior. Finally, one creates a layout marker file such that a design viewer can be used to highlight the defects.

## Slide 24: Example of faults
Input vector detects a fault if the response of the fault-free circuit and the faulty one are different
Faults that are detected by exactly the same input vectors are equivalent
Only one representative fault per class must be explicitly considered in test generation and fault simulation
a
b
c
x
y
h
x y h a0 b0 c0 a1 b1 c1
0 0 0 0 0 0 0 0 1
0 1 0 0 0 0 1 0 1
1 0 0 0 0 0 0 1 1
1 1 1 0 0 0 1 1 1
Notes: Let us now consider a simple circuit (in fact, a single 2-input AND gate) whose truth table is shown on the slide altogether with all output combinations caused by six possible single stuck-at faults affecting both inputs and the output. Clearly, an input vector detects a fault if the response of the fault-free circuit and the faulty one are different (we will be discussing this primary definition of a test vector in the next chapter in a more detail). As can be easily verified, faults a0 (line a stuck-at-0), b0 and c0 are detected by the input vector xy = 11. On the other hand faults a1 and b1 are detected by vectors 01 and 10, respectively. Finally, fault c1 can be detected by one of the following input patterns: 00, 01, or 10. It is worth noting that faults detected by exactly the same input vectors are equivalent. In our case, it applies to faults a0, b0 and c0 as all of them are detected by the same test patterns (here, just a single vector 11). The fault equivalency is one of the key properties used in test generation (and fault simulation) to reduce processing time as only selected faults need to be considered, as discussed on the next slides.

## Slide 25: Functionally equivalent faults
Let hu(x) be a faulty circuit version with fault u
Faults u and v are functionally equivalent iff hu(x) = hv(x); faulty versions have identical input-output behavior
Faults u and v are distinguishable if there is at least one test t such that hu(t) ≠ hv(t)
It suffices to consider only one representative fault from every equivalence class
n-input gate: there are 2(n+1) single stuck-at faults; n+2 faults need to be analyzed – stuck-at controlling value faults on inputs and the output are equivalent
Notes: If hu(x) is a faulty circuit version of h(x) with fault u being present, then two faults u and v are functionally equivalent if and only if hu(x) = hv(x), that is both faulty versions of h(x) have identical input-output behavior. The relation of functional equivalence partitions the set of all possible faults into functional equivalence classes. Consequently, it suffices to consider only one representative fault from every equivalence class. Although faults u and v above are not restricted to the same fault domain (u can be a bridging fault while v a stuck-at fault, or vice versa), we typically limit the analysis of equivalence relations to those among faults of the same type.
With any n-input gate we can associate 2(n+1) single stuck-at faults. For NAND gate all the input s-a-0 faults and the output s-a-1 are functionally equivalent (compare the previous slide). In general, for a gate with controlling value c and inversion i, all the input s-a-c faults and output s-a-(c  i) are functionally equivalent. Thus, for an n-input gate we need to consider only n+2 single stuck-at faults. This type of reduction of the fault list based on equivalence relations is referred to as equivalence fault collapsing or briefly fault collapsing.

## Slide 26: Functional equivalence
Functional equivalence usually cannot be directly applied because of complex, NP-complete, global analysis
No simple way to determine if the above faults are functionally equivalent
s-a-0
s-a-1
s-a-0
s-a-0
s-a-1
s-a-1
s-a-1
s-a-0
s-a-1
s-a-1
Equivalent?
Notes: Despite its very simple definition, functional fault equivalence is difficult to use in practice due to complex and time consuming global analysis of a circuit and the associated fault list. In fact, even to determine if two arbitrary faults are functionally equivalent is an NP-complete problem. For example, there is no simple way to decide whether faults shown on the slide are functionally equivalent. It could be done by computing the two faulty functions and showing that they are identical. This approach is clearly unfeasible for larger designs. The remedy to this problem is to determine groups of faults that are related in a structural fashion, as shown on the next slide.

## Slide 27: Structural equivalence
One can determine equivalent faults which are structurally related – structural equivalence
In the circuit Nu, the presence of the stuck-at fault u creates a set of lines with constant values
Removing all these lines (except primary outputs) gives a simplified circuit S(Nu), which realizes the same function as Nu
Two faults u and v are structurally equivalent if the corresponding simplified circuits S(Nu) and S(Nv) are identical
Notes: The structural equivalence is defined as follows. Let Nu represent a circuit N with the stuck-at fault u. The presence of this fault creates a set of lines with constant values. Removing all these lines (except primary outputs) gives a simplified circuit S(Nu), which realizes the same function as Nu. Two faults u and v are structurally equivalent if the corresponding simplified circuits S(Nu) and S(Nv) are identical. The next slide illustrates an example of such analysis.

## Slide 28: Example

Structurally equivalent faults are also functionally equivalent
Structural equivalence allows fault collapsing as a simple local analysis based on the circuit structure
0
s-a-0
s-a-1
0
Notes: Consider a circuit shown on the slide and two stuck-at faults marked with the bold red lines. The stuck-at-1 fault causes the output of the inverter to be permanently equal to 0. Hence the output of the AND gate is always 0, as well. That allows us to remove both the inverter and the AND gate, which yields a simplified circuit as shown on the left hand side of the slide. Clearly, one can arrive with the same sub-circuit when analyzing the stuck-at-0 fault. As a result, these two faults can be declared structurally equivalent. Obviously, structurally equivalent faults are also functionally equivalent. But not necessarily vice-versa. Consider again a circuit shown two slides earlier. The two stuck-at-1 faults presented there are functionally equivalent, but they are not structurally equivalent. This is due to the presence of reconvergent fan-outs. The advantage of structural equivalence relations is that they allow fault collapsing as a simple local analysis based on the circuit structure.

## Slide 29: Fault collapsing
Insert s-a-0 and s-a-1 faults on every signal source (gate output or primary input) and destination (gate input)
Traverse the circuit and construct structural equivalence classes
For a signal line with a fanout 1, the faults inserted at its source are structurally equivalent to the corresponding faults at its destination
For a gate with controlling value c and inversion i, any s-a-c input fault is structurally equivalent to the output s-a-(c  i)
From every equivalence class we retain one fault
Structural equivalence class determined in this way is confined to a fanout-free region of the circuit
A stem fault is not functionally equivalent with any of its fanout branches
Notes: This slide basically recapitulates the key steps of a fault collapsing process that is based on the structural equivalence relations. We begin by inserting s-a-0 and s-a-1 faults on every signal source (gate output or primary input) and destination (gate input). Then we traverse the circuit and construct structural equivalence classes along the way. For a signal line with a fan-out 1, the faults inserted at its source are structurally equivalent to the corresponding faults at its destination. Recall that for a gate with controlling value c and inversion i, any s-a-c input fault is structurally equivalent to the output s-a-(c  i). At the end, we retain one fault from every equivalence class. It is worth noting that a structural equivalence class determined in this way is confined to a fan-out-free region(FFR) of the circuit. This is because a stem fault is not functionally equivalent with any of its fan-out branches (though reconvergent fan-out may lead to structurally equivalent faults in different fan-out free regions). The equivalence classes obtained by using the approach presented here may not be the maximal ones. Still, this process achieves a substantial reduction of the initial fault list – typically around 50%. The next slide illustrates this phenomenon.
Note that the smallest FFR can be a single gate, hence collapsing the faults at a gate is the default methodology to create a short fault list in practice. Any fault collapsing beyond that is usually avoided due to computation time of the equivalence classes vs. simulation time of a pattern marking all equivalent faults.

## Slide 30: Structural fault collapsing
s-a-0
s-a-1
Fault collapsing reduces the set of faults by about 50%
Notes: Here, blue and red dots denote stuck-at-0 and stuck-at-1 faults, respectively. Initially, as indicated by the algorithm, s-a-0 and s-a-1 faults are put on every signal source (gate output or primary input) and destination (gate input). The subsequent animation steps illustrate which faults can be removed from the list since they structurally equivalent to others. In particular, we delete replicas of faults occurring on the same line. Next, we remove input faults of the inverter as they structurally equivalent to the (inverted) output faults of the same gate. Finally, we use the rules that govern the fault equivalency relations with respect to the inputs and the output of a single multiple-input gate. The result is shown at the bottom of the slide. As can be easily verified, once needs to consider only 10 out of initial 26 faults.

## Slide 31: Limitations of local analysis
Confined to fanout-free circuits as the analysis is limited to equivalences between single faults
A fault on stem is equivalent to a multiple fault of the fanout branches
s-a-1
s-a-0
Notes: Recall that the presented fault collapsing technique is confined to fan-out-free circuits as the analysis is limited to equivalences between single faults. Thus, the method will not identify faults such those shown on the slide as structurally equivalent. In fact, a fault on stem (not shown here) is equivalent to a multiple fault of the fan-out branches.

## Slide 32: Fanout-free circuits
In a fanout-free circuit, any test set that detects all SSFs on the primary inputs detects all SSFs
1
1
1 - 0
1 - 0
0 - 1
0 - 1
0
0
1
1
1
s-a-1
s-a-0
s-a-1
s-a-0
Notes: Further reduction of fault lists can be achieved by using the concept of dominance fault collapsing. First of all, it can be easily verified that in a fan-out-free circuit, any test set that detects all SSFs on the primary inputs detects all SSFs. To prove this property, let us assume, by contradiction, that a test set T detects all SSFs on primary inputs, but it does not detect internal SSFs. Clearly, it suffices to consider faults on the gate outputs as the whole circuit has a tree-like structure. In such a circuit, there must be a gate G such that T detects all faults on its inputs but (in accordance to our assumption) it does not detect a fault, say h, on its output. Let G be an AND gate. Then h cannot be s-a-0 fault since it is equivalent to any input s-a-0 fault (and thus is detectable). Similarly, h cannot be s-a-1, since such a fault dominates any input s-a-1 (and again is detectable as we detect all input s-a-1 faults). Consequently, there is no fault like h. Similar arguments can be used to prove that there are no undetectable faults on the outputs of OR, NAND or NOR gates. Hence, all internal faults in a tree-like circuit are detected.

## Slide 33: Fault dominance
A fault f is said to dominate another fault g if all tests for the second fault (g) detect the first fault (f); in other words, if f dominates g, then any test t that detects g will also detect f (on the same primary outputs)
It suffices to consider only the dominated faults, like g
If we fail to generate a test to detect g, there is no guarantee that f is covered since it is not represented directly
Th
Tg
g  s-a-1
h  s-a-0
Tg = 10 detects also h
Notes: Let Tg be the set of all tests that detect a fault g. If fault f dominates fault g, then any test t that detects g will also detect f (on the same primary outputs). Consequently, it suffices to consider only the dominated faults, like g. One has to remember, however, that if we fail to generate a test to detect g, there is no guarantee that f is covered since it is not represented directly. Consider, as an example, the NAND gate shown on the slide. Let g be a stuck-at-1 fault and h be a stuck-at-0 fault, as figure indicates. A test set Tg consists of only a single pattern, i.e., 10. Clearly, the same pattern can detect fault h, though there are other patterns (01, 00) with the same ability. As can be seen, Th includes Tg, and thus fault h dominates fault g. Therefore, it is unnecessary to consider the dominating fault h, since deriving a test to detect the dominated fault g ensures that both faults are detected. This simple relation can also be used to reduce the fault list size in the process of fault collapsing.

## Slide 34: Checkpoints
In a combinational circuit any test set that detects all SSFs on the primary inputs and the fanout branches (checkpoints), detects all SSFs
24 stuck-at faults
14 checkpoint faults
10 faults in the reduced set of faults
dominance
s-a-0
s-a-1
Notes: There is another interesting relationship between faults occurring in combinational circuits. It states that any test set that detects all SSFs on the primary inputs and the fan-out branches detects all SSFs. This particular fault sites are referred to as checkpoints. This is yet another basis for fault collapsing. The number c of checkpoints is given by I + (G + I)(f – q), where I is the number of primary inputs, G is the number of gates, f is the average fan-out size, and q is a compensation factor for those gate outputs whose f = 1 (for each individual gate g, qg = 1 if fan-out of g is 1, and qg = 0, otherwise). Since the number of fan-out branches is typically much larger than the number of primary inputs, the number of checkpoints can be approximated by (G + I)(f – q), and the fraction of eliminated faults (recall that we begin with 2n stuck-at faults) is equal to 1 – (2c/2n) = 1 – (f – q)/(1 + f – q) = 1/(1 + f – q).
The example animation shown on the slide begins with all checkpoint stuck-at faults (14 faults out of 24 possible in total). Then, we can easily identify two pairs of structurally equivalent faults (black dotted lines), and eventually two additional faults can be eliminated based on the fault dominance principle. For example, the stuck-at-1 fault on the input of the NOR gate is equivalent to a stuck-at-1 fault on the other input of the same gate (this fault is illustrated as a yellow dot), which dominates the stuck-at-1 fault on the input of the AND gate. The same rule applies to another stuck-at-1 fault on the input of the OR gate. The reduced fault list consists now of 10 faults only.

## Slide 35: Functional faults
Based entirely on the functional description like architecture and the instruction set; they include
  register decoding
  instruction decoding
  data storage
  data transfer
  data multiplication
There are reported functional tests generated for a 8-bit microprocessor that detected 96% of single stuck-at faults
Notes: Functional (behavioral) faults are defined in conjunction with a functional model of a circuit. For example, the effect of a functional fault may be to change the truth table of a component or to inhibit an RTL operation. When the behavior of a circuit is described in computer-readable form such as a hardware description language that resembles a programming language, then at the functional (behavioral) level the variables or operations are not necessarily electrical, but correspond to the specific application domain. Functional faults refer to incorrect execution of the language constructs used in the description. Examples of such faults include assertion faults, branch faults, register and instruction decoding faults, data transfer and manipulation faults, and so on. At the functional level, software test metrics such as statement coverage, branch coverage, and toggle coverage are also used though they do not conform to any specific fault model. There is always an interesting question regarding a structural fault coverage that can be delivered by means of tests developed for functional faults. The experimental results vary widely, but there are reported microprocessor test programs generated exclusively with the help of functional fault models that detect 96% of single stuck-at faults.

## Slide 36: Inductive fault analysis
A systematic approach to generate all the faults that are likely to occur in a specific IC using the technology and layout information
Four levels of abstraction
  process – e.g., pinhole in the SiO2 can be viewed as an open region in the SiO2 layer
  structure – e.g., contacts between layers
  circuit – e.g., short between two wires
  logic – e.g., stuck-at-1 fault
J.P. Shen, W. Maly, F.J. Ferguson, IEEE Design & Test, 1985
Notes:   Inductive Fault Analysis (IFA) was one of the first systematic procedures to predict all the faults that are likely to occur in MOS integrated circuits. It has been developed to arrive with accurate and realistic fault models that may represent defects that actually show up in circuits manufactured using a given fabrication process. It takes into account the technology and defect statistics in addition to the layout. IFA works with four levels of abstraction that comprise:
  a process level – e.g., pinhole in the SiO2 can be viewed as an open region in the SiO2 layer,
  a structure level – e.g., contacts between layers,
  a circuit level – e.g., short between two wires, and
  a logic level – e.g., stuck-at faults.

## Slide 37: Three major steps
Defect generation and analysis
  given an IC layout, spot defects are generated using statistical information about the process
  defects are screened for size, location, and electrical significance
Defect-to-fault translation
  every significant defect is analyzed and the circuit-level faulty behavior caused by the defect is extracted
  the extracted faulty behaviors constitute the primitive fault list
Fault classification and ranking
  the circuit faults are grouped and classified into fault types
  the relative likelihood of occurrence of each fault from the list is estimated to produce a ranked fault list
Notes: The three major steps of the IFA procedure are:
generation of physical defects using statistical data from the fabrication process,
extraction of circuit-level faults caused by these defects, and
classification of faults types and ranking of faults based on their likelihood of occurrence.
Hence, given the layout of an IC, a fault model and a ranked fault list can be automatically generated which take into account the technology, layout, and process characteristics. IFA assumes that spot or point defects are present in the chip. The density of such defects per unit area and the probability density function of the defect size are based on data obtained from actual experiments. Only single point defects are considered and these defects are generated randomly based on the above defect characterization. The shape of defects is assumed to be round or square.

## Slide 38: Primitive fault types
A single point defect (a region of extra or missing material) in a particular layer introduces a faulty behavior that belongs to a set of primitive fault types
Four categories
  shorts between two or more equipotential regions
  breaks which results in the separation of one equipotential regions into two or more regions
  introduction of a new device, unspecified in the original circuit description
  changes in the behavior of existing devices in the circuit
Types of circuit faults: line stuck-at, transistor stuck-at, floating line, bridging, miscellaneous
Notes: The point defect implies that the corresponding region either has extra material or missing material. Because a circuit is designed with purpose, its layers are meaningfully shaped and stacked. Hence, given a single point defect in a particular layer, only a limited number of possible fault types can result. This number is determined by the number of ways the topological adjacency relationships between nearby regions can be changed by the introduction of a physical defect. These changes, or manifestations of defects, are called primitive fault types. In examining the primitive fault types, one can see that typically a defect affects either the connectivity between active devices, the devices themselves, or both. Hence, primitive fault types can be loosely grouped into the following four categories:
shorts between two or more equipotential regions,
breaks which result in the separation of a single equipotential region into two or more regions,
introduction of new (that is, unspecified in the good circuit description) devices to the circuit, and
changes in the behavior of existing devices in the circuit.
In the fault extraction procedure, defects are first translated to primitive faults and then primitive faults are interpreted, in the electrical sense, to produce the circuit faults. Circuit faults are described in terms of electrical circuit and, possibly, logic circuit properties; whereas, descriptions of primitive faults can involve both structure-level and circuit-level information. Hence, primitive faults function as a bridge between defects at the process and structure levels and faults at the circuit and logical levels. By examining the primitive faults and interpreting their effects at the circuit and logical levels, an informal and useful classification of circuit faults can be produced. Keeping the classification simple, five types of circuit faults can be identified, as shown on the slide.

## Slide 39: Example of IFA application
Circuit: NMOS full adder (29 transistors)
Defects generated: 400 for each of the 12 defect types
Significance screening: 65% (or 3118 defects) removed due to the size, location, or electrical insignificance
Many of the remaining 1682 defects showed only minimal parametric degradation
Only 476 defects (10% of the total) produce faulty behavior at the circuit level with the following breakdown:
line stuck-at | 28%
transistor stuck-at | 15%
floating lines | 21%
bridges | 30%
miscellaneous | 6%
Notes: The slide shows an example of IFA application to an NMOS full adder. 400 defects were generated for each of the 12 defect types, for a total of 4800 defects processed. Approximately 65 percent, or 3118 defects, were removed by the size, location and electrical significance screening process. The remaining 1682 defects were interpreted and translated. Many of theme only degrade the AC performance of the circuit without changing the DC characteristics. Hence, of the original 4800 defects, only 476 (10%) actually produce significant faulty behaviors at the circuit level.
The results from this sample led to some interesting observations regarding non-classical faults. Only 28 percent of the faults, the line stuck-at faults, can be explicitly modeled by the classical line stuck-at fault model. This 28 percent includes both single and multiple line stuck-at faults. Less than 23 percent of the faults are actual single line stuck-at faults. Most of the transistor stuck-at faults can be implicitly modeled by the classical line stuck-at fault model. This can also be said of the floating line faults, although some floating lines may not stay in one logical state. Including the line stuck-at (28 percent), the transistor stuck-at (15 percent) and the floating line (21 percent) faults, at best, the classical fault model can only account for 64 percent of the faults. It should be noted, however, that this only illustrates the weakness of the classical fault model and not necessarily the weakness of test sets generated using such fault models. The same results seem to indicate that stuck-open faults only constitute a small percentage of the faults less than three percent, in the example). Although the example circuit is an NMOS circuit, there are not many reasons for a CMOS circuit to be different. The most prominent fault type is the bridging fault (30 percent). Many of the observed bridging faults were induced by extra polysilicon and can lead to sequential behavior.

## Slide 40: Empirical failure analysis
Four steps
  design and fabrication of a test chip that capture characteristics of CAD tools, cell libraries, and fabrication process
  derivation of a robust test set
  development of tools to perform automated diagnosis
  validation of results using an electron-beam voltage-contrast circuit prober
Test set
  complete for all multiple stuck-at, stuck-open, & transition faults
  significant coverage of bridging faults
  all faults covered at least twice under different conditions
A. Pancholy, J. Rajski, L.J. McNaughton, IEEE Design & Test, 1992
Notes: While inductive fault analysis addresses the process of deriving ranked fault lists. it has limited use in determining the effectiveness of existing fault models and the quality of test sets developed under different fault model assumptions. Empirical failure analysis offers a method that can be used to validate fault models. It has four key elements:
the design and fabrication of an “easily diagnosable” test chip, representative of the class of circuits being studied, the CAD tools used in its design, and the process used for its fabrication,
the derivation of an extremely robust test set, capable of detecting faults from a variety of different fault models,
the development of tools to perform automated diagnosis on faulty circuits, and their use to get measures of “effectiveness” of the fault models considered,
the validation of the results of the diagnosis using an electron-beam voltage contrast circuit prober.
Test chip. The basic philosophy behind design of the test chip is to make the structure easy to diagnose while keeping it representative of a realistic random logic environment. The parameters influencing the “realism” of the circuit include its size, its functional capability, the selection of standard cells used, their packing density, the number of I/O pins, and the internal fan-outs. Finally, a test set provides a complete coverage for all multiple stuck-at, stuck-open, and transition faults, as well a significant coverage of bridging faults. Moreover, all faults are covered at least twice under different conditions.

## Slide 41: Results of analysis
20.8% of faulty blocks (202 out of 970) have no diagnosed stuck-at faults, i.e., no faults exist in these blocks consistent with the single stuck-at fault model
28.9% of faulty blocks have exactly one suspected stuck-at fault, while another 31.9% have between 2 and 5 (both inclusive)
6.9% of all faulty blocks were diagnosed as containing transition faults only, i.e., 13.9% of all faulty blocks could not be diagnosed on the basis of the transition and single stuck-at fault models
Notes: Test chips were designed and fabricated as described earlier using a CMOS 1.5-micron, double-layer metal process. The automated diagnosis of 970 faulty blocks has distinguished two groups of results obtained for stuck-at faults and for transition faults, respectively. As for stuck-at faults, a relatively large number (202 out of 970, or 20.8%) of faulty blocks had no diagnosed stuck-at faults, i.e., no faults existed on any of these faulty blocks consistent with the single stuck-at fault model. The remaining 79.2% of faulty blocks had at least one suspected stuck-at fault, even though they may contain un-modeled faults in addition to the diagnosed stuck-at faults. Also, 28.9% of faulty blocks had exactly one suspected stuck-at fault, while another 31.9% had between two and five (both inclusive) diagnosed stuck-at faults. The number of faulty blocks with a larger number of diagnosed faults was lower with only 18.4% having between six and 30 (both inclusive) faults. No blocks with over 30 stuck-at faults were diagnosed.
The results show that the single stuck-at fault model is clearly inadequate in terms of defect modeling because a large number of faulty circuits (20.8% of all faulty blocks) existed in which no stuck-at faults could be diagnosed. It is of more interest, however, to get a measure of the defect level of a test set designed to cover all single stuck-at faults. This depends not only on the adequacy of the fault model (here – single stuck-at faults) but also on the tools used to generate the test set. The sequence and redundancy of the test set tend to affect its windfall coverage of other faults. In the experiment, the failing vectors were deleted for each faulty block tested with the extended test set from the (extended) test set to generate a modified test set containing only vectors that passed. Faults in the block in question were then simulated with the modified test set. It appears that for 132 (or 65.3%) of the 202 faulty blocks for which no single or multiple fault(s) could be diagnosed, the modified test sets still provided 100% coverage of single stuck-at faults. In other words, for 13.58% of all faulty blocks (20.8% x 65.3%) test sets could be devised to provide complete coverage of single stuck-at faults and still not detect their faulty behavior.
Transition fault analysis. Transition faults were diagnosed on all faulty blocks out of the original 970. The results revealed that in addition to the 79.2% of all faulty blocks that contained at least one stuck-at fault, 6.9% of all faulty blocks were diagnosed as containing transition faults only. Hence, 13.9% of all faulty blocks could not be diagnosed on the basis of the transition and single stuck-at fault models.