## Slide 1
Design for test
HEP
VLSI testing
Notes: Current trends in semiconductor technologies, as well as in design methodologies, readily indicate that the ever-increasing degree of integration of devices on a single substrate continuously demands more efforts in achieving zero-defect designs. Clearly, this ultimate quality goal cannot be met without including testability as a design objective. Although the process of integration, strongly supported by CAD tools, has already led to an improved quality of integrated circuits, adding testability to a number of criteria considered during design, such as performance, area, power, manufacturability, etc., may significantly enhance the reliability of products and their overall quality.

## Slide 2: Testing of sequential circuits
Functional and random tests have low fault coverage
It may take a large number of clock cycles to excite a fault, and to propagate it to primary outputs
It may take an extraordinary amount of processing to generate a test
It may take a long time to apply a test (the number of vectors can be larger than the number of faults)
Activity on the most significant bit of a 32-bit counter can only be observed after 231 clock cycles
Notes: The advent of new test methodologies is traditionally linked with problems that occurred when test generation methods, developed for combinational circuits, were to be applied to their sequential counterparts. It appears that functional or pseudorandom test patterns do not guarantee satisfactory fault coverage in this case. Some faults require excessive test time to get excited and/or propagated to the nearest observation points. Moreover, test generation procedures may require unacceptable processing time to arrive with a reasonable test set. In fact, there are no universal sequential ATPG tools that solve this problem in a satisfactory manner. Finally, even an exhaustive set of test patterns may not be sufficient to tackle all faults in sequential designs. As a result, test application time, as far as sequential circuits are concerned, may become unacceptable.

## Slide 3: Why DFT?
Problems with testing of complex ICs
  logic-to-pin ratio is too high and increasing
  circuit complexity is too high and increasing
  takes too long to generate tests
  volume of test data is too large and increasing
  performance testing is difficult
  problems in finding skilled resources
Substantial amount of time and effort can be saved if testing, at the expense of modest silicon area and possibly minimal performance degradation, is considered early in the design flow
Design for testability (DFT) – techniques making the final design easier to test
Notes: The growth in the cost of developing and applying tests is attributable to a trivial observation that complex integrated circuits pose very serious problems in testing and debugging. On the other hand, there is a continuing need for testing at various architectural stages. At the chip-level, for example, testability problems may surface because of:
a very high and increasing logic-to-pin ratio, which points out a highly unbalanced relationship between a limited number of input/output ports and unprecedentedly complex semiconductor devices which are accessible only through these terminals,
a circuit complexity which continues to grow as new submicron technologies offer higher densities and speeds,
an increasingly long test-pattern generation and test application time; it has been repeatedly reported that functional and random tests for general class of circuits containing memory elements have very low fault coverage; in the case of deterministic patterns, an extraordinary amount of processing time might be required to generate a test vector, and then it may take a large number of clock cycles to excite a fault and propagate it to primary outputs,
a prohibitively large volume of test data that must be kept by testing equipment,
cumbersome procedures to perform at-speed testing through external testing equipment,
incomplete knowledge of the gate level structure,
lack of methods and metrics to measure the completeness of testing schemes,
difficulties in finding skilled resources.
At the printed circuit board level, external testers require a sophisticated bed-of-nails fixture in order to access the pins of the chips on the board, if these circuits were designed without addressing testability issues. This expensive technique becomes impractical when a surface-mount technology is used with components mounted densely on both sides of the board. Also, as the board has to be removed from the system, system-level diagnosis becomes impossible.
It is imperative to keep all costs related to testing, and originating from the above problems, in reasonable bounds. It appears that this can be accomplished at the expense of a modest amount of area and possible minimal performance degradation such that a uniform and structured solution can be used in debugging, manufacturing, and system testing. This approach, or rather a collection of techniques which make the final design economically testable, is known as a process of design for testability (DFT). DFT is expected to produce circuits with adequate controllability and observability, satisfying several design rules which reduce test development costs, increase fault coverage, and finally, reduce defect levels.

## Slide 4: Controllability and observability
The key to structured DFT – ability to control and observe state variables
Controllability – ability to set an internal node to a required logic value
Observability of an internal node – ability to propagate its specific logic value to pseudo or primary outputs
Used to measure circuit testability by deterministic and pseudorandom patterns
Notes: Testability, although difficult to define and quantify because of the many different factors affecting costs and quality of testing, reflects ability of tests to detect, and possibly locate, failures causing malfunctioning of a circuit. There are two major concepts which are commonly used in assessing and enhancing testability: controllability and observability. Controllability is a measure of how difficult it is to set a line to a value necessary to excite a fault. Observability is a measure of how difficult it is to propagate a faulty signal from a line to a primary output. Controllability, in addition to its impact on a fault activation, also indirectly affects the ease with which the required signals can be set to propagate fault effects. The essence of DFT is to apply minor changes to the original circuit such that the resultant controllability and observability will be improved. The frequently used set of characteristics for controllability and observability of each node in a circuit includes three values representing the relative degree of difficulty of:
achieving 1 at the node (1-controllability),
achieving 0 at the node (0-controllability),
driving the fault effects from the node to a primary output.
These measures are used with respect to whether tests employed are pseudorandom or deterministic. In the latter case, all measures can guide ATPG. For pseudorandom patterns, the definitions of controllability and observability are restated as follows:
0-controllability (1-controllability) of a node is the probability that a randomly applied input vector will set the node to a value 0 (1),
observability of a line is the probability that a randomly applied input vector will sensitize one or more paths from that line to a primary output.
A circuit node will have a low controllability and/or observability if a unique test vector or a long test sequence is required to establish the state of this node and then to propagate this state to the outputs of the circuit.

## Slide 5: Ad hoc techniques
Provide easy reset
Control all internal oscillators and clocks
Eliminate asynchronous logic
No deep sequential logic
Break feedback loops
No redundant and wired logic
Bypass mode for embedded memories
Access to embedded blocks
Test points
Eliminate bus contentions
Circuit partitioning
Notes: Several design techniques have been used over the years to avoid potential testing problems. They are termed “ad hoc” approaches, as they do not provide any systematic (algorithmic) methodology improving testability across the entire circuit. They do provide, however, certain rules that must be obeyed in order to increase controllability and observability. These rules are, in different ways, implemented in more rigorous DFT designs, too. Some of them include the following solutions.
Test points can be added to a circuit to make it easier to either sensitize faults (control points) or to observe them (observation points).
In order to eliminate the need to synchronize the tester and pulses internal to a circuit, devices such as internally generated clocks and oscillators should be disabled during test.
Asynchronous logic should be avoided by designers as circuits with asynchronous feedback loops are susceptible to hazards. Although it is possible to omit a hazard by using an appropriate ATPG tool which takes into account delays in the circuit, it can be very expensive. In many cases (for example, pseudorandom testing) avoiding hazards is practically impossible.
Initialization. A sequential circuit must be brought into a known state before its actual testing. This can be achieved by using a customized initialization sequence. However, as such a sequence is usually devised by a designer, it is unlikely that it will exhibit enough simplicity to be recreated by ATPG. Thus, it is recommended to employ reset or set inputs to flip-flops or another simple presetting circuitry.
Logical redundancy. Unless added intentionally to eliminate hazards and races or to increase reliability, a logical redundancy is a highly undesirable phenomenon which should be completely avoided. The presence of redundancy causes ATPG to waste a lot of time while trying to generate nonexistent tests for redundant faults.
Global feedback paths. Since from the ATPG point of view the feedback paths may introduce very long gate paths, they should be eliminated. The simplest way of achieving this objective is to use control points or another logic to break the paths during testing.
Long counters and shift registers may require an unacceptable number of clock cycles to change the most significant bits. A common remedy is to add the control points, such that the counter (or a shift register) is partitioned into smaller units, which can be clocked a much lesser number of times to set more significant bits.
Memory arrays and other embedded structures. Memory arrays should be isolated from the remaining parts of a circuit for at least two reasons. First, it is very difficult to generate tests for circuits with memory blocks. Second, when separated, a stand-alone memory circuitry can be conveniently tested by means of a variety of test schemes developed particularly for these structures. The same methodology applies to other embedded blocks.
Illegal states. Since the ATPG software cannot recognize illegal states, they should be eliminated from designs. Otherwise, side effects of tests may prevent their use due to bus clashes and other conflicts.

## Slide 6: Partitioning
test2
test1
Simplified fault excitation, propagation and line value justification in ATPG
Functional logic C1
Functional logic C2
Notes: Yet another ad hoc technique is based on circuit partitioning of large combinational circuits. Because of the time complexity of test generation and fault simulation, it is justified to partition large circuits in order to test them separately. Partitioning simplifies the task of fault excitation, fault propagation, and line value justification in ATPG, in addition to increasing random pattern testability. The independent testing of the resultant partitions is carried out through the number of test points added to lines crossing partition boundaries. The slide illustrates such a partitioning of a circuit that consists of two blocks C1 and C2. Control inputs test1 and test2 are used to test separately either C1 (test1 test2 = 01), or C2 (test1 test2 = 10), or to put the circuit into a normal mode (test1 = 0 and test2 = 0).

## Slide 7: Scan-based designs
Two modes of operation:
  normal (mission) mode
  test (scan) mode
In normal mode sequential elements perform their regular system function
In test mode sequential elements connected into one or more shift registers
Testing of circuits with scan reduced to testing of combinational circuitry
Notes: In order to test complex circuits in a time and cost-effective manner, a number of structured design techniques have been proposed. They rest on the general concept of making all or some state variables (memory elements) directly controllable and observable. If this can be arranged, a circuit can be treated, as far as testing of combinational faults is concerned, as a combinational network. Perhaps the most used and best-known is a family of techniques termed scan designs. They assume that during testing all registers (flip-flops and latches) in a sequential circuit are connected into one or more shift registers or scan chains (paths). The circuit has two modes of operation:
normal mode – the memory elements perform their regular functions (as in an unmodified circuit),
test (scan) mode – all the memory elements connected into a shift register are used to shift in (or scan in) and out test data.

## Slide 8: Scan cell
Multiplexer used to select data source
  DI – input data in the normal mode
  SI – input data in the scan mode
Input “Scan enable” selects the mode of operation
Increased propagation delay of the flip-flop
Comprehensive support provided by CAD tools
Clock
DI
SI
Scan enable (SE)
D
Q
Notes: The scan-based designs must comply with a set of design rules and constraints. Usually, they are related to design methods for scan cells and consequently determine a type of DFT style which is adopted for a given circuit. One of the simplest solutions regarding scan cells is shown on the slide. This is so-called edge-triggered muxed-D scan cell, where an extra 2-input multiplexer is placed in the front of input D. The multiplexer uses a scan enable (SE) control input to select between the (regular) data input (DI) and the scan input (SI). In the normal (capture) mode, SE is set to 0. In the shift mode, SE is asserted, and input SI is now deployed to shift in new data to the D-type flip-flop while the content of the same flip-flop is being shifted out. The key advantage of using muxed-D scan cells is their compatibility with modern design styles using single-clock D flip-flops, and the comprehensive support provided by virtually all existing CAD tools. Clearly, the drawback is that each scan cell of this type adds a multiplexer delay to the functional paths. However, many companies synthesize and optimize their scan cell designs. Consequently, when DFT tools create and stitch scan chains, the initial design includes realistic timing, and it is not changed by scan insertion.

## Slide 9: Generic scan path
Serial input
scan-in SCI
Scan enable
0: normal operation
1: scan – a shift register is formed
Combinational circuit
D
D
D
D
D
Primary inputs
Primary outputs
Serial output
scan-out SCO
Notes: This slide illustrates a basic scan-path design. As can be seen, the circuit features three extra pins (scan enable, serial scan-in, serial scan-out) as well as area and performance overhead due to the multiplexers. When the scan enable signal is low, the circuit operates in its normal, that is, parallel-load mode, except for increased delays. In the test mode (scan enable is high), test patterns are shifted in through the scan-in terminal, and test responses are subsequently shifted out through the scan-out pin. This is further animated on the two following slides.

## Slide 10: Generic scan path
Serial output
scan-out SCO
D
D
D
D
D
Primary inputs
Primary outputs
Serial input
scan-in SCI
Combinational circuit
Scan enable
0: normal operation
1: scan – a shift register is formed
Notes: Circuit under test in the mission mode.

## Slide 11: Generic scan path
D
D
D
D
D
Primary inputs
Primary outputs
Serial input
scan-in SCI
Serial output
scan-out SCO
Combinational circuit
Scan enable
0: normal operation
1: scan – a shift register is formed
Notes: Circuit under test in the test (scan) mode.

## Slide 12: Safe scan shifting
Clock
Test mode
Disable clock gating
Avoidance of bus contention
0 – test mode
1 – normal mode
off
on
mode
Scan chain
Notes: As mentioned earlier, in order to implement a scan-based design, the design itself must comply with a set rules. Moreover, certain design styles may not be desired, as they limit the resultant fault coverage and effectively reduce benefits achievable due to scan-based test operations. Consider, as an example, clock gating – a common solution employed to reduced power dissipation by eliminating unnecessary switching activity. Although good for reducing power consumption, it may prevent the clock ports of some flip-flops from being directly controlled (and thus preventing a proper scan operations). As a result, modifications are necessary to allow the scan shift operations to be conducted on these memory elements. The clock gating function should be disabled at least during scan shift-in, as shown on the slide where the red OR gate disables the clock gating logic in the test mode. In reality, the clock gating circuitry is typically a bit more complicated (see slide 40), and if the clock gater is controlled by the test mode pin, then the fault coverage through the gater is lost so the gater is best controlled with the scan enable functionality.
Another example (the lower part of the slide) is related to bus contentions that occur when at least two bus drivers force opposite values onto a tri-state bus (it may even damage a chip). Typically, circuits are designed to avoid bus contentions. Much of the same can be said about ATPG that can ensure only one bus driver controls a bus. It may not be the case, however, during scan shift operations. Consequently, additional test logic is required to make sure that there is only a single driver controlling a bus at a time in the test mode. Such a solution (the red gates) is illustrated on the slide.

## Slide 13: Testing procedure
Sequential part
  enable scan mode
  shift register test – flush test (00110011…)
  shift through scan-in and measure on scan-out
Combinational part
  select scan mode
  scan in test pattern
  force primary input values and set normal mode
  capture the combinational logic response
  measure primary outputs
  set the scan mode
  scan out, combined with scan in for the next pattern
Notes: During testing the sequence of operations for scan-based designs is as follows:
select the test mode (memory elements form a shift register),
shift in test-pattern values into the flip-flops,
set the corresponding values on the primary inputs,
select the normal mode,
after the logic values have had time to settle, check the primary output values and subsequently capture a test response into the flip-flops,
select the test mode; shift out the flip-flop contents and compare them with good response values; the next input vector can be shifted in at the same time,
repeat steps 2 through 6 for successive test vectors.
The flip-flops are tested by means of a “flush test” consisting of either a string of 1s followed by a string of 0s, or a serial pattern 00110011… used to check if each flip-flop can hold 0 and 1 and make transitions.

## Slide 14: Parallel scan chains
Reduced test application time
Scan enable
D
D
D
D
D
SCI0
SCO0
D
D
D
D
D
D
SCI2
SCO2
D
D
D
D
D
D
SCI1
SCO1
Notes: The application of tests in a single scan environment requires a large number of clock cycles due to the inherent limitations of a single scan chain. This constraint can be overcome by using a test infrastructure where a test generator (a tester) feeds a multiplicity of scan paths, as shown on the slide. The serial outputs of the scan chains may drive inputs of a test response evaluator or be sent back to a tester. The use of multiple scan chains can significantly reduce the test application time. Since the scan paths may be of different lengths, every time a pattern is to be produced, the generator is run for c clock cycles, where c is the size of the longest scan chain.
Implementing a scan design comprises a number of steps. First, one has to identify and repair all scan design rule violations to convert the original design into a testable circuit. The testable device must guarantee the correct shift and capture operations. In particular, the clock skew between adjacent scan cells must be properly managed. A similar rule applies to distribution of a scan enable signal that may reach tens of thousands of scan cells. The next steps include decisions regarding the number of scan chains deployed, the types of scan cells, memory elements that are going to be excluded from the scan synthesis process, and the way the scan cells are arranged within the scan chains (scan stitching).

## Slide 15: Scan test
Scan input channels
Scan output channels
Primary in/out
Test time =
Scan cells
Scan chains
Frequency
Patterns

A T
E
Notes: The number of scan chains is typically determined by analyzing the input and output pins of the circuit to determine how many pins can be allocated for the scan use. Equally important are capabilities of the available automatic test equipment (ATE) represented here by its channels that can be designated for scan testing purposes. It is worth noting that a tester feeds not only scan serial inputs and receives data from scan serial outputs, but also provides data directly to the primary inputs of a circuit under test and observes its primary outputs. One limitation that can preclude many scan chains from being deployed is the presence of high-speed I/O pads. As mentioned earlier, the larger number of scan chains, the shorter test application time. In general, as shown on the slide, the resultant test time can be determined as a product of two factors: (1) the maximum length of the scan chains (it dictates the overall number of shift cycles needed to apply a single test pattern), and (2) the total number of scan test patterns (divided by the scan shift frequency).

## Slide 16: Benefits of scan
Highly effective and predictable process
Increased controllability, observability, thus testability
Simplified ATPG and fault simulation
Simple test protocol
Improved hardware debugging and verification
Improved fault diagnosis
Fundamental for built-in self-test
Notes: Several common advantages of scan-based DFT schemes can be easily pronounced. They include:
simplified test-pattern generation and test-pattern evaluation – testing the network is essentially the same as that of testing a combinational circuit,
simplified timing analysis – proper operation of the network is independent of clock characteristics and only requires the clock pulse to be active for a sufficient period,
simplified design validation – automated checks for design rule violation can be performed with relative ease,
very few additional external pins (usually three or four) are required to access the system flip-flops,
easier design debugging – the scan paths provide the direct access to many internal circuit nodes.

## Slide 17: Cost of scan
Additional hardware – two-port scan cells and extra routing (scan enable, clock trees, cells stitching)
Additional top level pins
  scan inputs
  scan outputs
  mode selection and/or shift clock
Performance impact can be minimized
Design effort cost
Security concerns
Notes: Clearly, there are some inevitable limitations of the scan designs. They introduce additional hardware (area overhead due to replacement of storage elements with scan cell; another factor is a routing cost related to scan chains, the distribution of scan enable signal, and the clocks), performance degradation (due to the presence of multiplexers in scan cell designs), and increased test application time (because of scan-in and scan-out operations). Furthermore, it might be difficult to test the circuit at its operational speeds and therefore the coverage of some faults, especially delays, can be low. In addition, all timing is usually controlled by an external clock, and there is a need to incorporate a design rule checking into CAD software in order to automate the design process. Recently, serious concerns regarding security issues have been raised as typical scan designs may allow unauthorized access to internal nodes of a design letting someone to recreate internal structure of a circuit based on data that has been shifted into scan chains and the resultant data observed on the outputs of successive scan chains.

## Slide 18: Scan test cost
Shift frequency
50 MHz
Gate count
10M
Scan chains
32
Padding ratio
1.4
Scan patterns
20K
ATE memory
150 MV
Reload penalty
2 s
Insertions
4
Tester rate
$0.05/s
Scan cells
500,000
Cells per scan
15,625
Longest scan chain
21,875
Cycles
437.5M
Scan test time
8.75 s
Reloads
3
Reload time
6.0 s
Time per device
59.0 s
Cost per device
$2.95
Notes: This table illustrates how one can estimate a cost of scan-based testing. Assume a 10M gates design with 0.5M memory elements. These storage devices are converted into scan cells forming 32 scan chains – 15,625 cells per scan chain on the average. Let us also assume that a padding ratio is equal to 1.4 (it defines the longest permissible scan chain relative to the average size). Hence, the longest scan chain is comprising 21,875 cells – this is also the actual number of shift clock cycles that must applied every test pattern. Since the number of scan patterns is 20,000, the resultant total number of clock cycles amounts to 437,500,000 pulses. With the 50 MHz scan shift frequency, it will take 8.75 seconds to apply the whole test set. As the ATE memory is capable of accommodating 150 MV (which is roughly 30% of the total number of scan shift cycles that we need to deliver), this tester memory has to be reloaded three times. If a single reload lasts approximately 2 seconds, then the total reload penalty sums up to 6 seconds. Eventually, the total test time equals 8.75 + 6 = 14.75 s. Now, each time a device is tested during the manufacturing and assembly process is referred to as a test “insertion”. Wafer-sort, burn-in or final package tests may serve as examples of insertions. Assuming, that the number of such insertions is four in our example, the final test time becomes equal to 14.75 times 4, i.e., 59 seconds. With a single second of tester time being worth $0.05, the scan test cost per device amounts to almost three dollars.

## Slide 19: Level sensitive scan design (LSSD)
Pioneered by IBM
Designed with hazard-free master-slave latches
Set of rules guide the design process
The rules primarily pertain to clocks which initiate state changes within the circuit
Circuit response independent of any delays
+L1
-L1
+L2
-L2
D
C
I
A
B
Notes: In addition to the most popular scan chain architectures, there are several forms of scan design proposed in the past such as the scan/set, the random-access scan, and the best-known – the level-sensitive scan design (LSSD) used in many IBM products. For the sake of illustration, we will briefly discuss the LSSD technique. The memory elements used by LSSD are implemented as latches in which the stored data cannot be changed by any input when the clocks are off. Moreover, each latch is augmented to form a shift-register latch by adding an extra latch (L2) with a separate clock input.

## Slide 20: Double-latch design
C
A
I
B
Scan-in
Scan-out
…
…
Primary inputs
Primary outputs
…
…
L1
L1
L1
L2
L2
L2
Functional logic
Notes: Interconnection of the latches into a shift register structure is done as shown on the slide, which demonstrates the general structure for a so-called LSSD double-latch design. In this approach, both latches, L1 and L2, are used as system latches, and the circuit output is taken from outputs of L2. Note that, in the normal mode, clocks C and B are used, while in the test mode, non-overlapping clocks A and B are used to prevent races.

## Slide 21: Single-latch design
C1
A
I
B
Scan-in
Scan-out
…
…
C2
L1
L1
L1
L1
Primary outputs
Primary inputs
L2
L2
L2
L2
Functional logic
Functional logic
Notes: Another LSSD approach, known as a single-latch design, is also used if it is desired to separate combinational circuits only by a single latch. In this solution, latches L2 are not employed to perform the system functions of the circuit. The scan path is denoted by the red line. Several variations of the original LSSD design have been also proposed, mostly to reduce logic complexity.

## Slide 22: Partial scan
Retains many advantages of full scan but seldom used
Introduces controllability and observability
Hard macros, time critical paths
Trade-off between hardware area and ATPG
Cost efficiency
  control area overhead
  control delay overhead
Notes: To reduce the costs of using scan designs, especially area overhead and performance degradation, several partial scan techniques have been proposed in which only a subset of the circuit memory elements are included in the scan path. Among these methods, there are three common strategies used to select the flip-flops to scan such that the cost of test pattern generation is reduced while the testability overheads are minimized. Chronologically, the first approach was to employ testability measures in the flip-flop selection process. It does not guarantee the optimal solution as testability measures are usually not accurate and do not characterize the global effects. The second group of methods is based on breaking cyclic paths in the CUT in order to reduce the number of the feedback loops and their sequential depth. The rationale behind these techniques is to reduce the high cost of sequential ATPG originating from the presence of these loops. A special variant of this method cuts all the feedback loops, so that during test the resulting circuit works as a pipeline where faults can be processed by a combinational ATPG. The third concept utilizes test pattern generation techniques. The partial scan can be conveniently integrated with various BIST schemes – see the next chapter.

## Slide 23: Boundary scan – objectives
To test interconnects between ICs
To diagnose defects
To test ICs, invoke internal BIST functionality
To test the board in the system in a cost effective way
IEEE standard 1149.1
C.M. Maunder, R.E. Tulloss, IEEE Computer Society Press, 1990
Notes: In order to invoke test procedures and to facilitate their correct execution at different levels of a circuit's architectural hierarchy such as the board, module or system level, certain design rules must be applied. In 1990, a new testing standard was adopted by the Institute of Electrical and Electronics Engineers, Inc., and it is now defined as the IEEE Standard 1149.1, IEEE Standard Test Access Port and Boundary-Scan Architecture. Its detailed overview can be found in the book by C.M. Maunder and R.E. Tulloss. The boundary-scan architectures not only allow for efficient fault detection at the board, module, or system levels, but also create an environment in which a fault diagnosis (location) at these architectural levels becomes a relatively simple task. A properly configured sequence of instructions may lead to isolation of faulty chips or interconnects in a timely fashion, thus enabling simple and fast repair procedures.

## Slide 24: Boundary scan architecture
TDI
TRST*
TCK
TMS
TDO
Optional
Instruction decoder
Instruction register
Circuit under test
Boundary scan register
Output buffer
Design specific registers
Device identification register
BR
TAP
Instructions
Clock DR
Shift DR
Update DR
Clock IR
Shift IR
Update IR
Reset
Enable
Select
…
Notes: The basic architecture of the boundary scan is incorporated at the integrated circuit level and essentially consists of a protocol by which various test functions can be carried out. In particular, the standard defines four (or optionally, five) new pins forming the test access port (TAP): two of them (test clock TCK and test mode select TMS) are used to control the protocol, while the remaining two pins (test data in TDI and test data out TDO) are employed to serially shift data into and out of the circuit. Application of a 0 at the optional test reset input TRST* asynchronously forces the test logic into its reset state. The standard also specifies a simple finite state machine called the TAP controller which is driven by TCK, TMS and TRST*. Every chip designed according to the standard contains a boundary-scan instruction register and an associated decode logic. It is used to set the mode of operation for selected data registers by means of boundary-scan instructions which always place data registers between TDI and TDO. Two registers must always be present: the bypass register and the boundary-scan register. Additional registers are allowed under the optional clause of the 1149.1, and they can be selected by sending the proper control sequences to the TAP controller. In particular, internal scan paths can be connected via this circuitry to the chip's scan-in and scan-out ports. It should be emphasized, however, that the normal input/output terminals of the mission logic are connected to the chip’s input/output pads through boundary-scan cells.

## Slide 25: TAP state diagram
Control signals from TMS
Run Test / Idle
Test Reset
1
0
0
Select DR scan
Capture DR
Shift DR
Exit1 DR
Pause DR
Exit2 DR
Update DR
0
0
1
0
1
0
0
0
1
1
1
1
0
1
Select IR scan
Capture IR
Shift IR
Exit1 IR
Pause IR
Exit2 IR
Update IR
0
0
1
0
1
0
0
0
1
1
1
1
0
1
1
power up / TRST* = 1 / TMS = 11111; IR(1…1) = BYPASS
TMS = 0…0; IR = RUNBIST
transient state
Notes: This slide presents a state transition graph of the test access port, regarded here as a simple finite state machine. The gray states are so-called transient states, while the white states represent the actual actions invoked by TAP. The automaton moves between successive states based on control information provided through input TMS. Interestingly, as required by the IEEE standard 1194.1, the FSM moves to its initialization state (the blue one on the slide) either when a circuit is powered up, or the optional input TRST* is asserted, or a sequence of five consecutive ones is applied to the control input TMS. The remaining transitions are illustrated on the slide. Abbreviations DR and IR correspond to a data register and an instruction register, respectively.

## Slide 26: Board testing
TAP
Core
logic
TAP
Core
logic
TAP
Core
logic
TAP
Core
logic
TDI
TDO
TCK
TMS
Notes: If integrated circuits are mounted in a board during testing, a typical test session is carried out in the following way. All TDIs and TDOs are daisy-chained from chip to chip. A sequence of instructions is shifted through the system in such a way that every chip receives its own content of the instruction register. These instructions place the appropriate parts of data registers (for example, scan paths, user-defined registers, but also boundary-scan registers, etc.) between TDI and TDO pins. Second, the test patterns are loaded, and the test instruction is executed. The resultant test response can be subsequently shifted out of selected registers. The boundary scan allows efficient testing of board interconnect using the EXTEST instruction, facilitates isolation and testing chips via the boundary registers or built-in self-test hardware using the INTEST or RUNBIST instructions, and makes it possible to capture snapshot observations of normal system data using the SAMPLE instruction. When no test actions are required in a given circuit, the BYPASS instruction puts a 1-bit length bypass register between TDI and TDO, thus forming a minimal scan path to and from other targeted chips.

## Slide 27: IEEE standard 1500
The IEEE 1500 describes a standardized interface allowing for
  ease of automation of wrapper creation
  manipulation of test patterns
  SOC test connections and test scheduling
Influenced by the IEEE standard 1149.1
Has a similar structure as that of 1149.1 but targeted towards testing cores in SoCs
Core test language (CTL) – the official mechanism for describing IEEE 1500 wrappers and test data associated with cores; CTL is defined in the IEEE P1450.6
Notes: The continuing standardization efforts have led to formulation of the IEEE standard 1500. It is a scalable standard architecture for enabling test reuse and integration for embedded cores and associated circuitry. It focuses on facilitating efficient test of digital aspects of systems on chip (SoCs). The IEEE 1500 has serial and parallel test access mechanisms (TAMs) - access is provided to embedded digital cores using the IEEE 1500 wrapper for controllability and observability of the cores - and a set of instructions suitable for testing cores, SoC interconnects, and circuitry. In addition, the IEEE 1500 defines features that enable core isolation and protection. It reduces test cost through improved automation, promotes good DFT schemes, and improves test quality through improved access.

## Slide 28: Standard 1500 wrapped core
WPP
WBR
Core
WPP
WBR
WBY
WIR
Functional inputs
Functional outputs
Wrapper parallel outputs (WPO)
Wrapper parallel inputs (WPI)
Wrapper serial input (WSI)
Wrapper serial output (WSO)
Wrapper serial control (WSC)
Test inputs
Test enable
Test outputs
FI
FO
FO
FI
Notes: The main building blocks of the IEEE 1500 wrapper are shown on the slide. The WIR (wrapper instruction register) enables all of the IEEE 1500 operations. The IEEE 1500 wrapper has several modes of operation. There are modes for functional (non-test) operation, inward facing (IF) test operation, and outward facing (OF) test operation. Different test modes also determine whether the serial test data mechanism (WSI–WSO) or the parallel test data mechanism (WPI–WPO), if present, is being utilized. The wrapper bypass register (WBY) provides a bypass path for the WSI – WSO terminals of the wrapper serial port (WSP). The wrapper boundary register (WBR) is the data register through which test data stimuli are applied and pattern responses are captured. The WPP is used for increased data bandwidth to the wrapped core.

## Slide 29: IEEE P1687
Standard for access and control of instrumentation embedded within a semiconductor device
Problems addressed:
  re-using on-chip test/debug IP at board/system level
  standardized hardware description language for internal TDRs
  standardized instrument procedure language
Efficient instrument connection architecture
Why not the boundary scan architecture 1149.1?
  1149.1 TDRs are fixed length
  1149.1 does not standardize internal scan description
  1149.1 does not standardize procedural language
Notes: This relatively new test standard is to develop a methodology for access to embedded test and debug features (but not the features themselves) via the IEEE 1149.1 Test Access Port (TAP) and additional signals that may be required. The elements of the methodology include a description language for the characteristics of the features and for communication with the features, and requirements for interfacing to the features.
Many technical details can be found on the web site http://grouper.ieee.org/groups/1687.

## Slide 30: IJTAG architecture
SIB
SIB
SIB
SIB
SIB
SIB
SIB
SIB
SIB
SIB
SIB
SIB
TAP CONTROLLER
TMS
TCK
TDO
TDI
MBIST
LBIST
EDT
SERDES
M2
M4
Notes: Consider a top-level module as shown on the slide. It contains an IEEE 1149.1-compatible TAP controller, four Segment Insertion Bit (SIB) modules, and two blocks named M2 and M4, respectively. Each block includes four instruments (for example, memory BIST, logic BIST, test compression, and high speed SerDes interface) operated by regular test-data registers (TDR). Operating means writing care bits into the TDR or reading values from it. A PDL retargeter (EDA tool) automatically applies control signals such as capture, shift, or update enable as needed.
In IJTAG, the ICL interconnection network and all non-leaf-level instrument modules in this interconnection network are universally addressed as the “ICL access network.” An interesting addition to this ICL access network is the use of SIB modules, which dynamically change the ICL access network configuration. SIBs are not part of IEEE P1687, but their usage is recommended. Usually, a PDL-retargeting EDA tool automatically sets the access network’s configuration while it is computing a solution for sending the user’s care bits to an instrument. The user also can manipulate it explicitly.
Assume a user wants to write a care bit into M4. There is no need to shift through M2. Instead, the shorter shift path is to configure the first level SIB to bypass M2 altogether so the shift path is from the TDI port, through the first level SIBs into M4 and, for example, the second SIB’s side input, then back through the TAP to TDO. The PDL-retargeting tool’s job is to figure this out. In IJTAG, the user only needs to express the intention to write a care bit into a selected instrument of M4. This is the key difference with other JTAG-based usages, where it is up the user to configure the access network explicitly.

## Slide 31: At-speed scan-based test
Apply test with system timing in the capture window
Multiple clock domains
Multiple frequencies
Clock skew between clock domains
On-chip PLL generated clocks
Invalidation of delay tests
Over-testing (testing of sequential false paths)
Design of scan enable signals
Notes: As a result of the emergence of new technologies, standard stuck-at scan tests may not be sufficient. There is a significant growth in the number of timing-related defects at 130 nm and below. At-speed scan testing is thus necessary to detect these faults. The most popular approach for at-speed scan requires more complex test patterns. The most desirable application of at-speed scan test involves loading values into the scan chains at a slow clock rate and then applying two cycles at the system clock frequency. At-speed patterns can use internal PLLs for the at-speed launch and to capture pulses to provide accurate clocking. Because two cycles are required in the functional mode of these tests, at-speed scan patterns are typically three to five times larger than a stuck at pattern set. Typically, ATPG tools can support at-speed scan tests that are simpler and require fewer patterns – these are called launch-off-shift patterns. Such tools impose more design constraints, however, and will test more nonfunctional logic, possibly reducing yield. The other problems that at-speed scan-based test is facing include multiple clock domains and possible clock skew between them, multiple clock frequencies, proper design of scan enable distribution network, and so on.

## Slide 32: Single capture (launch-off-shift)
Capture window: from last shift to capture
Scan enable has to propagate to all scan cells in less than one cycle
Over-testing – transitions launched from an illegal state
Delay test may be invalidated
last shift
capture
SE
Clk
capture mode
shift mode
loading
unloading
shift mode
Notes: The slide shows the basic timing for a scan pattern commonly referred to as a launch-off-last-shift or just launch-off-shift (LOS) vector (another name: a skewed load technique). In this technique, the transition occurs because of the last shift in the procedure of loading scan chains. This type of test patterns requires the scan enable (SE) signal (controlling multiplexers in scan cells) to transition from shift to capture mode at speed. Therefore, the scan enable must be globally routed and timed similar to a clock (Clk). A common approach is to have lots of local pipelines of the SE change with the system clock. Also, because launch-off-shift patterns detect certain number of faults in non-functional paths as well as in the scan path, the test coverage exaggerates the real coverage for faults that can impact yield. This phenomenon is known as over-testing, and it occurs due to transitions being initialized from (illegal) states that a circuit does not reach in the mission mode.

## Slide 33: Speed of loading
Timing in capture window crucial to at-speed testing
The loading and unloading frequency irrelevant to at-speed testing
Slower frequency to reduce power and other constraints
Faster frequency to reduce test application time
S
C
S
S
J. Rajski, BIST tutorial, ITC’96
Notes: As can be seen from the last two slides, the crucial for the proper arrangement of scan-based at-speed test is a capture window when clock is applied at the mission frequency. The loading (unloading) of scan chains can be done at much lower frequency, determined, for example, by power and heat dissipation constraints. Most EDA tools allow designers to define the timing for transition delay tests. Within a test procedure file, templates specify tester cycles and location of all events in each cycle. In particular, slow cycles are used for shifting and fast cycles for the launch and capture. It is also possible to have all clock cycles with the same period, and still offer the timing as shown on the slide. In such a case, one needs to skew the clock pulses within their cycle periods (provided that a tester can guarantee this capability).

## Slide 34: Double capture (launch-off-capture)
Launch from a semi-legal state
Reduced over-testing
Multiple time frame sequential fault simulation
Solution for non-scan elements
first capture & transition launch
capture
SE
Clk
last shift
Notes: In order to reduce a negative impact of over-testing on yield, so-called launch-off-capture (LOC) test patterns can be employed. In this approach (known also as a broadside or double capture technique), a capture window covers two consecutive clock cycles. After scanning-in a test pattern at a slow speed, the following clock pulse captures a test response and launches a transition. Subsequently, an at-speed functional clock is applied that captures the response. As can be seen, the second test vector is directly derived from the previous one by pulsing the clock and storing a circuit response in scan chains. Since this test pattern is produced by the circuit-under-test itself, the second launch step can be regarded as performed from a semi-legal state (as opposite to a test pattern provided directly by a tester). This reduces the over-testing effect, though it requires some sort of sequential fault simulation handling at least two consecutive clock cycles. The approach can be extended to multiple time frames by proper controlling the scan enable window duration.

## Slide 35: Launch-off-capture
C
last shift
launch
capture
first shift
SE
Clk
Loading of random state
1. Initialization of internal nodes
2. Deactivation of scan enable
3. Propagation of scan enable signal
4. Transition to a semi-legal state
5. Launch of transitions
1. Propagation of signals
2. Capture of responses
1. Activation of scan enable
2. Propagation of scan enable
3. First shift out of responses
Continued unloading of responses
Notes: This slide illustrates, in a more detailed fashion, successive steps of the launch-off-capture procedure presented earlier. It is also worth noting that some experiments indicate higher delay fault coverage that can be obtained due to the launch-off-shift scheme rather than its launch-off-capture counterpart. However, because of over-testing issue and a need to use at-speed scan enable signal, it is easier to lay out scan designs with the launch-off-capture approach as it has no timing constraints with respect to the scan enable. Furthermore, assuming that the initialization vector is a legal state, the actual test pattern is a legal state of the circuit as well. Consequently, it reduces the testing of false paths (often leading to yield loss). The primary disadvantage of the launch-off-capture scheme is the need to justify the test vector back on time frame to determine the initialization pattern. It results in increased test generation time and pattern count. This constraint also makes some faults untestable.
A simple comparison between LOS and LOC is that LOS often gets higher fault coverage because ATPG is much simpler as there is no need for sequential processing. LOC has often lower fault coverage but can get some detections not possible with LOS-like testing (e.g., stuck-at-1 fault on a 3-input AND gate inputs with three consecutive scan cells).

## Slide 36: Multiple clock domains
Objective: at-speed testing of logic within every clock domain and between clock domains
Test mode
CLK1
SE
CLK2
SE
CLK3
SE
Control
PLL
Scan chain
Notes: The next three slides illustrates some basic capture-clocking schemes that can be used for at-speed testing of designs with multiple clock domains. Clearly, the primary objective of any technique is to address the intra-clock-domain and inter-clock-domain delay fault detection problem (as indicated by red arrows). Depending on an adopted solution, the actual implementation may require a non-trivial scan enable signal generation circuitry as well as a customized timing-control structure to, for example, suppress selected pulses, if required.

## Slide 37: Multiple capture procedure
Captured and shifted data as a stimuli for other domains
The order of capture can change in different vectors
Several domains can capture at the same time if they interact only through non active domains
One scan enable signal can be used for all domains
S
S
S
S
S
S
S
S
S
D1
D2
D3
C
C
C
Notes: Also known as “the one-hot skewed-load” approach, this scheme tests all clock domains one by one. Its timing diagram is shown on the slide. It applies shift-followed-by-captured pulses to detect intra-clock-domain delay faults (in both synchronous and asynchronous clock domains), and each scan enable signal must switch operations from shift to capture within one clock cycle. However, the approach can be easily adopted to circuits with a single scan enable signal shared by all domains. It is worth noting, that a carefully chosen order of capture operations allows test data captured in one domain to act as test stimuli in other domains (in addition to their own shifted-in test patterns). The presented multiple capture procedure cannot be used to detect inter-clock-domain delay faults, and it has a relatively long test application time.

## Slide 38: Multiple frequencies – single capture
C
All intra and inter domain logic tested at speed
Combinational fault simulation adequate
Clk1
SE1
Clk2
SE2
Load / unload window
Capture window
C
Notes: The disadvantages of the previous scheme can be resolved by using the “launch aligned skewed-load” approach that aligns all last shift edges (as opposite to yet another technique referred to as the “capture aligned skewed-load” – not presented here – that aligns all capture edges). The major advantage of using this approach is that all intra-clock-domain and inter-clock-domain faults can be tested. The arrows shown on the slide indicate the delay faults that can be detected, both within domains of Clk1 and Clk2, as well as between these domains. With a larger number of clock domains, this scheme may require a more complex control circuitry, in particular a clock suppression device to enable or disable selected shift and capture pulses.

## Slide 39: Multiple frequencies – double capture
C
C
Clk1
SE1
Clk2
SE2
C
Notes: Similarly to single-capture at-speed scan-based tests, intra-clock domain and inter-clock domain delay faults can be tested within the framework of the double capture approach. The slide illustrates such an approach for two domains by using so-called the “launch aligned double capture scheme”. Recall that in this scheme two consecutive capture pulses are applied rather than shift-followed-by-capture pulses (here in the domain of clock Clk1). Again, the arrows indicate the delay faults that can be detected, both within domains of Clk1 and Clk2, as well as between them. As can be seen, the capture operation in the second domain forms a part of stimuli, which is subsequently used by the first domain when performing a double capture. One of the major drawbacks of the presented schemes is that a precise alignment of certain pulses is required. It complicates physical implementation for designs with asynchronous clock domains.

## Slide 40: Low power test
Toggling during test may result in power droop not occurring in the mission mode
Test schemes must fall within power consumption constraints
The power dissipation can increase 3x compared to functional mode
Scan patterns may consume 30x the mission mode’s peak power
Effects – damage, yield loss, reliability issues
Lack of correlation with functional operation
Notes: As we have shown so far, a variety of scan-based solutions had gained a broad acceptance as reliable test schemes. Scan toggling, however, can consume much more power than a circuit is rated for. With the switching activity going well beyond that of the mission mode, it is imperative to judiciously manage power in the test mode. Otherwise, the power dissipation can increase by a factor of 2 – 3 compared to the functional mode of operation, and is only expected to worsen with scan patterns consuming 30x over the mission mode’s peak power. The resulting higher junction temperature and increased peak power can easily lead to overheating or supply voltage noise – either of which can cause, at the very least, a device malfunction, and thus loss of yield, increased chip reliability degradation, or shorter product lifetime. Eventually, such elevated power dissipation may also result in a device permanent damage due to hot spots on the silicon.

## Slide 41: Reducing power dissipation
Solutions for scan testing in shift and capture
  test scheduling and vector reordering
  partitioning and modifications of scan chains
  transition blocking
  clock gating
  test points keeping the peak power below a threshold
  low-transition test pattern generators
Minimum transition fill
  patterns tailored to test application with low switching by assigning non-random values to unspecified positions causing power violations
  transitions during scan-in shifting minimized
Weighted transition metric counts the number of invoked transitions in scan cells, while taking into account their relative positions
Notes: Over the years, numerous techniques for power reduction during scan testing in both shift and capture modes have been proposed, focusing on test scheduling, test vector reordering, partitioning, and modifications of scan chains, transition blocking and clock gating, as well as test points insertion aimed at keeping the peak shift power below a given threshold. Similar schemes that rest on the above ideas have also been proposed for BIST applications, including low-transition test pattern generators, and gated scan cells. Other solutions tailor test patterns to the requirements of test application with the lowered switching activity. These schemes resolve test power problems by reassigning certain non-random values to unspecified positions of test cubes causing power violations, thus minimizing the number of transitions during scan loading. Power-aware ATPG may serve here as an example. Conventional deterministic test vectors can also yield patterns leading to a reduced switching activity. This is because their fill rates are usually low, and thereby, instead of random fill, such positions may assume values minimizing the amount of transitions during scan-in shifting. In particular, all don’t care bits can be mapped to the value of 0. A minimum transition fill replicates the value of the most recent care bit for all unspecified positions until the next care bit whose value will be used for the following (adjacent) positions.
Loading scan chains dissipates power dependent directly on the number of transitions that occur in the scan chains and other parts of the CUT. One can estimate the resultant switching activity by counting the number of invoked transitions in scan cells and taking into account their relative positions for all scan chains and all test patterns. Typically, a degree of switching is determined by a random fill, which is a side effect of feeding scan chains with various types of patterns.

## Slide 42: Gated scan cells
Design overhead – area and functional timing
Timing closure issues for launch-off-shift tests
Q
Q
D
Q
Q
D
Q
Q
D
Q
Q
D
SE
SCI
No switching during scan shift
S. Gerstendorfen, H.-J. Wunderlich, ITC’99
Notes: Since the switching activity at the combinational logic is caused by the state change at the scan cells, the test power can be reduced by preventing the transitions at the sequential state elements from propagating to the combinational logic during shift. This is achieved by inserting blocking gates between scan cell outputs and the logic they drive. During normal operation and during capture, the blocking gates are transparent due to de-asserting the signal controlling the blocking gates. During shift, the control signal is asserted to make all the blocking gates hold their values.
To reduce the hardware overhead and its impact on circuit performance due to the additional blocking gates, one may use supply gating transistors for the first-level combinational gates at the outputs of scan cells and/or insert the blocking gate only at power sensitive scan cells that are not on critical paths. It is worth noting that this method cannot reduce the power consumption at the clock tree. But it has no impact on test pattern count and test application time.

## Slide 43: Scan partitioning
scan path A
scan path B
scan path C
scan path A
scan path B
scan path C
Divide scan chains
Reduces peak and average toggling rates
Can be used with other low power techniques
L. Whetsel, ITC’00
Notes: Another simple low power solution is shown on this slide. It partitions scan chains in such a way that only a fraction of scan cells become the subject of the scan shift operations at a time. As can be seen, instead of uploading (downloading) the entire scan chain with a given test pattern or a test response (and thus invoking a large number of transitions), one can deliver the same test pattern in a broadcast mode with the scan clocking system being enabled in three non-overlapping phases. As a result, the total number of invoked transitions is significantly smaller. The presented solutions requires a more subtle scan clocking control and a bit more complex routing compared to conventional scan chain schemes.

## Slide 44: Clock gating
Easily disable switching in portion of design
  clock tree uses more than 50% of dynamic power
Popular hierarchy of clock gaters
To avoid glitches (otherwise a single AND gate would suffice)
GCLK
CLK
FROM SCAN
FUNC_EN
D
C
Q
CLK
GCLK
D
Q
Notes: The slide shows an example of a clock gater and the corresponding time waveforms. The clock enable signal (the output of the OR gate) is generated at the rising edge of CLK and is loaded into the flip-flop at the failing edge of CLK to become the input to the AND gate. This is the signal which is then used to enable or disable clocking for the subsequent flip-flops down the stream. It is worth noting that the presented solution prevents glitches (otherwise a single AND gate would suffice). Two inputs FUNC_EN and FROM SCAN controls the clock gater in the functional mode and in the test mode, respectively. Typically, the latter input can be provided by means of a designated scan cell.

## Slide 45: Hierarchy of clock gaters
Clock
Clock gaters disabled at the highest level
Notes: In a mission mode, functional enable logic fed by scan cells controls the clock gaters. To support scan shift operations, clock gaters are forced on when a test mode or scan enable are asserted. ATPG can justify the functional enable logic to its off state, thus preventing many downstream flip-flops from toggling. In test compression environment, it can be accomplished by using a relatively small amount of test data provided by scan chains in such a way that, during capture, scan values control the clock gaters. Clearly, the primary objective is to meet the power constraints by disabling flip-flops with as few additional specified bits as possible to minimize impact on compression. Furthermore, many designs may feature a hierarchy of clock gaters, to achieve both fine and coarse levels of control granularity, as shown on the slide. If no flip-flops in a specific area of the design observe faults, one may turn off a higher-level clock gater by using fewer specified bits. There are method for enhancing ATPG to reduce the capture power by controlling clock gaters.

## Slide 46: Hierarchy of clock gaters
Clock
0
0
Clock gaters disabled at the highest level
Notes: This example, as a follow up to the previous slide, illustrates how a given scan cell (in blue) can activate a clock gater, which in turn, freezes a number of clock gaters down the stream, thus eventually disabling a group of sequential elements and reducing the total test power dissipation.

## Slide 47: Low power scan operations
Scan enable
SE
SE
SE

XXXXX0XX0XXXX00X
XXXXXXXXXXXXXXX
XX1XX0XX01XXX0011
0
0
1
0
0
Control register
D. Czysz et al., IEEE Trans. CAD, 2009
…
Notes: Since deterministic tests have typically only a small fraction of bits specified with their sites confined to a few scan chains, one can feed such scan chains directly from a tester that replaces all don’t cares with a low toggling fill while delivering a constant 0 to all remaining chains. It significantly reduces the number of transitions during scan-in shifting without compromising test coverage. This slide shows a solution where input channels first deliver information to a control block, and then provide test patterns to CUT. The control block comprises XOR logic driven by compressed data stored in a register, and it outputs gating signals to AND gates such that either the tester or a constant value of zero feeds scan chains on a per pattern basis. The control circuitry selects gating signals for scan chains with specified bits such that the AND gate has 1 on its input. It allows the tester to drive these scan chains directly. The selection process continues until power limits are reached. As for the remaining scan chains, one can determine gating signals that were not encoded yet. Approximately, the tester can still feed 50% of such scan chains, while the others receive a constant 0.

## Slide 48: Two constant stimuli
Chart: 
| 1 | decompresor | 0
 | 25 | 25 | 50
Among non-target scan chains:
 50% receive 0
 25% receive 1
 25% fed by tester
SE
Scan enable
Test mode
SE
1
D

Control register
Scan enable control
0
Notes: In certain applications, it might be desirable or convenient to feed scan chains with both logic values of 0 and 1 acting as constant stimuli. Consider scan chains that were not the subject of encoding, as discussed earlier. The gating circuitry shown on the slide allows the tester to drive approximately 25% of such scan chains, while 50% of them receive a constant 0, and 25% have a constant 1. In other words, roughly 75% of scan chains with no specified bits will have no transitions at all. Indeed, as shown earlier, a gating signal reaches the AND gate and then a scan chain as a constant 0 with probability 0.5. On the other hand, in order to get a constant 1, two gating signals are needed - one set to 0 and driving the OR gate, and the other one set to 1 and feeding the AND gate. Clearly, the XOR network outputs this combination with probability 0.25.

## Slide 49: Capture and shift out
Scan enable
Scan enable
Test mode

Control register
SE
SE
SE
…
Notes: Test responses that exhibit high transition counts may contribute to bulk of power dissipation. Reduction of capture and shift-out power can be achieved due to error propagation sites that are typically confined to a few scan chains, only. One can avoid capturing data that would overwrite the otherwise constant values scanned in earlier. Although it may be safe, during capture, to maintain an asserted scan enable signal for a scan chain that loaded constant values, it is not safe to do so for a scan chain that loaded non-constant values from the tester. This is because scan paths are almost never timed to operate at functional frequencies. Hence, if one shifts a non-constant content of a scan chain at speed, the result can be unpredictable. Assuring reliable values in such scan chains requires, therefore, masking out many scan cells. To solve this problem, one may tie the control of the stimuli with that of scan enable such that only scan chains that load constant values are kept in the shift mode during capture.
This is the principle behind the solution shown on the slide (note that the Test Mode input is set to 1 for the entire test). We assume that the same controller is used for constant stimuli and scan enable. If a scan chain loads a constant value, then its scan enable is asserted during the capture cycle, and thus the content of this scan chain will remain unchanged. As a result, low-toggling scan unload will follow. For a scan chain which must be loaded by the tester, the corresponding low power controller output is 1, allowing the input Scan Enable to take over.

## Slide 50: Biasing circuitry
0
D
SE
Scan enable
Test mode
Control register

SE
SE
…
Notes: The fraction of scan chains driven by the tester can be changed in the manner shown on the slide by adding a biasing circuitry, i.e., the group of AND gates driven by the XOR network. With these gates in place, the tester is capable of driving approximately 25% of scan chains. This percentage can be reduced even further by adding more inputs to the AND gates. For example, the third input reduces the percentage of scan chains driven by the decompressor down to 12.5%, while the fraction of scan chains getting the constant value of 0 increases accordingly.