## Slide 1: VLSI testing
HEP
LAB 1 ATPG and fault simulation (1)

## Slide 2: Exercise 1: Path sensitization
Find test pattern for f/1
a
NOT 1
AND 1
OR 1
b
c
d
f
e
g
h
i
z
NAND 1
NOR1

## Slide 3: Exercise 1: Path sensitization
Find test pattern for f/1
a
NOT 1
AND 1
OR 1
b
c
d
f
e
g
h
i
z
NAND 1
NOR1
0
D
1
D
1
0
1
1
1
X
1
1
X

## Slide 4: Test pattern data for f/1
ASCII_PATTERN_FILE_VERSION = 2;
SETUP =
declare input bus "PI" = "/a", "/b", "/c", "/d", "/e”;
declare output bus "PO" = "/z";
end;
SCAN_TEST =
pattern = 0;
force "PI" "11011" 0;
measure "PO" "1" 1;
end;
Test pattern description file for f/1: c1_pat_f1.ascii
Test pattern: abcde =11011
Expected response z = 1
Primary inputs designators
Primary output designator
Test pattern for f/1: abcde = 11011

## Slide 5: Fault simulation
$TESSENT_PATH/tessent -shell \
-dofile fault_sim.do \
-logfile fault_sim.log -replace
Fault simulation runfile: fault_sim.run
set_context patterns -scan
read_verilog c1.v
set_current_design c1
set_system_mode analysis
// run fault simulation for f/1
set_pattern_source external c1_pat_f1.ascii
add_faults –All
create_patterns
report_statistics
report_faults -class DS
reset state
// run fault simulation for the other faults
// ...
Fault simulation dofile: fault_sim.do

## Slide 6: Fault simulation report for f/1
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 40
------------------- --------------
UC (uncontrolled) 24 (60.00%)
DS (det_simulation) 16 (40.00%)
-------------------------------------
Coverage
-------------------
test_coverage 40.00%
fault_coverage 40.00%
atpg_effectiveness 40.00%
-------------------------------------
#test_patterns 1
#simulated_patterns 1
CPU_time (secs) 1.7
-------------------------------------
Statistics: fault_sim.log
// command: report_faults -class DS
type code pin_pathname
---- ------ ------------------------------------
1 DS /not1/OUT
0 EQ /not1/IN
0 EQ /b
1 EQ /and1/IN1
0 DS /d
0 EQ /or1/IN1
0 DS /z
0 EQ /nor1/OUT
1 EQ /nor1/IN0
1 EQ /nor1/IN1
1 EQ /and1/OUT
1 EQ /nand1/OUT
0 EQ /nand1/IN0
0 EQ /nand1/IN1
0 EQ /or1/OUT
0 EQ /e
Detected faults: fault_sim.log
f/1

## Slide 7: Exercise 1: Path sensitization
Find test pattern for h/1
a
NOT 1
AND 1
OR 1
b
c
d
f
e
g
h
i
z
NAND 1
NOR1

## Slide 8: Exercise 1: Path sensitization
Find test pattern for h/1
a
NOT 1
AND 1
OR 1
b
c
d
f
e
g
h
i
z
NAND 1
NOR1
0
0
1
D
0
D
0
1
1
0
0
0

## Slide 9: Test pattern data for h/1
ASCII_PATTERN_FILE_VERSION = 2;
SETUP =
declare input bus "PI" = "/a", "/b", "/c", "/d", "/e”;
declare output bus "PO" = "/z";
end;
SCAN_TEST =
pattern = 0;
force "PI” "01001" 0;
measure "PO” "0" 1;
end;
Test pattern description file for f/1: c1_pat_h1.ascii
Test pattern: abcde = 01001
Expected response z = 1
Primary inputs designators
Primary output designator
Test pattern for h/1: abcde = 01001

## Slide 10: Fault simulation report for h/1
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 40
------------------- --------------
UC (uncontrolled) 24 (60.00%)
UO (unobserved) 6 (15.00%)
DS (det_simulation) 10 (25.00%)
-------------------------------------
Coverage
-------------------
test_coverage 25.00%
fault_coverage 25.00%
atpg_effectiveness 25.00%
-------------------------------------
#test_patterns 1
#simulated_patterns 1
CPU_time (secs) 1.5
-------------------------------------
Statistics: fault_sim.log
// command: report_faults -class DS
type code pin_pathname
---- ------ ------------------------------------
1 DS /or1/OUT
1 EQ /or1/IN0
1 EQ /or1/IN1
1 EQ /c
1 EQ /d
1 EQ /nand1/IN0
0 DS /nand1/OUT
0 EQ /nor1/IN1
1 DS /z
1 EQ /nor1/OUT
Detected faults: fault_sim.log
h/1

## Slide 11: Test pattern generation
$TESSENT_PATH/tessent -shell \
-dofile atpg.do \
-logfile atpg.log -replace
ATPG runfile: atpg.run
set_context patterns -scan
read_verilog c1.v
set_current_design c1
set_system_mode analysis
add_faults –All
create_patterns
report_statistics
report_faults -class DS
exit -d
ATPG dofile: atpg.do

## Slide 12: Test pattern generation report
// command: report_statistics
Statistics Report
Stuck-at Faults
--------------------------------------
Fault Classes #faults
(total)
--------------------- ---------------
FU (full) 40
------------------- ---------------
DS (det_simulation) 40 (100.00%)
--------------------------------------
Coverage
-------------------
test_coverage 100.00%
fault_coverage 100.00%
atpg_effectiveness 100.00%
--------------------------------------
#test_patterns 7
#simulated_patterns 7
CPU_time (secs) 1.6
--------------------------------------
Statistics: atpg.log

## Slide 13: Exercise 2: Deductive fault simulation
AND1
NOR1
OR1
AND2
OR2
d
a
b
c
e
f
j
i
g
h
k
z
0
1
0
1
0
0
0
0
0
0
1
1
La = {a1}
Lb = {b0}
Lc = {c1}
Ld = {d0}
Le = {e1}
Lf = Lf - Lb U f1 = {a1, f1}
Lg = {c1, g1}
Lh = {c1, h1}
Li = Lc - Ld U i1 = {c1, i1}
Lj = Lf U Lg U j0 = {a1, c1, f1, g1, j0}
Lk = Li U Le U k1 = {c1, e1, i1, k1}
Lz = Lj - Lk U z0 = {a1, f1, g1, j0, z0}

## Slide 14: Test pattern data
ASCII_PATTERN_FILE_VERSION = 2;
SETUP =
declare input bus "PI" = "/a", "/b", "/c", "/d", "/e";
declare output bus "PO" = "/z";
end;
SCAN_TEST =
pattern = 0;
force "PI" "01010" 0;
measure "PO" "1" 1;
end;
Test pattern description file
Test pattern: abcde =01010
Expected response z = 1
Primary inputs designators
Primary output designator

## Slide 15: Fault simulation
$TESSENT_PATH/tessent -shell \
-dofile fault_sim.do \
-logfile fault_sim.log -replace
Fault simulation runfile: fault_sim.run
set_context patterns -scan
read_verilog c2.v
set_current_design c2
set_system_mode analysis
// run fault simulation
set_pattern_source external c2_01010_1.pat
add_faults –All
create_patterns
report_statistics
report_faults -class DS
reset_state
// run fault simulation for the other patterns
// ...
Fault simulation dofile: fault_sim.do

## Slide 16: Fault simulation report for test: 01010
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 42
------------------- --------------
UC (uncontrolled) 31 (73.81%)
UO (unobserved) 2 ( 4.76%)
DS (det_simulation) 9 (21.43%)
-------------------------------------
Coverage
-------------------
test_coverage 21.43%
fault_coverage 21.43%
atpg_effectiveness 21.43%
-------------------------------------
#test_patterns 1
#simulated_patterns 1
CPU_time (secs) 1.7
-------------------------------------
Statistics: fault_sim.log
// command: report_faults -class DS
type code pin_pathname
---- ------ ------------------------------------
1 DS /a
1 EQ /and1/IN0
0 DS /nor1/OUT
1 EQ /nor1/IN0
1 EQ /nor1/IN1
1 EQ /and1/OUT
0 EQ /or2/IN0
0 DS /z
0 EQ /or2/OUT
Detected faults: fault_sim.log
g/1
j/0
z/0
f/1
j/0
a/1

## Slide 17: VLSI testing
HEP
LAB 2 ATPG and fault simulation (2)

## Slide 18: Exercise 1: Test set minimization
a
b
c
d
e
f
g
h
i
z
AND 1
AND 2
OR 1
NOR 1

## Slide 19: Fault table for all stuck-at faults
 | Faults |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Tests | abcd | a/0 | a/1 | b/0 | b/1 | c/0 | c/1 | d/0 | d/1 | e/0 | e/1 | f/0 | f/1 | g/0 | g/1 | h/0 | h/1 | i/0 | i/1 | z/0 | z/1
 | 0000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0001 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0101 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1001 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1101 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 20: Fault simulation report for test: 0000
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 42
------------------- --------------
UC (uncontrolled) 31 (73.81%)
UO (unobserved) 2 ( 4.76%)
DS (det_simulation) 9 (21.43%)
-------------------------------------
Coverage
-------------------
test_coverage 21.43%
fault_coverage 21.43%
atpg_effectiveness 21.43%
-------------------------------------
#test_patterns 1
#simulated_patterns 1
CPU_time (secs) 1.7
-------------------------------------
Statistics: fault_sim.log
// command: report_faults -class DS
type code pin_pathname
---- ------ ------------------------------------
1 DS /a
1 EQ /and1/IN0
0 DS /nor1/OUT
1 EQ /nor1/IN0
1 EQ /nor1/IN1
1 EQ /and1/OUT
0 EQ /or2/IN0
0 DS /z
0 EQ /or2/OUT
Detected faults: fault_sim.log

## Slide 21: Fault table for all stuck-at faults
 | Faults |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Tests | abcd | a/0 | a/1 | b/0 | b/1 | c/0 | c/1 | d/0 | d/1 | e/0 | e/1 | f/0 | f/1 | g/0 | g/1 | h/0 | h/1 | i/0 | i/1 | z/0 | z/1
 | 0000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0001 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0101 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1001 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1101 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 22: Fault table for all stuck-at faults
 | Faults |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Tests | abcd | a/0 | a/1 | b/0 | b/1 | c/0 | c/1 | d/0 | d/1 | e/0 | e/1 | f/0 | f/1 | g/0 | g/1 | h/0 | h/1 | i/0 | i/1 | z/0 | z/1
 | 0000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0001 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0101 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1001 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1010 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1101 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 23: Fault equivalence classes
F1 = {a/0, d/1, e/1, g/1, h/0, i/0, z/0}
F2 = {a/1, f/1, h/1}
F3 = {b/0, c/0, e/0}
F4 = {b/1}
F5 = {c/1}
F6 = {d/0}
F7 = {f/0}, undetectable fault
F8 = {g/0}
F9 = {i/1}
F10 = {z/1}
Reduction = 10/20

## Slide 24: Reduced fault table
 | Faults |  |  |  |  |  |  |  |  |  | 
Tests | abcd | a/0 | a/1 | b/0 | b/1 | c/1 | d/0 | g/0 | i/1 | z/1 | 
 | 0000 |  |  |  |  |  |  |  |  |  | 
 | 0001 |  |  |  |  |  |  |  |  |  | 
 | 0010 |  |  |  |  |  |  |  |  |  | 
 | 0011 |  |  |  |  |  |  |  |  |  | 
 | 0100 |  |  |  |  |  |  |  |  |  | 
 | 0101 |  |  |  |  |  |  |  |  |  | 
 | 0110 |  |  |  |  |  |  |  |  |  | 
 | 0111 |  |  |  |  |  |  |  |  |  | 
 | 1000 |  |  |  |  |  |  |  |  |  | 
 | 1001 |  |  |  |  |  |  |  |  |  | 
 | 1010 |  |  |  |  |  |  |  |  |  | 
 | 1011 |  |  |  |  |  |  |  |  |  | 
 | 1100 |  |  |  |  |  |  |  |  |  | 
 | 1101 |  |  |  |  |  |  |  |  |  | 
 | 1110 |  |  |  |  |  |  |  |  |  | 
 | 1111 |  |  |  |  |  |  |  |  |  | 

## Slide 25: Reduced fault table
 | Faults |  |  |  |  |  |  |  |  |  | 
Tests | abcd | a/0 | a/1 | b/0 | b/1 | c/1 | d/0 | g/0 | i/1 | z/1 | 
 | 0000 |  |  |  |  |  |  |  |  |  | Selected
 | 0001 |  |  |  |  |  |  |  |  |  | 
 | 0010 |  |  |  |  |  |  |  |  |  | 
 | 0011 |  |  |  |  |  |  |  |  |  | 
 | 0100 |  |  |  |  |  |  |  |  |  | 
 | 0101 |  |  |  |  |  |  |  |  |  | 
 | 0110 |  |  |  |  |  |  |  |  |  | 
 | 0111 |  |  |  |  |  |  |  |  |  | 
 | 1000 |  |  |  |  |  |  |  |  |  | 
 | 1001 |  |  |  |  |  |  |  |  |  | Selected
 | 1010 |  |  |  |  |  |  |  |  |  | Essential
 | 1011 |  |  |  |  |  |  |  |  |  | 
 | 1100 |  |  |  |  |  |  |  |  |  | Essential
 | 1101 |  |  |  |  |  |  |  |  |  | 
 | 1110 |  |  |  |  |  |  |  |  |  | Essential
 | 1111 |  |  |  |  |  |  |  |  |  | 
The minimal test set:
0000
1001
1010
1100
1110
The minimum number of tests = 5

## Slide 26: VLSI testing
HEP
LAB 3 ATPG and fault simulation (3)

## Slide 27: Exercise 1: Removal of redundancy

## Slide 28: Simulation of redundant circuit

## Slide 29: ATPG report
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 56
------------------- --------------
DS (det_simulation) 45 (80.36%)
RE (redundant) 11 (19.64%)
-------------------------------------
Coverage
-------------------
test_coverage 100.00%
fault_coverage 80.36%
atpg_effectiveness 100.00%
-------------------------------------
#test_patterns 5
#simulated_patterns 6
CPU_time (secs) 1.5
-------------------------------------
Statistics
// command: report_faults -class RE
type code pin_pathname
---- ------ ------------------------------------
1 RE /NAND1/OUT
0 EQ /NAND1/IN0
0 EQ /NAND1/IN1
0 EQ /b
1 RE /b
1 EQ /NAND1/IN0
1 RE /NOT1/OUT
0 EQ /NOT1/IN
1 EQ /AND1/IN1
1 RE /NAND3/IN0
1 RE /NAND2/IN1
Redundant faults

## Slide 30: Redundant logic

## Slide 31: After modification

## Slide 32: Comparison of waveforms

## Slide 33: Exercise 2: Test point insertion

## Slide 34: ATPG report
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 56
------------------- --------------
DS (det_simulation) 45 (80.36%)
RE (redundant) 11 (19.64%)
-------------------------------------
Coverage
-------------------
test_coverage 100.00%
fault_coverage 80.36%
atpg_effectiveness 100.00%
-------------------------------------
#test_patterns 5
#simulated_patterns 6
CPU_time (secs) 1.2
-------------------------------------
Statistics
// command: report_faults -class RE
type code pin_pathname
---- ------ ------------------------------------
1 RE /NAND1/OUT
0 EQ /NAND1/IN0
0 EQ /NAND1/IN1
0 EQ /b
1 RE /b
1 EQ /NAND1/IN0
1 RE /NOT1/OUT
0 EQ /NOT1/IN
1 EQ /AND1/IN1
1 RE /NAND3/IN0
1 RE /NAND2/IN1
Redundant faults

## Slide 35: New observation point

## Slide 36: ATPG report
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 66
------------------- --------------
DS (det_simulation) 58 (87.88%)
RE (redundant) 8 (12.12%)
-------------------------------------
Coverage
-------------------
test_coverage 100.00%
fault_coverage 87.88%
atpg_effectiveness 100.00%
-------------------------------------
#test_patterns 6
#simulated_patterns 8
CPU_time (secs) 1.2
-------------------------------------
Statistics
// command: report_faults -class RE
type code pin_pathname
---- ------ ------------------------------------
1 RE /NAND1/OUT
0 EQ /NAND1/IN0
0 EQ /NAND1/IN1
0 EQ /b
1 RE /b
1 EQ /NAND1/IN0
1 RE /NAND3/IN0
1 RE /NAND2/IN1
Redundant faults

## Slide 37: New test points

## Slide 38: ATPG report
// command: report_statistics
Statistics Report
Stuck-at Faults
-------------------------------------
Fault Classes #faults
(total)
--------------------- --------------
FU (full) 80
------------------- --------------
DS (det_simulation) 79 (98.75%)
RE (redundant) 1 ( 1.25%)
-------------------------------------
Coverage
-------------------
test_coverage 100.00%
fault_coverage 98.75%
atpg_effectiveness 100.00%
-------------------------------------
#test_patterns 10
#simulated_patterns 10
CPU_time (secs) 1.2
-------------------------------------
Statistics
// command: report_faults -class RE
type code pin_pathname
---- ------ ------------------------------------
1 RE /NAND3/IN0
Redundant faults

## Slide 39: Circuit with test points

## Slide 40: ATPG report
// command: report_statistics
Statistics Report
Stuck-at Faults
--------------------------------------
Fault Classes #faults
(total)
--------------------- ---------------
FU (full) 94
------------------- ---------------
DS (det_simulation) 94 (100.00%)
--------------------------------------
Coverage
-------------------
test_coverage 100.00%
fault_coverage 100.00%
atpg_effectiveness 100.00%
--------------------------------------
#test_patterns 13
#simulated_patterns 13
CPU_time (secs) 1.2
--------------------------------------
Statistics
// command: report_faults -class RE
type code pin_pathname
---- ------ ------------------------------------
// Warning: No faults reported.
Redundant faults

## Slide 41: VLSI testing
HEP
LAB 4
Pseudorandom testing

## Slide 42: Fibonacci LFSR
d
c
b
a

## Slide 43: Fibonacci LFSR
0
0
0
1
d
c
b
a

## Slide 44: Fibonacci LFSR
0
1
0
0
1
1
0
1
0
1
1
1
1
0
0
0
0
1
0
0
1
1
0
1
0
1
1
1
1
0
0
0
0
1
0
0
1
1
0
1
0
1
1
1
1
1
0
0
0
1
0
0
1
1
0
1
0
1
1
0
d
c
b
a

## Slide 45: Galois LFSR
d
c
b
a

## Slide 46: Galois LFSR
0
0
0
1
d
c
b
a

## Slide 47: Galois LFSR
0
1
1
1
1
0
1
0
1
1
0
0
1
0
0
0
0
1
1
1
1
0
1
0
1
1
0
0
1
0
0
0
0
1
0
0
1
1
0
1
0
1
1
1
1
1
1
1
1
0
1
0
1
1
0
0
1
0
0
0
d
c
b
a
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14

## Slide 48: Exercise 2
Test pattern generator
CUT
c6288
32
1
.
.
.
2
Select a proper primitive polynomial from Appendix 3

## Slide 49: Fault coverage
# test patterns | # effective patterns | # detected faults | fault coverage
1 |  |  | 
10 |  |  | 
20 |  |  | 
30 |  |  | 
40 |  |  | 
50 |  |  | 
60 |  |  | 
70 |  |  | 
80 |  |  | 
90 |  |  | 
100 |  |  | 
1000 |  |  | 
10000 |  |  | 
100000 |  |  | 

## Slide 50: Fault coverage
egrep "test_patterns|simulated_patterns|fault_coverage" c6288.log
Use the following command to extract the required statistics:
fault_coverage 33.41%
#test_patterns 1
#simulated_patterns 1
fault_coverage 60.80%
#test_patterns 10
#simulated_patterns 10
fault_coverage 72.00%
#test_patterns 20
#simulated_patterns 20
fault_coverage 79.82%
#test_patterns 30
#simulated_patterns 30
fault_coverage 87.77%
#test_patterns 39
#simulated_patterns 40

## Slide 51: Fault coverage
# test vectors | fault coverage | # detected faults
1 | 33.41% | 4864
10 | 60.80% | 8853
20 | 72.00% | 10483
30 | 79.82% | 11622
40 | 87.77% | 12780
50 | 93.63% | 13632
60 | 97.31% | 14169
70 | 98.27% | 14308
80 | 98.98% | 14412
90 | 99.27% | 14454
100 | 99.29% | 14456

## Slide 52: VLSI testing
HEP
LAB 5
Design for testability (DFT)

## Slide 53: Exercise 1: Scan insertion flow

## Slide 54: Leonardo Spectrum – design synthesis
load_library ../libs/ami05_worst.syn
read ../netlists/RTL/package_g12.vhd
read ../netlists/RTL/proc_timer.vhd
read ../netlists/RTL/proc_mv_sec.vhd
read ../netlists/RTL/proc_mux_z8.vhd
read ../netlists/RTL/proc_col_sec.vhd
read ../netlists/RTL/proc_fcomp_sec.vhd
read ../netlists/RTL/proc_comb_sec.vhd
read ../netlists/RTL/proc_block_match.vhd
optimize
report_area -cell
apply_rename_rules -ruleset VERILOG
auto_write ../netlists/top.gate.v
Leonardo Spectrum dofile
$LEONARDO_SPECTRUM_PATH/spectrum -file spectrum.batch \
-logfile ../logs/0_spec_synth.log
Leonardo Spectrum run file

## Slide 55: Tessent Scan – scan chains insertion
read_cell_library ../libs/atpg.lib
// Go to DFT mode
set_context dft -scan
read_verilog ../netlists/top.gate.v
analyze_control_signals –auto
// Insert scan chains
set_system_mode analysis
insert_test_logic -number 100
report_scan_chains
// Write netlist and setup files for ATPG
write_design -output_file ../netlists/gate_scan.v -replace
write_atpg_setup ./atpg -replace -procfile
exit
Tessent Scan dofile
$TESSENT_PATH/tessent -shell \
-dofile dfta.do \
-log ../logs/dfta.log -replace
Tessent Scan run file

## Slide 56: Exercise 2: Test generation flow

## Slide 57: Tessent Scan – scan chains insertion
read_cell_library ../libs/atpg.lib
// Go to DFT mode
set_context dft -scan
read_verilog ../netlists/cpu.v
analyze_control_signals -auto
// Insert scan chains
set_system_mode analysis
insert_test_logic -scan on -number 4
report_scan_chains
report_scan_cells
// Write netlist and setup files for ATPG
write_design -output_file ../netlists/cpu_scan.v -replace
write_atpg_setup ../2_atpg/atpg_setup -replace
exit
Tessent Scan dofile
$TESSENT_PATH/tessent –shell \
-dofile insert_scan.do \
-logfile insert_scan.log -replace
Tessent Scan run file

## Slide 58: FastScan – test pattern generation
read_cell_library ../libs/atpg.lib
set_context patterns -scan
read_verilog ../netlists/cpu_scan.v
set_current_design cpu
// Read atpg setup
dofile atpg_setup.dofile
// Go to atpg mode
set_system_mode analysis
// Pattern generation, default is stuck-at
create_patterns
report_statistics
// Save parallel and serial verilog patterns for simulation
write_patterns ../3_vsim/pat_stuck_par.v –verilog \
-parallel -replace
write_patterns ../3_vsim/pat_stuck_ser.v –verilog \
-begin 0 -end 2 -serial -rep
exit
Tessent FastScan dofile
$TESSENT_PATH/tessent –shell
-dofile atpg.do
-logfile atpg.log -replace
Tessent FastScan run file

## Slide 59: VLSI testing
HEP
LAB 6
Built-in Self-Test (BIST)

## Slide 60: Exercise 1: BIST

## Slide 61: BIST
Fault-free circuit |  |  | Fault A/0 |  | Fault A/1 | 
LFSR | Circuit output | MISR | Circuit output | MISR | Circuit output | MISR
ABC | XYZ | ABC | XYZ | ABC | XYZ | ABC
001 |  | 000 |  | 000 |  | 000

## Slide 62: BIST
Fault-free circuit |  |  | Fault A/0 |  | Fault A/1 | 
LFSR | Circuit output | MISR | Circuit output | MISR | Circuit output | MISR
ABC | XYZ | ABC | XYZ | ABC | XYZ | ABC
001 |  | 000 |  | 000 |  | 000
010 |  |  |  |  |  | 
101 |  |  |  |  |  | 
011 |  |  |  |  |  | 
111 |  |  |  |  |  | 
110 |  |  |  |  |  | 
100 |  |  |  |  |  | 
001 |  |  |  |  |  | 

## Slide 63: BIST
Fault-free circuit |  |  | Fault A/0 |  | Fault A/1 | 
LFSR | Circuit output | MISR | Circuit output | MISR | Circuit output | MISR
ABC | XYZ | ABC | XYZ | ABC | XYZ | ABC
001 | 100 | 000 |  | 000 |  | 000
010 | 101 |  |  |  |  | 
101 | 010 |  |  |  |  | 
011 | 010 |  |  |  |  | 
111 | 111 |  |  |  |  | 
110 | 011 |  |  |  |  | 
100 | 101 |  |  |  |  | 
001 | 100 |  |  |  |  | 

## Slide 64: BIST
Fault-free circuit |  |  | Fault A/0 |  | Fault A/1 | 
LFSR | Circuit output | MISR | Circuit output | MISR | Circuit output | MISR
ABC | XYZ | ABC | XYZ | ABC | XYZ | ABC
001 | 100 | 000 |  | 000 |  | 000
010 | 101 | 001 |  |  |  | 
101 | 010 | 111 |  |  |  | 
011 | 010 | 100 |  |  |  | 
111 | 111 | 011 |  |  |  | 
110 | 011 | 000 |  |  |  | 
100 | 101 | 110 |  |  |  | 
001 | 100 | 001 |  |  |  | 
fault-free signature

## Slide 65: BIST
Fault-free circuit |  |  | Fault A/0 |  | Fault A/1 | 
LFSR | Circuit output | MISR | Circuit output | MISR | Circuit output | MISR
ABC | XYZ | ABC | XYZ | ABC | XYZ | ABC
001 | 100 | 000 | 000 | 000 |  | 000
010 | 101 | 001 | 101 | 000 |  | 
101 | 010 | 111 | 101 | 101 |  | 
011 | 010 | 100 | 101 | 110 |  | 
111 | 111 | 011 | 011 | 001 |  | 
110 | 011 | 000 | 011 | 100 |  | 
100 | 101 | 110 | 101 | 111 |  | 
001 | 100 | 001 | 000 | 011 |  | 
signature for fault A/0
fault-free signature

## Slide 66: BIST
Fault-free circuit |  |  | Fault A/0 |  | Fault A/1 | 
LFSR | Circuit output | MISR | Circuit output | MISR | Circuit output | MISR
ABC | XYZ | ABC | XYZ | ABC | XYZ | ABC
001 | 100 | 000 | 000 | 000 | 100 | 000
010 | 101 | 001 | 101 | 000 | 010 | 001
101 | 010 | 111 | 101 | 101 | 010 | 000
011 | 010 | 100 | 101 | 110 | 010 | 010
111 | 111 | 011 | 011 | 001 | 111 | 111
110 | 011 | 000 | 011 | 100 | 111 | 001
100 | 101 | 110 | 101 | 111 | 010 | 101
001 | 100 | 001 | 000 | 011 | 100 | 001
signature for fault A/1
aliasing – circuit with fault A/1 classified as fault-free
signature for fault A/0
fault-free signature

## Slide 67: VLSI testing
HEP
LAB 7
Test Compression

## Slide 68: Exercise 1: Test compression flow

## Slide 69: Leonardo Spectrum – design synthesis
load_library ../libs/ami05_worst.syn
read ../netlists/alu.v
read ../netlists/dram.v
read ../netlists/regs.v
read ../netlists/idec.v
read ../netlists/cpu.v
optimize
report_area -cell
report_delay
set vhdl_write_use_packages {library ieee,adk; \ use ieee.std_logic_1164.all; \
use adk.adk_components.all; }
apply_rename_rules -ruleset VHDL
apply_rename_rules -ruleset VERILOG
auto_write ../netlists/cpu_gate.v
Leonardo Spectrum dofile
$LEONARDO_SPECTRUM_PATH/spectrum -file spectrum.batch \
-logfile ../logs/0_spec_synth.log
Leonardo Spectrum run file

## Slide 70: Tessent Scan – scan insertion
read_cell_library ../libs/atpg.lib
// Go to DFT mode
set_context dft -scan
read_verilog ../netlists/cpu_gate.v
analyze_control_signals -auto
// Insert scan chains
set_system_mode analysis
// Insert scan and ensure dedicated scan output pins
insert_test_logic -scan on -number 20
report_scan_chains
// Write netlist and setup files for Tessent FastScan
// and TestKompress
write_design -output_file ../netlists/cpu_scan.v -replace
write_atpg_setup ../2_fs_pg/cpu_scan -replace
write_atpg_setup ../3_tk_edt/cpu_scan -replace
exit
Tessent Scan dofile
$TESSENT_PATH/tessent -shell \
-dofile insert_scan.do \
-logfile ../logs/1_insert_scan.log \ -replace
Tessent Scan run file

## Slide 71: TestKompress – test generation
read_cell_library ../libs/atpg.lib
set_context patterns -scan
read_verilog ../netlists/cpu_scan.v
set_current_design cpu
// Read atpg setup
dofile cpu_scan.dofile
// Go to atpg mode
set_system_mode analysis
// Pattern generation, default is stuck-at
create_patterns
report_statistics
exit -d
Tessent TestKompress dofile
$TESSENT_PATH/tessent -shell \
-dofile atpg.do \
-logfile ../logs/2_atpg.log \
-replace
Tessent TestKompress run file

## Slide 72: TestKompress – EDT logic
read_cell_library ../libs/atpg.lib
set_context dft -edt
read_verilog ../netlists/cpu_scan.v
set_current_design cpu
// Read atpg setup
dofile cpu_scan.dofile
//Settings for EDT
set_edt_options -input_channels 4 -output_channels 4
// Go to atpg mode
set_system_mode analysis
// Create Patterns as a sanity check to make sure that
// you are getting the same coverage as FastScan
create_patterns
// Save the EDT logic and write out the synthesis
// scripts.
write_edt_files ../5_tk_pg/cpu_edt -verilog -replace
exit -d
Tessent TestKompress dofile
$TESSENT_PATH/tessent –shell \
-dofile tk_logic.do \
-logfile ../logs/3_tk_logic.log \
-replace
Tessent TestKompress run file

## Slide 73: Leonardo Spectrum – test logic synthesis
load_library ../libs/ami05_worst.syn
read ../netlists/cpu_scan.v
read ../5_tk_pg/cpu_edt_edt.v
read ../5_tk_pg/cpu_edt_edt_top.v
optimize -ef remap -ta ami05_worst -macro -hier preserve
write ../netlists/cpu_top_gate.v
Leonardo Spectrum dofile
$TESSENT_PATH/spectrum \
-file spectrum.batch \
-logfile ../logs/4_spec_synth.log
Leonardo Spectrum run file

## Slide 74: TestKompress – test generation
read_cell_library ../libs/atpg.lib
set_context patterns -scan
set_edt on
read_verilog ../netlists/cpu_top_gate.v
set_current_design cpu_edt_top
// Define scan chains and control signals
// use file created by Tessent TestKompress during
// RTL generation
dofile ./cpu_edt_edt.dofile
set_system_mode analysis
report_edt_configuration
// Add faults only to the core
add_faults cpu_i
// Generate patterns
create_patterns
// Report statistics
report_scan_volume
// Save out pattern
write_patterns patterns_edt.ascii -ascii -replace
exit -discard
Tessent TestKompress dofile
$TESSENT_PATH/tessent -shell
-dofile tk_pg.do \
-logfile ../logs/5_tk_pg.log \
-replace
Tessent TestKompress run file

## Slide 75: VLSI testing
HEP
LAB 8 Fault diagnosis

## Slide 76: Exercise 1: Logic-level diagnosis
Generate test patterns for circuit c1

## Slide 77: Test pattern generation
set_context patterns -scan
read_verilog ./netlist/c1.v
read_cell_library ../libs/atpg.lib
set_current_design c1
// Go to atpg mode
set_system_mode analysis
set_fault_type stuck
create_patterns
report_faults -class FULL
write_patterns ./patt/pat_all.ascii -ascii -rep
write_flat_model ./netlist/c1.flat -rep
exit -d
Tessent FastScan dofile: fs1.do
$TESSENT_PATH/tessent -shell
-dofile fs1.do
-log ./logs/fs1.log
-replace
Tessent FastScan run file: fs1.run

## Slide 78: Fault equivalence classes
Analyze the fault report and divide the faults into classes
F1 = {a0}
F2 = {i1, a1, f1}
F3 = {b0}
F4 = {e0, b1, c1}
F5 = {c1}
F6 = {j1, g1, h1, d0}
F7 = {h0, d1}
F8 = {e1}
F9 = {k0, i0, j0}
F10 = {f0}
F11 = {g0}
F12 = {k1}
Fault list report
0 DS /a
0 EQ /OR1/IN0
1 DS /OR1/OUT
1 EQ /OR1/IN0
1 EQ /OR1/IN1
1 EQ /a
1 EQ /AND1/IN0
0 DS /b
0 EQ /NOR1/IN0
0 DS /NOR1/OUT
1 EQ /NOR1/IN0
1 EQ /NOR1/IN1
1 EQ /b
1 EQ /c
0 DS /c
0 EQ /NOR1/IN1
1 DS /OR2/OUT
1 EQ /OR2/IN1
1 EQ /OR2/IN0
1 EQ /NOT1/OUT
0 EQ /NOT1/IN
0 EQ /d
1 EQ /AND1/IN1
0 DS /NOT1/OUT
1 EQ /NOT1/IN
1 EQ /d
0 EQ /OR2/IN1
1 DS /NOR1/OUT
0 DS /k
0 EQ /AND1/OUT
0 EQ /AND1/IN0
0 EQ /AND1/IN1
0 EQ /OR1/OUT
0 EQ /OR2/OUT
0 DS /OR1/IN1
0 DS /OR2/IN0
1 DS /k
1 EQ /AND1/OUT
The first fault in a list represents its class

## Slide 79: Fault simulation
ASCII_PATTERN_FILE_VERSION = 2;
SETUP =
declare input bus "PI" = "/a", "/b", "/c", "/d";
declare output bus "PO" = "/k";
end;
SCAN_TEST =
pattern = 0;
force "PI" "1010" 0;
measure "PO" "1" 1;
end;
Single test pattern: ./patt/p1.ascii
Divide the test pattern set into 5 isolated patterns
ASCII_PATTERN_FILE_VERSION = 2;
SETUP =
declare input bus "PI" = "/a", "/b", "/c", "/d";
declare output bus "PO" = "/k";
end;
SCAN_TEST =
pattern = 0;
force "PI" "1011" 0;
measure "PO" "0" 1;
end;
Single test pattern: ./patt/p2.ascii

## Slide 80: Fault simulation
set_context patterns -scan
read_verilog ./netlist/c1.v
read_cell_library ../libs/atpg.lib
set_current_design c1
set_system_mode analysis
set_fault_type stuck // set stuck-at fault model
add_faults -all
// Fault simulation for pattern #1
set_pattern_source external ./patt/p1.ascii -ascii
simulate_patterns // run fault simulation
report_statistics > ./patt/p1.fa
report_faults -class detected >> ./patt/p1.fa
// Fault simulation for pattern #2
reset_state
add_fault -all
set_pattern_source external ./patt/p2.ascii -ascii
simulate_patterns
report_statistics > ./patt/p2.fa
report_faults -class detected >> ./patt/p2.fa
// fault simulation - the other test patterns…
Tessent FastScan dofile: fs2.do
$TESSENT_PATH/tessent -shell \
-dofile fs2.do \
-log ./logs/fs2.log -replace
Tessent FastScan run file: fs2.run

## Slide 81: Fault simulation
# | Test pattern (abcd) | List of detected faults
1 | 1010 | a0 h0 k0
2 | 1011 | c0 e1 j1 k1
3 | 1101 | b0 e1 j1 k1
4 | 0110 | e1 i1 k1
5 | 0001 | e0 f0 g0 k0
Fault list report for test: 1001
0 DS /NOR1/OUT
1 EQ /NOR1/IN0
1 EQ /NOR1/IN1
1 EQ /b
1 EQ /c
0 DS /k
0 EQ /AND1/OUT
0 EQ /AND1/IN0
0 EQ /AND1/IN1
0 EQ /OR1/OUT
0 EQ /OR2/OUT
0 DS /OR2/IN0
F1001 = {e0, g0, k0}
Analyze the fault report and part the faults into classes

## Slide 82: Diagnostic tree

## Slide 83: Case study
# | Test pattern (abcd) | List of detected faults | Circuit under test | 
 |  |  | l | ll
1 | 1010 | a0 h0 k0 |  | 
2 | 1011 | c0 e1 j1 k1 |  | 
3 | 1101 | b0 e1 j1 k1 |  | 
4 | 0110 | e1 i1 k1 |  | 
5 | 0001 | e0 f0 g0 k0 |  | 
Diagnosed faults |  |  |  | 
Analyze the test responses and determine failures

## Slide 84: Diagnostic tree - circuit I

## Slide 85: Case study
# | Test pattern (abcd) | List of detected faults | Circuit under test | 
 |  |  | l | ll
1 | 1010 | a0 h0 k0 |  | 
2 | 1011 | c0 e1 j1 k1 |  | 
3 | 1101 | b0 e1 j1 k1 |  | 
4 | 0110 | e1 i1 k1 |  | 
5 | 0001 | e0 f0 g0 k0 |  | 
Diagnosed faults |  |  | e0 v f0 v g0 | 
Analyze the test responses and determine failures

## Slide 86: Diagnostic tree – circuit II

## Slide 87: Case study
# | Test pattern (abcd) | List of detected faults | Circuit under test | 
 |  |  | l | ll
1 | 1010 | a0 h0 k0 |  | 
2 | 1011 | c0 e1 j1 k1 |  | 
3 | 1101 | b0 e1 j1 k1 |  | 
4 | 0110 | e1 i1 k1 |  | 
5 | 0001 | e0 f0 g0 k0 |  | 
Diagnosed faults |  |  | e0 v f0 v g0 | k0
Analyze the test responses and determine failures

## Slide 88: Improving the fault resolution
Generate tests to distinguish among faults: e0 f0 g0
NOR1
e
OR1
a
b
d
AND1
i
j
k
NOT1
OR2
c
d
f
g
h
Consider 2 tests: 1001 and 0000
Save isolated test patterns and perform fault simulation

## Slide 89: Fault simulation
set_context patterns -scan
read_verilog ./netlist/c1.v
read_cell_library ../libs/atpg.lib
set_current_design c1
set_system_mode analysis
set_fault_type stuck // set stuck-at fault model
add_fault -all
set_pattern_source external ./patt/p6_e0f0_g0.ascii -ascii
Run // run fault simulation
report_statistics > ./patt/p6_e0f0_g0.fa
report_faults -class detected >> ./patt/p6_e0f0_g0.fa
reset_state
set_pattern_source external ./patt/p6_e0g0_f0.ascii -ascii
Run // run fault simulation
report_statistics > ./patt/p6_e0g0_f0.fa
report_faults -class detected >> ./patt/p6_e0g0_f0.fa
exit -d
Tessent FastScan dofile: fs3.do
$TESSENT_PATH/tessent -shell \
-dofile fs3.do \
-log ./logs/fs3.log –replace
Tessent FastScan run file: fs3.run

## Slide 90: Improving the fault resolution
Fault list report for test: 1001
0 DS /NOR1/OUT
1 EQ /NOR1/IN0
1 EQ /NOR1/IN1
1 EQ /b
1 EQ /c
0 DS /k
0 EQ /AND1/OUT
0 EQ /AND1/IN0
0 EQ /AND1/IN1
0 EQ /OR1/OUT
0 EQ /OR2/OUT
0 DS /OR2/IN0
Fault list report for test: 0000
0 DS /NOR1/OUT
1 EQ /NOR1/IN0
1 EQ /NOR1/IN1
1 EQ /b
1 EQ /c
0 DS /k
0 EQ /AND1/OUT
0 EQ /AND1/IN0
0 EQ /AND1/IN1
0 EQ /OR1/OUT
0 EQ /OR2/OUT
0 DS /OR1/IN1
F1001 = {e0, g0, k0}
F0000 = {e0, f0, k0}

## Slide 91: Enhanced diagnostic tree
Φ e0 f0 g0
e0 f0 g0
Φ
e0 g0
f0
e0
g0
Test vectors 1001 and 0000 distinguish three faults and allow explicit location of their source
Test 5: 0001
Test 6: 1001
Test 7: 0000

## Slide 92: VLSI testing
HEP
LAB 9
Iterative Diagnosis

## Slide 93: Iterative pattern generation
Invoke Tessent Diagnosis with the failure file from one device
set_context patterns -scan_diagnosis
read_flat_model netlist/tk_design.flat
set_diagnosis_options -bridge OFF -cell OFF
set_pattern_source external ./patt/pat.wgl -wgl
// run diagnosis
diagnose_failures fail1.log -output fail1.txt -rep
// create additional internal patterns
create_diagnosis_patterns -diagnosis_report fail1.txt
// save additional patterns
write_patterns ./patt/patt_iter.wgl -wgl -rep
exit -d
Diagnosis dofile: 1_iterative.dofile
$TESSENT_PATH/tessent -shell
-dofile 1_iterative.dofile
-log ./logs/1_iterative.log -rep
Diagnosis run file: 1_iterative.run

## Slide 94: Iterative pattern generation
Analyze the diagnosis report
#symptoms=2 #suspects=13 CPU_time=0.22sec fail_log=fail1.log
#failing_patterns=41, #passing_patterns=450
#unexplained_failing_patterns=19
4 37 57 65 86 103 110 116 187 196
208 268 271 274 275 305 310 315 336
symptom=1 #suspects=1 #explained_patterns=20
0 59 95 105 169 180 191 192 200 224
226 232 265 266 344 372 420 429 434 487
suspect score fail_match pass_mismatch type value pin_pathname cell_name net_pathname
-------------------------------------------------------------------------------------------------
1 96 20 0 OPEN/DOM both /DESTIN_DO[4] primary_output /DESTIN_DO[4]
-------------------------------------------------------------------------------------------------
symptom=2 #suspects=12 #explained_patterns=2
66 81
suspect score fail_match pass_mismatch type value pin_pathname cell_name net_pathname
-------------------------------------------------------------------------------------------------
1 91 2 0 STUCK 0 /cpu_i/uSDM/ix3179/Y nor03 /cpu_i/uSDM/nx3178
2 91 2 0 EQ1 1 /cpu_i/uSDM/ix3179/A0 nor03 /cpu_i/uSDM/nx2130
3 91 2 0 EQ1 1 /cpu_i/uSDM/ix3179/A1 nor03 /cpu_i/uSDM/nx2133
4 91 2 0 EQ1 1 /cpu_i/uSDM/ix3179/A2 nor03 /cpu_i/uSDM/nx2136
5 91 2 0 EQ1 1 /cpu_i/uSDM/ix746_ix17/Y aoi221 /cpu_i/uSDM/nx2130
6 91 2 0 EQ1 1 /cpu_i/uSDM/ix746_ix23/Y nor03 /cpu_i/uSDM/nx2133
7 91 2 0 EQ1 1 /cpu_i/uSDM/ix746_ix29/Y nor03 /cpu_i/uSDM/nx2136
8 91 2 0 EQ1 0 /cpu_i/uSDM/ix3171/A1 nor02_2x /cpu_i/uSDM/nx3178
9 91 2 0 STUCK 1 /cpu_i/uSDM/ix3171/Y nor02_2x /cpu_i/uSDM/nx3170
10 91 2 0 EQ9 1 /cpu_i/uSDM/ix625_ix13/A0 nand03 /cpu_i/uSDM/nx3170
11 91 2 0 STUCK 0 /cpu_i/uALU/modgen_or_2_ix11/B1 aoi221 /cpu_i/OPERAND_B_4
12 91 2 0 EQ11 0 /cpu_i/uALU/modgen_or_2_ix11/B0 aoi221 /cpu_i/uALU/nx2685
-------------------------------------------------------------------------------------------------
Diagnosis report: 1_iterative.log
This failure has 2 symptoms and 13 suspects.
The first symptom is a failure on the primary output and it is clear that the failure is isolated.
Symptom number 2 has several suspects that have the same score. However, this failure has only 2 explained patterns so the resolution is limited. In this case it is good candidate for iterative diagnostics.

## Slide 95: Emulation of the failure
Invoke Tessent Diagnosis with the following dofile which will emulate the failure and run the newly created iterative patterns
set_context patterns -scan_diagnosis
read_flat_model ./netlist/tk_design.flat
set_diagnosis -bridge OFF -cell OFF
set_pattern_source external ./patt/pat_iter.wgl –wgl
// emulate the failure
write_failures ./fail2_iter.log -rep -cycle \ /cpu_i/uSDM/ix3171/Y -stuck 1
exit -d
Diagnosis dofile: 2_defect.dofile
$TESSENT_TREE/bin/tessent \
-shell \
-dofile 2_defect.dofile \
-log ./logs/2_defect.log -rep
Diagnosis run file: 2_defect.run
This command emulates the failure and produces a new failure file

## Slide 96: Diagnosis performance
Invoke Tessent Diagnosis with both created pattern sets and failure files
set_context patterns -scan_diagnosis
read_flat_model netlist/tk_design.flat
set_diagnosis -bridge OFF -cell OFF
// read pattern files
set_pattern_source external ./patt/pat.wgl -wgl
set_pattern_source external ./patt/patt_iter.wgl -wgl -append
// read failure files
read_failure ./fail1.log
read_failure ./fail2_iter.log -append
// perform the diagnosis
diagnose_failures -internal
exit -d
Diagnosis dofile: 3_eval.dofile
$TESSENT_PATH/tessent -shell
-dofile 3_eval.dofile
-log ./logs/3_eval.log -rep
Diagnosis run file: 3_eval.run

## Slide 97: Diagnosis performance
Analyze the diagnosis report
symptom=2 #suspects=6 #explained_patterns=34
66 81 498 504 516 530 537 547 553 561
562 577 579 584 589 592 597 600 602 610
616 634 635 641 666 676 680 686 697 708
710 725 727 736
suspect score fail_match pass_mismatch type value pin_pathname cell_name net_pathname
-------------------------------------------------------------------------------------------------
1 94 34 0 STUCK 1 /cpu_i/uSDM/ix3171/Y nor02_2x /cpu_i/uSDM/nx3170
2 94 34 0 EQ1 1 /cpu_i/uSDM/ix625_ix13/A0 nand03 /cpu_i/uSDM/nx3170
3 60 34 57 INDETERMINATE 0 /cpu_i/uSDM/ix625_ix13/Y nand03 /cpu_i/SFR_DATA_4
4 60 34 57 EQ3 0 /cpu_i/uAOM/ix552/A1 mux21_ni /cpu_i/SFR_DATA_4
5 53 34 98 INDETERMINATE 0 /cpu_i/uAOM/ix135_ix3/B1 ao22 /cpu_i/uAOM/nx551
6 53 34 98 EQ5 0 /cpu_i/uAOM/ix135_ix3/B0 ao22 /cpu_i/nx1277
-------------------------------------------------------------------------------------------------
Diagnosis report: 1_iterative.log
After the iterative diagnosis only 6 suspects were reported for the symptom number 2

## Slide 98: VLSI testing
HEP
LAB 10 Memory built-in self-test

## Slide 99: Memory BIST architecture

## Slide 100: Data backgrounds for word memories
Use the programmable controller to generate multiple data backgrounds to detect all coupling faults between neighboring cells of the same word
Use the following data backgrounds:
0
1
0
1
0
1
0
1
D0
D1
D2
D3
D4
D5
D6
D7
B1
1
0
1
0
1
0
1
0
D0
D1
D2
D3
D4
D5
D6
D7
B2
Algorithm | 
# | Instruction
1 | ↑(wB1)
2 | ↓(rB1wB2)
3 | ↑(rB2)

## Slide 101: User-defined algorithm
Algorithm syntax
Algorithm (<AlgorithmName>) {
TestRegisterSetup {
AddressGenerator {
…
}
DataGenerator {
…
}
}
MicroProgram {
Instruction (<InstructionName 1>) {
…
}
Instruction (<InstructionName 2>) {
…
}
…
}
}
Modify the algorithm in the file to detect all possible coupling faults between neighboring cells in the word oriented memory
Each Instruction wrapper
represents one micro code
word

## Slide 102: User-defined algorithm
Address generator
AddressGenerator {
AddressRegister (A) {
LoadColumnAddress : 4'b0000;
LoadRowAddress : 4'b0000;
NumberY0Bits : 0;
NumberX0Bits : 0;
X1CarryIn : Y1CarryOut;
Y1CarryIn : none;
}
}
Data generator
DataGenerator {
LoadWriteData : 8'b01010101;
LoadExpectData : 8'b01010101;
}

## Slide 103: User-defined algorithm
Instruction 1: ↑(wB1)
Instruction (Instr_1) {
OperationSelect : Write;
AddressSelectCmd : Select_A;
X1AddressCmd : Increment;
Y1AddressCmd : Increment;
WriteDataCmd : DataReg;
NextConditions {
X1_EndCount : On;
Y1_EndCount : On;
}
}

## Slide 104: User-defined algorithm
Instruction 2: ↓(rB1wB2)
Instruction (Instr_2) {
OperationSelect : Read;
AddressSelectCmd : Select_A;
X1AddressCmd : Decrement;
Y1AddressCmd : Decrement;
ExpectDataCmd : DataReg;
InhibitLastAddressCount : On;
NextConditions {
X1_EndCount : On;
Y1_EndCount : On;
}
}

## Slide 105: User-defined algorithm
Instruction 3: ↑(rB2)
Instruction (Instr_3) {
OperationSelect : Read;
AddressSelectCmd : Select_A;
X1AddressCmd : Increment;
Y1AddressCmd : Increment;
ExpectDataCmd : DataReg;
InhibitLastAddressCount : On;
NextConditions {
X1_EndCount : On;
Y1_EndCount : On;
}
}

## Slide 106: Algorithm verification
Algorithm can be verified by dumping simulation data around the area of the fault-injected memory and the memory BIST controller
Invoke ModelSim algorithm simulation (makealg file) and analyze report to examine the number of compare failures.
Simulation Results Summary
--------------------------
Log File: ./outDir_etv/verilog.log_tapbistv
Date = Dec 15 11:21
# Number of Z Compare Events = 17
# Number of 1/0 Compare Events = 227
# Number of Compare Failures = 0
Log File: ./outDir_etv/verilog.log_membistpv_P1_top
Date = Dec 15 11:21
# Number of Z Compare Events = 0
# Number of 1/0 Compare Events = 37
# Number of Compare Failures = 2
Simulation report
The injected fault was correctly detected because there were 2 compare failures